Draft ETSI EN 303 215-5-1 V0.0.18 (2016-10)

Advanced Surface Movement Guidance and Control System (A-SMGCS);

Part 5: Harmonized Standard covering the essential requirements

of article 3.2 of the Directive 2014/53/EU

Sub-part 1: receivers and interrogators for

multilateration equipment in A-SMGCS

HARMONIZED EUROPEAN STANDARD

Reference

DEN/ERM-JTFEA-21

Keywords

Aeronautical, ATM, RED, Regulation, Multilateration, A-SMGCS

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-préfecture de Grasse (06) N° 7803/88

Important notice

The present document can be downloaded from:
http://www.etsi.org

The present document may be made available in electronic versions and/or in print. The content of any electronic and/or print versions of the present document shall not be modified without the prior written authorization of ETSI. In case of any existing or perceived difference in contents between such versions and/or in print, the only prevailing document is the print of the Portable Document Format (PDF) version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm except as authorized by written permission of ETSI.

The content of the PDF version shall not be modified without the written authorization of ETSI.

The copyright and the foregoing restriction extend to reproduction in all media.

Reproduction is only permitted for the purpose of standardization work undertaken within ETSI.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2015.

All rights reserved.
DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# Contents

Contents	3

Intellectual Property Rights	6

Foreword	6

Modal verbs terminology	7

Executive summary	7

Introduction	7

1.	Scope	8

2.	References	8

2.1.1.1	Normative references	8

2.1.1.2	Informative references	8

3.	Definitions, symbols and abbreviations	9

3.1.1.1	Definitions	9

3.1.1.2	Symbols	10

3.1.1.3	Abbreviations	11

4.	Technical requirements specifications	11

4.1	Applicability	11

4.1.1	Equipment with multiple functions	11

4.1.2	Equipment with integral antenna	11

4.1.3	Environmental profile	12

4.1.4	Conformance requirements	12

4.2	Transmitter requirements	12

4.2.1	Operating frequency	12

4.2.1.1	Description	12

4.2.1.2	Limits	12

4.2.1.3	Conformance	12

4.2.2	Frequency error	12

4.2.2.1	Description	12

4.2.2.2	Limits	12

4.2.2.3	Conformance	12

4.2.3	Transmitter Power	12

4.2.3.1	Description	12

4.2.3.2	Limits	13

4.2.3.3	Conformance	13

4.2.4	Spectrum mask	13

4.2.4.1	Description	13

4.2.4.2	Limits	15

4.2.4.3	Conformance	15

4.2.5	Inter-modulation attenuation	15

4.2.5.1	Description	15

4.2.5.2	Limits	15

4.2.5.3	Conformance	15

4.2.6	Transmitter Duty Cycle	15

4.2.6.1	Description	15

4.2.6.2	Limits	15

4.2.6.3	Conformance	15

4.2.7	Residual Power Output	15

4.2.7.1	Description	15

4.2.7.2	Limits	16

4.2.7.3	Conformance	16

4.3	Receiver requirements	16

4.3.1	Operating Frequency	16

4.3.1.1	Description	16

4.3.1.2	Limits	16

4.3.1.3	Conformance	16

4.3.2	Adjacent channel selectivity and Spurious responses	16

4.3.2.1	Description	16

4.3.2.2	Limits	16

4.3.2.3	Conformance	17

4.3.3	Inter-modulation response rejection	17

4.3.3.1	Description	17

4.3.3.2	Limits	17

4.3.3.3	Conformance	17

4.3.4	Co-channel rejection	17

4.3.4.1	Description	17

4.3.4.2	Limits	17

4.3.4.3	Conformance	17

4.3.5	Blocking	18

4.3.5.1	Description	18

4.3.5.2	Limits	18

4.3.5.3	Conformance	18

4.3.6	Receiver dynamic range / Maximum usable sensitivity	18

4.3.6.1	Description	18

4.3.6.2	Limits	18

4.3.6.3	Conformance	18

4.3.7	Spurious emissions	18

4.3.7.1	Description	18

4.3.7.2	Limits	18

4.3.7.3	Conformance	18

5.	Testing for compliance with technical requirements	19

5.1	Environmental conditions for testing	19

5.2	Interpretation of the measurement results	19

5.3	Test and General Conditions	20

5.3.1	Transmitter test signals	20

5.3.2	Simulated received signals	21

5.4	Transmitter Tests	22

5.4.1	Spectrum Test	22

5.4.1.1	Description	23

5.4.1.2	Test conditions	23

5.4.1.3	Method of measurement	23

5.4.1.4	Measurement procedure	23

5.4.2	Transmitter Power / Transmitter Duty Cycle	24

5.4.2.1	Description	24

5.4.2.2	Test conditions	24

5.4.2.3	Method of measurement	24

5.4.2.4	Measurement procedure	24

5.4.3	Inter-modulation attenuation	25

5.4.3.1	Description	25

5.4.3.2	Test conditions	25

5.4.3.3	Method of measurement	26

5.4.3.4	Measurement procedure	26

5.4.4	Residual Power Output	27

5.4.4.1	Description	27

5.4.4.2	Test conditions	27

5.4.4.3	Method of measurement	27

5.4.4.4	Measurement procedure	27

5.5	Receiver requirements	28

5.5.1	Operating Frequency and Receiver dynamic range (Maximum usable) sensitivity	28

5.5.1.1	Description	28

5.5.1.2	Test conditions	28

5.5.1.3	Method of measurement	28

5.5.1.4	Measurement procedure	28

5.5.2	Adjacent channel selectivity and Spurious responses	29

5.5.2.1	Description	29

5.5.2.2	Test conditions	29

5.5.2.3	Method of measurement	29

5.5.2.4	Measurement procedure	30

5.6.3	Inter-modulation response rejection (for 4.3.3)	30

5.6.3.1	Description	30

5.6.3.2	Test conditions	30

5.6.3.3	Method of measurement	30

5.6.3.4	Measurement procedure	31

5.6.4	Co-channel rejection (for 4.3.4)	32

5.6.4.1	Description	32

5.6.4.2	Test conditions	32

5.6.4.3	Method of measurement	32

5.6.4.4	Measurement procedure	32

5.6.5	Blocking (for 4.3.5)	33

5.6.5.1	Description	33

5.6.5.2	Test conditions	33

5.6.5.3	Method of measurement	33

5.6.5.4	Measurement procedure	33

5.6.6	Spurious emissions (for 4.3.7)	34

5.6.6.1	Description	34

5.6.6.2	Test conditions	34

5.6.6.3	Method of measurement	34

5.6.6.4	Measurement procedure	34

Annex A (informative): Relationship between the present document and the essential requirements of Directive 2014/53/EU	36

Annex B (informative): Bibliography	37

Annex C (informative): Change History	38

History	39

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This draft Harmonized European Standard (EN) has been produced by ETSI Specialist Task Force 485 under ETSI Technical Committee Electromagnetic compatibility and Radio spectrum Matters (ERM) and is now submitted for the combined Public Enquiry and Vote phase of the ETSI standards EN Approval Procedure.

The present document is intended to become a Harmonized Standard, referencing the Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC ("the RE Directive") [i.1].

The requirements relevant to Directive 2014/53/EU [i.1] are summarised in annex A.

NOTE:	Other requirements and other EU Regulations and/or Directives may be applicable to the product(s) falling within the scope of the present document.

The present document is part 5, sub-part 1, of a multi-part deliverable covering Advanced Surface Movement Guidance and Control System (A-SMGCS), as identified below:

Part 1:	"Community Specification for application under the Single European Sky Interoperability Regulation EC 552/2004 for A-SMGCS Level 1 including external interfaces";

Part 2:	"Community Specification for application under the Single European Sky Interoperability Regulation EC 552/2004 for A-SMGCS Level 2 including external interfaces";

Part 3:	"Community Specification for application under the Single European Sky Interoperability Regulation EC 552/2004 for a deployed cooperative sensor including its interfaces";

Part 4: 	"Community Specification for application under the Single European Sky Interoperability Regulation EC 552/2004 for a deployed non-cooperative sensor including its interfaces";

Part 5:	"Harmonized EN covering the essential requirements of article 3.2 of the RE Directive for multilateration equipment";

Sub-part 1:	"Receivers and Interrogators";

Sub-part 2:	"Reference and Vehicle Transmitters";

Part 6:	"Harmonized EN covering the essential requirements of article 3.2 of the RE Directive for deployed surface movement radar sensors".

| Proposed national transposition dates |
| --- |
| Date of latest announcement of this EN (doa): | 3 months after ETSI publication |
| Date of latest publication of new National Standard or endorsement of this EN (dop/e): | 6 months after doa |
| Date of withdrawal of any conflicting National Standard (dow): | 18 months after doa |

# Modal verbs terminology

In the present document "shall", "shall not", "should", "should not", "may", "may not", "need", "need not", "will", "will not", "can" and "cannot" are to be interpreted as described in clause 3.2 of the ETSI Drafting Rules (Verbal forms for the expression of provisions).

"must" and "must not" are NOT allowed in ETSI deliverables except when used in direct citation.

# Executive summary

The present document covers the essential requirements for efficient use of radio spectrum of multilateration sensors in the 1030 MHz and 1090 MHz bands used for Advanced-Surface Movement Guidance and Control Systems.

# Introduction

The present document is part of a set of standards developed by ETSI and is designed to fit in a modular structure to cover all radio and telecommunications terminal equipment within the scope of the RE Directive [i.1].

The present document states the minimum performance requirements for receivers and interrogators used in multilateration equipment in an Advance Surface Movement Guidance and Control System (A-SMGCS) necessary for a harmonised standard covering the RE Directive [i.1].

The present document may be used for the conformity assessment of the performance of the equipment.

# Scope

The present document applies to the following equipment types:

Interrogators transmitting in the 1030 MHz band, used in multilateration equipment in an Advanced Surface Movement Guidance and Control System (A-SMGCS);

Receivers, receiving in the 1090 MHz band, used in multilateration equipment in an Advanced Surface Movement Guidance and Control System (A-SMGCS);

The present document does not apply to equipment which includes a transponder function.

NOTE:  EN 303 213-5-2 covers transponder equipment.

The present document states the essential requirements of a harmonized standard for receivers and interrogators used in multilateration equipment in an Advanced Surface Movement Guidance and Control System (A-SMGCS).

This harmonized standard is intended to cover the provisions of Directive 2014/53/EU [i.1], article 3.2, which states that "... radio equipment shall be so constructed that it both effectively uses and supports the efficient use of radio spectrum in order to avoid harmful interference.“

In addition to the present document, other ENs that specify technical requirements in respect of essential requirements under other parts of article 3 of the RE Directive [i.1] as well as essential requirements under the Single European Sky Interoperability Regulation (as amended) [i.2] and related implementing rules may apply to equipment within the scope of the present document.

Antennas for this equipment are considered to be passive without additional amplifier.

# References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC ("the RE Directive")

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication, ETSI cannot guarantee their long term validity.

#### Normative references

The following referenced documents are necessary for the application of the present document.

[1]	ICAO Annex 10, Volume IV, ”Surveillance and Collision Avoidance systems“, 5th edition, July 2014, including amendments up to amendment 89.

[2]	EUROCAE ED-117A (September 2016): "MOPS for Mode S Multilateration Systems for Use in A-SMGCS".

[3]	to be continued.

#### Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC.

[i.2]	Regulation (EC) 552/2004 of the European Parliament and Council of 10 March 2004 on the interoperability of the European Air Traffic Management network (the interoperability Regulation). Official Journal L 096, 31/03/2004 P. 0026 - 0042.

[i.3]	ETSI EG 201 399: "Electromagnetic compatibility and Radio spectrum Matters (ERM); A guide to the production of candidate Harmonized Standards for application under the RE Directive".

[i.4]	ECC/Recommendation (02)05 (2012): "Unwanted emissions".

[i.5]	ERC/Recommendation 74-01 (2011): "Unwanted emissions in spurious domain".

[i.6]	ITU Recommendation M.1177-4 (2011): "Techniques for measurement of unwanted emissions of radar equipment".

[i.7]	ITU-R Recommendation SM.329-12 (2012): “Unwanted emissions in the spurious domain”.

NOTE: 	More stringent requirements envisioned for future versions of ITU-R Recommendations, ECC/Recommendations and ERC Recommendations may need to be considered in a future version of the present document.

[i.8]	Directive 98/34/EC of the European Parliament and of the Council of 22 June 1998 laying down a procedure for the provision of information in the field of technical standards and regulations and of rules on Information Society services as amended by Directive 98/48/EC of the European Parliament and of the Council of 20 July 1998 and by Council Directive 2006/96/EC of 20 November 2006.

[i.9]	ITU Recommendation ITU-R SM.1541-5 (08/2013) “Unwanted emissions in the out-of-band domain”

[i.11]	ETSI TR 100 028(V1.4.1): "Electromagnetic compatibility and Radio spectrum Matters (ERM); Uncertainties in the measurement of mobile radio equipment characteristics".

[i.12]	EUROCAE ED-73E (2011): "MOPS for Secondary Surveillance Radar Mode S Transponders".

# Definitions, symbols and abbreviations

#### Definitions

For the purposes of the present document, the terms and definitions given in the RE Directive [i.1] apply:

advanced surface movement guidance and control system (A-SMGCS): a system providing routing, guidance, surveillance and control to aircraft and effected vehicles in order to maintain movement rate under all local weather conditions within the aerodrome visibility operational level (AVOL) whilst maintaining the required level of safety.

conducted measurements: measurements which are made using a wired connection to the EUT

conducted spurious emissions: Conducted spurious emissions are RF emissions appearing at the RF output port on a frequency or frequencies which are outside the necessary bandwidth and the level of which may be reduced without affecting the corresponding transmission of information. Conducted spurious emissions include harmonic emissions, parasitic emissions, intermodulation products and frequency conversion products, but exclude out of band emissions.

duty cycle: the fraction of time that the interrogator is transmitting to the total time. Due to the nature of the interrogation messages (combination of pulse-position and phase modulation), the entire time of transmission from rise of the first interrogation pulse (P1) to the decay of the last interrogation pulse (P4 or P6) of one message is considered to be active transmission time.

This is defn used elsewhere:

duty cycle (DC): ratio expressed as a percentage, of the cumulative duration of transmissions Ton_cum within an observation interval Tobs.  on an observation bandwidth Fobs

environmental profile: range of environmental conditions under which the EUT is declared by the manufacturer to comply with the provisions of this document

ground based multilateration equipment or ground station: aeronautical station equipment intended for use in an A-SMGCS multilateration component.

NOTE: A ground station can include sensor, interrogator and/or transponder components. A ground station can be fixed or mobile.

inactive state: the entire period between transmissions, less 10 μs transition periods preceding and following the transmission.

integral antenna: an antenna which is integrated into the EUT without the use of an external connector, and which is considered to be part of the EUT.

interrogator: aeronautical station equipment including at least one transmitter designed to produce aeronautical mobile service signals at 1030 MHz.

multilateration: surveillance technique which provides position derived from the secondary surveillance radar (SSR) transponder signals (replies or squitters) primarily using time difference of arrival (TDOA) techniques.

NOTE: Additional information, including identification, can be extracted from the received signals.

out of band emissions: power transmitted at frequencies outside the bandwidth of the transmitter but within the specified spectral mask

radiated measurements: measurements which involve the measurement of a radiated field in the vicinity of the EUT

receiver: a EUT which includes the capability to convert RF signals into binary content.

reference bandwidth: The bandwidth required for uniquely defining the OoB domain emission limits.

resolution bandwidth: bandwidth that is used for measurements used for spectral measurements.

sensor: aeronautical station equipment including at least one receiver designed to receive aeronautical mobile service signals at 1030 and/or 1090 MHz.

spurious emissions: power transmitted at frequencies outside the specified spectral mask.

transmitter: a EUT  which includes the capability to convert binary content into RF signals.

Transmitter bandwidth: tbd

transponder: aeronautical station equipment including at least one transmitter designed to produce aeronautical mobile radionavigation service signals at 1090 MHz and zero or more receivers designed to receive aeronautical mobile radionavigation service signals at 1030 MHz.  Note: For purposes of this document, ground vehicle locators and reference transmitters which do not contain receivers for the purpose of replying to interrogation are included in the transponder definition.

equipment under test (EUT): a system of constituents provided by the manufacturer for qualification under this document.

#### Symbols

For the purposes of the present document, the following symbols apply:

BN	Necessary bandwidth

dB	deciBel

dBpp	power in dB relative to peak power

dBm	power in dB relative to 1 milliwatt

dBW	power in dB relative to 1 Watt

µs	Microsecond

(	Ohm

PD	Probability of detection

t	Time

(	Wavelength

#### Abbreviations

For the purposes of the present document, the following abbreviations apply:

AC	Alternating Current

ADS-B	Automatic Dependant Surveillance Broadcast

A-SMGCS	Advanced Surface Movement Guidance and Control System

CAS	Collision Avoidance System

CW	Continuous Wave

DME	Distance Measuring Equipment

EUT	Equipment Under Test

ICAO	International Civil Aviation Organization

IFF	Interrogate Friend or Foe

MLAT	Multilateration

MOPS	Minimum Operational Performance Specification

MTL	Minimum Triggering Level

OoB	Out-of-Band

PEP 	Peak Envelope Power

RED	Radio Equipment Directive

RF	Radio Frequency

SLS	Side Lobe Suppression

SNR	Signal to noise ratio

SSR	Secondary Surveillance Radar

PEP	Peak Envelope Power

RBW	Resolution Bandwidth (Measurement Bandwidth for emission measurement)

RBWref	Reference Bandwidth

# Technical requirements specifications

## Applicability

### Equipment with multiple functions

Any ground station which includes the interrogator function shall comply with the requirements in section [4..2].

Any ground station which includes the sensor function shall comply with the requirements in section [4..3].

If a ground station includes the sensor function and any transmitter, the [spurious emissions] requirements in section 4.2.3.9 shall only apply during the inactive state of the transmitter.

### Equipment with integral antenna

For the purposes of conducted measurements of EUT with integral antenna, a 50 ( RF connection point shall be provided for test purposes. The connection point should correspond to the input of the integral antenna. The connection point may be a modification made for the purposes of testing and need not be a permanent part of the EUT when made available for sale.

### Environmental profile

The technical requirements of the present document apply under the environmental profile for operation of the EUT, which shall be declared by the supplier. The equipment shall comply with all the technical requirements of the present document at all times when operating within the boundary limits of the environmental profile.

## Transmitter requirements

The transmitter requirements concern interrogators of a multilateration system used in Advanced Surface Movement Guidance and Control Systems.

### Frequency error

#### Description

The frequency error is the difference between the actual carrier frequency and its nominal value of 1030 MHz.

#### Limits

The absolute value of the frequency error shall not exceed 0,01 MHz.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

NOTE: the test procedure ignores frequency excursions during the phase reversal. Further information is given in 3.1.2.1.1. ICAO Annex 10V4v [].

Conformance shall be established under normal and extreme test conditions.

### Transmitter Peak Envelope Power

#### Description

Peak envelope power is the average power supplied to the antenna transmission line during one radio frequency cycle at the crest of the modulation envelope.

NOTE: The Transmitter power needs to achieve the value needed to meet operational performance. The Transmitter maximum power must be set up to meet the power limit indicated in the individual Frequency Licence.

#### Limits

The manufacturer shall announce the rated output power of the transmitter.

Note: This figure is required by the operator to determine a minimum distance to receiving units.

The nominal transmitter output power shall be determined under normal and extreme conditions and with only short Mode S uplink messages. It is recommended to use the same normal and extreme test conditions for transmitter and receiver.

The peak envelope power of the transmitter measured under normal test conditions shall not vary by more than 2 dB from the rated output power.

The peak envelope power of the transmitter measured under extreme test conditions shall not vary by more than + 2 dB and -3 dB from the rated output power.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

Conformance shall be established under normal and extreme test conditions.

As stated in EG 201 399, clause 7.1.3, conformance tests shall be conducted with maximum output power. If the output levels are configurable, then several levels of output power may be tested. For the purpose of the present document it is normally sufficient to perform the measurements for the lowest and the highest declared output power level.

### Spectrum mask

#### Description

A spectrum mask is a set of limit lines applied to a plot of a transmitter spectrum. The purpose is to constrain emissions at frequencies in the Out of Band domain which lies immediately outside the intended operating channel.

For the purposes of the present document, the out of band domain extends to +/- 125 MHz about the nominal operating frequency of 1030 MHz.

#### Limits

The measured spectrum shall be below:

the limit lines shown in Figure 1
 		OR
-13 dBm 
whichever is less stringent.

figure 1 - Required spectrum limits for interrogator transmitter (mask from ICAO Annex 10, Volume 4, figure 3-2 and modified to be consistent with ITU-RR article 3 [i.?])

One additional step: +/- 125 MHz at -50dB, then down to -60dB (rationale: 40dB/decade from ECC REC 02 05 as well as an extrapolation of the ICAO mask (last paragraph of rationale doc))

Instead, the ICAO mask was extrapolated from the last three steps to determine when the mask would intercept the -60 dB point.  A value of approximately 125 MHz was reached.  125 MHz is also the point reached when extrapolating the mask from the -40 dB (i.e., 40 MHz) by -40 dB per decade -- as described in ECC REC (02) 05, Figure A2.1 Emission Mask for radars --  until the spurious limit is reached.

Borders of the graphic:

30MHz

5th harmonic (6.5 GHz)

A new mask as results of calculations for the limits has been provided by Felix.

We decided not to have a more stringent requirement on the spectrum mask than ICAO

CEPT 74-01 and REC329 (ITU) are conflicting:

- CEPT 74-01: multilateration systems fall into “aids to air navigation” (not a radar system)

- ITU REC 329 : fixed radio determination systems: there is a limit -30dBm or -100dBc, whichever is less stringent

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Inter-modulation attenuation

#### Description

Intermodulation attenuation is the capability of a transmitter to avoid the generation of signals in the non-linear elements caused by the presence of the carrier and an interfering signal entering the transmitter via the antenna.

It is specified as the ratio, in dB, of the carrier power level to the power level of the third order intermodulation product.

#### Limits

The intermodulation attenuation ratio shall be at least 60 dB in the presence of an interfering signal at equal power level as the carrier. The interfering signal shall have a frequency range from 960MHz to 1215MHz (DME band).

Note: The 60dB limit is consistent with the spurious emissions requirement and with ETSI 300 676-1 [ref?])

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Transmitter Duty Cycle

#### Description

The duty cycle is a function of the airport and depends on the fit-for-purpose requirements.

#### Limits

Not applicable.

#### Conformance

Not applicable.

### Residual Power Output

#### Description

The residual power output is the power output when idle. The idle state is the period between intended transmissions but when the EUT is otherwise active.

#### Limits

#### The residual power output shall be not greater than -47dBm.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

## Receiver requirements

### Operating Frequency Range

#### Description

#### The operating frequency range is the frequency range around the nominal operating frequency over which reception of signals can be achieved.

#### Limits

Receivers shall operate with the rated sensitivity for signals with a carrier frequency of 1090 MHz and the following frequency offsets:

- Mode 3AC +/- 3 MHz

- Mode S +/- 1 MHz.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Adjacent channel selectivity and Spurious responses

#### Description

#### Adjacent channel selectivity and Spurious response rejection are the ability of the EUT to avoid erroneous reception of signals from outside the desired frequency band.  Limits are evaluated assuming the signal is constructed as a valid Mode S waveform except that the frequency is altered.

#### Limits

Although the 1090 MHz IFF system has only a single frequency channel, DME systems may occupy adjacent frequency allocations within the aviation band.  It is important that the receiver reject signals which are out of band while retaining sufficient bandwidth for acceptable multilateration performance.  Since multilateration receivers used in ASMGCS may also be required to process ADS-B messages, the limits below are consistent with ED-129 section 2.6.2 Table 2.

The EUT shall not respond to valid signals at the frequency offsets and levels in Table X.

Or

At the frequency offsets given in Table X, the level of valid signal that the EUT responds to shall be not less than the levels shown in the Table.

| Frequency (MHz) | Minimum Input Level Above Specified Receiver Sensitivity (dB) |
| --- | --- |
| +/- 12.5 | >=3 |
| +/- 19 | >= 20 |
| +/- 29 | >= 40 |
| +/- 46 | >=60 |

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Inter-modulation response rejection

#### Description

The intermodulation response rejection is a measure of the capability of the receiver to receive a wanted modulated signal without exceeding a given degradation due to the presence of two or more unwanted signals with a specific frequency relationship relative to the receiver frequency.

#### Limits

At any frequency combination from -78 MHz to -10 MHz and from +10 MHz to +78 MHz  from the receiver frequency of 1090 MHz, the unwanted signals shall not reduce the rate of correctly received and decoded squitter messages by more than 5% if their signal level is 12 dB or more below the level of the wanted signal.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Co-channel rejection

#### Description

Co-channel rejection is the receiver's ability to receive a wanted signal in the presence of an unwanted signal, with both signals being at the nominal receiver frequency. An unwanted signal is a signal that has a signal level 12 dB or more below the level of the wanted signal.

#### Limits

The unwanted signal shall not reduce the rate of correctly received and decoded squitter messages from the wanted Mode S signal by more than 5 %.

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Blocking

#### Description

Blocking is a measure of the capability of the receiver to receive a wanted signal without exceeding a given degradation due to the presence of a strong unwanted  signal.

#### Limits

The rate of correctly received and decoded squitter messages from the wanted Mode S signal shall be reduced by no more than 5% in the presence of unwanted signals specified in Table Y.

Table Y: Blocking signals

| Frequency | Level |
| --- | --- |
| -78 MHz to -10 MHz relative to 1090 MHz | 20 dB above the level of the wanted signal |
| +10 MHz to +78 MHz relative to 1090 MHz | 20 dB above the level of the wanted signal |

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

### Receiver dynamic range / Maximum usable sensitivity

#### Description

The receiver dynamic range shall be declared by the manufacturer.

#### Limits

Receivers shall operate throughout the receiver dynamic range for signals with a carrier frequency of 1090 MHz with at least a PD of 90%.

#### Conformance

### Spurious emissions

#### Description

Spurious emissions are unwanted emissions in the spurious domain radiated by the equipment or its antenna.

For transmitters, the spurious domain is all frequencies apart from the channel on which the transmitter is intended to operate and the Out of Band domain.

For receivers, the spurious domain is all frequencies.

#### Limits

The power of any unwanted emission in the spurious domain shall not exceed the values given in Table 19.

Table 19: Spurious domain emission limits

| Frequency State | 47 MHz to 74 MHz 87,5 MHz to 118 MHz 174 MHz to 230 MHz 470 MHz to 790 MHz | Other frequencies below 1 000 MHz | Frequencies above 1 000 MHz |
| --- | --- | --- | --- |
| TX mode | -54 dBm | -36 dBm | -30 dBm |
| RX and all other modes | -57 dBm | -57 dBm | -47 dBm |

#### Conformance

The conformance tests for this requirement shall be as defined in clause 5.x.y.

[Conformance shall be established under normal and extreme test conditions.]

# Testing for compliance with technical requirements

## Environmental conditions for testing

Tests defined in the present document shall be carried out at representative points within the boundary limits of the declared operational environmental profile.

Where technical performance varies subject to environmental conditions, tests shall be carried out under a sufficient variety of environmental conditions (within the boundary limits of the declared operational environmental profile) to give confidence of compliance for the affected technical requirements.

For equipment designed for outdoor use tests shall include, as a minimum, ambient temperatures of -25°C, 25°C and 40°C surrounding the supplier provided weatherproof enclosure.  For equipment designed to be installed in equipment rooms, the test shall include, as a minimum, an ambient temperature of 25°C around the EUT.

Note: For each test the ambient

## Interpretation of the measurement results

The interpretation of the results recorded in a test report for the measurements described in the present document shall be as follows:

the measured value related to the corresponding limit will be used to decide whether an equipment meets the requirements of the present document;

the value of the measurement uncertainty for the measurement of each parameter shall be included in the test report;

the recorded value of the measurement uncertainty shall be, for each measurement, equal to or lower than the figures in table <n>.

For the test methods, according to the present document, the measurement uncertainty figures shall be calculated and shall correspond to an expansion factor (coverage factor) k = 1,96 or k = 2 (which provide confidence levels of respectively 95 % and 95,45 % in the case where the distributions characterising the actual measurement uncertainties are normal (Gaussian)). Principles for the calculation of measurement uncertainty are contained in TR 100 028 [<m>], in particular in annex D of the TR 100 028-2 [<n>].

Table <n> is based on such expansion factors.

Table 1: maximum measurement uncertainty

| Parameter | Uncertainty |
| --- | --- |
| Adjacent channel power | ±2,5 dB |
| Adjacent channel rejection | ±4 dB |
| Blocking and desensitization | ±4 dB |
| Carrier power (normal and extreme test conditions) | ±0,75 dB |
| Conducted spurious emissions: below 1 GHz between 1 GHz and 4 GHz | ±3 dB ±6 dB |
| Conducted spurious radiation: below 1 GHz between 1 GHz and 4 GHz | ±3 dB ±6 dB |
| Cabinet radiation |  |
| Cross modulation rejection | ±4 dB |
| Frequency error | ±1 × 10-9 |
| Intermodulation | ±3 dB |
| Intermodulation response rejection | ±3 dB |
| Keying transient frequency behaviour | ±3 dB |
| Receiver dynamic range | ±2 dB |
| Receiver sensitivity | ±3 dB |
| Spurious response rejection | ±4 dB |
| Transient frequency behaviour | ±250 Hz |

## Test and General Conditions

### Transmitter test signals

For the purposes of the present document a transmitter test signal is a modulated carrier generated by the EUT to facilitate a particular test. The EUT should be capable of generating the following test signals:

Test signal 1: (D-M2)		Maximum duty cycle, short Mode S interrogations with all “0” data content

Test signal 2: (D-M3)		Maximum duty cycle, short Mode S interrogations with all “1” data content

Test signal 3: 				Maximum duty cycle, Mode A interrogation

Test signals may be generated autonomously by the EUT when configured for test mode, or by applying external commands or other stimulation.  Operation in a test mode may involve suitable temporary internal modifications of the EUT or the use of special software. Details of the method chosen and the test signals shall be recorded in the test report.

5.3.1.2	Test signal 1

When test signal 1 is specified below, a signal shall be generated with the following characteristics:

Transmission rate: Maximum constant rate such that the manufacturer’s rated maximum duty cycle is not exceeded.
The following example shows the calculation for a rated maximum duty cycle of 1%.  The short Mode S interrogation contains the P1, P2 and P6 pulses.  The P1 and P2 pulses are 0,80 microseconds long and the P6 pulse is 16,25 microseconds long.  In total, the short Mode S interrogation results in 17,85 microseconds of active transmission.  The maximum transmission rate that does not exceed 1% (i.e., 10 milliseconds per second of transmission time) is 560 Hz.

Waveform: Short Mode S Interrogation, reference ICAO Annex 10, Volume 4, sections 3.1.2.1 and 3.1.2.11.4.

Frequency: 1030 MHz

Message content: All “zeroes” (i.e., the minimum number of phase transitions)

Amplitude: Maximum rated power level

5.3.1.4 	Test signal 2

When test signal 2 is specified below, a signal shall be generated with the following characteristics:

Transmission rate: Maximum rate such that the manufacturer’s rated maximum duty cycle is not exceeded.

Waveform: Short Mode S Interrogation, reference ICAO Annex 10, Volume 4, sections 3.1.2.1 and 3.1.2.11.4.

Frequency: 1030 MHz

Message content: All “ones” (i.e., the maximum number of phase transitions)

Amplitude: Maximum rated power level

5.3.1.2 	Test signal 3 (Optional)

Where appropriate, a test signal shall be used with the following characteristics:

This test signal shall be used for transmitters with Mode A/C interrogation capability. When test signal 3 is specified below, a signal shall be generated with the following characteristics:

Transmission rate: At least 50 Hz, a higher rate is preferable to increase the speed of test measurements.
Note: If this will exceed the manufacturer’s rated maximum duty cycle the maximum rated rate shall be used and shall be noted in the test report.

Waveform: Mode A interrogation, reference ICAO Annex 10, Volume 4, sections 3.1.1.1.
Note: If the transmitter supports suppression pulses, they shall be included

Frequency: 1030 MHz

Message content: Not applicable

Amplitude: Maximum rated power level for all pulses.

### Simulated received signals

For the purposes of the present document a receiver test signal is an unmodulated or modulated carrier applied to the EUT to facilitate a particular test. The EUT shall be capable of tolerating the following test signals.  Note, when multiple test signals are used in the same test, the frequency sources for each test signal shall be non-coherent.

The EUT shall be able to report each message received.  The report shall include the complete Mode S message and the time of receipt at the receiver or the recording device with at least 10 millisecond resolution.  Message reports from multilateration receivers can generally be collected using a computer and standard communication network analysis software.  Operation of the EUT in a test mode is permissible and may involve suitable temporary internal modifications of the EUT or the use of special software. Details of the method chosen and how the reports were collected shall be recorded in the test report.

Test signal 4: Modulated Mode S Extended Squitter message (desired signal)

Test signal 5: Unmodulated carrier (undesired signal

Test signal 6: Modulated Mode S Extended Squitter message (undesired signal)

5.3.1.2	Test signal 4

When test signal 4 is specified below, a signal shall be injected with the following characteristics:

Transmission rate: 100 Hz

Waveform: Mode S Extended squitter, reference ICAO Annex 10, Volume 4, section 3.1.2.2.

Frequency: 1090 MHz, unless otherwise specified by the test

Message content: Arbitrary data content with a known Aircraft Address and valid CRC
For example: 0x88ABC123XXXXXXXXXXXXXXXXXXXX is a valid DF-17 squitter with the Aircraft Address of “ABC123”.

Amplitude: As specified by the test

Pulse on/off ratio: At least 40 dB

5.3.1.2	Test signal 5

Where test signal 5 is specified below, a signal shall be injected with the following characteristics:

Transmission rate: Not applicable

Waveform: Unmodulated carrier

Frequency: As specified in the test.

Message content: Not applicable

Amplitude: As specified by the test

Pulse on/off ratio: Not applicable

5.3.1.2	Test signal 6

When test signal 6 is specified below, a signal shall be injected with the following characteristics:

Transmission rate: 6000 Hz

Waveform: Mode S Extended squitter, reference ICAO Annex 10, Volume 4, section 3.1.2.2.

Frequency: As specified by the test

Message content: Arbitrary data content with a known Aircraft Address and valid CRC
Note: The data content shall be distinct from Test signal 4.
For example: 0x88BADBADXXXXXXXXXXXXXXXXXXXX is a valid DF-17 squitter with the Aircraft Address of “BADBAD”.

Amplitude: As specified by the test

Pulse on/off ratio: At least 40 dB

Normal test conditions

Extreme test conditions

### Test power source

### Artificial antenna

### Equipment without an external RF connector

### Conducted and radiated measurements

### Measuring receiver

## Transmitter Tests

### Spectrum Test

Requirements to be tested:

- Operating frequency (Reference)

- Frequency error (Reference)

- Spectrum mask (Reference)

#### Description

The purpose of this test is to establish that the transmitter is operating at the correct frequency and within the required frequency error.  In addition, the in band, out of band and spurious frequency domains are measured for compliance.  All tests are performed at the maximum rated transmit power and duty cycle to show that the spectrum is met under these conditions.  Since the modulation of the Mode A/C interrogation is a subset of the Mode S interrogation only the Mode S interrogation is tested.

#### Test conditions

The Mode S interrogation spectrum is data dependent. The broadest spectrum is generated by an interrogation that contains all binary ONEs. The highest spectrum is generated by an interrogation that contains all binary ZEROs.  Therefore during test, the 0 dB reference will be determined using a test signal with all ZEROs, while compliance to the mask will use a test signal containing all binary ONEs.

The 0 dB reference shall be aligned with the maximum of the measured spectrum.

The EUT shall be configured to generate test signals 1 and 2 as indicated in the procedure.

When measuring the spurious domain, ITU-R recommendation <REFERENCE> indicates that a spectrum analyzer receiver bandwidth of 1 MHz be used for frequencies of 1 GHz and above, and a bandwidth of 100 kHz be used below 1 GHz.  However, since the spectrum mask of the desired signal spans the 1 GHz boundary, a receiver bandwidth of 1 MHz shall be used for frequencies of 905 MHz and above. For frequencies lower than 905 MHz the receiver bandwidth shall be 100 kHz.  The spurious domain compliance limit will not be adjusted for the change in receiver bandwidth.

The measurement shall be performed with the EUT operating at its maximum rated power level, as declared by the manufacturer.

#### Method of measurement

The measurement shall be a conducted measurement using a connection to the EUT antenna interface.  All amplitudes shall be adjusted for cable loss to be representative of the antenna interface of the EUT.

Care should be taken that the peak level of the signal into the test equipment is not so high as to cause broadening of the spectrum or increased harmonics due to non-linear effects in the test equipment.  For example, a notch filter at 1030 MHz may be necessary for accurate measurements in the spurious domain.  Particular care should also be taken at the harmonics of the transmit frequency.

Unless otherwise noted below, the spectrum analyser shall be configured to the following settings:

- Trigger level

- Max hold, RMS?

- Trace properties?

- Sweep properties?

Receiver BW, resolution BW, video BW, etc.?

#### Measurement procedure

- Record the manufacturer’s rated power level.

- Attach the EUT antenna port to the spectrum analyzer.

- Configure the EUT to produce test signal 1 at the maximum rated power level.

- Set up the spectrum analyzer with a receiver bandwidth of 1 kHz and a video bandwidth of 1 kHz.

- Measure the frequency of the peak of the spectrum and compare to 1030 MHz (center frequency and frequency error).

- Set up the spectrum analyzer with a receiving bandwidth of 1 MHz and a video bandwidth of 1 MHz.

- Measure the spectrum from 905 MHz to 1155 MHz and record the peak amplitude of the spectrum as a reference for 0 dBc (spectrum mask).

- Switch the EUT to produce test signal 2 at the same power level.

- Measure the spectrum from 905 MHz to 1155 MHz and compare it to the spectrum mask (spectrum mask).

- Measure from 1155 MHz to 6,2 GHz (fifth harmonic) and compare to the spectrum mask (spectrum mask).

- Switch the spectrum analyzer to a receiving bandwidth of 100 kHz and a video bandwidth of 100 kHz

- Measure from 30 MHz to 905 MHz and compare to the lower frequency limit of the spectrum mask (spectrum mask).

### Transmitter Power / Transmitter Duty Cycle

#### Description

The purpose of this test is to establish that the transmitter is operating at the correct transmit power.  The test also verifies that this power level is sustained at the maximum duty cycle.

Requirements to be tested:

- Transmit power (Reference)

- Duty cycle (Reference)

#### Test conditions

Note that the peak power tolerance is a function of test condition.

The EUT shall be configured to generate test signals 2 and 3 as indicated in the procedure.

The measurement shall be performed with the EUT operating at its maximum operating power level, as declared by the provider.

#### Method of measurement

The measurement shall be a conducted measurement using a connection to the EUT antenna interface.  All amplitudes shall be adjusted for cable loss to be representative of the antenna interface of the EUT.

The power meter shall be configured to the following settings:

- Trigger level

- Trigger hold off time of 20 microseconds

- Max hold, RMS?

- Trace properties / persistence?

#### Measurement procedure

- Record the manufacturer’s rated output power and duty cycle of the transmitter.

- Set up EUT to produce test signal 2.

- Record the start-to-start time of subsequent messages.

- Calculate the message rate in Hz as 1.0 / (start-to-start time).

- Verify that the average message rate is within +/- 1 Hz of the rate needed to produce the manufacturer’s maximum rated duty cycle. (Transmit duty cycle)

- Set up the power meter with zero trigger delay to capture the P1 pulse.

- Record the minimum and maximum values for the peak power of the P1 pulse over one minute.

- Set up the power meter with 2,0 microsecond trigger delay to capture the P2 pulse.

- Record the minimum and maximum values for the peak power of the P2 pulse over one minute.

- Set up the power meter with 3,5 microsecond trigger delay to capture the P6 pulse.

- Record the minimum and maximum values for the peak power of the first microsecond of the P6 pulse over one minute.

- Verify that the minimum and maximum power levels recorded are within the required tolerance of the manufacturer’s rated maximum power. (Transmit power)

- For transmitters with Mode A/C interrogation capability, execute the following additional steps.

- Set up the EUT to produce test signal 3.

- Set up the power meter with appropriate trigger delay to capture the P1 pulse.
Note: Depending on the manufacturer’s implementation of suppression pulses, different trigger delay timing may be needed.  The delay to the P1 pulse shall be noted in the test report.

- Record the minimum and maximum values for the peak power of the P1 pulse over one minute.

- Set up the power meter with appropriate trigger delay to capture the P3 pulse.
Note: Depending on the manufacturer’s implementation of the suppression pulse, different trigger delay timing may be needed.  The delay to the P3 pulse shall be noted in the test report.

- Record the minimum and maximum values for the peak power of the P3 pulse over one minute.

- Set up the power meter with appropriate trigger delay to capture the P4 pulse.
Note: Depending on the manufacturer’s implementation of the suppression pulse, different trigger delay timing may be needed.  The delay to the P4 pulse shall be noted in the test report.

- Record the minimum and maximum values for the peak power of the P4 pulse over one minute.

- Verify that the minimum and maximum power levels recorded are within the required tolerance of the manufacturer’s rated maximum power. (Transmit power)

### Inter-modulation attenuation

#### Description

The purpose of this test is to establish that the transmitter does not generate unwanted signals in the presence of an interfering signal entering the transmitter via the antenna due to inter-modulation effects in the transmitter's non-linear elements.

#### Test conditions

External test equipment will be used to create an interfering test signal with amplitudes and frequencies indicated in the procedure.  External test equipment will be used for analyzing the resulting transmitter output signal.

#### Method of measurement

Figure 1:  Measurement Arrangement

The measurement arrangement shown in Figure 1 shall be used.

The transmitter shall be connected to a 50 Ω 10 dB power attenuator and via a directional coupler to a spectrum analyser. An additional attenuator may be required between the directional coupler and the spectrum analyser to avoid overloading the spectrum analyser.

In order to reduce the influence of mismatch errors it is important that the 10 dB power attenuator is coupled to the transmitter under test with the shortest possible connection.

The interfering test signal source is connected to the other end of the directional coupler via a 50 Ω 20 dB power attenuator.

The interfering signal source may be a either a transmitter providing the same power output as the transmitter under test and be of a similar type or a signal generator and a linear power amplifier capable of delivering the same output power as the transmitter under test.

The directional coupler shall have an insertion loss of less than 1 dB, a sufficient bandwidth and a directivity of more than 20 dB.

The transmitter under test and the test signal source shall be physically separated in such a way that the measurement is not influenced by direct radiation.

#### Measurement procedure

- The transmitter under test shall be unmodulated and the spectrum analyser adjusted to give a maximum indication with a frequency scan width of 500 kHz.

- The interfering test signal source shall be unmodulated and the frequency shall be within 10 MHz to 185 MHz above the frequency of the transmitter under test.

- The frequency shall be chosen in such a way that the intermodulation components to be measured do not coincide with other spurious components.

- The power output of the interfering test signal source shall be adjusted to the carrier power level of the transmitter under test by the use of a power meter.

- The intermodulation component shall be measured by direct observation on the spectrum analyser and the ratio of the largest third order intermodulation component to the carrier recorded.

- This measurement shall be repeated with the interfering test signal source at a frequency within 10 MHz to 70 MHz below the frequency of the transmitter under test.

- Verify that for each frequency, the inter-modulation attenuation ratio is at least the level required.

### Residual Power Output

#### Description

This test will verify that the output power of the transmitter when in idle (i.e. non-transmitting) state does not exceed the specified maximum.

#### Test conditions

The measurement shall be performed with the EUT operating but not transmitting.

#### Method of measurement

The measurement shall be a conducted measurement using a connection to the EUT antenna interface.  All amplitudes shall be adjusted for cable loss to be representative of the antenna interface of the EUT.

The power meter shall be configured to the following settings:

- Trigger level

- Trigger hold off time of 20 microseconds

- Max hold, RMS

#### Measurement procedure

- Connect the power measuring equipment to the BS antenna connector.

- Switch off the EUT and set it into idle mode (i.e. not transmitting)

- Measure the power of the  output signal over a period of 2 minutes. The power is determined by calculating the RMS value of the signal taken at the measurement filter output.

## Receiver requirements

### Operating Frequency and Receiver dynamic range (Maximum usable) sensitivity

#### Description

The purpose of this test is to establish the sensitivity of the receiver at the intended operating frequency.  The receiver is tested with a known input waveform and verified to report the correct data content at the required probability of detection.  The amplitude is varied to determine the maximum amplitude where the receiver achieves the required probability of detection.

Requirements to be tested:

- Operating frequency (Reference)

- Receiver dynamic range (Reference)

#### Test conditions

The manufacturer may declare different rated values for each condition and these shall be recorded in the test report.

External test equipment will be used to stimulate the EUT with test signal 4 at the amplitudes indicated in the procedure.  External test equipment will be used to collect the reception reports for each injected message.

#### Method of measurement

The test waveform shall be injected using conduction into the EUT antenna interface.  All amplitudes shall be adjusted for cable loss to be representative of the antenna interface of the EUT.  The message receipt reports will be collected and the average rate of message receipt will be calculated.

Unless otherwise noted below, the signal generator shall be configured to…

#### Measurement procedure

- Record the manufacturer’s rated sensitivity as used in test <reference> Operating Frequency and Receiver Dynamic Range.

- Configure the EUT to receive and report messages for recording.

- Configure the recording device to record message reports.

- Verify that no message reports are being generated.

- Configure the signal generator to produce test signal 4 at the rated sensitivity and inject messages for at least 100 seconds.

- Review the recorded reports to count the number of reports which match the expected message content.

- Divide the number of successfully received messages by the elapsed time from the first to last report and verify that the average receive rate was at least 225 Hz.

- Configure the signal generator to produce test signal 4 at an amplitude equal to the maximum receive amplitude.
Maximum receive amplitude = (Rated sensitivity + rated dynamic range)

- Configure the signal generator to produce test signal 4 at the rated sensitivity and inject messages for at least 100 seconds.

- Review the recorded reports to count the number of reports which match the expected message content.

- Divide the number of successfully received messages by the elapsed time from the first to last report and verify that the average receive rate was at least 225 Hz.

### Adjacent channel selectivity and Spurious responses

#### Description

The purpose of this test is to establish the selectivity of the receiver by measuring the rate of detection of properly formed messages injected outside of the intended operating frequency.  The amplitude of injected messages is adjusted to verify that an appropriate number of messages are rejected.

Requirements to be tested:

- Adjacent channel selectivity and spurious responses (Reference)

References for receiver pass band and receiver selectivity:

| Frequency | Amplitude Relative to Rated Sensitivity in dB | Reference |
| --- | --- | --- |
| +/- 12.5 MHz | >=3 | Alt ED-129 2.6.2 Table 2 for MLAT |
| +/- 19 MHz | >= 20 | Alt ED-129 2.6.2 Table 2 for MLAT |
| +/- 29 MHz | >= 40 | Alt ED-129 2.6.2 Table 2 for MLAT |
| +/- 46 MHz | >=60 | Alt ED-129 2.6.2 Table 2 for MLAT Alt ED-129 2.6.2 is consistent with ICAO Annex 10 at +/- 46MHz |

Requirements to be tested:

- Adjacent channel selectivity and spurious responses (Reference)

#### Test conditions

External test equipment will be used to stimulate the EUT with test signal 4 at the amplitudes and frequencies indicated in the procedure.  External test equipment will be used to collect the reception reports for each injected message.

#### Method of measurement

The test waveform shall be injected using conduction into the EUT antenna interface.  All amplitudes shall be adjusted for cable loss to be representative of the antenna interface of the EUT.  The message receipt reports will be collected and the average rate of message receipt will be calculated.

Unless otherwise noted below, the signal generator shall be configured to…

#### Measurement procedure

- Record the manufacturer’s rated sensitivity and dynamic range.

- Configure the EUT to receive and report messages for recording.

- Configure the recording device to record message reports.

- Configure the signal generator to produce test signal 4 at 3 dB higher than the rated sensitivity at 1102,5 MHz and inject messages for at least 100 seconds.

- Review the recorded reports to count the number of reports which match the expected message content.

- Divide the number of successfully received messages by the elapsed time from the first to last report and verify that the average receive rate was less than 225 Hz.

- Repeat steps 4 through 6 for the following frequencies and amplitudes.

| Frequency (MHz) | Injected Input Level Above Rated Receiver Sensitivity (dB) |
| --- | --- |
| 1077,5 | 3 |
| 1109 | 20 |
| 1071 | 20 |
| 1119 | 40 |
| 1061 | 40 |
| 1136 | 60 |
| 1044 | 60 |

### Inter-modulation response rejection (for 4.3.3)

#### Description

The purpose of this test is to establish that inter-modulation caused by two unwanted out-of-band signals  does not degrade the reception probability when their signal level is below the specified limit.

#### Test conditions

#### Method of measurement

Figure 2:  Measurement Arrangement

#### Measurement procedure

The measurement procedure shall be as follows:

- Three signal generators, A, B and C, shall be connected to the receiver Via a combining network.

The wanted signal, provided by signal generator A, shall be at the nominal frequency of the receiver and shall have normal test modulation.

The first unwanted signal, provided by signal generator B, shall be unmodulated and adjusted to a frequency f1 at 10 MHz above the nominal frequency of the receiver.

The second unwanted signal, provided by signal generator C, shall be modulated with signal D-M3 and adjusted to a frequency f2 at 20 MHz above the nominal frequency of the receiver.

- Initially, signal generators B and C (unwanted signals) shall be switched off (maintaining the output impedance).

The level of the wanted signal from generator A shall be adjusted to the level which is 20 dB above the maximum usable sensitivity.

- Signal generators B and C shall then be switched on; the levels of the two unwanted signals shall be maintained equal and shall be adjusted until a successful message ratio of less than 5 % is obtained;

- The normal test signal shall then be transmitted repeatedly whilst observing in the successful message reception ratio;

The levels of the unwanted signals shall be reduced in steps by 2 dB.

The procedure shall be continued until the successful message ratio is above 95%. The level of the input signals shall then be noted.

- The level of the unwanted signals shall be increased by 1 dB and the new Value noted;

- The normal test signal shall then be transmitted repeatedly whilst observing in the successful message reception ratio;

The levels of the unwanted signals shall be reduced in steps by 1 dB and the new Value noted.

The average of the Values noted in steps 4. and 5. (which provides the level corresponding to the successful message ratio of 95 %) shall be noted.

- For each configuration of the unwanted signals, the intermodulation response rejection shall be expressed as the ratio, in dB, of the average level noted in step 5. to the level of the wanted signal, at the receiver input. This ratio shall be recorded.

- The measurement shall be repeated with the unwanted signal generator B at the frequency 10 MHz below that of the wanted signal and the frequency of the unwanted signal generator C at the frequency 20 MHz below that of the wanted signal.

- The intermodulation response rejection for the given frequency combination is the lower of the two Values recorded in step 6.

- Repeat the test steps 1. to 9. with various frequency combinations that fulfil

fc = 2 * f1 - f2

with an offset of f2 in the range of +20MHz to +78MHz and -20MHz to -78MHz.

- The intermodulation response rejection of the EUT is the lowest of the values recorded in step 9.

### Co-channel rejection (for 4.3.4)

#### Description

This test verifies that the receiver's reception probability is not degraded in the presence of an unwanted modulated signal at the same frequency when its signal level is below the specified limit.

#### Test conditions

#### Method of measurement

Figure 2:  Measurement Arrangement

#### Measurement procedure

- Two signal generators A and B shall be connected to the test fixture via a combining network. The wanted signal, represented by signal generator A, shall be at the nominal frequency of the receiver and shall have normal test modulation (Test signal 2).

- The unwanted signal, represented by signal generator B, shall be modulated with the same signal.

- Both input signals shall be at the nominal frequency of the receiver under test.

- Initially the unwanted signal shall be switched off (maintaining its output impedance).

- The level of the wanted signal from generator A shall be adjusted to a level which is 20 dB above the level equivalent to the limit of the average usable sensitivity, for the category of equipment used.

- The unwanted signal from generator B shall then be switched on and its level shall be adjusted until a successful response ratio of less than 10 % is obtained.

- The normal test signal 1 shall be transmitted repeatedly whilst observing the successful message reception ratio.

- The level of the unwanted signal shall be reduced by 1 dB for each occasion that a successful response is not obtained.

- The procedure shall be continued until a rate of 95% is achieved.

- The level of the input signal shall then be noted.

- For each frequency of the unwanted signal, the co-channel rejection ratio shall be expressed as the ratio, in dB, of the average level recorded in step 10. to the level of the wanted signal.

- The measurement shall be repeated for displacements of the unwanted signal of ±1.2 MHz.

- The co-channel rejection ratio of the equipment under test shall be expressed as the lowest of the three values expressed in dB, recorded in step 12.

### Blocking (for 4.3.5)

#### Description

With this test it will be verified that a single unwanted out-of-band signal cannot degrade the reception probability when its signal level is below the specified limit.

#### Test conditions

#### Method of measurement

Figure 3:  Measurement Arrangement

#### Measurement procedure

- Two signal generators A and B shall be connected to the receiver via a combining network.

- The wanted signal, represented by signal generator A, shall be at the nominal frequency of the receiver and shall have normal test modulation (Test signal 2)

- The unwanted signal, provided by signal generator B, shall be unmodulated and shall be at a frequency from 10 MHz to 78 MHz away from the nominal frequency of the receiver.

- Initially the unwanted signal shall be switched off.

- The level of the wanted signal from generator A shall be adjusted to a level which is 20 dB above the level of the limit of the average usable sensitivity.

- The unwanted signal shall then be switched on and its level shall be adjusted until a successful reception ratio of less than 10 % is obtained.

- The normal test signal 2 shall be transmitted repeatedly whilst observing the successful reception rate.

- The level of the unwanted signal shall be reduced in steps by 1 dB.

- The procedure shall be continued until the successful reception rate is above 95%.

- The level of the input signal shall then be noted.

- For each frequency, the blocking or desensitization shall be expressed as the level in dB noted in step 10.

- The measurement shall be repeated for frequencies within the range defined in step 3 at 1 MHz steps.

- The blocking or desensitization of the equipment under test shall be expressed as the level of the unwanted signal, at the receiver location, corresponding to the lowest value recorded in step 11.

### Spurious emissions (for 4.3.7)

#### Description

This test will measure the spurious emissions radiated by the receiver via its antenna and verify that their level is below the specified limits.

#### Test conditions

#### Method of measurement

Spurious radiation shall be measured as the power level of any discrete signal at the RF input terminal of the receiver.

Figure 3:  Measurement Arrangement

#### Measurement procedure

- Connect the receiver input terminal to a spectrum analyser or selective voltmeter having an input impedance of 50 Ω and switch the receiver on.

- If the detecting device is not calibrated in terms of power input, the level of any detected components shall be determined by a substitution method using a signal generator.

- The measurements shall extend over the frequency range of 9 kHz to 4 GHz.

- Verify that the measured emissions are below the specified limits.

# Annex A (informative):
Relationship between the present document and the essential requirements of Directive 2014/53/EU

The present document has been prepared by ETSI in response to mandate M/405 from the European Commission to provide a means of conforming to the essential requirements of Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC radio Equipment Directive [i.1].

Once the present document is cited in the Official Journal of the European Union under that Directive, compliance with the normative clauses of the present document given in table […] confers, within the limits of the scope of the present document, a presumption of conformity with the corresponding essential requirements of that Directive, and associated EFTA regulations.

# Table <A.1>: Correspondence between the present document and
Article 3.2 of Directive 2014/53/EU

| Requirement Description | Limits | Measurement Method |
| --- | --- | --- |
| No | Name | Description Reference | Reference | Reference |
| 1 |  | 4.2.1.1 | 4.2.1.1.2 |  |
| 2 |  | 4.2.1.2 | 4.2.1.2.2 |  |
| 3 |  | 4.2.1.3 | 4.2.1.3.2 |  |
| 4 |  | 4.2.1.4 | 4.2.1.4.2 |  |
| 5 |  | 4.2.2.1 | 4.2.2.1.1 |  |

Presumption of conformity stays valid only as long as a reference to the present document is maintained in the list published in the Official Journal of the European Union. Users of the present document should consult frequently the latest list published in the Official Journal of the European Union.

Other Union legislation may be applicable to the product(s) falling within the scope of the present document.

Key to columns:

Requirement:

No	A unique identifier for one row of the table which may be used to identify a requirement or its test specification.

Description	A textual reference to the requirement.

Clause Number	Identification of clause(s) defining the requirement in the present document unless another document is referenced explicitly.

Requirement Conditionality:

U/C	Indicates whether the requirement is to be unconditionally applicable (U) or is conditional upon the manufacturers claimed functionality of the equipment (C).

Condition	Explains the conditions when the requirement shall or shall not be applicable for a technical requirement which is classified "conditional".

Test Specification:

E/O	Indicates whether the test specification forms part of the Essential Radio Test Suite (E) or whether it is one of the Other Test Suite (O).

NOTE:	All tests whether "E" or "O" are relevant to the requirements. Rows designated "E" collectively make up the Essential Radio Test Suite; those designated "O" make up the Other Test Suite; for those designated "X" there is no test specified corresponding to the requirement. The completion of all tests classified "E" as specified with satisfactory outcomes is a necessary condition for a presumption of conformity. Compliance with requirements associated with tests classified "O" or "X" is a necessary condition for presumption of conformity, although conformance with the requirement may be claimed by an equivalent test or by manufacturer's assertion supported by appropriate entries in the technical construction file.

Clause Number	Identification of clause(s) defining the test specification in the present document unless another document is referenced explicitly. Where no test is specified (that is, where the previous field is "X") this field remains blank.

# Annex B (informative):
Bibliography

<Publication>: "<Title>".

<Publication>: "<Title>".

<Publication>: "<Title>".

<Publication>: "<Title>".

<Publication>: "<Title>".

<Publication>: "<Title>".

# Annex C (informative):
Change History

| Date | Version | Information about changes |
| --- | --- | --- |
| February 2015 | 0.0.9 |  |
| March 2015 | 0.0.10 | Version prepared by the Rapporteur |

# History

| Document history |
| --- |
| 0.0.5 | - | - |
| 0.0.6 | - | - |
| 0.0.9 | 05.02.2015 | Complete document review during STF Meeting (STF 485) |
| 0.0.10 | 13.03.2015 | Early internal draft for internal STF discussion (STF 485) |

Latest changes made on 2015-03-13

# Comments

Task for Roy to continue the list.

Are there definitions, symbols, abbreviations in other Parts of EN 303 213?

If so, we should refer to them rather than duplicate.

Also, we will not need duplicated terms in parts -5-1 and -5-2.

Suggest putting A-SMGCS in the abbreviations and then the description in the Foreward or Introduction.

In other ENs we are adopting a standard definition of duty cycle that requires an observation bandwidth and and an observation time..

If we want something special in 303 215 then we should either

- call it something different.

- Specify the difference in a measurement procedure.

How is an appropriate observation bandwidth determined?

What is included in Ton_cum?  For example, if a single transmission consists of two short pulses and one long pulse, do we use the time from beginning of pulse 1 to the end of pulse 3?  Or the sum of the length of the three pulses?  If we’re going to change this definition at this point, we need to be very explicit on how to determine it.

We define no limit on duty cycle in this document, so the definition is not terribly important.  However, since we ask the manufacturer to specify the maximum duty cycle, then verify that the unit is, in fact, operating at that rating, we must make sure that the manufacturer understands this definition of duty cycle so they can declare the correct rating.

Here we are using a generally understood term to mean something specific to this EN.

These definitions have been in the draft since last year, why are we second guessing them now?

Does keeping this definition reduce the usefulness of the document?

As above

Remove. Not used in document.

As for Receiver

Remove. This term not used in the document.

We should move this to the Scope or somewhere similar.

A Note is only informative.

Definitions must not contain requirements. This may not be a technical requirement but it is modifying the Scope of the EN.

Agreed.  This note should be moved to the Scope section immediately after the sentence “The present document does not apply to equipment which includes a transponder function.”

We should not use NB in a standard. It is really a spectrum planning concept, not a characteristic of an indivual EUT.

Agree, remove this definition. It is no longer used in the document.

Remove. No longer used in document.

Remove. No longer used in document.

Symbols for resolution bandwidth needed? (e.g.RBW-ref). f and f_o to be added!?

Remove. Not used.

Remove not used.

Not used.

Remove. Not used (also in table twice)

Remove. Not used.

Remove. Not used.

We cannot have a statement of this form. I moved this detail to the Scope.

Move to 5.3.

I disagree. This is a physical requirement on the EUT.  The manufacturer must provide this test point.  This is not something that the lab does when running the test.

This is too vague. Also it is a requirement on the testing rather than on the EUT. It is in section 5, so propose to delete here.

Do we need that section?

4.2.1 and 4.2.2 should be combined.

Add normative reference.

Add normative reference.

This is a useful way of specifying that testing shall be done at extreme conditions.

Proposed new wording. Otherwise we are placing a requirement on the person doing the testing rather than the EUT.

Section numbering to be adjusted due to switch of sections.

Move to testing section

Move to testing section. Delete ref to EG 201 399 unless it is an essential part of the test method.

+/-78 for 1090 MHz

Is 1090 MHz in par t-5-2, so not covered here?

Right, 1090 emission is in 5-2.

We do not want to be more strict than ICAO. There is one open issue of where the diagram should stop.

What is the limit of -60dB? Linear connection in the lograrithmic graph between -50 and -60.

-100 dBc?

To be replaced by new drawing as output from 22nd September STF485 meeting.

Tha mask picture shall be moved to the limits section.

To implement that into the figure.

To implement into figure!

Remove all of this text once figure is incorporated.

Move to test method.

Is this EN, EG, TS ?

Section needs attention. Check with ICAO requirements. Maybe some hint can be found in ITU1446 (1546) ( 3.3.2).

Probably not needed for this requirement.

Propose delete.

If there is no requirement, then we do not need a clause in the technical requirements section.

We may want to add an explanation, but that goes elsewhere.

We should add text here saying the manufacturer shall declare the rated duty cycle (like we do in section 4.2.2)

Is the RPO limit applied in 960 – 1215 MHz, or in 1030 +/- 4 MHz or what?

Is there a spurious emissions limit that applies elsewhere?

Spurious emission is under the transmit spectrum.  Residual power is when idle, and is frequency agnostic (think zero span mode).

The test section should specify a frequency range to actually measure across so that the correct test equipment is used.  I’d expect this to be the same range as the spectrum measurement.

Probably not needed for this requirement.

I propose that we just say “rated sensitivity” here. Then

- we can define it in section 3

- In section 5 we have a procedure for finding it, even if that is a declaration by the manufacturer.

That way we have it all in one place and can alter it or epply a requirement if necessary.

Probably not needed for this requirement.

What is the technical term for this frequency allocation?

Move to a NOTE or the Description.

The choice depends on how the test is run. Is the level increased until there is a response, or is it one test at the high level?

Checking on how we run this test now.

Probably not needed for this requirement.

Probably not needed for this requirement.

Probably not needed for this requirement.

Probably not needed for this requirement.

If there is no specific requirement, then we do not need this clause.

IS there a requirement on rated sensitivity?

No, it depends on the deployment.  We are having the manufacturer declare the level and then verify that their rating is correct.

AIUI, in part -5-1 we have EUT that Tx on 1030 and Rx on 1090 and EUT that Rx on 1090.

For Rx only devices the spurious emissions spec should be the standard one  I have pasted in.

For Tx/Rx devices we may need to modify it with the residual power output specification.

We have a choice.

Write a spurious emission spec for all EUT with different limits for different modes, or

Write separate specs for Txs and Rxs

We addressed this in the Applicability section 4.1.1. Spurious emissions for units with both the sensor and interrogation functions only need to be met when the transmitter is idle.  Otherwise the transmitter spectrum applies.

Are there EUT that have a Tx in idle mode while a Rx is running? If so, we will need a row for this.

Probably not needed for this requirement, but may want extreme voltage conditions

Phrase some words to outline that for each test it is separately outlined if it needs to be conducted in standard or standard and extreme conditions.

I have done this in section 4. But we need a section defining normal and extreme conditions.

Is it in another Part of EN 303 213?
If not we can copy from another standard.

Has to be checked (test lab!?)

Reference for the nomenclature “D-M” ???

Not sure if this is still test signal is used in the tests below

Get a valid message.

Get a valid message.

Here are some clauses found in other RF standards. If they are not covered in other Parts of EN 303 213, we can copy them from the other standards.

Ideally the name of the test should be the same as the requirement, but this is not absolutely essential if the clause is called up by number.

Do we need a description, since there is one in section 4.

For transmitters with adjustable power levels, should we also test at lower power levels, perhaps minimum rated power?

That was the old part “conditions of measurements” in the requirements section. Please have a look into this text and the proposed text just below here and check for inconsistencies and errors.

I suggest we do not say this in the test  procedures but instead specify it in the technical requirements.

(The requirement is then on the performance of the EUT rather than on the conduct of the test.)

I’m proposing this solution, I don’t know if we came to a consensus on this point.

Review other ETSI documents to determine if this level of detail is consistent.

If this is a requirement, then it should have a clause in section 4. Or we specify maximum DC in the test conditions.

Needed to test power variability?

This seems to be mutiple tests in one.

This is not necessarily a problem, but it must align with the requirements in section 4 – even if the clause in section 4 just says Limits: pass the test in clause 5.x.y.

We provided no limits in the limit section for Transmit Duty Cycle.  Perhaps this test is not needed?  Otherwise, I’m assuming we want the manufacturer to declare a maximum duty cycle and verify it.  If for no other reason than to make sure that “test signal 2” is actually appropriately stressing the transmitter.

Agree with Chris. If it is a technical requirement, then it should be mentioned in section 4.

Option to omit this and following steps if we don’t choose to explicitly test Mode AC interrogations.

This implies that the P4 pulse will always be present.  It is not required by ICAO, but given that this is for ASMGCS systems Mode AC only (i.e., short P4 pulse) should be used.  Not sure if ED-117A explicitly requires short P4.

See also step 6 below. Frequencies can be specificed in the Limits in section 4, or in the test procedure. But we must not be vague.

In this case, is the requirment

- That the test is done at one frequnecy and the EUT must pass

- There are no frequencies in the range at which the EUT will fail?

Take care to keep the limits in section 4.

Step 7 could be deleted.

Do we need to define idle mode better? If the EUT has more than one non-Tx mode (eg, standby, off, calibrate, warm up…) then the test may need to be done in each mode.

This is not listed as a requirement in section 4.

4.3.6 says dynamic range is declared by the manufacturer.

If this is a requirement then we need to think about how to specify it. As written it is a licence for the EUT to do anything it wants.

Do we need a ‘desired’ Mode A/C test signal?  Do we want to test sensitivity for Mode A/C also?

Are there additional signal generator parameters beyond the test signal description?

Review other ETSI documents to determine if this level of detail is consistent.

As noted above, we should keep the limits in section 4.

Section 5 is measurements.

As Step 7.

Chris to write a rationale for the table.

Done.

Are there additional signal generator parameters beyond the test signal description?

Review other ETSI documents to determine if this level of detail is consistent.

As above

Better to say something like 3 other combinations… or to give specific frequencies.

This is a good example. The procedure returns a value for the measurement that cn be comapred with the limit.

Check against latest skeleton. This is a moving goalpost.

In other RF standards there are normally Annexes on radiated measurements and test chambers.