THE CONCEPT OF UNIQUE IDENTITY

The Internet of Things embodies the means by which one thing can communicate with another thing via the Internet.  Here a thing is an “entity” as shown in the graphic below where an object communicates to another object or a person, legal or real.  For that “entity” to communicate it must possess an identifier.

Figure 1 — Ontology of identity

A telephone number is a good example of an identifier of an object on a network.  Internationally, the telephone number is comprised of several parts.

Figure 2 — ITU telephone network numbering plan

Another example of an identifier of an object on a network is an I.P. address.  Using IPv4 the 32-bit address of 192.168.0.6 can be illustrated as shown in Figure 3.

Figure 3 — Internet Protocol (I.P.) address using IPv4

In both of the above Figures (2 and 3), users of the network have agreed upon a common numbering system.  This common agreement permits each station on the telephone network or each device on the Internet to be able to communicate with any other device on these common networks.

The Internet of Things has no such universal numbering.

Extant Numbering Systems for RFID

There are several existing systems to uniquely identify physical objects in an RFID context.  These include:

- ISO/IEC 15459-1:2006, Information technology — Unique identifiers — Part 1: Unique identifiers for transport units

- ISO/IEC 15459-2:2006, Information technology — Unique identifiers — Part 2: Registration procedures

- ISO/IEC 15459-3:2006, Information technology — Unique identifiers — Part 3: Common rules for unique identifiers

- ISO/IEC 15459-4:2006, Information technology — Unique identifiers — Part 4: Unique identifiers for individual items

- ISO/IEC 15459-5:2007, Information technology — Unique identifiers — Part 5: Unique identifier for returnable transport items (RTIs)

- ISO/IEC 15459-6:2007, Information technology — Unique identifiers — Part 6: Unique identifier for product groupings

- ISO/IEC CD15459-7, Information technology — Unique identifiers — Part 7: Product packaging

- ISO/IEC 15963:2004, Information technology — Radio frequency identification for item management — Unique identification for RF tags

- ISO/IEC 7816-5:2004, Identification cards — Integrated circuit cards — Part 5: Registration of application providers,

- ISO/IEC 7816-6:2004, Identification cards — Integrated circuit cards — Part 6: Inter-industry data elements for interchange

- EPCglobal Tag Data Standards, Version 1.5

Figure 4 shows the memory layout of ISO/IEC 18000-6, Type C and ISO/IEC 18000-3, Mode 3 RF tags.  UIIs are encoded in Memory Bank ‘01’ as shown in Figure 5.  The 15459 series deals specifically with Unique Item Identifiers (UIIs), including the means to identify physical objects according to ISO TC 122’s 1736x series and EPC.

ISO/IEC 18000-6C and -3m3 and EPCglobal Memory Architecture

Figure 4 — 18000-6C & 3m3, Memory structure

Figure 5 — 18000-6C & 3m3, Memory Bank (MB) “012”

Unique Identifier of a Physical Object (UII)

The UII can follow one of two formats, designated by the state of Bit 17h of Memory Bank “012”.  If Bit 17 is a “1” what follows at Bit 18h is an AFI (Application Family Identifier).  The AFI formats are shared between JTC 1/SC 31 and JTC 1/SC 17 (Integrated Circuit Cards) and their values are as shown in Table 1.  The values under the control of JTC 1/SC 31 are shown in Table 2.

Table 1 – AFI values

| AFI most significant nibble | AFI least significant nibble | Meaning | Examples / note |
| --- | --- | --- | --- |
| 0 | 0 | All families and subfamilies | No applicative pre-selection |
| X | 0 | All families and subfamilies | No applicative pre-selection |
| X | Y | Only the Yth subfamily of family X |  |
| 1 | 0, Y | Transport | Mass transit, Bus, Airline |
| 2 | 0, Y | Financial | IEP, Banking, Retail |
| 3 | 0, Y | Identification | Access control |
| 4 | 0, Y | Telecommunication | Public telephony |
| 5 | 0, Y | Medical |  |
| 6 | 0, Y | Multimedia | Internet services |
| 7 | 0, Y | Gaming |  |
| 8 | 0, Y | Data storage | Portable files |
| 9 | 0, Y | GS1 system for Application Identifiers | Managed by JTC 1/SC 31 |
| A | 0, Y | ISO/IEC JTC 1SC 31 | Data Identifiers as defined in ISO/IEC 15418 |
| B | 0, Y | UPU | Managed by JTC 1/SC 31 |
| C | 0, Y | IATA | Managed by JTC 1 |
| D | 0, Y | RFU | Managed by JTC 1/SC 17 |
| E | 0, Y | RFU | Managed by JTC 1/SC 17 |
| F | 0, Y | RFU | Managed by JTC 1/SC 17 |

Table 2 – AFI values assigned by JTC 1/SC 31

| Organization: function | AFI byte | Data Format binary | OID for UII | Data Format for additional memory | Root-OID for other data |
| --- | --- | --- | --- | --- | --- |
| ISO/IEC 17367: Supply chain applications of RFID – Product tagging [separate UII memory, with Data Identifiers in separate memory] | A1 | xxx01010 (means DI) | 1 0 15459 4 | xxx01010 (means DI) | 1 0 15418 1 (“1” suffix is to identify DIs, “0” for AIs) |
| ISO/IEC 17365: Supply chain applications of RFID – Transport unit [separate UII memory, with Data Identifiers in separate memory] | A2 | xxx01010 | 1 0 15459 1 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17364: Supply chain applications of RFID – Returnable transport item [separate UII memory, with Data Identifiers in separate memory] | A3 | xxx01010 | 1 0 15459 5 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17367: Supply chain applications of RFID – Product tagging, containing hazardous materials [separate UII memory, with Data Identifiers in separate memory] | A4 | xxx01010 | 1 0 15459 4 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17366: Supply chain applications of RFID – Product packaging [separate UII memory, with Data Identifiers in separate memory] | A5 | xxx01010 | 1 0 15459 4 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17366: Supply chain applications of RFID – Product packaging, containing hazardous materials [separate UII memory, with Data Identifiers in separate memory] | A6 | xxx01010 | 1 0 15459 4 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17365: Supply chain applications of RFID – Transport unit, containing hazardous materials [separate UII memory, with Data Identifiers in separate memory] | A7 | xxx01010 | 1 0 15459 1 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17364: Supply chain applications of RFID – Returnable transport item, containing hazardous materials [separate UII memory, with Data Identifiers in separate memory] | A8 | xxx01010 | 1 0 15459 5 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17363: Supply chain applications of RFID – Freight containers [separate UII memory, with Data Identifiers in separate memory] | A9 | xxx01101 | 1 0 10891 0 | xxx01010 | 1 0 15418 1 |
| ISO/IEC 17363: Supply chain applications of RFID – Freight containers, containing hazardous materials [separate UII memory, with Data Identifiers in separate memory] | AA | xxx01101 | 1 0 10891 0 | xxx01010 | 1 0 15418 1 |
| IATA: baggage handling [separate UII memory] | C1 | xxx01100 | 1 0 15961 12 1 | xxx01100 | 1 0 15961 12 |
| EDItEUR: library items | C2 | xxx00110 | 1 0 15961 8 1 |  | 1 0 15961 8 |
| ISBT item level blood products 7 | C3 |  |  |  |  |

If Bit 17h is a “0” what follows, beginning at Bit 20h is an EPC format.  Table 3 shows an illustrative example of an EPC, specifically a Serialized GTIN.

Table 3 – EPC UII

|  | Header | Filter Value | Partition | Company Prefix | Item Reference | Serial Number |
| --- | --- | --- | --- | --- | --- | --- |
| SGTIN-96 | 8 bits | 3 bits | 3 bits | 20-40 bits | 24-4 bits | 38 bits |
|  | 0011 0000 | TDS Tbl 5 | TDS Tbl 6 |  |  |  |

The EPC UII can take many different forms including the identity of a physical object for sale (SGTIN), a shipping container (SSCC), a returnable transport item (GRAI), an asset identifier (GIAI), a serialized location code (SGLN), a serialized service code (GSRN), or a serialized document number (GDTI).  Further there are permutations of these types of identification, which has been assigned a unique header.  These headers begin at Bit 20h of Memory Bank “01” (Figures 4 and 5).  A listing of these headers, as of 1 March 2008 can be found in Table 4.

Table 4 – EPC Headers

| Header Value (binary) | Header Value (hex) | Encoding Length (Bits) | Encoding scheme |
| --- | --- | --- | --- |
| 0000 0000 | 00 | NA | Unprogrammed tag |
| 0000 0001 | 01 | NA | Reserved for future use |
| 0000 001x | 02, 03 | NA | Reserved for future use |
| 0000 01xx | 04, 05 06, 07 | NA | Reserved for future use |
| 0000 1000 to 0000 1111 | 08 to 0F | NA | Available after 2009-07-01 |
| 0001 0000 to 0010 1011 | 10 to 2B | NA | Reserved for future use |
| 0010 1100 | 2C | 96 | GDTI-96 |
| 0010 1101 | 2D | 96 | GSRN-96 |
| 0010 1110 | 2E | 96 | Reserved for future use |
| 0010 1111 | 2F | 96 | DoD-96 |
| 0011 0000 | 30 | 96 | SGTIN-96 |
| 0011 0001 | 31 | 96 | SSCC-96 |
| 0011 0010 | 32 | 96 | SGLN-96 |
| 0011 0011 | 33 | 96 | GRAI-96 |
| 0011 0100 | 34 | 96 | GIAI-96 |
| 0011 0101 | 35 | 96 | GID-96 |
| 0011 0110 | 36 | 198 | SGTIN-198 |
| 0011 0111 | 37 | 170 | GRAI-170 |
| 0011 1000 | 38 | 202 | GIAI-202 |
| 0011 1001 | 39 | 195 | SGLN-195 |
| 0011 1010 | 3A | 113 | GDTI-113 |
| 0011 1011 to 0011 1111 | 3B to 3F | NA | Reserved for future use |
| 0100 0000 to 0111 1111 | 40 to 7F | NA | Available after 2009-07-01 |
| 1000 0000 to 1011 1111 | 80 to BF | NA | Available after 2009-07-01 |
| 1100 0000 to 1100 1101 | C0 to CD | NA | Available after 2009-07-01 |
| 1100 1110 | CE | NA | Available after 2009-07-01 |
| 1100 1111 to 1111 1110 | CF to FE | NA | Available after 2009-07-01 |
| 1111 1111 | FF | NA | Reserved for future headers longer than 8 bits |

As can be seen above, of the 256 possible values available with an 8-bit code, EPCglobal has used 14 of these codes.

Unique Tag Identification (TID)

ISO/IEC 15963 is the overarching standard to uniquely identify an RF tag (TID), as opposed to the physical object to which it is attached.  An “allocation class” is an 8-bit value used to classify organizations allowed to allocate unique tag identification.  A unique TID consists of three fields, as shown in Table 5.

Table 5 — Structure of the permanent unique TID

| AC | TID issuer registration number | Serial number |
| --- | --- | --- |
| 8 bits | Size defined by AC value | Size defined by AC and TID issuer value |
| MSB |  |  | LSB |

The registration authorities identified in Table 6 assign the length of the RF tag unique identifier.

Table 6 — Classes of TID issuer

| Allocation class value | Class | TID issuer identifier size | Serial number size | Registration authority (of TID issuer registration number) |
| --- | --- | --- | --- | --- |
| 000xxxxx | INCITS 256 | per ANS INCITS 256 | per ANS INCITS 256 | autoid.org |
| 001x xxxx to 1101 xxxx | RFU | N/A | N/A | Reserved for future use by ISO |
| '11100000' | ISO/IEC 7816-6 | 8 bits | 48 bits | APACS (ISO/IEC 7816-6 registration authority) |
| '11100001' | ISO/TS 14816 | per NEN | per NEN | NEN (ISO/TS 14816 registration authority) |
| '11100010' | GS1 | per GS1 | per GS1 | GS1 |
| 1110 0011 to 1111 1111 | RFU | N/A | N/A | Reserved for future use by ISO |

Table 7 provides a listing of selected ISO/IEC 15963 Allocation Classes and their associated TID and serial number length.  This listing includes all assignments made pursuant to ASC INCITS 256.

Table 7 – ISO/IEC 15963 Tag IDs including all ASC INCITS 256 assignments

|  | Total bits | Allocation Class (AC) | Tag ID registration number | Serial number |
| --- | --- | --- | --- | --- |
| Standard |  | 8 bits | Size defined by AC value | Size defined by AC and UID value |
| INCITS 256 | 64 | 000x xxxx |  |  |
| INCITS 256, 18000-7 | 32 | 000x xxxx | 000x xxxx |  |
| ISO 18000-7 | 48 | 000x xxxx | xxxx xxxx | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-7 (Savi) | 48 | 0001 0001 | 0000 0100 | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-2, Type A (7816-6) | 56 + AC | 1110 0000 | xxxx xxxx (per 7816-6) | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-3m3 (non-EPC) | 16 - 496 | 1110 0000 | xxxx xxxx xxxx - xxxx xxxx xxxx | Maximum 496 bits |
| ISO 18000-3m3 (EPC) | 16 - 496 | 1110 0010 | xxxx xxxx xxxx -xxxx xxxx xxxx | Maximum 496 bits |
| ISO 18000-4 (Intermec – 7816-6) | 56 | 1110 0000 | xxxx xxxx (per 7816-6) | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-4 (Intermec – 256) | 56 | 0001 0010 | xxxx xxxx (Unassigned) | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-4 (Siemens/Nedap 7816-6) (see 18000-4 for details) | 32 | N/A | xxxx xxxx (per 7816-6) | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-6A | 64 | 1110 0010 | xxxx xxxx xxxx - xxxx xxxx xxxx | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-6B | 64 | 0001 0011 | xxxx xxxx xxxx - xxxx xxxx xxxx | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-6C (7816) | 64 | 1110 0000 | (per 7816-6) | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO 18000-6C (EPC) | 16 - 496 | 1110 0010 | xxxx xxxx xxxx - xxxx xxxx xxxx | TBD - 18000-6C, Table 1 states a maximum of 496 bits |
| ISO/IEC 24730 | 48 | 0000 0000 | xxxx - xxxx | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |
| ISO/IEC 24730 (WhereNet) | 48 | 0000 0000 | 0000 0000 | xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx |

ISO/IEC 7816 describes how to encode a TID with ISO/IEC 15963’s Allocation Class of “E0”.  Table 8 shows the format for an ISO/IEC 7816 TID.  The first field after the Allocation Class is the TID issuer code.  Table 9 shows the 7816-6 TID issuer codes assigned as of 2007-09-28.

Table 8 – ISO/IEC 7816-6 TID format

| MSB |  | LSB |
| --- | --- | --- |
| 64 57 | 56 49 | 48 1 |
| “E0” | IC Mfg code | IC manufacturer serial number |

Table 9 – ISO/IEC 7816-6 issuer codes (as of 2007-09-28)

| Identifier | Company | Country |
| --- | --- | --- |
| '01' | Motorola | UK |
| '02' | STMicroelectronics SA | France |
| '03' | Hitachi, Ltd | Japan |
| '04' | Philips Semiconductors | Germany |
| '05' | Infineon Technologies AG | Germany |
| '06' | Cylink | USA |
| '07' | Texas Instrument | France |
| '08' | Fujitsu Limited | Japan |
| '09' | Matsushita Electronics Corporation, Semiconductor Co. | Japan |
| '0A' | NEC | Japan |
| '0B' | Oki Electric Industry Co. Ltd | Japan |
| '0C' | Toshiba Corp. | Japan |
| '0D' | Mitsubishi Electric Corp. | Japan |
| '0E' | Samsung Electronics Co. Ltd | Korea |
| '0F' | Hynix | Korea |
| '10' | LG-Semiconductors Co. Ltd | Korea |
| '11' | Emosyn-EM Microelectronics | USA |
| '12' | INSIDE Technology | France |
| '13' | ORGA Kartensysteme GmbH | Germany |
| '14' | SHARP Corporation | Japan |
| '15' | ATMEL | France |
| '16' | EM Microelectronic-Marin SA | Switzerland |
| '17' | KSW Microtec GmbH | Germany |
| '18' | ZMD AG | Germany |
| '19' | XICOR, Inc. | USA |
| '1A' | Sony Corporation | Japan |
| '1B' | Malaysia Microelectronic Solutions Sdn. Bhd | Malaysia |
| '1C' | Emosyn | USA |
| '1D' | Shanghai Fudan Microelectronics Co. Ltd. | P.R. China |
| '1E' | Magellan Technology Pty Limited | Australia |
| '1F' | Melexis NV BO | Switzerland |
| '20' | Renesas Technology Corp. | Japan |
| '21' | TAGSYS | France |
| 22' | Transcore | USA |
| '23' | Shanghai belling corp., ltd. | China |
| '24' | Masktech Germany Gmbh | Germany |
| '25' | Innovision Research and Techology Plc | UK |
| '26' | Hitachi ULSI Systems Co., Ltd. | Japan |
| '27' | Cypak AB | Sweden |
| '28' | Ricoh | Japan |
| '29' | ASK | France |
| '2A' | Unicore Microsystems, LLC | Russian Federation |
| '2B' | Dallas Semiconductor/Maxim | USA |
| '2C' | Impinj, Inc. | USA |
| '2D' | RightPlug Alliance | USA |
| '2E' | Broadcom Corporation | USA |
| '2F' | MStar Semiconductor, Inc | Taiwan, ROC |
| '30' | eeDar Technology Inc. | USA |
| ‘31’ | RFIDsec | Denmark |
| ‘32’ | Schweizer Electronic AG | Germany |
| ‘33’ | AMIC Technology Corp | Taiwan |

The EPCglobal Tag Data Standard describes how to encode a TID with ISO/IEC 15963’s Allocation Class of “E2”.  Figure 6 shows the proposed format for an EPC TID.  The first field after the Allocation Class is the TID issuer code.  Table 10 shows the EPCglobal Tag mask-designer identifier code assignments.

| MEM BANK # | MEM BANK NAME | MEM BANK BIT ADDRESS | BIT ADDRESS |
| --- | --- | --- | --- |
| 102 | TID | D0h-DFh | User Memory Size [15:0] |
|  |  | C0h-CFh | BlockPermaLock Block Size [15:0] |
|  |  | B0h-BFh | BlockErase Size [15:0] |
|  |  | A0h-AFh | BlockWrite Size [5:0] | BlockErase Size [25:16] |
|  |  | 90h-9Fh | BlockWrite Size [21:6] |
|  |  | 80h-8Fh | Sensor Memory Address [11:0] | BWS [25:22] |
|  |  | 70h-7Fh | Optional Command Support [9:0] | SMA [17:12] |
|  |  | 60h-6Fh | Features Header #1 | Max EPC Size [4:0] | OCS [12:10] |
|  |  | 50h-5Fh | Serial Number [15:0] |
|  |  | 40h-4Fh | Serial Number [31:16] |
|  |  | 30h-3Fh | Serial Number [47:32] |
|  |  | 20h-2Fh | Serialization Header | Serial Number [55:48] |
|  |  | 10h-1Fh | TAG MDID [3:0] | TAG MODEL NUMBER [11:0] |
|  |  | 00h-0Fh | E2h | XTID | TAG MASK DESIGNER ID [10:4] |

Figure 6 — Proposed EPCglobal TID

Table 10 – EPCglobal task mask-designer codes

Not publicly available

Top Arc of an Object Identifier (OID)

Another format for numbering has been recommended in meetings of the ITU-T.  This recommendation is to encode a {joint-iso-itu} level arc for a service provider identification (SPID) in the format {joint-iso-itu-t(2) spid(28)} or “2.28”.

Four recommendations/standards are being considered by ITU-T

X.spid, Trusted Service Provider Identity (SPID)

This Recommendation | International Standard specifies the trusted Service Provider Identity system, including the construction of a SPID identifier within a new OID namespace {joint-iso-itu-t(2) spid(28)}. This text will be jointly developed by Q.10/17 and ISO/IEC JTC1/SC6.

F.spid, Administration of Service Provider Identity

This Recommendation specifies how trusted SPID identity is maintained, including registration of service providers into the SPID Name System and associated Registry Information Service.

X.sns, SPID Name System (SNS)

This Recommendation | International Standard specifies a SPID identifier resolver system provided using BIND - similar to ENUM and EPCglobal's Object Name System platforms.  The SNS would support a trusted, ultra high availability, low latency, distributed name system that resolves a SPID identifier to Dynamic Delegation Discovery System (DDDS) pointers to network based locations containing trusted SPID related network management identities (credentials, identifiers, attributes, and pattern representations) that are highly time-dependent.  The specification will describe necessary pointer attributes and provide for alternative and extensible DDDS implementations.

X.sreg, SPID Registry Information Service (SREG)

This Recommendation specifies an XML based schema for accessing non-time-dependent, latency-tolerant SPID registration information. SREG is a specialized information type that uses existing Internet Registration Information Service (IRIS) specifications for discovery and secure response-query to available registry information.

This text will be developed in coordination with Q.2/17.

The implication of the use of the ITU-T proposed recommendations is that a new top arc would need to be added to all RF tag communications.

IMPLICATIONS FOR THE FUTURE

The choices for a unique coding structure for the Internet of Things, as discussed above fall into three categories.

- Use of Unique Item Identifier (UII)

- Use of Unique Tag ID (TID)

- Adding something new, e.g. OID Top Arc (SPID)

The impact of the third option is that all existing tags would be rendered obsolete and only tags that have the new encoding would be capable of “internet connectivity”.  This implies that all silicon would need to be re-spun to add the new top arc.

The impact of the second option is that currently, in supply chain management applications, the first Memory Bank read is MB “01” encoding the UII, not MB “10” encoding the TID.  For “internet connectivity” and if Unique Tag ID would be used, a separate read command would need to be issued or the protocol modified, as currently it backscatters PC+UII.

The impact of the first option is for a body such as ISO or ITU-T to take over the remaining EPCglobal headers to create a truly universal coding system, that takes advantage of binary encoding as opposed to character-based encoding.  EPCglobal cannot be the registrar for headers other than for its own use.  It is proposed that EPCglobal be permitted 24 headers (10 more than they have already deployed).  The remaining 232 headers would be controlled by ISO/ITU-T.

It is believed that the first option is the best option for a universal coding system for the Internet of Things.

Respectfully submitted,

Craig K. Harmon

President & CEO

Bibliography

- Rutkowski, Anthony M., Identity Definition Correspondence Group Baseline Material, ITU-T Seoul, KR, January 2008, T05-IDM.GSI-080118-TD-GEN-0002!!MSW-E.doc

- Brock, David L., The Electronic Product Code (EPC), A Naming Scheme for Physical Objects, MIT AutoID Center, 2001 MIT-AUTOID-WH-002.pdf

- ISO/IEC 7816-5, Identification cards — Integrated circuit cards  Part 5: Registration of application providers

- ISO/IEC 7816-6, Identification cards — Integrated circuit cards  Part 6: Interindustry data elements for interchange

- ISO/IEC 15693-3, Identification cards — Contactless integrated circuit(s) cards — Vicinity cards — Part 3: Anticollision and transmission protocol

- ISO/IEC 15963, Information technology — Radio frequency identification for item management — Unique identification for RF tags

- ISO/IEC 18000-3, Information technology — Radio frequency identification for item management: — Part 3: Parameters for air interface communications at 13,56 MHz

- ISO/IEC 18000-6, Information technology — Radio frequency identification for item management: — Part 6: Parameters for air interface communications at 860 MHz to 960 MHz

- EPC TDS, EPCglobal Tag Data Standards Version 1.4 Candidate Specification February 1, 2008

- EPC TDS, EPCglobal Tag Data Standards Version 1.5

- UHF Gen 2, EPC Radio-Frequency Identity Protocols Class-1 Generation-2 UHF RFID Protocol for Communications at 860 MHz-960 MHz Version 1.2.9

- HF Gen 2, EPC Radio-Frequency Identity Protocols Class-1 Generation-2 HF RFID Protocol for Communications at 13.56 MHz Version 1.0.1

# Footnotes

The “00” international access was established by the International Telecommunications Union (ITU).  There is also a North American Numbering Plan (NANP) where “011” is used for international access.  The NANP is implemented by Anguilla, Antigua and Barbuda, Bahamas, Barbados, Bermuda, British Virgin Islands, Canada, Cayman Islands, Dominica, Dominican Republic, Grenada, Jamaica, Montserrat, Saint Kitts and Nevis, Saint Lucia, Saint Vincent and the Grenadines, Trinidad and Tobago, Turks and Caicos Islands, United States, including Guam,  Northern Mariana Islands,  Puerto Rico,  U.S. Virgin Islands,  and American Samoa.