## Slide 1: Open Source Projects Collaborations with ONAP
2018-09-21
ShiTao Li, Huawei
Rapporteur of ETSI GS NFV-SOL 001

## Slide 2: Topics
ETSI NFV descriptor model is used in ONAP
Collaboration between ETSI NFV and ONAP members

## Slide 3: ETSI NFV descriptor model is used in ONAP

## Slide 4: ONAP: onboard ETSI NFV VNF: ETSI GS NFV-SOL 001 & ETSI GS NFV-SOL 004
ONAP DM
HEAT
Onboarding
ONAP internal DM
Composition
ONAP internal DM
Orchestration
ONAP internal DM
Operation
ETSI GS NFV-SOL 001
ETSI GS NFV-SOL 004
On boarding time: support multiple options,
  ETSI GS NFV-SOL001 & ETSI GS NFV-SOL004 based model is one of the options
Run time: 2 internal DM options,
  ONAP R2+ Design-Time Resource DM clean version (based on ETSI GS NFV-SOL001 ) enhancement for VoLTE, vCPE (stretch goal)
  ONAP SDC TOSCA AID enhancement for vCPE
DM: Data model

## Slide 5: Two internal DMs used in ONAP R2 and R3
SDC AID model
R2/R3 Model
  Based on ECOMP
  ~40 node types, ~60 data types
  Implemented by using HEAT + TOSCA
  Supported by vCPE use case
  Using heat model as on-boarding model
  https://wiki.onap.org/display/DW/SDC+Data+model
  Introduced by many ETSI NFV members
  Reference ETSI NFV specs (ETSI GS NFV-IFA011, ETSI GS NFV-SOL001)
  ~10 node types, ~40 data types
  Implemented by using TOSCA
  Supported by VoLTE use case
  Same with on-boarding model
  ONAP R2+ Design-Time Resource DM clean version

## Slide 6: ONAP R3(Casablanca release) Model
This model is based on ETSI GS NFV-IFA011 v 2.4.1 and ETSI GS NFV-SOL001 v 0.6.0.
https://wiki.onap.org/display/DW/ONAP+R3+Resource+Design+Time+Model+Clean+Version
Support only one VNF deployment flavour
Support VnfExtCpd exposed by VduCpd
Does not support scalingAspect
Does not support instantiation level
Does not support VNF lifecycle interface

## Slide 7: ONAP R3 extends
Those are the examples that ONAP R3 Model adds new properties on top of the ETSI NFV model.
https://wiki.onap.org/display/DW/ONAP+R3+Resource+Design+Time+Model+Clean+Version

## Slide 8: Collaboration between ETSI NFV and ONAP members

## Slide 9: Collaboration Between ETSI NFV and ONAP members
Base module
Add-on module
VF module
ETSI NFV updates the scaling model, so it can be easily mapped to the SDC AID model.
Some of the ONAP requirements are accepted by ETSI NFV spec also.

## Slide 10: ONAP: onboarding ETSI NFV VNFD
Service Designer defines the “Service A’” model which includes VNF 1’. Included is the definition of the input level data that must be supplied with the Service A instantiation request, and the associated data transformation and mapping to the VNF 1’ “deployment data” and “application data”.
ONAP SD, VNFD
VNF 1’
Service A’
ONAP Design-time
Translate
VNF 1
SOL004 (VNF Package) SOL001 (VNFD)
Enrich
Service Designer enriches the “VNF 1” model to describe the input level data that must be supplied with the instantiation request to configure the application data, optimization information for specific network cloud environments, and the data transformation and mapping to VNF configuration API(s).
ONAP Run-time
Translation involves creating an equivalent VNF model in ONAP based on the formal ETSI spec. I.e., translation results in an ONAP representation of VNF 1 (blue) that has only “deployment data” specified.

## Slide 11: Thank you!