|  | GSMOBA-09013 |
| --- | --- |
| European Telecommunications Standards Institute GSM Onboard Aircraft Meeting # 11 Oslo, Norway, January 27 – 28, 2009 |  |

| Source: | AeroMobile |
| --- | --- |
| Date: | January 21, 2009 |
| Title: | Proposed change in subsection 4.6.4 of TS 102576 |
| Document for: | Decision |
| Agenda | tbd |

Proposed change in the subsection 4.6.4

Proposal:

Subsection 4.6.4 describes a measurement procedure to estimate the attenuation of aircraft at window. AeroMobile believe that there is significant empirical evidence that unless RF shielding on the windows is used the attenuation value can be down to 0 dB. Some sources even estimate a possible amplification (Att < 0 dB). Therefore it is suggested that a generic value of 0 dB is applied rather than allowing the parameter to be measured. In this the underlying assumption is that the margin of error by performing a single set of measurements is larger than relying on the empirical evidence available. Therefore the changes as shown in this document are suggested.

Decision:

If agreed it is proposed to modify the subsection 4.6.4 as defined below:

********************** Proposed change **********************

### 4.6.4 	Attenuation of aircraft at window

#### 4.6.4.1	Test purpose

To define the attenuation of the aircraft at the window for each frequency band covered by the NCU.

#### 4.6.4.2	Methods of estimation

The value of Attaircraft_window(n) shall for all frequencies be set to 0 dB, unless RF shielding on the windows is applied, in which case a value in accordance with the attenuation resulting from the shielding shall be used.

********************** End of change **********************