# Source:	SIEMENS AG
hannsjuergen.schwarzbauer@siemens.com

# Title:	Comments on M3UA TSS&TP v0.0.3 (DTS/MTS-00087)

# Agenda item:	MTP-IPT

| Decision |  |
| --- | --- |
| Discussion | X |
| Information |  |

Document for:

Abstract:

The comments given below need to be included in the final version of the M3UA TSS&TP before finally approving this document.

General comments:

- There are several tests which test the version number. Most of them are marked with 'Requires clarification in the IG'. This change is now included in the ID draft-ietf-sigtran-rfc3332bis-02.txt.

It is proposed to:

- replace the above text in quotation marks throughout the document with:
“Clarification contained in draft-ietf-sigtran-rfc3332bis-02.txt.”

- add the above mentionned Internet-Draft also to the References section.

Technical comments:

- TPId: M3UA_SGP_ASPSM_I_003

The reason given is wrong. Unexpected Message MAY be sent.

Action: Change the reason and do not force the sending the ERROR Message.

- TPId: M3UA_SGP_ASPTM_V_014

There is no requirement that two ASPs per AS have to be supported.

Action: Make these Optional.

- TPId: M3UA_SGP_ASPTM_V_015

There is no requirement that two ASPs per AS have to be supported.

Action: Make these Optional.

- TPId: M3UA_SGP_ASPTM_I_009

There is no requirement that two ASPs per AS have to be supported.

Action: Make these Optional.

# Footnotes

SIEMENS AG, Munich, Germany

Tel.:		+49 89 722 24236/Fax +49 89 722 130 24236

EMail:		 hannsjuergen.schwarzbauer@siemens.com