ETSI DTS/MTS-IPT-017 V0.0.2 (2006-12)

Technical Specification

Methods for Testing and Specification (MTS);

Internet Protocol Testing (IPT): IPv6 Mobility;

Interoperability Test Suite

Reference

DTS/MTS-IPT-017-IPv6-MobITS

Keywords

Testing, IPv6, Interoperability, IP, Mobility

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, send your comment to:
editor@etsi.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM and UMTSTM are Trade Marks of ETSI registered for the benefit of its Members.
TIPHONTM and the TIPHON logo are Trade Marks currently being registered by ETSI for the benefit of its Members. 3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	4

Foreword	4

Introduction	4

1	Scope	5

2	References	5

3	Definitions, symbols and abbreviations	5

3.1	Abbreviations	5

4	IPv6 Mobility Interoperability Test Specification	6

4.1	Test Descriptions	6

4.1.1	Index of test grouping	6

4.1.2	TDs extracted from RFC3775 [3] “Mobility Support in IPv6”	7

4.1.3	TDs extracted from RFC3776 [4] “Using IPsec to Protect Mobile IPv6 Signaling Between Mobile Nodes and Home Agents”	100

History	128

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Specification (TS) has been produced by ETSI Technical Committee MTS.

# Introduction

IPv6 is the next generation Internet. It gives vastly increased address space and true end-to-end communication. It has improved security and mobility features and allows 'plug-and-play' connection to the network. The complexity of implementing IPv6 technology and the relative openness of IETF standards means that wide-ranging and effective testing of IPv6 products will be one of the key factors in ensuring the deployment, interoperability, security and reliability of the IPv6 infrastructure.

The present document specifies interoperability tests for IPv6 Mobility. The test suite results from and analysis of RFC3775 and RFC3776, the extraction of the requirements contained in these documents, and a selection of the requirements which could be tested by interoperability means.

The methodology and framework used to analyse the RFCs, to extract the requirements, write the Test Purposes, and the test descriptions is described in ETSI TS 102 551 [1].The reader is strongly encouraged to read TS 102 551 [1] in order to make the best usage of the present document.

# Scope

The present document specifies the interoperability Test Descriptions (TDs) with integrated Test Purposes (TPs) for the IPv6 Mobility standards. The TDs are presented in the tabular form specified in ETSI TS 102 424 [1] and the TPs are defined using the TPLan notation also described in ETSI ES 202 553.

# References

For the purposes of this Technical Report (TR), the following references apply:

[1]	TS 102 351 : "Methods for Testing and Specification (MTS); Internet Protocol Testing (IPT); IPv6 Testing: Methodology and Framework".

[2]	ES 202 553: "Methods for Testing and Specification (MTS); TPLan: A notation for expressing test Purposes"

[3]	RFC3775 "Mobility Support in IPv6"

[4]	RFC3776 "Using IPsec to Protect Mobile IPv6 Signaling Between Mobile Nodes and Home Agents"

[5]	TS 102 559 : "Methods for Testing and Specification (MTS); Internet Protocol Testing (IPT): IPv6 Mobility; Requirements Catalogue"

# Definitions, symbols and abbreviations

## Abbreviations

For the purposes of the present document, the following abbreviations apply:

CN	Correnpondent Node

EUT	Equipment Under Test

HA	Home Agent

HS	Host

i/f	interface

LL	Link Local

M/cast	Multicast

MN	Mobile Node

MTU	Maximum Transmission Unit

PMTU	Path MTU

QE	Qualified Equipment

RT	Router

SL	Site Local

TP	Test Purpose

TD	Test Description

TPLan	Test Purpose Language

TSS	Test Suite Structure

# IPv6 Mobility Interoperability Test Specification

## Test Descriptions

Test Description presentation and concepts are explained in TS 102 551 [1].

Requirements referred to within the Test Description (example: RQ_001_1016) are all contained in TS 102 559 [5], the IPv6 Mobility “Requirements catalogue”.

### Index of test grouping

In the present document, tests have been grouped according to the original RFC clause numbers from which they were extracted.

In the table below, each close number (example: “§5.1”) refers to the clause number of the RFC from which the requirements covered by the Tests Descriptions were extracted.

Note that Test Descriptions covering requirements coming from more than one clause are repeated in the relevant clause.

TDs extracted from RFC3775 “Mobility Support in IPv6”	7

§5.1 Binding Updates to Home Agents	7

§5.2.5 Return Routability Procedure	8

§5.2.6 Authorizing Binding Management Messages	9

§8.4 IPv6 Home Agents		11

§8.5 IPv6 Mobile Nodes		12

§9 Correspondent Node Operation	12

§9.3.1 Receiving Packets with Home Address Option	16

§9.3.2 Sending Packets to a Mobile Node	23

§9.3.4 Receiving ICMP Error Messages	24

§9.3 Packet Processing		26

§9.4.1 Receiving Home Test Init Messages	27

§9.4.2 Receiving Care-of Test Init Messages	28

§9.4 Return Routability Procedure	29

§9.5.1 Receiving Binding Updates	30

§9.5.2 Requests to Cache a Binding	32

§9.5.4 Sending Binding Acknowledgements	36

§9.5.5 Sending Binding Refresh Requests	37

Binding Cache Management (was: §9.6 Cache Replacement Policy)	39

§10 Home Agent Operation	41

§10.5  Dynamic Home Agent Address Discovery	42

§10.6 Sending Prefix Information to the Mobile Node	43

§10.6.2 Scheduling Prefix Deliveries	44

§10.6.3  Sending  Advertisements	48

§10.6 Sending Prefix Information to the Mobile Node	48

§10.3.2  Primary Care-of Address De-Registration	49

§10.3.1  Primary Care-of Address Registration	51

§10.3 Processing Bindings	58

§10.4.1  Intercepting Packets for a Mobile Node	59

§10.4.2 Processing Intercepted Packets	62

§10.4.3  Multicast Membership Control	65

§10.4.5 Handling ReverseTunneled Packets	66

§10.4.6 Protecting  Return Routability packets	67

§11 Mobile Node Operation	70

§11.3 Packet Processing		70

§11.3.1 Sending Packets While Away From Home	71

§11.4 Home Agent and Prefix Management	74

§11.4.1 Dynamic Home Agent Address Discovery	76

§11.4.2 Sending Mobile Prefix Solicitations	78

§11.4.3 Receiving Mobile Prefix Advertisements	81

§11.5 Movement		82

§11.5.1 Movement Detection	84

§11.5.2 Forming New Care-of Addresses	85

§11.5.3 Using Multiple Care-of Addresses	87

§11.5.4 Returning Home	88

§11.6.3 Protecting Return Routability Packets	90

§11.6 Return Routability Procedure	91

§11.6.1 Sending Test Init Messages	92

§11.6.2 Receiving Test Messages	93

§11.7.1 Sending Binding Updates To The Home Agent	93

§11.7.2 Correspondent registration	98

§11.7.3 Receiving Binding Acknowledgements	99

§11.7.4 Receiving Binding Refresh Requests	99

TDs extracted from RFC3776 “Using IPsec to Protect Mobile IPv6 Signaling Between Mobile Nodes and Home Agents”	100

§4.1 Mandatory Support		100

§4.2 Policy Requirements	108

§4.3 IPsec Protocol Processing	110

### TDs extracted from RFC3775 [3] “Mobility Support in IPv6”

###### §5.1 Binding Updates to Home Agents

| Test Description |
| --- |
| Identifier: | TD_MOB_1016_01 | Test Purpose: | TP_MOB_1016_01 |
| Summary: | 'Home Agent supports transport_mode_ESP protection of Binding Update messages' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1016 |
| with { QE1 disconnected and QE1 configured to protect any Binding_Update packet using transport_mode_ESP } ensure that { when { QE1 is connected to a foreign_network and QE1 receives a packet from QE4 indicating that a response is required } then { QE1 sends response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is disconnected QE1 is configured to protect Binding Update packets using transport mode ESP |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Connect QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1017_01 | Test Purpose: | TP_MOB_1017_01 |
| Summary: | 'Mobile Node uses transport_mode_ESP to protect Binding Update messages' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1017 |
| with { QE1 configured to accept only a Binding_Update secured using transport_mode_ESP } ensure that { when { EUT moves to a foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected to Home Network 1 QE1 configured to serve as Home Agent for EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Configure QE1 to accept only ESP protected binding update messages |  |  |
| 2 | Move EUT to foreign network 1 |  |  |
| 3 | Wait a few seconds to allow EUT to attempt to register with QE1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 5 | Check: Does QE4 receive an Echo Reply from EUT? | Yes | No |
| Observations: |  |

###### §5.2.5 Return Routability Procedure

| Test Description |
| --- |
| Identifier: | TD_MOB_1047_01 | Test Purpose: | TP_MOB_1047_01 |
| Summary: | 'Correspondent Node completes Return Routability Procedure before accepting a Binding Update from a mobile node' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1047 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization and QE1 unreachable from QE4 -- QE4 cannot complete RRP } ensure that { when { QE4 is requested to send a packet to the EUT indicating that a response is required } then { EUT sends no response directly to QE4 } } |
| Pre-test conditions: | Not testable by interoperability means Not possible for a QE to send a BU without completing the RRP ! |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

###### §5.2.6 Authorizing Binding Management Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1068_01 | Test Purpose: | TP_MOB_1068_01 |
| Summary: | 'Correspondent Node does not establish any binding with a lifetime greater than MAX_RR_BINDING_LIFETIME' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1068 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 } ensure that { when { EUT establishes a binding to QE4} then { EUT and QE4 are able to communicate directly within the binding_lifetime and EUT and QE4 are unable to communicate directly after MAX_RR_BINDING_LIFETIME } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to perform Route Optimization QE4 is configured to perform Route Optimization QE4 is connected to Foreign Network 1 and registered to its Home Agent QE1 QE3 is configured with the same (home) address as QE4 QE3 is disconnected from Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4? | YES | NO |
| 3 | Wait a few seconds (to let QE4 and EUT perform the Return Routability Procedure and establish Bindings) |  |  |
| 4 | Disconnect QE1 from Home Network 1 |  |  |
| 5 | Cause EUT to send an Echo Request to the home address of QE4 |  |  |
| 6 | Check: does EUT receive an Echo Reply from QE4? (this ensures that EUT and QE4 have established a Binding) | YES | NO |
| 7 | Connect QE3 to Home Network 1 |  |  |
| 8 | Disconnect QE4 from Foreign Network 1 |  |  |
| 9 | Cause EUT to send an Echo Request to the home address of QE4 |  |  |
| 10 | Check: does EUT receive an Echo Reply from QE4? | NO | YES |
| 11 | Wait 420 seconds==MAX_RR_BINDING_LIFETIME (Binding between EUT and QE4 Bindings has expired) |  |  |
| 12 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 13 | Check: does EUT receive an Echo Reply from QE3 (which is a clone of QE4)? | YES | NO |
| Observations: | Once the Bindings have expired the Correspondent Node can no longer communicate directly with the Mobile Node and will send the Echo Request to the Home Address of the Mobile Node via the Home Agent. In our case, QE3 respond because it is configured with the same address as QE4. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1068_02 | Test Purpose: | TP_MOB_1068_02 |
| Summary: | 'Mobile Node does not establish any binding with a lifetime greater than MAX_RR_BINDING_LIFETIME' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1068 |
| --NOT interop TESTABLE -- ==> there is no Interoperability method to guarantee that a -- Mobile Node (on a foreign network) will use its Home Address -- to send a new packet (instead of using its Care-of-Address). with { EUT configured to perform route_optimization and EUT away_from_home and EUT registered to QE1 and QE4 configured to perform route_optimization } ensure that { when { EUT establishes a binding to QE4 } then { EUT and QE4 are able to communicate directly within the binding_lifetime and EUT and QE4 are unable to communicate directly after MAX_RR_BINDING_LIFETIME } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEANS There is no Interoperability method to guarantee that a Mobile Node (on a foreign network) will use its Home address to send a new packet (instead of using its Care-of-Address). |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

###### §8.4 IPv6 Home Agents

| Test Description |
| --- |
| Identifier: | TD_MOB_1803_01 | Test Purpose: | TP_MOB_1803_01 |
| Summary: | 'Home Agent discards packets received from a non registered mobile node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_05 |
| References: | RQ_001_1803 |
| with { EUT disconnected from home_network 1 and QE2 configured to use the same IP_address as EUT and QE1 away_from_home and QE1 registered to QE2 and QE1 configured to perform route_optimization and QE4 configured to perform route_optimization } ensure that { when { QE2 is disconnected from home_network and EUT is connected to home_network and QE1 is requested to send a packet to QE4 indicating that a response is required } then { QE3 indicates no receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is disconnected. QE2 serves as Home Agent on Home Network 1 with the same address as EUT. QE1 is connected to Foreign Network 1 and registered to its Home Agent QE2. QE1 is configured to perform Route Optimization. QE4 is configured to perform Route Optimization. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE2 |  |  |
| 2 | Connect EUT to Home Network 1 |  |  |
| 3 | Cause QE1 to send an Echo Request to QE4 |  |  |
| 4 | Check: does QE1 receive an Echo Reply | No | Yes |
| Observations: | Ensure that QE1 use its Home Address when pinging QE4 (Home Address Option present in IPV6 packet). |

###### §8.5 IPv6 Mobile Nodes

| Test Description |
| --- |
| Identifier: | TD_MOB_1810_01 | Test Purpose: | TP_MOB_1810_01 |
| Summary: | 'MN is able to receive tunneled multicast packets from HA' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1810 |
| with { EUT subscribed to a global_multicast_group and EUT away_from_home and EUT registered to QE1 } ensure that { when { QE3 is requested to send a packet to the global_multicast_group } then { QE3 indicates no receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 EUT has registered to multicast group FF1E::1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Cause QE3 to send an Echo Reply to multicast address FF1E::1 |  |  |
| 3 | Check: does QE3 receive an Echo Reply | Yes | No |
| Observations: |  |

###### §9 Correspondent Node Operation

| Test Description |
| --- |
| Identifier: | TD_MOB_1013_01 | Test Purpose: | TP_MOB_1013_01 |
| Summary: | 'Home Agent supports the protection of Binding Update message' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1013 |
| with { QE1 at_home and QE1 configured to protect any Binding_Update } ensure that { when { QE1 moves to a foreign_network and QE4 is requested to send a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 is configured to protect Binding Update messages |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (for QE1 to establish a binding with EUT) |  |  |
| 3 | Cause QE4 to send an Echo Request to the home address of QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply? | Yes | No |
| Observations: | If EUT does not support protection of Binding Update, then it is unable to accept the binding. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1013_02 | Test Purpose: | TP_MOB_1013_02 |
| Summary: | 'Mobile Node supports the protection of Binding Update message' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1013 |
| with { EUT at_home and QE1 configured to accept only a secured Binding_Update } ensure that { when { EUT moves to a foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to home network 1. QE1 is configured to accept only protected Binding Update messages. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (for EUT to establish a binding with QE1) |  |  |
| 3 | Cause QE4 to send an Echo Request to the home address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_01 | Test Purpose: | TP_MOB_1082_01 |
| Summary: | 'Home Agent uses a Security Association to protect integrity and authenticity of Mobile_Prefix_Solicitations and Advertisements' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1607 |
| with { QE1 at_home and QE1 configured to protect Mobile_Prefix_Solicitations and QE1 configured to accept only secured Mobile_Prefix_Advertisements and QE1 configured to have a short prefix_lifetime --(suggest 30s) } ensure that { when { QE1 moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT QE1 is configured to protect Mobile Prefix Solicitation messages QE1 is configured to only accept protected Mobile Prefix Advertisement messages EUT is configured to advertise a prefered prefix lifetime of 20 sec EUT is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that initial lifetime of the home address of QE1 has expired |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_02 | Test Purpose: | TP_MOB_1082_02 |
| Summary: | 'Mobile Node uses a Security Association to protect integrity and authenticity of Mobile Prefix Solicitaions and Advertisements' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1663, RQ_001_1664 |
| with { EUT at_home and QE1 configured to accept only secured Mobile_Prefix_Solicitations and QE1 configured to protect Mobile_Prefix_Advertisements and EUT configured to have a short prefix_lifetime (--suggest 30s)' } ensure that { when { EUT moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to the EUT indicating that response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE1 is configured to only accept protected Mobile Prefix Solicitation messages QE1 is configured to protect Mobile Prefix Advertisement messages QE1 is configured to advertise a prefered prefix lifetime of 20 sec QE1 is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that EUT has send a Mobile Prefix Solicitation message and received a Mobile Prefix Advertisement message |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §9.3.1 Receiving Packets with Home Address Option

| Test Description |
| --- |
| Identifier: | TD_MOB_1412_01 | Test Purpose: | TP_MOB_1412_01 |
| Summary: | 'Correspondent Node receives packets directly from the Mobile Node when a binding exists or Mobile Node believes in its existence' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1412 |
| with { QE4 away_from_home and QE4 registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 having established a binding with EUT } ensure that { when { EUT is requested to send a packet to QE4 indicating that a response is required } then { EUT indicates receipt of the response directly from QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 EUT is configured to support route optimization QE4 is configured to support route optimization QE4 has established a binding with EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 from Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | yes | no |
| Observations: | Actually it would be sufficient to check whether EUT actually receives the ECHO request from QE4. However I don't know yet how we should test that. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1413_01 | Test Purpose: | TP_MOB_1413_01 |
| Summary: | 'Correspondent Node drops packets containing Home Address option (but no Binding Update) when there is no corresponding Binding Cache entry' |
| Roles: | Correspondent_Node, Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1413, RQ_001_1413, RQ_001_1427 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and EUT having no Binding_Cache_entry for QE4 and QE4 having a Binding_Cache_entry for EUT } ensure that { when { EUT receives a packet directly from QE4 indicating that a response is required } then { EUT sends no response to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT configured to perform route optimization QE3 configured to perform route optimization QE4 configured to perform route optimization EUT disconnected QE3 is connected to Home Network 2 QE3 is configured to have the same address as EUT QE4 connected to Foreign Network 1 and registered to its Home Agent QE1 QE4 has established a binding with QE3 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE3 from Home Network 2 |  |  |
| 2 | Connect EUT to Home Network 2 |  |  |
| 3 | Cause QE4 to send an Echo Request to EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT | NO | YES |
| Observations: | Step 3 : QE4 MUSTt use its Home Address when pinging EUT (Home Address Option present in IPv6 packet) |

| Test Description |
| --- |
| Identifier: | TD_MOB_1413_02 | Test Purpose: | TP_MOB_1413_02 |
| Summary: | 'Correspondent Node drops packets containing Home Address option (but no Binding Update) and send a Binding Error message to the Mobile Node, when there is no corresponding Binding Cache entry' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1413 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and EUT having no Binding_Cache_entry for QE4 and QE4 having a Binding_Cache_entry for EUT } ensure that { when { EUT receives a packet directly from QE4 indicating that a response is required } then { EUT sends no response to QE4 before EUT and QE4 are able to communicate } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN Mobile Node may ignore the Binding Error from Correspondent Node |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1414_01 | Test Purpose: | TP_MOB_1414_01 |
| Summary: | 'When using Route Optimization, a Correspondent Node drops any packet in which the Home Address option (but not Binding Update) does not match the Home Address recorded in its Binding Cache' |
| Roles: | Correspondent_Node, Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1414, RQ_001_1414, RQ_001_1427 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and QE4 having established a binding with EUT } ensure that { when { EUT receives a packet from QE4 containing a Home_Address_Option not set to the Home_Address of QE4 } then { EUT discards the packet } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to perform route optimization. QE4 is configured to perform route optimization. QE3 is configured to perform route optimization. QE5 is configured to perform route optimization. QE4 is connected to Foreign Network 1 and registered with QE1. QE4 has established a binding with EUT. QE5 is disconnected. QE5 is configured with the same link-layer Address as QE4. QE5 is configured with a Home Address which is not the same as QE4. QE5 is configured to be a Mobile Node to Home Network 1. QE5 is configured to register with its Home Agent QE1. QE3 is disconnected. QE3 is configured with the same addresses as EUT. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect EUT |  |  |
| 2 | Disconnect QE4 |  |  |
| 3 | Reboot QE1 (mobility support only) |  |  |
| 4 | Connect QE3 on Home Network 2 |  |  |
| 5 | Connect QE5 on Foreign Network 1 |  |  |
| 6 | Wait a few seconds (for QE5 to register with its Home Agent QE1) |  |  |
| 7 | Cause QE3 to send an Echo Request to the Home Address of QE5 |  |  |
| 8 | Check: does QE3 receive an Echo Reply from QE5 | YES | NO |
| 9 | Disconnect QE3 from Home Network 2 |  |  |
| 10 | Reconnect EUT to Home Network 2 |  |  |
| 11 | Cause QE5 to send an Echo Request to EUT |  |  |
| 12 | Check: Does QE5 receive an Echo Reply from EUT? | NO | YES |
| Observations: | Step 7 causes QE5 to establish a binding with QE3. QE3 and QE5 share the same Care-Of Address, but do not have the same Home Address. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1414_02 | Test Purpose: | TP_MOB_1414_02 |
| Summary: | 'When using Route Optimization, a Correspondent Node drops any packet in which the Home Address option (but not Binding Update) does not match the Home Address recorded in its Binding Cache and send a Binding Error mess |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1414 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and QE4 having established a binding with EUT } ensure that { when { EUT receives a packet from QE4 containing a Home_Address_Option not set to the Home_Address of QE4 } then { EUT discards the packet before EUT and QE4 are able to communicate } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN Mobile Node may ignore the Binding Error from Correspondent Node |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1415_01 | Test Purpose: | TP_MOB_1415_01 |
| Summary: | 'A Correspondent Node drops packets in which the Source Address does not match the care-of address recorded in the corresponding Binding Cache Entry' |
| Roles: | Correspondent_Node, Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1415, RQ_001_1415, RQ_001_1427 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and QE4 having established a binding with EUT } ensure that { when { EUT receives a packet from QE4 containing a Home_Address_Option set to the Home_Address of QE4 and containing a Source_Address not set to the Care_Of_Address of QE4 } then { EUT discards the packet } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to perform route optimization. QE3 is configured to perform route optimization. QE4 is configured to perform route optimization. QE5 is configured to perform route optimization. QE4 is connected to Foreign Network 1 and registred with QE1. QE4 has established a binding with EUT. QE5 is disconnected. QE5 is configured to be a Mobile Node to Home Network 1. QE5 is configured to use QE1 as Home Agent. QE5 is configured with the same Home Address address as QE4. QE5 is configured with a Link-Layer address which is not the same as QE4. QE3 is disconnected. QE3 is configured with the same addresses as EUT. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect EUT |  |  |
| 2 | Disconnect QE4 |  |  |
| 3 | Reboot QE1 (restart mobility support) |  |  |
| 4 | Connect QE3 on Home Network 2 |  |  |
| 5 | Connect QE5 on Foreign Network 1 |  |  |
| 6 | Wait a few seconds (for QE5 to register with its Home Agent QE1) |  |  |
| 7 | Cause QE3 to send an Echo Request to the Home Address of QE5 |  |  |
| 8 | Check: does QE3 receive an Echo Reply from QE5? | YES | NO |
| 9 | Disconnect QE3 from Home Network 2 |  |  |
| 10 | Connect EUT to Home Network 2 |  |  |
| 11 | Cause QE5 to send an Echo Request to EUT |  |  |
| 12 | Check: Does QE5 receive an Echo Reply from EUT? | NO | YES |
| Observations: | Step 7 causes QE5 to establish a binding with QE3. QE3 and QE5 share the Home Care-Of Address, but have different Care-Of addresses. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1415_02 | Test Purpose: | TP_MOB_1415_02 |
| Summary: | 'A Correspondent Node drops packets in which the Source Address does not match the care-of address recorded in the corresponding Binding Cache Entry and sends a Binding Error message to the Mobile Node' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1415 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 and QE4 having established a binding with EUT } ensure that { when { EUT receives a packet from QE4 containing a Home_Address_Option set to the Home_Address of QE4 and containing a Source_Address not set to the Care_Of_Address of QE4 } then { EUT discards the packet before QE4 and the EUT are able communicate } } --**********************************************************************-- --* This TP is phrased as a conformance test *-- --**********************************************************************-- --TP id : TP_MOB_1661_01 --summary : 'MN sends Mobil Prefix Solicitation to HA when its home address -- becomes invalid' --RQ ref : RQ_001_1661 --Role : Mobile_Node --config : CF_MOB_03 --TD ref : TD_MOB_1661_01 -- with { EUT away_from_home -- and EUT registered to QE1 -- } -- ensure that -- { when { EUT 'has its home address which becomes invalid' } -- then { EUT 'update the prefix lifetime information for its home address' } -- } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN Mobile Node may ignore the Binding Error from Correspondent Node |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

###### §9.3.2 Sending Packets to a Mobile Node

| Test Description |
| --- |
| Identifier: | TD_MOB_1423_01 | Test Purpose: | TP_MOB_1423_01 |
| Summary: | 'Correspondent Node sends packets directly to Mobile Node when a binding already exists' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1423 |
| with { QE4 away_from_home and QE4 registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 having established a binding with EUT and EUT having established a binding with QE4 } ensure that { when { QE4 sends a packet to the EUT indicating that a response is required } then { QE4 indicates receipt of the response directly from EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 EUT is configured to support route optimization QE4 is configured to support route optimization QE4 has established a binding with EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 from Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §9.3.4 Receiving ICMP Error Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1429_01 | Test Purpose: | TP_MOB_1429_01 |
| Summary: | 'Correspondent Node deletes a binding cache entry if it receives persistent ICMP Destination Unreachable messages' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1429 |
| -- EUT=CN2 -- QE1=HA1 -- QE4=MN1 with { QE4 'away from home and registered to QE1' and EUT 'having established a binding with QE4' } ensure that { when { QE4 'returns home' and QE4 'is unable to update its binding with EUT' and EUT is requested to 'send packets to QE4' } then { EUT 'is temporarily unable to communicate with QE4' and EUT 'is able to communicate again with QE4 before the end of the binding lifetime' } } |
| Pre-test conditions: | QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 EUT and QE4 have established binding QE4 is configured not to ask Binding Acknowledgements The tester is aware of the lifetime of these bindings and of the remaining binding lifetime when he starts this test. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE4 from Foreign Network 1 |  |  |
| 2 | Cause router R1 to disable its interface connected to Foreign Network 1 |  |  |
| 3 | Connect QE4 to Home Network 1 |  |  |
| 4 | Wait a few seconds to let QE4 perform the "return home" procedure. (a protocol analyzer can be used to ensure that the "return home" procedure is finished) Note that EUT will not receive Binding Update messages from QE4 (because R1 is disconnected from Foreign Network 1) and still thinks that QE4 is in Foreign Network 1. |  |  |
| 5 | Cause R1 to enable its interface connected to Foreign Network 1 |  |  |
| 6 | Cause EUT to send an Echo Request message to the Home Address of QE4 (the IPv6 destination address of the Echo Request sent should still be the former care-of-address of QE4 in Foreign Network 1) |  |  |
| 7 | Check: does EUT receive an Echo Reply from QE4? (EUT will receive an ICMP "Destination Unreachable" message from router R3) | NO | YES |
| 8 | Cause EUT to continuously send Echo Request messages to the Home Address of QE4 (EUT will receive persistent ICMP "Destination Unreachable" messages from router R3) |  |  |
| 9 | Check: after several unsuccessfull Echo Request messages, does EUT receive Echo Replies from QE4? | YES | NO |
| 10 | Check: when EUT receives the first Echo Reply from QE4, have the previous EUT <--> QE4 Bindings expired? | NO | YES |
| Observations: | Note1: If EUT received no Binding Update message when EUT returned home, and EUT manages to re-establish communication with QE4 before the expiration of the EUT <--> QE4 bindings, then this implies that the ICMP Destination Unreachable messages caused EUT to delete these bindings and to use the Home Address of QE4 instead its previous care-of-address as IPv6 destination address. Note2: RFC3775 states in clause 9.3.4 that "persistent ICMP messages lead to the deletion of the Binding", yet there is no detail about the amount of ICMP error messages that will cause the deletion to occur… Hence this TD might lead to inconclusive verdicts. Note 3 - Step 2: beware of interface buffers, which can keep and then retransmit paquets emitted before the interface is disabled! Do not unplug, but use "ifconfig" or equivalent... |

###### §9.3 Packet Processing

| Test Description |
| --- |
| Identifier: | TD_MOB_1344_01 | Test Purpose: | TP_MOB_1344_01 |
| Summary: | 'Correspondent Node discard received packets containing Type 2 Routing Headers' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1344 |
| with { EUT disconnected and QE4 configured to have the same link_local_address as EUT and QE4 connected to Home_Network 2 and QE4 registered to QE1 and QE4 having established a binding with QE3 } ensure that { when { QE4 is disconnected and EUT is connected to Home_Network 1 and QE3 is requested to send a packet to the EUT indicating that a response is required -- QE3 sends packets containing -- Routing Headers Type 2 and QE5 is requested to send a packet to the EUT indicating that a response is required } -- QE5 sends packets not containing -- Routing Headers Type 2 then { QE3 indicates no receipt of the response from the EUT and QE5 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). EUT is disconnected. QE4 is configured with the same link-layer address as EUT. QE4 is connected to Home Network 2 and registered with its Home Agent QE1. QE4 has established a binding with QE3. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE4 |  |  |
| 2 | Connect EUT to Home Network 2 |  |  |
| 3 | Cause QE3 to send an Echo Request to EUT |  |  |
| 4 | Check: does QE3 receive an Echo Reply from EUT? | NO | YES |
| 5 | Cause QE5 to send an Echo Request to EUT |  |  |
| 6 | Check: does QE5 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §9.4.1 Receiving Home Test Init Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1348_01 | Test Purpose: | TP_MOB_1348_01 |
| Summary: | 'Correspondent Node is able to participate in Return Routability Procedure' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1050, RQ_001_1051, RQ_001_1348 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT is requested to send a packet to QE4 indicating that a response is required } then { EUT indicates receipt of the response directly from QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE4 is configured to perform route optimization EUT is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 so sent an Echo Request to EUT |  |  |
| 2 | Check: Does QE4 receive a reply from EUT? | Yes | No |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routability Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1, the Home Agent of QE4 |  |  |
| 5 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive an Echo Reply from QE4? | Yes | No |
| Observations: | Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Cannot send the Echo Request from QE4 because nothing guarantees that QE4 would use its Home Address. |

###### §9.4.2 Receiving Care-of Test Init Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1348_01 | Test Purpose: | TP_MOB_1348_01 |
| Summary: | 'Correspondent Node is able to participate in Return Routability Procedure' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1050, RQ_001_1051, RQ_001_1348 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT is requested to send a packet to QE4 indicating that a response is required } then { EUT indicates receipt of the response directly from QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE4 is configured to perform route optimization EUT is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 so sent an Echo Request to EUT |  |  |
| 2 | Check: Does QE4 receive a reply from EUT? | Yes | No |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routability Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1, the Home Agent of QE4 |  |  |
| 5 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive an Echo Reply from QE4? | Yes | No |
| Observations: | Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Cannot send the Echo Request from QE4 because nothing guarantees that QE4 would use its Home Address. |

###### §9.4 Return Routability Procedure

| Test Description |
| --- |
| Identifier: | TD_MOB_1348_01 | Test Purpose: | TP_MOB_1348_01 |
| Summary: | 'Correspondent Node is able to participate in Return Routability Procedure' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1050, RQ_001_1051, RQ_001_1348 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT is requested to send a packet to QE4 indicating that a response is required } then { EUT indicates receipt of the response directly from QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE4 is configured to perform route optimization EUT is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 so sent an Echo Request to EUT |  |  |
| 2 | Check: Does QE4 receive a reply from EUT? | Yes | No |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routability Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1, the Home Agent of QE4 |  |  |
| 5 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive an Echo Reply from QE4? | Yes | No |
| Observations: | Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Cannot send the Echo Request from QE4 because nothing guarantees that QE4 would use its Home Address. |

###### §9.5.1 Receiving Binding Updates

| Test Description |
| --- |
| Identifier: | TD_MOB_1817_01 | Test Purpose: | TP_MOB_1817_01 |
| Summary: | 'Correspondent Node registers the binding when it receives a BU from Mobile Node' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1817 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { QE4 is requested to send a packet directly to EUT indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and registered to its Home Agent QE1 QE4 is configured to perform Route Optimization EUT is configured to perform Route Optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home address of QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | YES | NO |
| 3 | Disconnect QE1 from Home Network 1 |  |  |
| 4 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 5 | Check: does EUT receive an Echo Reply from QE4 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1065_01 | Test Purpose: | TP_MOB_1065_01 |
| Summary: | 'Correspondent Node sends a Binding_Acknowledgement message upon receipt of a Binding Update message containing A-Flag set to 1' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1065, RQ_001_1350 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured 'to request Binding_Acknowledgements from correspondent nodes' and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { EUT sends the response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and has registered to ist Home Agent QE1 QE4 configured to perform route optimization EUT is configured to perform route optimization QE4 is configured to ask Correspondent Node for Binding Acknowledgement QE4 and EUT have never communicated yet and don't know each other (no binding established, no cache entries). |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: Does EUT receive an Echo Reply from QE4? | YES | NO |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routing Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1 from Home Network 1 |  |  |
| 5 | Cause EUT to sent an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive an Echo Reply from QE4? | YES | NO |
| Observations: | Note1: Configuring QE4 to ask Binding Acknoledgement from Correspondent Nodes ensures that its Binding Update message will have the A-Flag set to 1. Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Note2: Cannot send the Echo Request from QE4 (as described in Tesp Purpose) because nothing guarantees that QE4 would use its Home Address. |

###### §9.5.2 Requests to Cache a Binding

| Test Description |
| --- |
| Identifier: | TD_MOB_1457_01 | Test Purpose: | TP_MOB_1457_01 |
| Summary: | 'Correspondent Node creates a new entry in its binding cache when receiving a valid Binding Update' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1457 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { EUT sends response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and registered to its Home Agent QE1 QE4 is configured to perform route optimization EUT is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: Does EUT receive a reply from QE4? | Yes | No |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routing Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1, the Home Agent of QE4 |  |  |
| 5 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive a reply from QE4? | Yes | No |
| Observations: | Note1: Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Note2: Cannot send the Echo Request from QE4 (as described in Tesp Purpose) because nothing guarantees that QE4 would use its Home Address. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1458_01 | Test Purpose: | TP_MOB_1458_01 |
| Summary: | 'Correspondent Node updates a binding cache entry on receipt of a valid Binding Update' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1458 |
| with { QE4 away_from_home and QE4 registered to QE1 and EUT having established a binding with QE4 } ensure that { when { QE4 moves to another foreign_network and EUT is requested to send a packet to QE4 indicating that a response is required } then { EUT indicates receipt of the response directly from QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT and QE4 have established bindings |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | move QE4 to Foreign Network 2 |  |  |
| 2 | wait a few seconds (to let QE4 update its bindings with QE1 and with EUT) |  |  |
| 3 | Disconnect QE1 from Home Network 1 |  |  |
| 4 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 5 | Check: does EUT receive an Echo Reply from QE4 ? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1486_01 | Test Purpose: | TP_MOB_1486_01 |
| Summary: | 'Correspondent Node deletes any Binding Cache entry after the expiration of the binding lifetime' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1461, RQ_001_1486 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 } ensure that { when { EUT establishes a binding to QE4} then { EUT and QE4 are able to communicate directly within the binding_lifetime and EUT and QE4 are unable to communicate directly after the binding_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to perform Route Optimization QE4 is configured to perform Route Optimization QE4 is connected to Foreign Network 1 and registered to QE1 EUT is configured to have a lifetime at one minute |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | YES | NO |
| 3 | QE1 is disconnected from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| 6 | Wait a minute (to let the binding between QE4 and EUT expire) |  |  |
| 7 | Cause QE4 to send an Echo Request to EUT |  |  |
| 8 | Check: does QE4 receive an Echo Reply from EUT ? | NO | YES |
| Observations: | Ensure that QE4 use its Home Address when pinging EUT (Home Address Option present in IPV6 packet) |

| Test Description |
| --- |
| Identifier: | TD_MOB_1465_01 | Test Purpose: | TP_MOB_1465_01 |
| Summary: | 'Correspondent Node deletes any existing related bindings on receipt of a Binding Update requesting to delete a binding' |
| Roles: | Correspondent_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1465, RQ_001_1465, RQ_001_1466, RQ_001_1470 |
| with { EUT away_from_home and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 having established a binding with EUT } ensure that { when { EUT returns home } then { QE4 and the EUT are able to communicate with EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT is configured to perform route optimization QE4 is configured to perform route optimization QE4 has established a binding to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

###### §9.5.4 Sending Binding Acknowledgements

| Test Description |
| --- |
| Identifier: | TD_MOB_1065_01 | Test Purpose: | TP_MOB_1065_01 |
| Summary: | 'Correspondent Node sends a Binding_Acknowledgement message upon receipt of a Binding Update message containing A-Flag set to 1' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1065, RQ_001_1350 |
| with { QE4 away_from_home and QE4 registered to QE1 and QE4 configured 'to request Binding_Acknowledgements from correspondent nodes' and QE4 configured to perform route_optimization and EUT configured to perform route_optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { EUT sends the response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and has registered to ist Home Agent QE1 QE4 configured to perform route optimization EUT is configured to perform route optimization QE4 is configured to ask Correspondent Node for Binding Acknowledgement QE4 and EUT have never communicated yet and don't know each other (no binding established, no cache entries). |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: Does EUT receive an Echo Reply from QE4? | YES | NO |
| 3 | Wait a few seconds to allow QE4 and EUT to perform Return Routing Procedure and establish Bindings. |  |  |
| 4 | Disconnect QE1 from Home Network 1 |  |  |
| 5 | Cause EUT to sent an Echo Request to the Home Address of QE4 |  |  |
| 6 | Check: Does EUT receive an Echo Reply from QE4? | YES | NO |
| Observations: | Note1: Configuring QE4 to ask Binding Acknoledgement from Correspondent Nodes ensures that its Binding Update message will have the A-Flag set to 1. Disconnecting the Home Agent QE1 garantees that traffic will not go through if Route Optimization didn't succeed. Note2: Cannot send the Echo Request from QE4 (as described in Tesp Purpose) because nothing guarantees that QE4 would use its Home Address. |

###### §9.5.5 Sending Binding Refresh Requests

| Test Description |
| --- |
| Identifier: | TD_MOB_1483_01 | Test Purpose: | TP_MOB_1483_01 |
| Summary: | 'Correspondent Node tries to refresh a binding cache entry before it expires' |
| Roles: | Correspondent_Node, Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1483, RQ_001_1483 |
| with { QE4 away_from_home and QE4 registered to QE1 and EUT having established a binding with QE4 and EUT established 'in continuous unbounded communication with QE4' } ensure that { when { QE4 sends a packet to the EUT after the binding_lifetime indicating that a response is required } then { QE4 indicates receipt of the response directly from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is connected to Foreign Network 1 and registered to QE1 EUT having established a binding with QE4 EUT is configured to have a binding lifetime at one minute |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | wait 45 seconds after the registration between EUT and QE4 |  |  |
| 2 | Cause QE4 to send an series of Echo Request during 30 seconds to EUT |  |  |
| 3 | After one minute and 5 seconds, disconnect QE1 from Home Network 1 |  |  |
| 4 | Check: are more one Echo Request of the series dropped ? | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1485_01 | Test Purpose: | TP_MOB_1485_01 |
| Summary: | 'Correspondent Node stops retransmitting Binding Refresh Requests messages when it receives a Binding Update' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1485 |
| --************************************************************************-- --* However we wrap this up, it is a conformance test, not interop *-- --************************************************************************-- with { QE4 away_from_home and QE4 registered to QE1 and EUT having established a binding with QE4 } ensure that { when { EUT 'tries to refresh its binding with QE4' and EUT receives 'a message indicating that the refresh is successful' } then { EUT 'stops sending refresh requests to QE4' } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN depending of the implementation to reduce the handover |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

###### Binding Cache Management (was: §9.6 Cache Replacement Policy)

| Test Description |
| --- |
| Identifier: | TD_MOB_1390_01 | Test Purpose: | TP_MOB_1390_01 |
| Summary: | 'Correspondent Node maintains a seperate binding cache for each of its unicast routable addresses' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1390 |
| with { EUT configured to have 2 global_addresses and QE4 away_from_home and QE4 registered to QE1 and EUT having established a binding to QE4 using its first global_address and QE1 disconnected from the network } ensure that { when { EUT is requested to send a packet to QE4 containing a source_address set to its second global_address } then { QE4 does not indicate receipt of the packet } } --TP id : TP_MOB_1429_01 --summary : 'Correspondent Node deletes a binding cache entry if it receives -- persistent ICMP Destination Unreachable messages' --RQ ref : RQ_001_1429 --Role : Correspondent_Node --config : CF_MOB_04 --TD ref : TD_MOB_1429_01 --***********************************************************************-- --* The imprecision in this requirement and the lack of clear guidance *-- --* on how many ICMP DU messages will cause the the deletion of the *-- --* binding cache entry make this almost impossible to test by IOP *-- --* methods. It should be removed from the IOP test suite. *-- --***********************************************************************-- -- with { QE4 away_from_home -- and QE4 registered to QE1 -- and EUT having established a binding with QE4 -- } -- ensure that -- { when { QE4 returns home -- and QE4 is unable to update its binding to the EUT -- and EUT is requested to send packets to QE4 } -- then { EUT 'is temporarily unable to communicate with QE4' -- and EUT is able to communicate with QE4 -- before the binding_lifetime expires } -- } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEANS That relates to internal operations |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1486_01 | Test Purpose: | TP_MOB_1486_01 |
| Summary: | 'Correspondent Node deletes any Binding Cache entry after the expiration of the binding lifetime' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1461, RQ_001_1486 |
| with { EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE4 away_from_home and QE4 registered to QE1 } ensure that { when { EUT establishes a binding to QE4} then { EUT and QE4 are able to communicate directly within the binding_lifetime and EUT and QE4 are unable to communicate directly after the binding_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to perform Route Optimization QE4 is configured to perform Route Optimization QE4 is connected to Foreign Network 1 and registered to QE1 EUT is configured to have a lifetime at one minute |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to the Home Address of QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | YES | NO |
| 3 | QE1 is disconnected from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| 6 | Wait a minute (to let the binding between QE4 and EUT expire) |  |  |
| 7 | Cause QE4 to send an Echo Request to EUT |  |  |
| 8 | Check: does QE4 receive an Echo Reply from EUT ? | NO | YES |
| Observations: | Ensure that QE4 use its Home Address when pinging EUT (Home Address Option present in IPV6 packet) |

###### §10 Home Agent Operation

| Test Description |
| --- |
| Identifier: | TD_MOB_1807_01 | Test Purpose: | TP_MOB_1807_01 |
| Summary: | 'If HA support the multicast group membership control protocols, HA must be capable to determine which multicast data packets to forward via the tunnel to MN' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1561, RQ_001_1807 |
| -- Config-HA with { QE1 connected to home_network and QE1 subscribed to a global_multicast_group and QE3 subscribed to another global_multicast_group } ensure that { when { QE1 moves to a foreign_network and QE1 registers to EUT } then { QE1 receives packets from its global_multicast_group } } --****************************************************-- --* RFC3776 - Security for Mobility --****************************************************-- |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEANS You do not know if the Home Agent do not forward the multicast packets or if the Mobile Node drops this packets. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1557_01 | Test Purpose: | TP_MOB_1557_01 |
| Summary: | 'HA tunnels multicast packets with a global scope to the mobile node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1372, RQ_001_1557, RQ_001_1557 |
| with { QE1 subscribed to a global_multicast_group and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the global_multicast_group indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 has registered to multicast group FF1E::1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Cause QE3 to send an Echo Request to the multicast address FF1E::1 |  |  |
| 3 | Check: does QE3 receives an Echo Reply | Yes | No |
| 4 | Disconnect EUT |  |  |
| 5 | Cause QE3 to send an Echo Request to the multicast address FF1E::1 |  |  |
| 6 | Check: does QE3 receives an Echo Reply | No | Yes |
| Observations: | FF1E::1 is a global scope, non reserved, multicast group |

###### §10.5  Dynamic Home Agent Address Discovery

| Test Description |
| --- |
| Identifier: | TD_MOB_1804_01 | Test Purpose: | TP_MOB_1804_01 |
| Summary: | 'Home Agent is able to participate in Dynamic Home Agent Address Discovery' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1368, RQ_001_1804 |
| with { QE1 at_home and QE1 not configured to have its Home_Agent_address available } ensure that { when { QE1 moves to a foreign_network and QE4 is requested to send a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is disconnected from Home Network 1 QE1 is unaware of the address of its Home Agent |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 4 | Check: does QE4 reveive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

###### §10.6 Sending Prefix Information to the Mobile Node

| Test Description |
| --- |
| Identifier: | TD_MOB_1592_01 | Test Purpose: | TP_MOB_1592_01 |
| Summary: | 'HA schedules the delivery of the prefix information when a new prefix is added to its home subnet interface' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1370, RQ_001_1592, RQ_001_1805 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { EUT generates a new prefix to the home_address of QE1 before (QE4 sends a packet to QE1 using the new home_address and indicating that a response is required) } then { QE4 indicates receipt of a response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Foreign Network 1 QE1 registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to generate a new prefix added on its home subnet interface |  |  |
| 2 | Wait for at least 3.5 seconds |  |  |
| 3 | Check: Does QE1 indicate a new home address? | yes | no |
| Observations: | MIN_DELAY_BETWEEN_RAS (3.0s) + MAX_RA_DELAY_TIME (0.5s) = 3.5s (cf. RFC2561) |

###### §10.6.2 Scheduling Prefix Deliveries

| Test Description |
| --- |
| Identifier: | TD_MOB_1812_01 | Test Purpose: | TP_MOB_1812_01 |
| Summary: | 'HA deliveries new prefix information when lifetime information (valid or preferred lifetime) of the prefix changes' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1812 |
| with { QE1 away_from_home and QE1 registered to EUT and EUT configured to have a short prefix_lifetime on the Home_Network of QE1 --(suggest 30s) } ensure that { when { EUT is requested to configure a new prefix_lifetime for QE1 } then { QE1 and QE4 are able to communicate using the new prefix after the original prefix_lifetime expires } } --TP id : TP_MOB_1602_01 --summary : 'If the bindings of MN expire before BU then HA stops sending MPAs' --RQ ref : RQ_001_1602 --Role : Home_Agent --config : CF_MOB_02 --TD ref : TD_MOB_1602_01 --XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX-- --X Not interoperability X-- --XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXxxxxx-- -- with { QE1 away_from_home -- and QE1 registered to EUT -- } -- ensure that -- { when { QE1 'is disconnected' from 'the foreign network' -- and EUT 'indicates the binding of QE1 expired' -- } -- then { EUT sends 'no other messages to QE1' before 'new registation' } -- } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Foreign Network 1 QE1 registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Configure EUT with new, higher, valid lifetime |  |  |
| 2 | Wait for expiration of the original prefix lifetime |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1592_01 | Test Purpose: | TP_MOB_1592_01 |
| Summary: | 'HA schedules the delivery of the prefix information when a new prefix is added to its home subnet interface' |
| Roles: | Home_Agent | Configuration: | 7 |
| References: | RQ_001_1370, RQ_001_1592, RQ_001_1805 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { EUT generates a new prefix to the home_address of QE1 before (QE4 sends a packet to QE1 using the new home_address and indicating that a response is required) } then { QE4 indicates receipt of a response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Foreign Network 1 QE1 registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to generate a new prefix added on its home subnet interface |  |  |
| 2 | Wait for at least 3.5 seconds |  |  |
| 3 | Check: Does QE1 indicate a new home address? | yes | no |
| Observations: | MIN_DELAY_BETWEEN_RAS (3.0s) + MAX_RA_DELAY_TIME (0.5s) = 3.5s (cf. RFC2561) |

| Test Description |
| --- |
| Identifier: | TD_MOB_1600_01 | Test Purpose: | TP_MOB_1600_01 |
| Summary: | 'HA retransmits periocally unsolicited Advertisement until the receipt of a Mobile_Prefix_Solicitation from MN' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1600, RQ_001_1813 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE1 is disconnected from the foreign_network before EUT generates a new prefix to the home_address of QE1 before QE1 is connected to the foreign_network after 1 minute before QE4 sends a packet to QE1 using the new home_address and indicating that a response is required } then { QE4 indicates receipt of a response from QE1 } } --TP id : TP_MOB_1591_01 --summary : 'HA delivers new prefix information when the state of the flags -- changes for the prefix of the MN registered' --RQ ref : RQ_001_1591 --Role : Home_Agent --config : CF_MOB_02 --TD ref : TD_MOB_1591_01 --XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX-- --X Not interoperability X-- --XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX-- -- with { QE1 away_from_home -- and QE1 registered to EUT -- } -- ensure that -- { when { EUT generates 'a new state of the flags on the prefix of its home subnet interface' } -- then { QE1 indicates 'a new state on its home address' } -- } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected in Foreign Network 1 QE1 is registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect EUT |  |  |
| 2 | Cause EUT to generate a new prefix added on its home subnet interface |  |  |
| 3 | Wait for one minute |  |  |
| 4 | Reconnect EUT to home network |  |  |
| 5 | Check: Does QE1 indicate a new home address? | yes | no |
| Observations: | It is not clear to me why a delay of 'one' minute is suggested here |

| Test Description |
| --- |
| Identifier: | TD_MOB_1603_01 | Test Purpose: | TP_MOB_1603_01 |
| Summary: | 'HA transmits again unsolicited Mobile_Prefix_Advertisement after the prolongation of the binding of the Mobile Node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1603 |
| with { QE1 away_from_home and QE1 is registered to the EUT and QE1 and the EUT configured to have a short binding_lifetime -- (Suggest 30s) } ensure that { when { QE1 is disconnected from the foreign_network before the binding_lifetime expires between QE1 and the EUT before QE1 is connected to another foreign_network } then { QE1 and QE4 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Foreign Network 1 QE1 registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 |  |  |
| 2 | Wait until QE1's binding to EUT expires |  |  |
| 3 | Cause EUT to generate a new prefix added on its home subnet interface |  |  |
| 4 | connect QE1 to foreign network 2 |  |  |
| 5 | Check: Does QE1 indicate a new home address? | yes | no |
| Observations: |  |

###### §10.6.3  Sending  Advertisements

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_01 | Test Purpose: | TP_MOB_1082_01 |
| Summary: | 'Home Agent uses a Security Association to protect integrity and authenticity of Mobile_Prefix_Solicitations and Advertisements' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1607 |
| with { QE1 at_home and QE1 configured to protect Mobile_Prefix_Solicitations and QE1 configured to accept only secured Mobile_Prefix_Advertisements and QE1 configured to have a short prefix_lifetime --(suggest 30s) } ensure that { when { QE1 moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT QE1 is configured to protect Mobile Prefix Solicitation messages QE1 is configured to only accept protected Mobile Prefix Advertisement messages EUT is configured to advertise a prefered prefix lifetime of 20 sec EUT is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that initial lifetime of the home address of QE1 has expired |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1? | YES | NO |
| Observations: |  |

###### §10.6 Sending Prefix Information to the Mobile Node

| Test Description |
| --- |
| Identifier: | TD_MOB_1592_01 | Test Purpose: | TP_MOB_1592_01 |
| Summary: | 'HA schedules the delivery of the prefix information when a new prefix is added to its home subnet interface' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1370, RQ_001_1592, RQ_001_1805 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { EUT generates a new prefix to the home_address of QE1 before (QE4 sends a packet to QE1 using the new home_address and indicating that a response is required) } then { QE4 indicates receipt of a response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Foreign Network 1 QE1 registered to EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to generate a new prefix added on its home subnet interface |  |  |
| 2 | Wait for at least 3.5 seconds |  |  |
| 3 | Check: Does QE1 indicate a new home address? | yes | no |
| Observations: | MIN_DELAY_BETWEEN_RAS (3.0s) + MAX_RA_DELAY_TIME (0.5s) = 3.5s (cf. RFC2561) |

###### §10.3.2  Primary Care-of Address De-Registration

| Test Description |
| --- |
| Identifier: | TD_MOB_1526_01 | Test Purpose: | TP_MOB_1526_01 |
| Summary: | 'Home Agent rejects De-Registration Binding Update if no entry exists in its Binding Cache for the Mobile Node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_05 |
| References: | RQ_001_1526, RQ_001_1526, RQ_001_1527, RQ_001_1535 |
| with { EUT disconnected from Home_Network and QE2 configured to have the same IP_address as EUT and QE1 connected to a foreign_network and QE1 registered to QE2 } ensure that { when { QE2 is disconnected from Home_Network and EUT is connected to Home_Network and QE1 returns home } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE2 is configured to serve the Home Network 1 QE2 and EUT are configured with the same IP address EUT is disconnected from Home Network 1 QE1 is connected to Foreign Network 1 and registered to its Home Agent QE2 QE2 is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | QE2 is diconnected from Home Network 1 |  |  |
| 2 | EUT is connected to Home Network 1 |  |  |
| 3 | Move QE1 to Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 ? | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1528_01 | Test Purpose: | TP_MOB_1528_01 |
| Summary: | 'When accepting Care of Address de-registration Binding Update, Home Agent deletes any existing entry in its Binding Cache for the Mobile Node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1528, RQ_001_1529 |
| with { QE1 away_from_home and QE1 registered to EUT and QE4 able to communicate with QE1 and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 returns home } then { QE4 and QE1 are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured not to perform route optimization QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Home Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 deregister to EUT) |  |  |
| 3 | Disconnected EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request directly to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply directly from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1528_01 | Test Purpose: | TP_MOB_1528_01 |
| Summary: | 'When accepting Care of Address de-registration Binding Update, Home Agent deletes any existing entry in its Binding Cache for the Mobile Node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1528, RQ_001_1529 |
| with { QE1 away_from_home and QE1 registered to EUT and QE4 able to communicate with QE1 and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 returns home } then { QE4 and QE1 are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured not to perform route optimization QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Home Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 deregister to EUT) |  |  |
| 3 | Disconnected EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request directly to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply directly from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1534_01 | Test Purpose: | TP_MOB_1534_01 |
| Summary: | 'Home Agent stops intercepting packets for the mobile node on acceptance of the Primary Care of Address De-Registration Binding Update' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1534 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE1 returns home and EUT is disconnected from the home_network } then { QE4 and QE1 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Home Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 register to EUT) |  |  |
| 3 | EUT is disconnected from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

###### §10.3.1  Primary Care-of Address Registration

| Test Description |
| --- |
| Identifier: | TD_MOB_1818_01 | Test Purpose: | TP_MOB_1818_01 |
| Summary: | 'A Binding Update contains a Home Address destination option.' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1818 |
| with { QE1 at_home } ensure that { when { QE1 moves to a foreign_network and QE1 sends a Binding_Update containing no Home_Address_Destination_Option } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | Not testable by interoperability means |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: | It is not possible to send a Binding Update containing no Home Address! |

| Test Description |
| --- |
| Identifier: | TD_MOB_1825_01 | Test Purpose: | TP_MOB_1825_01 |
| Summary: | 'When Home Agent processes a Binding Update secured by IPsec, the contents of Home Address Option is not checked' |
| Roles: | Home_Agent | Configuration: | CF_MOB_05 |
| References: | RQ_001_1825 |
| with { QE1 configured not to perform Route_Optimization and QE1 away_from_home and QE1 registered to EUT and EUT configured to accept any secured Binding_Update from QE1 and QE1 configured to send only a secured Binding_Update to EUT } ensure that { when { QE1 sends a Binding_Update secured by IPsec containing a Home_Address_Option not indicating its Home_Address } then { EUT accepts the packet } } |
| Pre-test conditions: | Not testable by IOP means |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1826_01 | Test Purpose: | TP_MOB_1826_01 |
| Summary: | 'Home Agent updates the entry in its Binding Cache upon receipt of a Binding Update' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1826 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 moves to another foreign_network } then { QE3 and QE1 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT QE1 is configured not to perform Route Optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 2 |  |  |
| 2 | Cause QE3 to send an Echo request to the Home Address of QE1 |  |  |
| 3 | Check: does QE3 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1494_01 | Test Purpose: | TP_MOB_1494_01 |
| Summary: | 'Home Agent returns a type "132" Binding Aknowledgment upon receipt of a Binding Update which Home Address is not on link' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1494 |
| with { QE1 disconnected from the home_network and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 is connected to a foreign_network and EUT receives a Binding_Update containing a Home_Address not on_link } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN no node can answer to an address which is not on link |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1496_01 | Test Purpose: | TP_MOB_1496_01 |
| Summary: | 'Correspondent Node sends a type "131" Binding Acknowledgment when receiving a Home Registration Binding Update' |
| Roles: | Correspondent_Node, Correspondent_Node, Mobile_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1496, RQ_001_1496 |
| with { EUT at_home and QE5 at_home and QE5 configured 'to use EUT as Home Agent' } ensure that { when { QE5 moves to a foreign_network } then { QE3 and QE5 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 2 QE5 is connected to Home Network 2 QE5 is configured to use EUT as Home Agent |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE5 to Foreign Network 2 |  |  |
| 2 | Cause QE3 to send an Echo Request to the Home Address of QE5 |  |  |
| 3 | Check: does QE3 receive an Echo Reply from QE5 | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1497_01 | Test Purpose: | TP_MOB_1497_01 |
| Summary: | 'Home Agent creates a new entry in its Binding Cache upon receipt of a Binding Update' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1497 |
| with { QE1 at_home and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 moves to a foreign_network } then { QE4 is able to communicate with QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 is configured not to perform Route Optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 register to EUT) |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1500_01 | Test Purpose: | TP_MOB_1500_01 |
| Summary: | 'Home Agent maintains a Binding Cache entry from receipt of a Binding Update until the Binding Lifetime expires' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1497, RQ_001_1500, RQ_001_1522 |
| with { QE1 at_home and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate within the Binding_Lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 is configured not to perform Route Optimization EUT is configured to set the binding lifetime to 2 minutes QE3 is discinnected from Home Network 1 QE3 is configured with the same ethernet address as QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive en Echo Reply from QE1 | YES | NO |
| 5 | Disconnect QE1 from Foreign Network 1 |  |  |
| 6 | Wait a period a little less long than the Binding Lifetime |  |  |
| 7 | Connected QE3 to Home Network 1 |  |  |
| 8 | Wait for the expiration of the binding lifetime |  |  |
| 9 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 10 | Check: does QE4 receive en Echo Reply from QE1 | NO | YES |
| Observations: | DAD occurs at step 7 |

| Test Description |
| --- |
| Identifier: | TD_MOB_1501_01 | Test Purpose: | TP_MOB_1501_01 |
| Summary: | 'Home Agent performs Duplicate Address Detection on home link before sending a Binding Aknowledgment' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1501, RQ_001_1502, RQ_001_1503 |
| with { QE1 at_home and QE3 disconnected from home_network and QE3 having the same home_address as QE1 } ensure that { when { QE1 is disconnected from the home_network and QE3 is connected to the home_network and QE1 is connected to a foreign_network } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE3 is manually configured with the same Home Address as QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 register to EUT) |  |  |
| 3 | Disconnect QE3 from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1503_01 | Test Purpose: | TP_MOB_1503_01 |
| Summary: | 'Home Agent returns a type "134" Binding Aknowledgement when Duplicate Address Detection for the Home Address / Link Local Address fails' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1503 |
| with { QE1 disconnected from home_network and QE3 connected to home_network and QE3 configured to have the same link_local_address as QE1 } ensure that { when { QE1 is connected to a foreign_network } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is disconnected from Home Network 1 QE3 is connected on Home Network QE3 is manually configured with the same link-local address as QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | QE1 is connected to Foreign Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1507_01 | Test Purpose: | TP_MOB_1507_01 |
| Summary: | 'Home Agent removes binding when the associated prefix valid lifetime expires' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1507 |
| with { QE1 away_from_home and QE1 registered to the EUT and QE1 configured not to perform Route_Optimization } ensure that { when { the prefix_lifetime expires at the EUT } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to accept only secured Mobile Prefix Solicitations. QE1 is configured to send unsecured Mobile Prefix Solicitations. QE1 is configured not to perform Route Optimization QE1 is connected to Foreign Network 1 and registered to its Home Agent R1 is configured to advertise a valid prefix lifetime of 1 minute |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a minute (to let the prefix A become invalid) |  |  |
| 2 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1510_01 | Test Purpose: | TP_MOB_1510_01 |
| Summary: | 'Home Agent returns a Binding Acknowledgment in response to a Binding Update' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1510, RQ_001_1501, RQ_001_1510, RQ_001_1511, RQ_001_1516, RQ_001_1517, RQ_001_2002, RQ_001_2013, RQ_001_2029 |
| with { QE1 at_home } ensure that { when { QE1 moves to a foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let the QE1 register with si Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1500_01 | Test Purpose: | TP_MOB_1500_01 |
| Summary: | 'Home Agent maintains a Binding Cache entry from receipt of a Binding Update until the Binding Lifetime expires' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1497, RQ_001_1500, RQ_001_1522 |
| with { QE1 at_home and QE1 configured not to perform Route_Optimization } ensure that { when { QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate within the Binding_Lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 is configured not to perform Route Optimization EUT is configured to set the binding lifetime to 2 minutes QE3 is discinnected from Home Network 1 QE3 is configured with the same ethernet address as QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let QE1 register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive en Echo Reply from QE1 | YES | NO |
| 5 | Disconnect QE1 from Foreign Network 1 |  |  |
| 6 | Wait a period a little less long than the Binding Lifetime |  |  |
| 7 | Connected QE3 to Home Network 1 |  |  |
| 8 | Wait for the expiration of the binding lifetime |  |  |
| 9 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 10 | Check: does QE4 receive en Echo Reply from QE1 | NO | YES |
| Observations: | DAD occurs at step 7 |

###### §10.3 Processing Bindings

| Test Description |
| --- |
| Identifier: | TD_MOB_1366_01 | Test Purpose: | TP_MOB_1366_01 |
| Summary: | 'Home Agent returns a Binding_Acknowledgement message in response to a Binding Update message' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1366 |
| with { QE1 at_home } ensure that { when { QE1 moves to a foreign_network and QE1 receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response} } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to foreign network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1? | YES | NO |
| Observations: |  |

###### §10.4.1  Intercepting Packets for a Mobile Node

| Test Description |
| --- |
| Identifier: | TD_MOB_1536_01 | Test Purpose: | TP_MOB_1536_01 |
| Summary: | 'HA interceipts packets for registered mobile node on the home network and uses reverse tunnel encapsulation' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1364, RQ_001_1536, RQ_001_1551, RQ_001_1568 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { QE3 is requested to send a packet to QE1 indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and has registered to its Home Agent EUT QE1 is configured NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: Does QE3 receive an Echo Reply from QE1 | Yes | No |
| Observations: | Very Similar to TD_MOBILITY_1547_01 |

| Test Description |
| --- |
| Identifier: | TD_MOB_1537_01 | Test Purpose: | TP_MOB_1537_01 |
| Summary: | 'HA multicasts Neighbor Advertisement in Home network in order to intercept packets for mobile node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1537, RQ_001_1537, RQ_001_1539, RQ_001_1540, RQ_001_1541, RQ_001_1542, RQ_001_1543, RQ_001_1544 |
| with { QE1 at home and QE1 having established communication to QE3 } ensure that { when { QE1 moves to a foreign_network } then { QE3 updates its Neighbor_Discovery_cache_entry for the link_local_address of QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1. QE3 has already sent packets to the home address of QE1. QE4 is configured with the same link-layer address as QE1 and with the Home Address of QE1. Configure R2 to advertise Prefix A instead of Prefix C. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (for QE1 to register with its Home Agent EUT) |  |  |
| 3 | Disconnect EUT |  |  |
| 4 | Connect Home Network 1 and Home Network 2 together |  |  |
| 5 | Cause QE3 to send an Echo Request to the home address of QE1 |  |  |
| 6 | Check: does EUT receive an Echo Reply | No | Yes |
| Observations: | Explanation: If EUT behaves correctly (ie sends a NA) then QE3 will send the Echo Request to the link-layer address of EUT and will not receive any Echo Reply. If EUT behaves incorrectly (ie sends no NA) then QE3 will send the Echo Request to the link-layer address of QE1, which is equal to QE4's one and will receive any Echo Reply. HN1 and HN2 are connected together to avoid QE4 performing DAD and advertising itself. Note: go through steps 1 to 5 quickly enough to avoid neighbor cache expiry on QE3, |

| Test Description |
| --- |
| Identifier: | TD_MOB_1538_01 | Test Purpose: | TP_MOB_1538_01 |
| Summary: | 'HA multicast Neighbor Advertisement to intercept the packets to the link_local_address of a registered mobile node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1538, RQ_001_1538, RQ_001_1539, RQ_001_1540, RQ_001_1541, RQ_001_1542, RQ_001_1543, RQ_001_1544 |
| with { QE1 at_home and QE1 using the same Interface_ID for its link_local_address and its home_address and QE3 having established communication to the link_local_address of QE1 } ensure that { when { QE1 moves to a foreign_network } then { QE3 updates the Neighbor_Discovery_cache_entry for the link_local_address of QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1. QE1 uses the same Interface ID for both its link-local address and its home address. QE3 has already sent packets to the link-local address of QE1. QE4 is configured with the same link-layer address as QE1. Configure R2 to advertise Prefix A instead of Prefix C. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (for QE1 to register with its Home Agent EUT) |  |  |
| 3 | Disconnect EUT |  |  |
| 4 | Connect Home Network 1 and Home Network 2 together |  |  |
| 5 | Cause QE3 to send an Echo Request to the link-local address of QE1 |  |  |
| 6 | Check: does EUT receive an Echo Reply | No | Yes |
| Observations: | Explanation: QE1 sends Binding Updates with the L flag activated (same interface ID for link-local and home addresses) If EUT behaves correctly (ie sends a NA) then QE3 will send the Echo Request to the link-layer address of EUT and will not receive any Echo Reply. If EUT behaves incorrectly (ie sends no NA) then QE3 will send the Echo Request to the link-layer address of QE1, which is equal to QE4's one and will receive any Echo Reply. HN1 and HN2 are connected together to avoid QE4 performing DAD and advertising itself. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1547_01 | Test Purpose: | TP_MOB_1547_01 |
| Summary: | 'HA act as proxy for a registered mobile node and reply to any received Neighbor Solicitations for it' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1547, RQ_001_1547, RQ_001_1548, RQ_001_1549 |
| with { QE3 'is disconnected' and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is connected to its home_network and QE3 is requested to send a packet to QE1 indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE3 is disconnected QE1 is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Connect QE3 to Home Network 1 |  |  |
| 2 | Cause QE3 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE3 receive an Echo Reply | Yes | No |
| Observations: | Very Similar to TD_MOBILITY_1536_01 |

###### §10.4.2 Processing Intercepted Packets

| Test Description |
| --- |
| Identifier: | TD_MOB_1536_01 | Test Purpose: | TP_MOB_1536_01 |
| Summary: | 'HA interceipts packets for registered mobile node on the home network and uses reverse tunnel encapsulation' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1364, RQ_001_1536, RQ_001_1551, RQ_001_1568 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { QE3 is requested to send a packet to QE1 indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and has registered to its Home Agent EUT QE1 is configured NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: Does QE3 receive an Echo Reply from QE1 | Yes | No |
| Observations: | Very Similar to TD_MOBILITY_1547_01 |

| Test Description |
| --- |
| Identifier: | TD_MOB_1552_01 | Test Purpose: | TP_MOB_1552_01 |
| Summary: | 'HA does not tunnel packets to the link_local_address of mobile node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1552, RQ_001_1552, RQ_001_1553 |
| with { QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the link_local_address of QE1 indicating that a response is required } then { QE3 indicates no receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Reply to the link-layer address of QE1 |  |  |
| 2 | Check: does QE3 receive an Echo Reply | No | Yes |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1555_01 | Test Purpose: | TP_MOB_1555_01 |
| Summary: | 'HA does not tunnel multicast packets with a scope smaller than global to the mobile node ' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1555, RQ_001_1556, RQ_001_1555, RQ_001_1556 |
| with { QE1 subscribed to a link_local_multicast_group and QE1 subscribed to a organization_local_multicast_group and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the link_local_multicast_group indicating that a response is required and QE3 is requested to send a packet to the organization_local_multicast_group indicating that a response is required } then { QE3 indicates no receipt of any response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 QE1 has registered to multicast group FF12::1 QE1 has registered to multicast group FF18::1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the multicast address FF12::1 |  |  |
| 2 | Check: does QE3 receive an Echo Reply | No | Yes |
| 3 | Cause QE3 to send an Echo Request to the multicast address FF18::1 |  |  |
| 4 | Check: does QE3 receive an Echo Reply | No | Yes |
| Observations: | FF12::1 is a link-local scope, non reserved, multicast address. FF18::1 is an organization-local scope, non reserved, multicast address. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1555_01 | Test Purpose: | TP_MOB_1555_01 |
| Summary: | 'HA does not tunnel multicast packets with a scope smaller than global to the mobile node ' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1555, RQ_001_1556, RQ_001_1555, RQ_001_1556 |
| with { QE1 subscribed to a link_local_multicast_group and QE1 subscribed to a organization_local_multicast_group and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the link_local_multicast_group indicating that a response is required and QE3 is requested to send a packet to the organization_local_multicast_group indicating that a response is required } then { QE3 indicates no receipt of any response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 QE1 has registered to multicast group FF12::1 QE1 has registered to multicast group FF18::1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the multicast address FF12::1 |  |  |
| 2 | Check: does QE3 receive an Echo Reply | No | Yes |
| 3 | Cause QE3 to send an Echo Request to the multicast address FF18::1 |  |  |
| 4 | Check: does QE3 receive an Echo Reply | No | Yes |
| Observations: | FF12::1 is a link-local scope, non reserved, multicast address. FF18::1 is an organization-local scope, non reserved, multicast address. |

| Test Description |
| --- |
| Identifier: | TD_MOB_1557_01 | Test Purpose: | TP_MOB_1557_01 |
| Summary: | 'HA tunnels multicast packets with a global scope to the mobile node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1372, RQ_001_1557, RQ_001_1557 |
| with { QE1 subscribed to a global_multicast_group and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the global_multicast_group indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Home Network 1 QE1 has registered to multicast group FF1E::1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Cause QE3 to send an Echo Request to the multicast address FF1E::1 |  |  |
| 3 | Check: does QE3 receives an Echo Reply | Yes | No |
| 4 | Disconnect EUT |  |  |
| 5 | Cause QE3 to send an Echo Request to the multicast address FF1E::1 |  |  |
| 6 | Check: does QE3 receives an Echo Reply | No | Yes |
| Observations: | FF1E::1 is a global scope, non reserved, multicast group |

###### §10.4.3  Multicast Membership Control

| Test Description |
| --- |
| Identifier: | TD_MOB_1560_01 | Test Purpose: | TP_MOB_1560_01 |
| Summary: | 'if multicast forwarding is not supported, HA ignores muticast group membership control messages' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1560 |
| with { QE1 subscribed to a global_multicast_group and EUT unable to support multicast_data_packet_forwarding and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE3 is requested to send a packet to the global_multicast_group } then { QE3 indicates no receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 QE1 has registered with its Home Agent EUT EUT does not support multicast data packet forwarding |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE1 to register to multicast group FF1E::1 |  |  |
| 2 | Cause QE3 to send an Echo Reply to multicast address FF1E::1 |  |  |
| 3 | Check: does QE3 receive an Echo Reply | No | Yes |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1807_01 | Test Purpose: | TP_MOB_1807_01 |
| Summary: | 'If HA support the multicast group membership control protocols, HA must be capable to determine which multicast data packets to forward via the tunnel to MN' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1561, RQ_001_1807 |
| -- Config-HA with { QE1 connected to home_network and QE1 subscribed to a global_multicast_group and QE3 subscribed to another global_multicast_group } ensure that { when { QE1 moves to a foreign_network and QE1 registers to EUT } then { QE1 receives packets from its global_multicast_group } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEANS You do not know if the Home Agent do not forward the multicast packets or if the Mobile Node drops this packets. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

###### §10.4.5 Handling ReverseTunneled Packets

| Test Description |
| --- |
| Identifier: | TD_MOB_1536_01 | Test Purpose: | TP_MOB_1536_01 |
| Summary: | 'HA interceipts packets for registered mobile node on the home network and uses reverse tunnel encapsulation' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1364, RQ_001_1536, RQ_001_1551, RQ_001_1568 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { QE3 is requested to send a packet to QE1 indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and has registered to its Home Agent EUT QE1 is configured NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: Does QE3 receive an Echo Reply from QE1 | Yes | No |
| Observations: | Very Similar to TD_MOBILITY_1547_01 |

| Test Description |
| --- |
| Identifier: | TD_MOB_1536_01 | Test Purpose: | TP_MOB_1536_01 |
| Summary: | 'HA interceipts packets for registered mobile node on the home network and uses reverse tunnel encapsulation' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1364, RQ_001_1536, RQ_001_1551, RQ_001_1568 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { QE3 is requested to send a packet to QE1 indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and has registered to its Home Agent EUT QE1 is configured NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: Does QE3 receive an Echo Reply from QE1 | Yes | No |
| Observations: | Very Similar to TD_MOBILITY_1547_01 |

###### §10.4.6 Protecting  Return Routability packets

| Test Description |
| --- |
| Identifier: | TD_MOB_1371_01 | Test Purpose: | TP_MOB_1371_01 |
| Summary: | 'Home Agent supports ESP protection of Home Test and Home Test Init messages' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1371 |
| with { QE4 configured to perform route_optimization and QE1 configured to perform route_optimization and QE1 configured to protect return_routability_packets using ESP } ensure that { when { QE1 moves to a Foreign_Network before QE4 sends a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response directly from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). QE4 is configured to perform route optimization. QE1 is configured to perform route optimization. QE1 is configured to protect return routability packets using ESP. QE1 connected to Home Network 1. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive Echo Reply | Yes | No |
| 5 | Disconnect EUT |  |  |
| 6 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 7 | Check: does QE4 receive Echo Reply | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2014_01 | Test Purpose: | TP_MOB_2014_01 |
| Summary: | 'Home Agent supports Home Test Init secured using tunnel_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1571, RQ_001_2034, RQ_001_2035 |
| with { QE1 configured to protect any Home_Test_Init to EUT using tunnel_mode_ESP and EUT configured to accept only Home_Test_Init secured using tunnel_mode_ESP from QE1 and QE1 configured to perform route_optimization and QE4 configured to perform route_optimization and QE1 is away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Home Test Init sent to EUT using tunnel mode ESP EUT is configured to accept only Home Test Init protected using tunnel mode ESP from QE1 QE1 configured to perform Route Optimization QE4 configured to perform Route Optimization QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Wait a few second (to let QE1 register to QE4) |  |  |
| 3 | Disconnect EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1574_01 | Test Purpose: | TP_MOB_1574_01 |
| Summary: | 'Home Agent supports the protection of Home Test and Home Test Init messages' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1574 |
| with { QE4 configured to perform route_optimization and QE1 configured to perform route_optimization and QE1 away_from_home and QE1 registered to EUT and QE1 configured to protect return_routability_packets } ensure that { when { QE1 receives a packet from QE4 indicating that a response is required } then { QE1 sends the response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE4 is configured to perform route optimization QE1 is configured to perform route optimization QE1 is away from home and registered to EUT QE1 is configured to protect return routability packets with QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| 3 | Wait a few seconds (to let QE4 and QE1 process the return routability procedure) |  |  |
| 4 | Disconnect EUT from Home Network 1 |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 6 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: | RRP is performed during first echo exchange |

###### §11 Mobile Node Operation

| Test Description |
| --- |
| Identifier: | TD_MOB_1003_01 | Test Purpose: | TP_MOB_1003_01 |
| Summary: | 'MN continues to communicate after moving to a new link' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1002, RQ_001_1003, RQ_001_1004 |
| with { EUT connected in home_network and EUT registered to QE1 and EUT and QE4 established in communication } ensure that { when { EUT moves to a foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | Yes | No |
| 3 | Move EUT to Foreign Network 1 |  |  |
| 4 | wait a few seconds (to let the EUT register with its Home Agent). |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT ? | Yes | No |
| Observations: |  |

###### §11.3 Packet Processing

| Test Description |
| --- |
| Identifier: | TD_MOB_1003_01 | Test Purpose: | TP_MOB_1003_01 |
| Summary: | 'MN continues to communicate after moving to a new link' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1002, RQ_001_1003, RQ_001_1004 |
| with { EUT connected in home_network and EUT registered to QE1 and EUT and QE4 established in communication } ensure that { when { EUT moves to a foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } --xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx-- |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | Yes | No |
| 3 | Move EUT to Foreign Network 1 |  |  |
| 4 | wait a few seconds (to let the EUT register with its Home Agent). |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT ? | Yes | No |
| Observations: |  |

###### §11.3.1 Sending Packets While Away From Home

| Test Description |
| --- |
| Identifier: | TD_MOB_1820_01 | Test Purpose: | TP_MOB_1820_01 |
| Summary: | 'When Home Agent receives a packet from Mobile Node using reverse tunneling, it forwards the encapsulated packet to Correspondent Node' |
| Roles: | Home_Agent, Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1820, RQ_001_1820 |
| with { QE1 away_from_home and QE1 registered to EUT and QE1 configured not to perform Route_Optimization } ensure that { when { EUT is disconnected } then { QE1 and QE4 are unable to communicate with QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to EUT QE1 is configured NOT to perform Route Optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address to QE1 |  |  |
| 2 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| 3 | Disconnect EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address to QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1003_01 | Test Purpose: | TP_MOB_1003_01 |
| Summary: | 'MN continues to communicate after moving to a new link' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1002, RQ_001_1003, RQ_001_1004 |
| with { EUT connected in home_network and EUT registered to QE1 and EUT and QE4 established in communication } ensure that { when { EUT moves to a foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to send an Echo Request to QE4 |  |  |
| 2 | Check: does EUT receive an Echo Reply from QE4 ? | Yes | No |
| 3 | Move EUT to Foreign Network 1 |  |  |
| 4 | wait a few seconds (to let the EUT register with its Home Agent). |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT ? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1612_01 | Test Purpose: | TP_MOB_1612_01 |
| Summary: | 'When MN starts a transport-level connections at Home, it conserves that connection away_from_home' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1612 |
| with { EUT connected in home_network and EUT having established a transport_connection to QE3 } ensure that { when { EUT moves to a foreign_network } then { EUT and QE3 are able to communicate using the transport_connection } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to establish a transport-level connection (telnet, ftp, ssh, etc.) with QE3 |  |  |
| 2 | Move EUT to foreign network 1 |  |  |
| 3 | Check: Is the transport-level connection established in step 1 still alive? | yes | no |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1613_01 | Test Purpose: | TP_MOB_1613_01 |
| Summary: | 'When MN starts a transport-level connections in Foreign network, it conserves this connection into another Foreign network' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1613 |
| with { EUT away_from_home and EUT registered to QE1 and EUT having established a transport_connection to QE3 } ensure that { when { EUT moves to another foreign_network } then { EUT and QE3 are able to communicate using the transport_connection } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause EUT to establish a transport-level (telnet, ftp, ssh or similar) connection with QE1 |  |  |
| 2 | Move EUT to foreign network 2 |  |  |
| 3 | Check: Is the transport level connection established in step 1 still alive? | yes | no |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1614_01 | Test Purpose: | TP_MOB_1614_01 |
| Summary: | 'MN sends packets directly to the correspondent node when a binding exists' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1614 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and EUT having established a binding to QE4 } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { EUT sends the response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected in Foreign Network 1 and registered to its Home Agent QE1 EUT configured to perform route optimization QE4 configured to perform route optimization EUT has established a binding to QE4 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: Does QE4 receive an Echo Reply from EUT ? | yes | no |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1615_01 | Test Purpose: | TP_MOB_1615_01 |
| Summary: | 'MN uses reverse tunneling to the correspondent node when no binding exists' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1615, RQ_001_1615, RQ_001_1819 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured not to perform Route_Optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected in Foreign Network 1 and registered to its Home Agent QE1 EUT configured to perform route optimization QE4 configure NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Check: Does QE4 receive an Echo Reply from EUT ? | yes | no |
| 3 | Disconnect QE1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 5 | Check: Does QE4 receive an Echo Reply from EUT ? | no | yes |
| Observations: |  |

###### §11.4 Home Agent and Prefix Management

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_01 | Test Purpose: | TP_MOB_1082_01 |
| Summary: | 'Home Agent uses a Security Association to protect integrity and authenticity of Mobile_Prefix_Solicitations and Advertisements' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1607 |
| with { QE1 at_home and QE1 configured to protect Mobile_Prefix_Solicitations and QE1 configured to accept only secured Mobile_Prefix_Advertisements and QE1 configured to have a short prefix_lifetime --(suggest 30s) } ensure that { when { QE1 moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response from QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is connected to Foreign Network 1 and registered to its Home Agent EUT QE1 is configured to protect Mobile Prefix Solicitation messages QE1 is configured to only accept protected Mobile Prefix Advertisement messages EUT is configured to advertise a prefered prefix lifetime of 20 sec EUT is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that initial lifetime of the home address of QE1 has expired |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_02 | Test Purpose: | TP_MOB_1082_02 |
| Summary: | 'Mobile Node uses a Security Association to protect integrity and authenticity of Mobile Prefix Solicitaions and Advertisements' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1663, RQ_001_1664 |
| with { EUT at_home and QE1 configured to accept only secured Mobile_Prefix_Solicitations and QE1 configured to protect Mobile_Prefix_Advertisements and EUT configured to have a short prefix_lifetime (--suggest 30s)' } ensure that { when { EUT moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to the EUT indicating that response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE1 is configured to only accept protected Mobile Prefix Solicitation messages QE1 is configured to protect Mobile Prefix Advertisement messages QE1 is configured to advertise a prefered prefix lifetime of 20 sec QE1 is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that EUT has send a Mobile Prefix Solicitation message and received a Mobile Prefix Advertisement message |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §11.4.1 Dynamic Home Agent Address Discovery

| Test Description |
| --- |
| Identifier: | TD_MOB_1655_01 | Test Purpose: | TP_MOB_1655_01 |
| Summary: | 'Mobile Node already registered to a Home Agent uses that Home Agent for any new registrations' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_06 |
| References: | RQ_001_1655, RQ_001_1655 |
| with { EUT configured 'to use DHAAD' and EUT away_from_home and EUT registered to QE1 and QE2 disconnected from Home_Network 1 } ensure that { when { QE1 is disconnected from Home_Network 1 and QE2 is connected to Home_Network 1 and EUT moves to another foreign_network } then { QE4 and EUT are unable to communicate within MAX_BINDACK_TIMEOUT -- EUT tries to register with QE1 and QE4 is able to communicate after MAX_BINDACK_TIMEOUT } -- EUT registered to QE2 } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to use DHAAD QE2 is configured to serve as home agent for home network 1 QE2 is disconnected EUT connected to foreign network 1 and registered to QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 |  |  |
| 2 | Connect QE2 to Home Network 1 |  |  |
| 3 | Move EUT to foreign network 2 |  |  |
| 4 | Cause QE4 to continuously send ICMP ECHO requests to EUT |  |  |
| 5 | Check: Does QE4 receive ICMP ECHO replies from EUT? | No | Yes |
| 6 | Wait for MAX_BINDACK_TIMEOUT seconds or more (EUT should still be trying to register to QE1 until this delay expires) |  |  |
| 7 | Check: Does QE4 receive ICMP ECHO replies from EUT? (EUT should now have successfully registered to QE2) | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1657_01 | Test Purpose: | TP_MOB_1657_01 |
| Summary: | 'Mobile Node attemps Dynamic Home Agent Address Discovery if it cannot contact its current Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_06 |
| References: | RQ_001_1657 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { QE1 is disconnected from the Home_Network and EUT moves to another foreign_network } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE2 is configured to be Home Agent on Home Network 1 EUT is connected to Foreign Network 1 and is registered to ist Home Agent QE1 QE1 is configured to have a Binding Lifetime at one minute |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 from Home Network 1 |  |  |
| 2 | Move EUT to Foreing Network 2 |  |  |
| 3 | Wait a few seconds (for EUT to try to bind to Home Agent) |  |  |
| 4 | Cause QE3 to send an Echo Request to the Home Address of EUT |  |  |
| 5 | Check: does QE3 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1385_01 | Test Purpose: | TP_MOB_1385_01 |
| Summary: | 'Mobile Node supports Dynamic Home Agent Address Discovery' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1385 |
| with { EUT registered to QE1 and EUT disconnected and EUT configured not to perform Route_Optimization and QE4 configured not to perform Route_Optimization } ensure that { when { QE1 is requested to modify its IP_address before the EUT is connected to a foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect EUT from Home Network 1 |  |  |
| 2 | Configure QE1 with a new IP address on prefix_B |  |  |
| 3 | Connect EUT to Foreign Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 5 | Check: Does QE4 receives an Echo Reply ? | YES | NO |
| Observations: |  |

###### §11.4.2 Sending Mobile Prefix Solicitations

| Test Description |
| --- |
| Identifier: | TD_MOB_1661_01 | Test Purpose: | TP_MOB_1661_01 |
| Summary: | 'MN sends Mobil Prefix Solicitation to HA when its home address becomes invalid' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1661, RQ_001_1661, RQ_001_1662, RQ_001_1665 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { EUT 'has its home address which becomes invalid' } then { EUT 'update the prefix lifetime information for its home address' } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign network 1 |  |  |
| 2 | Wait for original Home address lifetime to expire |  |  |
| 3 | Cause QE4 to send an Echo Request to EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_02 | Test Purpose: | TP_MOB_1082_02 |
| Summary: | 'Mobile Node uses a Security Association to protect integrity and authenticity of Mobile Prefix Solicitaions and Advertisements' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1663, RQ_001_1664 |
| with { EUT at_home and QE1 configured to accept only secured Mobile_Prefix_Solicitations and QE1 configured to protect Mobile_Prefix_Advertisements and EUT configured to have a short prefix_lifetime (--suggest 30s)' } ensure that { when { EUT moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to the EUT indicating that response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE1 is configured to only accept protected Mobile Prefix Solicitation messages QE1 is configured to protect Mobile Prefix Advertisement messages QE1 is configured to advertise a prefered prefix lifetime of 20 sec QE1 is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that EUT has send a Mobile Prefix Solicitation message and received a Mobile Prefix Advertisement message |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1082_02 | Test Purpose: | TP_MOB_1082_02 |
| Summary: | 'Mobile Node uses a Security Association to protect integrity and authenticity of Mobile Prefix Solicitaions and Advertisements' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1014, RQ_001_1082, RQ_001_1663, RQ_001_1664 |
| with { EUT at_home and QE1 configured to accept only secured Mobile_Prefix_Solicitations and QE1 configured to protect Mobile_Prefix_Advertisements and EUT configured to have a short prefix_lifetime (--suggest 30s)' } ensure that { when { EUT moves to a foreign_network before its prefix_lifetime expires before QE4 sends a packet to the EUT indicating that response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 QE1 is configured to only accept protected Mobile Prefix Solicitation messages QE1 is configured to protect Mobile Prefix Advertisement messages QE1 is configured to advertise a prefered prefix lifetime of 20 sec QE1 is configured to advertise a valid prefix lifetime of 30 sec |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait 30 sec so that EUT has send a Mobile Prefix Solicitation message and received a Mobile Prefix Advertisement message |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §11.4.3 Receiving Mobile Prefix Advertisements

| Test Description |
| --- |
| Identifier: | TD_MOB_1384_01 | Test Purpose: | TP_MOB_1384_01 |
| Summary: | 'MN reconfigures its home address according to the prefix information in a Mobile_Prefix_Advertisement' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1384 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { QE1 is requested to modify its home_network prefix } then { QE4 and the EUT are able to communicate using the new home_address } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT connected to foreign network 1 EUT registered to QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE1 to change the prefix on its home subnet interface |  |  |
| 2 | Wait for some seconds to allow EUT to retrieve new home address |  |  |
| 3 | Check: Does EUT indicate a new home address? | Yes | No |
| Observations: |  |

###### §11.5 Movement

| Test Description |
| --- |
| Identifier: | TD_MOB_1809_01 | Test Purpose: | TP_MOB_1809_01 |
| Summary: | 'Mobile Nodes support returning home' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1808, RQ_001_1809 |
| with { EUT away_from_home and QE4 able to communicate with EUT } ensure that { when { EUT returns home } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1809_01 | Test Purpose: | TP_MOB_1809_01 |
| Summary: | 'Mobile Nodes support returning home' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1808, RQ_001_1809 |
| with { EUT away_from_home and QE4 able to communicate with EUT } ensure that { when { EUT returns home } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1380_01 | Test Purpose: | TP_MOB_1380_01 |
| Summary: | 'Mobile Node supports care-of address formation' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1380 |
| with { EUT connected to home_network and QE4 able to communicate with EUT } ensure that { when { EUT moves to a foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let the EUT register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Resquest to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1683_01 | Test Purpose: | TP_MOB_1683_01 |
| Summary: | 'Mobile Node generates a new primary Care of Address after having moved' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1380, RQ_001_1683, RQ_001_1690 |
| with { EUT away_from_home and QE4 able to communicate with EUT } ensure that { when { EUT moves to another foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Wait a few seconds (to let the EUT register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

###### §11.5.1 Movement Detection

| Test Description |
| --- |
| Identifier: | TD_MOB_1678_01 | Test Purpose: | TP_MOB_1678_01 |
| Summary: | ' MN discover a new default router when it detects the default router is no longer bi-directionally reachable ' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1678 |
| with { EUT connected in home_network and QE1 disconnected } ensure that { when { EUT moves to a foreign_network and EUT receives a packet from QE3 indicating that a response is required and containing a destination_address set to the Care_of_Address of the EUT } then { QE3 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is disconnected EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Cause QE3 to send an Echo Request to the new Care-of Address of EUT |  |  |
| 3 | Check: does QE3 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1824_01 | Test Purpose: | TP_MOB_1824_01 |
| Summary: | 'When Mobile Node detects a L3 handover, it constructs a new Care-of Address, it select a new default router and register the new address to its Home Agent and the Correspondent Nodes which it is performing route optimi |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1682, RQ_001_1824 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and EUT having established a binding to QE4 } ensure that { when { EUT moves to another foreign_network } then { QE4 and EUT are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT is configured to perform Route Optimization QE4 is configured to perform Route Optimization EUT has established a binding with the Corespondent Node QE4 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Moves EUT to Foreign Network 2 |  |  |
| 2 | Wait a few seconds (to let EUTupdate its bindings to QE1 and QE4) |  |  |
| 3 | Disconnect QE1 from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1824_01 | Test Purpose: | TP_MOB_1824_01 |
| Summary: | 'When Mobile Node detects a L3 handover, it constructs a new Care-of Address, it select a new default router and register the new address to its Home Agent and the Correspondent Nodes which it is performing route optimi |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1682, RQ_001_1824 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and EUT having established a binding to QE4 } ensure that { when { EUT moves to another foreign_network } then { QE4 and EUT are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT is configured to perform Route Optimization QE4 is configured to perform Route Optimization EUT has established a binding with the Corespondent Node QE4 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Moves EUT to Foreign Network 2 |  |  |
| 2 | Wait a few seconds (to let EUTupdate its bindings to QE1 and QE4) |  |  |
| 3 | Disconnect QE1 from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

###### §11.5.2 Forming New Care-of Addresses

| Test Description |
| --- |
| Identifier: | TD_MOB_1683_01 | Test Purpose: | TP_MOB_1683_01 |
| Summary: | 'Mobile Node generates a new primary Care of Address after having moved' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1380, RQ_001_1683, RQ_001_1690 |
| with { EUT away_from_home and QE4 able to communicate with EUT } ensure that { when { EUT moves to another foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Wait a few seconds (to let the EUT register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1684_01 | Test Purpose: | TP_MOB_1684_01 |
| Summary: | 'Mobile Node generates a new primary Care of Address when the current one is deprecated' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_07 |
| References: | RQ_001_1684 |
| with { EUT away_from_home and QE3 configured as default_router for EUT and QE2 able to communicate with EUT } ensure that { when { QE3 stops advertizing the old prefix before (QE3 starts advertizing a new prefix before QE2 is requested to send a packet to the EUT indicating that a response is required) } then { QE2 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN Impossible to know when the Care-of address registration will take place Depending of the implementation to reduce the handover |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1005_01 | Test Purpose: | TP_MOB_1005_01 |
| Summary: | 'When away, Mobile Node is addressable at one or more Care of Addresses' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1005 |
| with { EUT at_home and QE6 'advertising a second prefix on Foreign Network 1' } ensure that { when { EUT moves to Foreign_Network 1 } then { QE4 and EUT are able to communicate using first and second Care_of_address } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 Both R1 and R3 have two global addresses, one on Prefix B and one on Prefix E R3 advertises prefix B and prefix E on Foreign Network 1 QE1, QE4 and R2 have a static route for prefix E and are able to reach a node with a prefix E on Foreign Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to EUT on its care-of address generated using prefix E |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| 4 | Cause QE4 to send an Echo Request to EUT on its care-of address generated using prefix B |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

###### §11.5.3 Using Multiple Care-of Addresses

| Test Description |
| --- |
| Identifier: | TD_MOB_1683_01 | Test Purpose: | TP_MOB_1683_01 |
| Summary: | 'Mobile Node generates a new primary Care of Address after having moved' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1380, RQ_001_1683, RQ_001_1690 |
| with { EUT away_from_home and QE4 able to communicate with EUT } ensure that { when { EUT moves to another foreign_network } then { QE4 and the EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Wait a few seconds (to let the EUT register with its Home Agent) |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1693_01 | Test Purpose: | TP_MOB_1693_01 |
| Summary: | ' MN accepts packets at its previous CoA after registering its new primary CoA ' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1693 |
| with { EUT away_from_home and EUT registered to QE1 and QE8 advertizing a new prefix -- thus causing a new care-of -- address to be generated } ensure that { when { QE8 stops advertizing the old prefix before (QE8 starts advertizing a new prefix before EUT receives a packet from QE3 indicating that a response is required and containing a destination_address set to the old Care_Of_Address of the EUT) } then { QE3 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN Impossible to know when the Care-of address registration will take place Depending of the implementation to reduce the handover |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1694_01 | Test Purpose: | TP_MOB_1694_01 |
| Summary: | 'Mobile Node invalidates all associated Care of Addresses when the corresponding router is unreachable' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1694 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { EUT moves to another foreign_network } then { QE1 and the EUT are unable to communicate using the old Care_of_Address } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Cause QE4 to send an Echo Request to EUT on its old care-of address of the Foreign Network 1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT ? | NO | YES |
| Observations: |  |

###### §11.5.4 Returning Home

| Test Description |
| --- |
| Identifier: | TD_MOB_1702_01 | Test Purpose: | TP_MOB_1702_01 |
| Summary: | 'Mobile Node replies to Neighbor Solicitations for its Home Address after returning home and having sent a Binding Update' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1695, RQ_001_1702, RQ_001_1702, RQ_001_1703 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { EUT returns home and QE1 is disconnected from the home_network } then { QE4 and the EUT are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | QE1 is disconnected from Home Network 1 |  |  |
| 2 | Move EUT to Home Network 1 |  |  |
| 3 | Cause QE4 send an Echo Request to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT | NO | YES |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1700_01 | Test Purpose: | TP_MOB_1700_01 |
| Summary: | 'Mobile Node does not perform Duplicate Address Detection when returning home before the expiry of its bindings' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1700 |
| with { EUT away_from_home and EUT registered to QE1 and QE1 is disconnected and QE3 having the same Home_Address as EUT and QE3 having the same ethernet_address as QE1 } ensure that { when { EUT returns home before the binding_lifetime expires and QE3 is disconnected and QE1 is connected to the Home_Network } then { EUT and QE4 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 QE3 is disconnected from Home Network 1 QE3 is configured with the same address as EUT and the same ethernet address as QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnected QE1 from Home Network 1 |  |  |
| 2 | Connected QE3 to Home Network 1 |  |  |
| 3 | Move EUT to Home Network 1 |  |  |
| 4 | Wait a very few seconds (two seconds, to let Mobile Node send Binding Update to its Home Agent) |  |  |
| 5 | Disconnect QE3 to Home Network 1 |  |  |
| 6 | Connect QE1 to Home network 1 |  |  |
| 7 | Wait a few seconds (to let EUT de-register with its Home Agent QE1) |  |  |
| 8 | Cause QE4 to send an Echo Request to EUT |  |  |
| 9 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1701_01 | Test Purpose: | TP_MOB_1701_01 |
| Summary: | 'Mobile Node performs Duplicate Address Detection when returning home after its bindings have expired' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1701 |
| with { EUT away_from_home and EUT registered to QE1 and EUT binding_lifetime expired at QE1 and QE4 connected to home_network using the same Home_Address as EUT } ensure that { when { EUT returns home } then { EUT is unable to communicate } -- DAD fails } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to have a Binding LifeTime at one minute EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 QE4 is manually configured with the same address as EUT QE4 is disconnected |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Disconnect QE1 |  |  |
| 2 | Wait one minute (to let the Binding of EUT expire) |  |  |
| 3 | Connect QE4 to Home Network 1 |  |  |
| 4 | Move EUT to Home Network 1 |  |  |
| 5 | QE4 is disconnected from Home Network 1 |  |  |
| 6 | Cause QE1 to send an Echo Request to the Home Address of EUT |  |  |
| 7 | Check: does QE1 receive an Echo Reply from EUT | NO | YES |
| Observations: |  |

###### §11.6.3 Protecting Return Routability Packets

| Test Description |
| --- |
| Identifier: | TD_MOB_1725_01 | Test Purpose: | TP_MOB_1725_01 |
| Summary: | 'Mobile Node support the protection of Home Test and Home Test Init messages' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1725 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization and QE1 configured to protect return_routability_packets } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { EUT sends a response directly to QE4 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT is configured to perform route optimization QE4 is configured to perform route optimization QE1 is configured to protect return routability packets by Ipsec with EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

###### §11.6 Return Routability Procedure

| Test Description |
| --- |
| Identifier: | TD_MOB_1063_01 | Test Purpose: | TP_MOB_1063_01 |
| Summary: | 'Mobile Node is able to participate in Return Routability Procedure' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1048, RQ_001_1063, RQ_001_1709, RQ_001_1063, RQ_001_1064, RQ_001_1744, RQ_001_1745, RQ_001_1750, RQ_001_1751, RQ_001_1754, RQ_001_1759 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response directly from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 EUT is configured to perform route optimization QE4 is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Causet QE4 to send an Echo Request message to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive Echo Replies from EUT? | Yes | No |
| 3 | Wait a few seconds to ensure that EUT and QE4 have had time to complete the Return Routability Procedure |  |  |
| 4 | Disconnect QE1 from the network |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: | If the Mobile Node still manages to communicate with the Corresponding Node once the Home Agent is disconnected from the network, this shows that is is using Route Optimization and hence that it managed to perform the Return Routability Procedure. |

###### §11.6.1 Sending Test Init Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1063_01 | Test Purpose: | TP_MOB_1063_01 |
| Summary: | 'Mobile Node is able to participate in Return Routability Procedure' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1048, RQ_001_1063, RQ_001_1709, RQ_001_1063, RQ_001_1064, RQ_001_1744, RQ_001_1745, RQ_001_1750, RQ_001_1751, RQ_001_1754, RQ_001_1759 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured to perform route_optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response directly from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 EUT is configured to perform route optimization QE4 is configured to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Causet QE4 to send an Echo Request message to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive Echo Replies from EUT? | Yes | No |
| 3 | Wait a few seconds to ensure that EUT and QE4 have had time to complete the Return Routability Procedure |  |  |
| 4 | Disconnect QE1 from the network |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: | If the Mobile Node still manages to communicate with the Corresponding Node once the Home Agent is disconnected from the network, this shows that is is using Route Optimization and hence that it managed to perform the Return Routability Procedure. |

###### §11.6.2 Receiving Test Messages

| Test Description |
| --- |
| Identifier: | TD_MOB_1724_01 | Test Purpose: | TP_MOB_1724_01 |
| Summary: | 'Mobile Node falls back to tunneling if correspondent refuses Route Optimization' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1724 |
| with { EUT away_from_home and EUT registered to QE1 and EUT configured to perform route_optimization and QE4 configured not to perform Route_Optimization } ensure that { when { EUT receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and has registered to its Home Agent QE1 EUT is configured to perform route optimization QE4 is configured NOT to perform route optimization |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive an Echo Reply from EUT | Yes | No |
| Observations: | As QE4 is configured to refuse Route Optimisation, EUT can only fall back to tunneling. |

###### §11.7.1 Sending Binding Updates To The Home Agent

| Test Description |
| --- |
| Identifier: | TD_MOB_1727_01 | Test Purpose: | TP_MOB_1727_01 |
| Summary: | 'Mobile Node registers its new primary Care-Of Address after changing it' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1727 |
| with { EUT away_from_home and EUT registered to QE1 } ensure that { when { EUT moves to another foreign_network and EUT receives a packet from QE4 indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and is registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receives an Echo Reply from EUT? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1768_01 | Test Purpose: | TP_MOB_1768_01 |
| Summary: | 'Mobile Node sends Binding Update before expiry of the binding lifetime' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1728, RQ_001_1768 |
| with { EUT away_from_home and EUT registered to QE1 and EUT able to communicate with QE4 } ensure that { when { QE4 (is requested to send a packet to the EUT indicating that a response is required) after the binding_lifetime } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a period equal to the Binding Lifetime |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1733_01 | Test Purpose: | TP_MOB_1733_01 |
| Summary: | 'Mobile Node sends Binding Update messages to its Home Agent until it receives a matching Binding_Acknowledgement message, before MAX_BINDACK_TIMEOUT seconds' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1733 |
| with { EUT at_home and EUT configured to have its Home_Agent_address available and QE1 disconnected } ensure that { when { EUT moves to a foreign_network and QE1 is connected after 15 seconds -- ~ MAX_BINDACK_TIMEOUT / 2 } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 EUT is aware of the address of its Home Agent QE1 is disconnected from Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait 20 seconds (EUT will try to bind to QE1) |  |  |
| 3 | Connect QE1 to Home Network 1 |  |  |
| 4 | Wait a few seconds (to let EUTde-register to QE1) |  |  |
| 5 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1734_01 | Test Purpose: | TP_MOB_1734_01 |
| Summary: | 'When Mobile Node knows several Home Agent (returned during DHAAD), Mobile Node tries to register with other Home Agents when registration fails with the first one' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_06 |
| References: | RQ_001_1734 |
| with { EUT not configured to have its Home_Agent_address available and QE1 configured to have a Home_Agent_Preference greater than QE2 } ensure that { when { QE1 is disconnected and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate after MAX_BINDACK_TIMEOUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is unaware the address of its Home Agent QE2 is configured to serve as Home Agent in the Home Network 1 QE1 is configured with a Home Agent Preference higher than QE2 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | NO | YES |
| 5 | Wait two minutes |  |  |
| 6 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 7 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1740_01 | Test Purpose: | TP_MOB_1740_01 |
| Summary: | 'Mobile Node attempts to register all of its home addresses' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1740 |
| with { EUT disconnected and EUT configured to have 2 home_addresses } ensure that { when { EUT is connected to a foreign_network and QE4 is requested to send a packet indicating that a response is required to the first home_address of EUT and QE4 is requested to send a packet indicating that a response is required to the second home_address of EUT } then { QE4 indicates receipt of the first response and QE4 indicates receipt of the second response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1 EUT is configured to have two different home addresses |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let EUT register to QE1) |  |  |
| 3 | Cause QE4 to send an Echo Request to the first home address of EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| 5 | Cause QE4 to send an Echo Request to EUT to the second home address of EUT |  |  |
| 6 | Check: does QE4 receive an Echo Reply from EUT? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1742_01 | Test Purpose: | TP_MOB_1742_01 |
| Summary: | 'Mobile Node does not attempt to use its home address if registration with Home Agent fails due to DAD' |
| Roles: | Mobile_Node, Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1742, RQ_001_1742, RQ_001_1770 |
| with { QE3 configured to have the home_address of EUT } ensure that { when { EUT moves to a foreign_network } -- the registering of EUT has failed then { EUT does not use its Home_Address to communicate } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN It is not possible to control that Mobile Node doesn't use its Home Address |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1743_01 | Test Purpose: | TP_MOB_1743_01 |
| Summary: | 'Mobile Node goes on registering home addresses when the registration of one of them fails' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1743 |
| with { EUT disconnected and EUT configured to have 2 home_addresses and QE3 configured to use the first home_address of EUT } ensure that { when { EUT is connected to a foreign_network and EUT receives a packet from QE4 containing a destination_address set to EUT home_address 2 and indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN You do not know how the Home Addresses are listed, so you can't guarantee that the address which failed is not the first or the last. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1814_01 | Test Purpose: | TP_MOB_1814_01 |
| Summary: | 'Mobile Node sends Binding Update messages to its Home Agent until it receives a matching Binding_Acknowledgement message, without time limit if it knows only one Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1814 |
| with { EUT at_home and EUT configured to have its Home_Agent_address available and QE1 disconnected } ensure that { when { EUT moves to a foreign_network and QE1 is connected after MAX_BINDACK_TIMEOUT and QE4 is requested to send a packet to QE1 indicating that a response is required } then { QE4 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Home Network 1. EUT is aware of the address of its Home Agent QE1. QE1 is disconnected. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait 2 minutes (more than MAX_BINDACK_TIMEOUT seconds) |  |  |
| 3 | Connect QE1 to Home Network 1 |  |  |
| 4 | Wait a few seconds (to let EUT establish a binding with QE1) |  |  |
| 5 | Cause QE4 to send an Echo Request to the home address of EUT |  |  |
| 6 | Check: does QE4 receives an Echo reply from EUT ? | Yes | No |
| Observations: |  |

###### §11.7.2 Correspondent registration

| Test Description |
| --- |
| Identifier: | TD_MOB_1744_01 | Test Purpose: | TP_MOB_1744_01 |
| Summary: | 'Mobile Node uptdates its bindings with correspondent nodes after changing its primary care-of address' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1744 |
| with { EUT away_from_home and EUT registered to QE1 and EUT having established a binding to QE4 } ensure that { when { EUT moves to another foreign_network and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT having established a binding with QE4 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 2 |  |  |
| 2 | Cause QE4 to send directly an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive directly an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1753_01 | Test Purpose: | TP_MOB_1753_01 |
| Summary: | 'Mobile Node is able to delete a binding with a correspondent node' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1753 |
| with { EUT away_from_home and EUT registered to QE1 and EUT having established a binding with QE4 } ensure that { when { EUT returns home and QE4 is requested to send a packet to EUT indicating that a response is required } then { QE4 indicates receipt of the response from the EUT} } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 EUT having established a binding with QE4 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Home Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

###### §11.7.3 Receiving Binding Acknowledgements

| Test Description |
| --- |
| Identifier: | TD_MOB_1768_01 | Test Purpose: | TP_MOB_1768_01 |
| Summary: | 'Mobile Node sends Binding Update before expiry of the binding lifetime' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_1728, RQ_001_1768 |
| with { EUT away_from_home and EUT registered to QE1 and EUT able to communicate with QE4 } ensure that { when { QE4 (is requested to send a packet to the EUT indicating that a response is required) after the binding_lifetime } then { QE4 indicates receipt of the response from the EUT } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is connected to Foreign Network 1 and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a period equal to the Binding Lifetime |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

###### §11.7.4 Receiving Binding Refresh Requests

| Test Description |
| --- |
| Identifier: | TD_MOB_1776_01 | Test Purpose: | TP_MOB_1776_01 |
| Summary: | 'Mobile Node updates binding with correspondent node upon receipt of a Binding Refresh Request' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1383, RQ_001_1776 |
| with { EUT away_from_home and EUT registered to QE1 and EUT having established a binding with QE4 } ensure that { when { QE4 sends a Binding_Refresh_Request } then { QE4 and the EUT are able to communicate directly after the original binding_lifetime } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN depending of the implementation to reduce the handover |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_1776_01 | Test Purpose: | TP_MOB_1776_01 |
| Summary: | 'Mobile Node updates binding with correspondent node upon receipt of a Binding Refresh Request' |
| Roles: | Correspondent_Node | Configuration: | CF_MOB_04 |
| References: | RQ_001_1383, RQ_001_1776 |
| with { EUT away_from_home and EUT registered to QE1 and EUT having established a binding with QE4 } ensure that { when { QE4 sends a Binding_Refresh_Request } then { QE4 and the EUT are able to communicate directly after the original binding_lifetime } } |
| Pre-test conditions: | NOT TESTABLE BY INTEROPERABILITY MEAN depending of the implementation to reduce the handover |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| Observations: |  |

### TDs extracted from RFC3776 [4] “Using IPsec to Protect Mobile IPv6 Signaling Between Mobile Nodes and Home Agents”

###### §4.1 Mandatory Support

| Test Description |
| --- |
| Identifier: | TD_MOB_2013_01 | Test Purpose: | TP_MOB_2013_01 |
| Summary: | 'Mobile Node sends Binding Update secured using transport_mode_ESP to its Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2013, RQ_001_2031 |
| with { EUT configured to protect any Binding_Update to QE1 using transport_mode_ESP and QE1 configured to accept only Binding_Update secured using transport_mode_ESP from EUT } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Binding Update sent to QE1 using transport mode ESP QE1 is configured to accept only Binding Update protected using transport mode ESP from EUT EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let EUT register to QE1) |  |  |
| 3 | Cause QE4 to send an Echo Request to EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2013_02 | Test Purpose: | TP_MOB_2013_02 |
| Summary: | 'Home Agent sends Binding_Acknowledgement secured using transport_mode_ESP to a Mobile Node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2013, RQ_001_2031 |
| with { EUT configured to protect any Binding_Acknowledgement to QE1 using transport_mode_ESP and QE1 configured to accept only a Binding_Acknowledgement secured using transport_mode_ESP from EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 is able to communicate with QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Binding Acknoledgement sent to QE1 using transport mode ESP QE1 is configured to accept only Binding Acknoledgement protected using transport mode ESP from EUT QE1 is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few second (to let QE1 register to EUT) |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2016_01 | Test Purpose: | TP_MOB_2016_01 |
| Summary: | 'Home Agent supports Mobile_Prefix_Solicitation secured using transport_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2016, RQ_001_2031 |
| with { QE1 configured to protect any Mobile_Prefix_Solicitation to EUT using transport_mode_ESP and EUT configured to accept only a Mobile_Prefix_Solicitation secured using transport_mode_ESP from QE1 and QE6 configured to have a prefix_lifetime of 1 minute and QE1 away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 is able to communicate with QE1 after the prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Mobile Prefix Solicitation sent to EUT using transport mode ESP EUT is configured to accept only Mobile Prefix Solicitation protected using transport mode ESP from QE1 R1 is configured to have a valid prefix lifetime at 1 minute QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few minutes (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2016_02 | Test Purpose: | TP_MOB_2016_02 |
| Summary: | 'Mobile Node supports Mobile_Prefix_Advertisement secured using transport_mode_ESP' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2016, RQ_001_2031 |
| with { QE1 configured to protect any Mobile_Prefix_Advertisement to EUT using transport_mode_ESP and EUT configured to accept only Mobile_Prefix_Advertisement secured using transport_mode_ESP from QE1 and EUT away_from_home and EUT registered to QE1 and QE6 configured to have a prefix_lifetime of 1 minute } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 and EUT are able to communicate after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Mobile Prefix Advertisement sent to EUT using transport mode ESP EUT is configured to accept only Mobile Prefix Advertisement protected using transport mode ESP from QE1 R1 is configured to have a valid prefix lifetime at 1 minute EUT is away from Home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few minutes (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2017_01 | Test Purpose: | TP_MOB_2017_01 |
| Summary: | 'Mobile Node sends Mobile_Prefix_Solicitation secured using transport_mode_ESP to its Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2017, RQ_001_2030 |
| with { EUT configured to protect any Mobile_Prefix_Solicitation to QE1 using transport_mode_ESP and QE1 configured to accept only a Mobile_Prefix_Solicitation secured using transport_mode_ESP from EUT and QE6 configured to have a prefix_lifetime of 1 minute and EUT away_from_home and EUT registered to QE1 } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 and EUT are able to communicate after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Mobile Prefix Solicitation sent to QE1 using transport mode ESP QE1 is configured to accept only Mobile Prefix Solicitation protected using transport mode ESP from EUT R1 is configured to have a valid prefix lifetime at 1 minute EUT is away from Home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few more one minute (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2017_02 | Test Purpose: | TP_MOB_2017_02 |
| Summary: | 'Home Agent sends Mobile_Prefix_Advertisement secured using transport_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2017, RQ_001_2030 |
| with { EUT configured to protect any Mobile_Prefix_Advertisement to QE1 using transport_mode_ESP and QE1 configured to accept only a Mobile_Prefix_Advertisement secured using transport_mode_ESP from EUT and QE1 away_from_home and QE1 registered to EUT and QE6 configured to have a prefix_lifetime of 1 minute } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 is able to communicate with QE1 after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Mobile Prefix Advertisement sent to QE1 using transport mode ESP QE1 is configured to accept only Mobile Prefix Advertisement protected using transport mode ESP from EUT R1 is configured to have a valid prefix lifetime at 1 minute QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few more one minute (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2018_01 | Test Purpose: | TP_MOB_2018_01 |
| Summary: | 'Mobile Node sends payload_packet tunneled to its Home Agent secured using tunnel_mode_ESP' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2018 |
| with { EUT configured to protect any payload_packet to QE1 using tunnel_mode_ESP and QE1 configured to accept only a payload_packet secured using tunnel_mode_ESP from EUT and EUT configured not to perform Route_Optimization and EUT away_from_home and EUT registered to QE1 } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect payload packets sent to QE1 using tunnel mode ESP QE1 is configured to accept only payload packets protected using tunnel mode ESP from EUT EUT configured not to perform Route Optimization EUT is away from home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2018_02 | Test Purpose: | TP_MOB_2018_02 |
| Summary: | 'Home Agent sends payload_packet tunneled to Mobile Node secured using tunnel_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2018 |
| with { EUT configured to protect any payload_packet to QE1 using tunnel_mode_ESP and QE1 configured to accept only a payload_packet secured using tunnel_mode_ESP from EUT and QE1 configured not to perform Route_Optimization and QE1 away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect payload packets sent to QE1 using tunnel mode ESP QE1 is configured to accept only payload packets protected using tunnel mode ESP from EUT QE1 configured not to perform Route Optimization QE1 is away from home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of the QE1 |  |  |
| 2 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2018_03 | Test Purpose: | TP_MOB_2018_03 |
| Summary: | 'Mobile Node supports payload_packet secured using tunnel_mode_ESP' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2018 |
| with { QE1 configured to protect any payload_packet to EUT using tunnel_mode_ESP and EUT configured to accept only a payload_packet secured using tunnel_mode_ESP from QE1 and EUT configured not to perform Route_Optimization and EUT away_from_home and EUT registered to QE1 } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect payload packets sent to EUT using tunnel mode ESP EUT is configured to accept only payload packets protected using tunnel mode ESP from QE1 EUT configured not to perform Route Optimization EUT is away from home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2018_04 | Test Purpose: | TP_MOB_2018_04 |
| Summary: | 'Home Agent supports payload_packet tunneled from Mobile Node and secured using tunnel_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2018 |
| with { QE1 configured to protect any payload_packet to EUT using tunnel_mode_ESP and EUT configured to accept only a payload_packet secured using tunnel_mode_ESP from QE1 and QE1 configured not to perform Route_Optimization and QE1 away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 is able to communicate with QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect payload packets sent to EUT using tunnel mode ESP EUT is configured to accept only payload packets protected using tunnel mode ESP from QE1 QE1 configured not to perform Route Optimization QE1 is away from home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2019_01 | Test Purpose: | TP_MOB_2019_01 |
| Summary: | 'Mobile Node supports multicast group membership control packets tunneled from its Home Agent proctected by ESP with the tunnel mode' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2019 |
| with { QE1 configured to protect any multicast_group_membership_control_packet to EUT using tunnel_mode_ESP and EUT configured to accept only a multicast_group_membership_control_packet from QE1 secured using tunnel_mode_ESP and EUT configured to subscribed to a global_multicast_group and EUT away_from_home and EUT registered to QE1 } ensure that { when { QE3 sends a packet to the global_multicast_group indicating that a response is required } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to secured multicast group membership control packets tunneled to EUT by ESP with tunnel mode EUT is configured to accept only protected multicast group membership control packets tunneled from QE1 by ESP with tunnel mode EUT is configured to subcribed to a multicast group MG1 with a global scope EUT away from home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Address of multicast group MG1 |  |  |
| 2 | Check: does QE3 receieve an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2019_02 | Test Purpose: | TP_MOB_2019_02 |
| Summary: | 'Home Agent supports multicast group membership control packets tunneled from Mobile Node proctected by ESP with the tunnel mode' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2019 |
| with { QE1 configured to protect any multicast_group_membership_control_packet to EUT using tunnel_mode_ESP and EUT configured to accept only a multicast_group_membership_control_packet from QE1 secured using tunnel_mode_ESP and QE1 configured to subscribed to a global_multicast_group and QE1 away_from_home and QE1 registered to EUT } ensure that { when { EUT sends a packet to the global_multicast_group indicating that a response is requested } then { QE3 indicates receipt of the response } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to secured multicast group membership control packets tunneled to EUT by ESP with tunnel mode EUT is configured to accept only protected multicast group membership control packets tunneled from QE1 by ESP with tunnel mode QE1 is configured to subcribed to a multicast group MG1 with a global scope QE1 away from home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE3 to send an Echo Request to the Address of multicast group MG1 |  |  |
| 2 | Check: does QE3 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

###### §4.2 Policy Requirements

| Test Description |
| --- |
| Identifier: | TD_MOB_2026_01 | Test Purpose: | TP_MOB_2026_01 |
| Summary: | 'When Mobile Node returns home and is configured with manualy established Security Associations, it makes inactive security policies concerning tunneled traffic with Home Agent without deleting Security Associations' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2026 |
| with { EUT configured 'with manually established Security Associations and Policies' and EUT configured to protect packets to QE1 using tunnel_mode_ESP and QE1 configured to accept only a packets secured using tunnel_mode_ESP and EUT configured not to perform Route_Optimization and EUT away_from_home and EUT registered to QE1 } ensure that { when { EUT moves to another foreign_network after EUT returns home } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). EUT is configured with manually established Security Associations and Policies. EUT is configured to secure packets tunneled to QE1 using tunnel mode ESP. QE1 is configured to accept only packets protected using tunnel mode ESP. EUT is configured not to perform Route Optimization. EUT is away from home and has registered to its Home Agent QE1. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Home Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Move EUT to Foreign Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply ? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2026_02 | Test Purpose: | TP_MOB_2026_02 |
| Summary: | 'When Mobile Node returns home and is configured with manualy established Security Associations, Home Agent makes inactive security policies concerning tunneled traffic with Mobile Node without deleting Security Associa |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2026 |
| with { EUT configured 'with manually established Security Associations and Policies' and EUT configured to protect packets to QE1 using tunnel_mode_ESP and QE1 configured to accept only a packets secured using tunnel_mode_ESP and QE1 configured not to perform Route_Optimization and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE1 moves to another foreign_network after QE1 returns home } then { QE4 is able to communicate with QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). EUT is configured with manually established Security Associations and Policies. EUT is configured to secure packets tunneled to QE1 using tunnel mode ESP. QE1 is configured to accept only packets protected using tunnel mode ESP. QE1 is configured not to perform Route Optimization. QE1 is away from home and has registered to its Home Agent EUT. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Home Network 1 |  |  |
| 2 | Wait a few seconds |  |  |
| 3 | Move QE1 to Foreign Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply ? | Yes | No |
| Observations: |  |

###### §4.3 IPsec Protocol Processing

| Test Description |
| --- |
| Identifier: | TD_MOB_2017_01 | Test Purpose: | TP_MOB_2017_01 |
| Summary: | 'Mobile Node sends Mobile_Prefix_Solicitation secured using transport_mode_ESP to its Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2017, RQ_001_2030 |
| with { EUT configured to protect any Mobile_Prefix_Solicitation to QE1 using transport_mode_ESP and QE1 configured to accept only a Mobile_Prefix_Solicitation secured using transport_mode_ESP from EUT and QE6 configured to have a prefix_lifetime of 1 minute and EUT away_from_home and EUT registered to QE1 } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 and EUT are able to communicate after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Mobile Prefix Solicitation sent to QE1 using transport mode ESP QE1 is configured to accept only Mobile Prefix Solicitation protected using transport mode ESP from EUT R1 is configured to have a valid prefix lifetime at 1 minute EUT is away from Home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few more one minute (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2017_02 | Test Purpose: | TP_MOB_2017_02 |
| Summary: | 'Home Agent sends Mobile_Prefix_Advertisement secured using transport_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2017, RQ_001_2030 |
| with { EUT configured to protect any Mobile_Prefix_Advertisement to QE1 using transport_mode_ESP and QE1 configured to accept only a Mobile_Prefix_Advertisement secured using transport_mode_ESP from EUT and QE1 away_from_home and QE1 registered to EUT and QE6 configured to have a prefix_lifetime of 1 minute } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 is able to communicate with QE1 after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Mobile Prefix Advertisement sent to QE1 using transport mode ESP QE1 is configured to accept only Mobile Prefix Advertisement protected using transport mode ESP from EUT R1 is configured to have a valid prefix lifetime at 1 minute QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few more one minute (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2013_01 | Test Purpose: | TP_MOB_2013_01 |
| Summary: | 'Mobile Node sends Binding Update secured using transport_mode_ESP to its Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2013, RQ_001_2031 |
| with { EUT configured to protect any Binding_Update to QE1 using transport_mode_ESP and QE1 configured to accept only Binding_Update secured using transport_mode_ESP from EUT } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Binding Update sent to QE1 using transport mode ESP QE1 is configured to accept only Binding Update protected using transport mode ESP from EUT EUT is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move EUT to Foreign Network 1 |  |  |
| 2 | Wait a few seconds (to let EUT register to QE1) |  |  |
| 3 | Cause QE4 to send an Echo Request to EUT |  |  |
| 4 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2013_02 | Test Purpose: | TP_MOB_2013_02 |
| Summary: | 'Home Agent sends Binding_Acknowledgement secured using transport_mode_ESP to a Mobile Node' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2013, RQ_001_2031 |
| with { EUT configured to protect any Binding_Acknowledgement to QE1 using transport_mode_ESP and QE1 configured to accept only a Binding_Acknowledgement secured using transport_mode_ESP from EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 is able to communicate with QE1 } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Binding Acknoledgement sent to QE1 using transport mode ESP QE1 is configured to accept only Binding Acknoledgement protected using transport mode ESP from EUT QE1 is connected to Home Network 1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Wait a few second (to let QE1 register to EUT) |  |  |
| 3 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 4 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2016_01 | Test Purpose: | TP_MOB_2016_01 |
| Summary: | 'Home Agent supports Mobile_Prefix_Solicitation secured using transport_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2016, RQ_001_2031 |
| with { QE1 configured to protect any Mobile_Prefix_Solicitation to EUT using transport_mode_ESP and EUT configured to accept only a Mobile_Prefix_Solicitation secured using transport_mode_ESP from QE1 and QE6 configured to have a prefix_lifetime of 1 minute and QE1 away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 is able to communicate with QE1 after the prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Mobile Prefix Solicitation sent to EUT using transport mode ESP EUT is configured to accept only Mobile Prefix Solicitation protected using transport mode ESP from QE1 R1 is configured to have a valid prefix lifetime at 1 minute QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few minutes (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 send an Echo Request to the Home Address of QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply from QE1 ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2016_02 | Test Purpose: | TP_MOB_2016_02 |
| Summary: | 'Mobile Node supports Mobile_Prefix_Advertisement secured using transport_mode_ESP' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2016, RQ_001_2031 |
| with { QE1 configured to protect any Mobile_Prefix_Advertisement to EUT using transport_mode_ESP and EUT configured to accept only Mobile_Prefix_Advertisement secured using transport_mode_ESP from QE1 and EUT away_from_home and EUT registered to QE1 and QE6 configured to have a prefix_lifetime of 1 minute } ensure that { when { a Security_Association is established between EUT and QE1 } then { QE4 and EUT are able to communicate after prefix_lifetime } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Mobile Prefix Advertisement sent to EUT using transport mode ESP EUT is configured to accept only Mobile Prefix Advertisement protected using transport mode ESP from QE1 R1 is configured to have a valid prefix lifetime at 1 minute EUT is away from Home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Wait a few minutes (to let the exchange of MPA / MPS be carried out) |  |  |
| 2 | Cause QE4 send an Echo Request to the Home Address of EUT |  |  |
| 3 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2014_01 | Test Purpose: | TP_MOB_2014_01 |
| Summary: | 'Home Agent supports Home Test Init secured using tunnel_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_1571, RQ_001_2034, RQ_001_2035 |
| with { QE1 configured to protect any Home_Test_Init to EUT using tunnel_mode_ESP and EUT configured to accept only Home_Test_Init secured using tunnel_mode_ESP from QE1 and QE1 configured to perform route_optimization and QE4 configured to perform route_optimization and QE1 is away_from_home and QE1 registered to EUT } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Home Test Init sent to EUT using tunnel mode ESP EUT is configured to accept only Home Test Init protected using tunnel mode ESP from QE1 QE1 configured to perform Route Optimization QE4 configured to perform Route Optimization QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Wait a few second (to let QE1 register to QE4) |  |  |
| 3 | Disconnect EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE1 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2014_02 | Test Purpose: | TP_MOB_2014_02 |
| Summary: | 'Mobile Node supports Home Test secured using tunnel_mode_ESP' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2034, RQ_001_2035 |
| with { QE1 configured to protect any Home_Test to EUT using tunnel_mode_ESP and EUT configured to accept only a Home_Test secured using tunnel_mode_ESP from QE1 and EUT configured to perform Route_Optimization and QE4 configured to perform route_optimization and EUT is away_from_home and EUT registered to QE1 } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) QE1 is configured to protect Home Test sent to EUT using tunnel mode ESP EUT is configured to accept only Home Test protected using tunnel mode ESP from QE1 EUT configured to perform Route Optimization QE4 configured to perform Route Optimization EUT is away from Home and has registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 2 | Wait a few second (to let EUT register to QE4) |  |  |
| 3 | Disconnect QE1 from Home Network |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT ? | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2015_01 | Test Purpose: | TP_MOB_2015_01 |
| Summary: | 'Mobile Node sends Home Test Init secured using tunnel_mode_ESP to its Home Agent' |
| Roles: | Mobile_Node | Configuration: | CF_MOB_03 |
| References: | RQ_001_2034 |
| with { EUT configured to protect any Home_Test_Init to QE1 using tunnel_mode_ESP and QE1 configured to accept only Home_Test_Init secured using tunnel_mode_ESP from EUT and EUT configured to perform route_optimization and QE4 configured to perform route_optimization } ensure that { when { a Security_Association is established between EUT and QE1 and EUT moves to a foreign_network } then { QE4 and EUT are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Home Test Init sent to QE1 using tunnel mode ESP QE1 is configured to accept only Home Test Init protected using tunnel mode ESP from EUT EUT configured to perform Route Optimization QE4 configured to perform Route Optimization EUT is away from Home and registered to its Home Agent QE1 |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address to EUT |  |  |
| 2 | Wait a few second (to let QE4 register to EUT) |  |  |
| 3 | Disconnect QE1 from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address to EUT |  |  |
| 5 | Check: does QE4 receive an Echo Reply from EUT | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2015_02 | Test Purpose: | TP_MOB_2015_02 |
| Summary: | 'Home Agent sends Home Test secured using tunnel_mode_ESP' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2034 |
| with { EUT configured to protect any Home_Test to QE1 using tunnel_mode_ESP and QE1 configured to accept only Home_Test secured using tunnel_mode_ESP from EUT and QE1 configured to perform Route_Optimization and QE4 configured to perform Route_Optimization } ensure that { when { a Security_Association is established between EUT and QE1 and QE1 moves to a foreign_network } then { QE4 and QE1 are able to communicate directly } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments) EUT is configured to protect Home Test sent to QE1 using tunnel mode ESP QE1 is configured to accept only Home Test protected using tunnel mode ESP from EUT QE1 configured to perform Route Optimization QE4 configured to perform Route Optimization QE1 is away from Home and registered to its Home Agent EUT |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 2 | Wait a few second (to let QE4 register to QE1) |  |  |
| 3 | Disconnect EUT from Home Network 1 |  |  |
| 4 | Cause QE4 to send an Echo Request to the Home Address of QE1 |  |  |
| 5 | Check: does QE4 receive an Echo Reply from QE4 | YES | NO |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2039_01 | Test Purpose: | TP_MOB_2039_01 |
| Summary: | 'Home Agent update its security association entries when the Mobile Node change of foreign network' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2039 |
| with { EUT configured to protect any Binding_Acknowledgement to QE1 using tunnel_mode_ESP and QE1 configured to accept only a Binding_Acknowledgement secured using tunnel_mode_ESP from EUT and QE1 away_from_home and QE1 registered to EUT } ensure that { when { QE1 moves to another foreign_network } then { QE4 and QE1 are able to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). EUT is configured to secure Binding Acknowledgement using ESP transport mode. QE1 is configured to accept only Binding Acknowledgement protected by ESP transport mode. QE1 is connected to Foreign Network 1 and has registered to its Home Agent EUT. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 2 |  |  |
| 2 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply ? | Yes | No |
| Observations: |  |

| Test Description |
| --- |
| Identifier: | TD_MOB_2040_01 | Test Purpose: | TP_MOB_2040_01 |
| Summary: | 'Home Agent does not take into account a Binding Update not secured' |
| Roles: | Home_Agent | Configuration: | CF_MOB_02 |
| References: | RQ_001_2040 |
| with { and EUT configured to accept only a Binding_Update secured using tunnel_mode_ESP and QE1 configured to send any Binding_Update not secured } ensure that { when { QE1 moves to a foreign_network } then { QE4 and QE1 are unable to communicate } } |
| Pre-test conditions: | The cleaning procedure has been run (see configuration comments). EUT is configured to accept only Binding Update protected by ESP with transport mode. QE1 is configured to send unprotected Binding Update. |
| Step | Test Sequence | Verdict |
|  |  | Pass | Fail |
| 1 | Move QE1 to Foreign Network 1 |  |  |
| 2 | Cause QE4 to send an Echo Request to QE1 |  |  |
| 3 | Check: does QE4 receive an Echo Reply ? | No | Yes |
| Observations: |  |

Annex A (informative):
Interoperability Testing Configurations

The following architectural configurations are referenced in the IPv6 Mobility Interoperability Test Descriptions specified in the present document. They are intended to give a general rather than specific view of the possible roles of the EUT and its associated QE(s) and the relationships between them.

The CF_Mob-Basic_01 configuration is not referenced in any of the Test Description, however all other configurations are subset of the architecture described in CF_Mob-Basic_01. Hence, replicating CF_Mob-Basic_01 in a test bed will save a lot of time to a tester willing to test all the Test Descriptions of the present document.

Annex B (informative):
IPv6 Interoperability Test Purposes

The Test Suite Structure is based on the IPv6 Mobility RFCs and the IPv6 Requirements Catalogue nodes. It is defined by the groups within the following TPLan specification of test purposes. The numbering is not contiguous so that new TPs can be added at a later date without the need to completely renumber the TSS groups.

TSS     : MOB

Title   : 'IOP - Mobility'

Version : 1.0.0

Date    : 29.11.2006

Author  : 'STF276 - Task 4'

-- Last $Rev: 430 $

-- Last $Author: vreck $

-- $Date: 2007-03-15 16:25:18 +0100 (Thu, 15 Mar 2007) $

--***Cross references***

xref RQ_001 {RFC3775,

RFC3776}

xref CF_MOB_02 {Configs_IOP_SEC.pdf}

xref CF_MOB_03 {Configs_IOP_SEC.pdf}

xref CF_MOB_04 {Configs_IOP_SEC.pdf}

xref CF_MOB_05 {Configs_IOP_SEC.pdf}

xref CF_MOB_06 {Configs_IOP_SEC.pdf}

xref CF_MOB_07 {Configs_IOP_SEC.pdf}

--***Definitions***

-- Entities

---- Primary Configuration entites

def entity EUT

def entity QE1

def entity QE2

def entity QE3

def entity QE4

def entity QE5

def entity QE6

def entity QE7

def entity QE8

---- Supplementary entities

def entity binding

def entity Binding_Cache_entry

def entity default_router

def entity foreign_network

def entity global_multicast_group

def entity home

def entity home_network

def entity link_local_multicast_group

def entity Neighbor_Discovery_cache_entry

def entity network

def entity organization_local_multicast_group

def entity Security_Association

def entity Security_Policy

def entity transport_connection

-- Messages

def event Binding_Acknowledgement

def event Binding_Refresh_Request

def event Binding_Update

{ Home_Address,

Home_Address_Destination_Option }

def event Home_Test

def event Home_Test_Init

def event Mobile_Prefix_Advertisements {Mobile_Prefix_Advertisement}

def event Mobile_Prefix_Solicitations {Mobile_Prefix_Solicitation}

def event multicast_group_membership_control_packet

def event packets {packet}

def event payload_packet

def event return_routability_packets

-- Procedures

def event IKEv2

def event multicast_data_packet_forwarding

def event route_optimization

-- Values

def value accept

def value binding_lifetime

def value care_of_address

def value ESP

def value ethernet_address

def value global_address

def value global_addresses

def value home_address

def value home_addresses

def value Home_Agent_address

def value Home_Agent_Preference

def value Interface_ID

def value IP_address

def value IPsec

def value lifetime

def value link_local_address

def value MAX_BINDACK_TIMEOUT

def value MAX_RR_BINDING_LIFETIME

def value on_link

def value packet {Authentication_Header,

destination_address,

ESP_Header,

Home_Address_Option,

sequence_number,

source_address}

def value prefix

def value prefix_lifetime

def value transport_mode_ESP

def value tunnel_mode_ESP

-- Units

def unit minute

def unit seconds

-- Conditions

def condition at_home

def condition available

def condition away_from_home

def condition connected

def context {~connected [to]}

def condition configured

def condition disconnected

def context {~disconnected [from]}

def condition registered

def context {~registered to}

def condition required

def condition subscribed

def context {~subscribed to}

def condition unreachable

def context {~unreachable from}

-- Keywords - Preconditions

def word communication

def word established

def word implement

def word perform

def word protect

def word use

-- Keywords - Stimuli

def word advertizing

def word communicate

def word configure

def word detects

def word expired

def word generates

def word modify

def word moves

def word reboot

def word registers

def word requested

def context {is ~requested to}

def context {is ~requested to ~configure}

def context {is ~requested to ~modify}

def word returns

def context {~returns ~home}

def word send

def context {is requested to ~send}

def word set

def context {~set to}

def word starts

def context {~starts advertizing}

def word stops

def context {~stops advertizing}

def word support

-- Keywords - Responses

def word accepts

def word deletes

def word discards

def word establishes

def word expires

def word implemented

def word indicate

def word indicates

def word only

def word receipt

def context {~indicates ~receipt of}

def word response

def context {sends no ~response}

def word secured

def word updates

def word using

-- Keywords - Glue

def word able

def word another

def word any

def word are

def word at

def word between

def word by

def word directly

def word does

def word even

def word first

def word for

def word greater

def word have

def word having

def word its

def word least

def word more

def word new

def word offered

def word old

def word on

def word original

def word own

def context {~its ~own}

def word previously

def word same

def word second

def word short

def word than

def word unable

def word used

--************************************--

--* RFC3775 Mobility Support in IPv6 *--

--************************************--

Group 1 'RFC 3775'

Group 1.1 'Group A'

TP id   : TP_MOB_1724_01

summary : 'Mobile Node falls back to tunneling if correspondent refuses

Route Optimization'

RQ ref  : RQ_001_1724

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1724_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured not to perform Route_Optimization

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1744_01

summary : 'Mobile Node uptdates its bindings with correspondent nodes

after changing its primary care-of address'

RQ ref  : RQ_001_1744

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1744_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT having established a binding to QE4

}

ensure that

{ when {     EUT moves to another foreign_network

and QE4 is requested to send a packet to EUT

indicating that a response is required }

then {     QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1457_01

summary : 'Correspondent Node creates a new entry in its binding cache

when receiving a valid Binding Update'

RQ ref  : RQ_001_1457

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1457_01

with {     QE4 away_from_home

and QE4 registered to QE1

and QE4 configured to perform route_optimization

and EUT configured to perform route_optimization

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { EUT sends response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1753_01

summary : 'Mobile Node is able to delete a binding with a correspondent node'

RQ ref  : RQ_001_1753

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1753_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT having established a binding with QE4

}

ensure that

{ when {     EUT returns home

and QE4 is requested to send a packet to EUT

indicating that a response is required }

then {     QE4 indicates receipt of the response from the EUT}

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1486_01

summary : 'Correspondent Node deletes any Binding Cache entry

after the expiration of the binding lifetime'

RQ ref  : RQ_001_1486 ,RQ_001_1461

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1486_01

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

}

ensure that

{ when {    EUT establishes a binding to QE4}

then {    EUT and QE4 are able to communicate directly

within the binding_lifetime

and EUT and QE4 are unable to communicate directly

after the binding_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1068_01

summary : 'Correspondent Node does not establish any binding with

a lifetime greater than MAX_RR_BINDING_LIFETIME'

RQ ref  : RQ_001_1068

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1068_01

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

}

ensure that

{ when {     EUT establishes a binding to QE4}

then {     EUT and QE4 are able to communicate directly

within the binding_lifetime

and EUT and QE4 are unable to communicate directly

after MAX_RR_BINDING_LIFETIME }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1068_02

summary : 'Mobile Node does not establish any binding with

a lifetime greater than MAX_RR_BINDING_LIFETIME'

RQ ref  : RQ_001_1068

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1068_02

--NOT interop TESTABLE

-- ==> there is no Interoperability method to guarantee that a

-- Mobile Node (on a foreign network) will use its Home Address

-- to send a new packet (instead of using its Care-of-Address).

with {     EUT configured to perform route_optimization

and EUT away_from_home

and EUT registered to QE1

and QE4 configured to perform route_optimization

}

ensure that

{ when {     EUT establishes a binding to QE4 }

then {     EUT and QE4 are able to communicate directly

within the binding_lifetime

and EUT and QE4 are unable to communicate directly

after MAX_RR_BINDING_LIFETIME }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1483_01

summary : 'Correspondent Node tries to refresh a binding cache entry

before it expires'

RQ ref  : RQ_001_1483

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1483_01

with {     QE4 away_from_home

and QE4 registered to QE1

and EUT having established a binding with QE4

and EUT established 'in continuous unbounded communication with QE4'

}

ensure that

{ when { QE4 sends a packet to the EUT

after the binding_lifetime

indicating that a response is required }

then { QE4 indicates receipt of the response directly from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1390_01

summary : 'Correspondent Node maintains a seperate binding cache for each

of its unicast routable addresses'

RQ ref  : RQ_001_1390

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1390_01

with {     EUT configured to have 2 global_addresses

and QE4 away_from_home

and QE4 registered to QE1

and EUT having established a binding to QE4

using its first global_address

and QE1 disconnected from the network

}

ensure that

{ when { EUT is requested to send a packet to QE4

containing a source_address

set to its second global_address }

then { QE4 does not indicate receipt of the packet  }

}

TP id   : TP_MOB_1458_01

summary : 'Correspondent Node updates a binding cache entry on receipt

of a valid Binding Update'

RQ ref  : RQ_001_1458

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1458_01

with {     QE4 away_from_home

and QE4 registered to QE1

and EUT having established a binding with QE4

}

ensure that

{ when {     QE4 moves to another foreign_network

and EUT is requested to send a packet to QE4

indicating that a response is required }

then { EUT indicates receipt of the response directly from QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1776_01

summary : 'Mobile Node updates binding with correspondent node upon receipt

of a Binding Refresh Request'

RQ ref  : RQ_001_1776 , RQ_001_1383

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1776_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT having established a binding with QE4

}

ensure that

{ when { QE4 sends a Binding_Refresh_Request }

then { QE4 and the EUT are able to communicate directly

after the original binding_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1348_01

summary : 'Correspondent Node is able to participate in Return

Routability Procedure'

RQ ref  : RQ_001_1348 , RQ_001_1050, RQ_001_1051

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1348_01

with {     QE4 away_from_home

and QE4 registered to QE1

and QE4 configured to perform route_optimization

and EUT configured to perform route_optimization

}

ensure that

{ when { EUT is requested to send a packet to QE4

indicating that a response is required }

then { EUT indicates receipt of the response directly from QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1063_01

summary : 'Mobile Node is able to participate in Return Routability

Procedure'

RQ ref  : RQ_001_1063 , RQ_001_1048 , RQ_001_1709,

RQ_001_1007, RQ_001_1723, RQ_001_1750

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1063_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { QE4 indicates receipt of the response directly from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1047_01

summary : 'Correspondent Node completes Return Routability Procedure

before accepting a Binding Update from a mobile node'

RQ ref  : RQ_001_1047

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1047_01

with {     QE4 away_from_home

and QE4 registered to QE1

and QE4 configured to perform route_optimization

and EUT configured to perform route_optimization

and QE1 unreachable from QE4 -- QE4 cannot complete RRP

}

ensure that

{ when { QE4 is requested to send a packet to the EUT

indicating that a response is required }

then { EUT sends no response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1485_01

summary : 'Correspondent Node stops retransmitting Binding Refresh Requests

messages when it receives a Binding Update'

RQ ref  : RQ_001_1485

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1485_01

--************************************************************************--

--*  However we wrap this up, it is a conformance test, not interop      *--

--************************************************************************--

with {     QE4 away_from_home

and QE4 registered to QE1

and EUT having established a binding with QE4

}

ensure that

{ when {     EUT 'tries to refresh its binding with QE4'

and EUT receives 'a message indicating that

the refresh is successful' }

then { EUT 'stops sending refresh requests to QE4' }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1725_01

summary : 'Mobile Node support the protection of Home Test and

Home Test Init messages'

RQ ref  : RQ_001_1725

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1725_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE1 configured to protect return_routability_packets

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { EUT sends a response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1065_01

summary : 'Correspondent Node sends a Binding_Acknowledgement message upon

receipt of a Binding Update message containing A-Flag set to 1'

RQ ref  : RQ_001_1065, RQ_001_1350

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1065_01

with {     QE4 away_from_home

and QE4 registered to QE1

and QE4 configured 'to request Binding_Acknowledgements from

correspondent nodes'

and QE4 configured to perform route_optimization

and EUT configured to perform route_optimization

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { EUT sends the response directly to QE4 }

}

End Group -- Group A

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

Group 1.2 'Group B'

TP id   : TP_MOB_1382_01

summary : 'Mobile Node is able to receive and process Binding Acknowledgements'

RQ ref  : RQ_001_1382

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1382_01

with {     EUT away_from_home

and EUT registered to QE1

and QE1 disconnected

and QE3 having the same Home_Address as EUT

and QE3 having the same ethernet_address as QE1

}

ensure that

{ when {     EUT returns home before the binding_lifetime expires

and QE3 is disconnected

and QE1 is connected to the Home_Network }

then {     EUT and QE4 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1700_01

summary : 'Mobile Node does not perform Duplicate Address Detection

when returning home before the expiry of its bindings'

RQ ref  : RQ_001_1700

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1700_01

with {     EUT away_from_home

and EUT registered to QE1

and QE1 is disconnected

and QE3 having the same Home_Address as EUT

and QE3 having the same ethernet_address as QE1

}

ensure that

{ when {     EUT returns home before the binding_lifetime expires

and QE3 is disconnected

and QE1 is connected to the Home_Network }

then {     EUT and QE4 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1693_01

summary : ' MN accepts packets at its previous CoA after registering

its new primary CoA '

RQ ref  : RQ_001_1693

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1693_01

with {     EUT away_from_home

and EUT registered to QE1

and QE8 advertizing a new prefix   -- thus causing a new care-of

-- address to be generated

}

ensure that

{ when {         QE8 stops advertizing the old prefix

before (QE8 starts advertizing a new prefix

before  EUT receives a packet from QE3

indicating that a response is required

and containing a destination_address

set to the old Care_Of_Address of the EUT) }

then { QE3 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1678_01

summary : ' MN discover a new default router when it detects the default

router is no longer bi-directionally reachable '

RQ ref  : RQ_001_1678

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1678_01

with {     EUT connected in home_network

and QE1 disconnected

}

ensure that

{ when {     EUT moves to a foreign_network

and EUT receives a packet from QE3

indicating that a response is required

and containing a destination_address

set to the Care_of_Address of the EUT }

then { QE3 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1507_01

summary : 'Home Agent removes binding when the associated prefix valid

lifetime expires'

RQ ref  : RQ_001_1507

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1507_01

with {     QE1 away_from_home

and QE1 registered to the EUT

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { the prefix_lifetime expires at the EUT }

then { QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1501_01

summary : 'Home Agent performs Duplicate Address Detection on home link

before sending a Binding Aknowledgment'

RQ ref  : RQ_001_1501 , RQ_001_1502 , RQ_001_1503

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1501_01

with {     QE1 at_home

and QE3 disconnected from home_network

and QE3 having the same home_address as QE1

}

ensure that

{ when {     QE1 is disconnected from the home_network

and QE3 is connected to the home_network

and QE1 is connected to a foreign_network }

then { QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1500_01

summary : 'Home Agent maintains a Binding Cache entry from receipt of a

Binding Update until the Binding Lifetime expires'

RQ ref  : RQ_001_1497, RQ_001_1500 , RQ_001_1522

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1500_01

with {     QE1 at_home

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { QE1 moves to a foreign_network }

then { QE4 and QE1 are able to communicate

within the Binding_Lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1497_01

summary : 'Home Agent creates a new entry in its Binding Cache

upon receipt of a Binding Update'

RQ ref  : RQ_001_1497

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1497_01

with

{

QE1 at_home

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { QE1 moves to a foreign_network }

then { QE4 is able to communicate with QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1826_01

summary : 'Home Agent updates the entry in its Binding Cache

upon receipt of a Binding Update'

RQ ref  : RQ_001_1826

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1826_01

with {     QE1 away_from_home

and QE1 registered to EUT

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { QE1 moves to another foreign_network }

then { QE3 and QE1 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1494_01

summary : 'Home Agent returns a type "132" Binding Aknowledgment

upon receipt of a Binding Update which Home Address

is not on link'

RQ ref  : RQ_001_1494

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1494_01

with {    QE1 disconnected from the home_network

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when {     QE1 is connected to a foreign_network

and EUT receives a Binding_Update

containing a Home_Address not on_link }

then {     QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1503_01

summary : 'Home Agent returns a type "134" Binding Aknowledgement when

Duplicate Address Detection for the Home Address / Link

Local Address fails'

RQ ref  : RQ_001_1503

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1503_01

with {     QE1 disconnected from home_network

and QE3 connected to home_network

and QE3 configured to have the same link_local_address as QE1

}

ensure that

{ when { QE1 is connected to a foreign_network }

then { QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1684_01

summary : 'Mobile Node generates a new primary Care of Address

when the current one is deprecated'

RQ ref  : RQ_001_1684

Role    : Mobile_Node

config  : CF_MOB_07

TD ref  : TD_MOB_1684_01

with {     EUT away_from_home

and QE3 configured as default_router for EUT

and QE2 able to communicate with EUT

}

ensure that

{ when {         QE3 stops advertizing the old prefix

before (QE3 starts advertizing a new prefix

before  QE2 is requested to send a packet to the EUT

indicating that a response is required) }

then {         QE2 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1683_01

summary : 'Mobile Node generates a new primary Care of Address after

having moved'

RQ ref  : RQ_001_1683 , RQ_001_1380 , RQ_001_1690

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1683_01

with {     EUT away_from_home

and QE4 able to communicate with EUT

}

ensure that

{ when { EUT moves to another foreign_network }

then { QE4 and the EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1465_01

summary : 'Correspondent Node deletes any existing related bindings

on receipt of a Binding Update requesting

to delete a binding'

RQ ref  : RQ_001_1465

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1465_01

with {     EUT away_from_home

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 having established a binding with EUT

}

ensure that

{ when { EUT returns home }

then { QE4 and the EUT are able to communicate with EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1496_01

summary : 'Correspondent Node sends a type "131" Binding Acknowledgment

when receiving a Home Registration Binding Update'

RQ ref  : RQ_001_1496

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1496_01

with {     EUT at_home

and QE5 at_home

and QE5 configured 'to use EUT as Home Agent'

}

ensure that

{ when { QE5 moves to a foreign_network }

then { QE3 and QE5 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1528_01

summary : 'When accepting Care of Address de-registration Binding

Update, Home Agent deletes any existing entry in its

Binding Cache for the Mobile Node'

RQ ref  : RQ_001_1528 , RQ_001_1529

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1528_01

with {     QE1 away_from_home

and QE1 registered to EUT

and QE4 able to communicate with QE1

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { QE1 returns home }

then { QE4 and QE1 are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1526_01

summary : 'Home Agent rejects De-Registration Binding Update if no

entry exists in its Binding Cache for the Mobile Node'

RQ ref  : RQ_001_1526

Role    : Home_Agent

config  : CF_MOB_05

TD ref  : TD_MOB_1526_01

with {     EUT disconnected from Home_Network

and QE2 configured to have the same IP_address as EUT

and QE1 connected to a foreign_network

and QE1 registered to QE2

}

ensure that

{ when {     QE2 is disconnected from Home_Network

and EUT is connected to Home_Network

and QE1 returns home }

then {     QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1380_01

summary : 'Mobile Node supports care-of address formation'

RQ ref  : RQ_001_1380

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1380_01

with {     EUT connected to home_network

and QE4 able to communicate with EUT

}

ensure that

{ when { EUT moves to a foreign_network }

then { QE4 and the EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1809_01

summary : 'Mobile Nodes support returning home'

RQ ref  : RQ_001_1809 , RQ_001_1808

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1809_01

with {     EUT away_from_home

and QE4 able to communicate with EUT

}

ensure that

{ when { EUT returns home }

then { QE4 and the EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1005_01

summary : 'When away, Mobile Node is addressable at one or

more Care of Addresses'

RQ ref  : RQ_001_1005

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1005_01

with

{

EUT at_home

and QE6 'advertising a second prefix on Foreign Network 1'

}

ensure that

{ when { EUT moves to Foreign_Network 1 }

then { QE4 and EUT are able to communicate

using first and second Care_of_address }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1702_01

summary : 'Mobile Node replies to Neighbor Solicitations for

its Home Address after returning home

and having sent a Binding Update'

RQ ref  : RQ_001_1702 , RQ_001_1695

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1702_01

with {     EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {     EUT returns home

and QE1 is disconnected from the home_network }

then { QE4 and the EUT are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1701_01

summary : 'Mobile Node performs Duplicate Address Detection

when returning home after its bindings have expired'

RQ ref  : RQ_001_1701

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1701_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT binding_lifetime expired at QE1

and QE4 connected to home_network

using the same Home_Address as EUT

}

ensure that

{ when { EUT returns home }

then { EUT is unable to communicate } -- DAD fails

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1768_01

summary : 'Mobile Node sends Binding Update before expiry of the

binding lifetime'

RQ ref  : RQ_001_1768 , RQ_001_1728

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1768_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT able to communicate with QE4

}

ensure that

{ when { QE4 (is requested to send a packet to the EUT

indicating that a response is required)

after the binding_lifetime }

then { QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1694_01

summary : 'Mobile Node invalidates all associated Care of Addresses

when the corresponding router is unreachable'

RQ ref  : RQ_001_1694

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1694_01

with {     EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when { EUT moves to another foreign_network }

then { QE1 and the EUT are unable to communicate

using the old Care_of_Address }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1510_01

summary : 'Home Agent returns a Binding Acknowledgment in response to

a Binding Update'

RQ ref  : RQ_001_1510

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1510_01

with { QE1 at_home }

ensure that

{ when { QE1 moves to a foreign_network }

then { QE4 and the EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1534_01

summary : 'Home Agent stops intercepting packets for the mobile

node on acceptance of the Primary Care of Address

De-Registration Binding Update'

RQ ref  : RQ_001_1534

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1534_01

with {     QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {     QE1 returns home

and EUT is disconnected from the home_network }

then { QE4 and QE1 are able to communicate }

}

End Group -- Group B

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

Group 1.3 'Group C'

TP id   : TP_MOB_1344_01

summary : 'Correspondent Node discard received packets containing

Type 2 Routing Headers'

RQ ref  : RQ_001_1344

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1344_01

with {     EUT disconnected

and QE4 configured to have the same link_local_address as EUT

and QE4 connected to Home_Network 2

and QE4 registered to QE1

and QE4 having established a binding with QE3

}

ensure that

{ when {     QE4 is disconnected

and EUT is connected to Home_Network 1

and QE3 is requested to send a packet to the EUT

indicating that a response is required

-- QE3 sends packets containing

-- Routing Headers Type 2

and QE5 is requested to send a packet to the EUT

indicating that a response is required }

-- QE5 sends packets not containing

-- Routing Headers Type 2

then {     QE3 indicates no receipt of the response from the EUT

and QE5 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1003_01

summary : 'MN continues to communicate after moving to a new link'

RQ ref  : RQ_001_1003 , RQ_001_1004 , RQ_001_1002

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1003_01

with {     EUT connected in home_network

and EUT registered to QE1

and EUT and QE4 established in communication

}

ensure that

{ when {      EUT moves to a foreign_network

and QE4 is requested to send a packet to EUT

indicating that a response is required }

then { QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1614_01

summary : 'MN sends packets directly to the correspondent node when

a binding exists'

RQ ref  : RQ_001_1614

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1614_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and EUT having established a binding to QE4

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { EUT sends the response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1412_01

summary : 'Correspondent Node receives packets directly from the Mobile Node

when a binding exists or Mobile Node believes in its existence'

RQ ref  : RQ_001_1412

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1412_01

with {     QE4 away_from_home

and QE4 registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 having established a binding with EUT

}

ensure that

{ when { EUT is requested to send a packet to QE4

indicating that a response is required }

then { EUT indicates receipt of the response directly from QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1423_01

summary : 'Correspondent Node sends packets directly to Mobile Node

when a binding already exists'

RQ ref  : RQ_001_1423

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1423_01

with {     QE4 away_from_home

and QE4 registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 having established a binding with EUT

and EUT having established a binding with QE4

}

ensure that

{ when { QE4 sends a packet to the EUT

indicating that a response is required }

then { QE4 indicates receipt of the response directly from EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1615_01

summary : 'MN uses reverse tunneling to the correspondent node when

no binding exists'

RQ ref  : RQ_001_1615

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1615_01

with {     EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured not to perform Route_Optimization

}

ensure that

{ when { EUT receives a packet from QE4

indicating that a response is required }

then { QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1592_01

summary : 'HA schedules the delivery of the prefix information when a new

prefix is added to its home subnet interface'

RQ ref  : RQ_001_1592 , RQ_001_1370 , RQ_001_1805

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1592_01

with {     QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {         EUT generates a new prefix to the home_address of QE1

before (QE4 sends a packet to QE1

using the new home_address

and indicating that a response is required) }

then {         QE4 indicates receipt of a response from QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1600_01

summary : 'HA retransmits periocally unsolicited Advertisement until

the receipt of a Mobile_Prefix_Solicitation from MN'

RQ ref  : RQ_001_1600 , RQ_001_1813

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1600_01

with {     QE1 away_from_home

and QE1 registered to EUT }

ensure that

{ when {        QE1 is disconnected from the foreign_network

before EUT generates a new prefix to the home_address of QE1

before QE1 is connected to the foreign_network after 1 minute

before QE4 sends a packet to QE1

using the new home_address

and indicating that a response is required }

then {        QE4 indicates receipt of a response from QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1812_01

summary : 'HA deliveries new prefix information when lifetime information

(valid or preferred lifetime) of the prefix changes'

RQ ref  : RQ_001_1812

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1812_01

with {     QE1 away_from_home

and QE1 registered to EUT

and EUT configured to have a short prefix_lifetime on the

Home_Network of QE1 --(suggest 30s)

}

ensure that

{ when { EUT is requested to configure a new prefix_lifetime

for QE1 }

then { QE1 and QE4 are able to communicate

using the new prefix

after the original prefix_lifetime expires }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1603_01

summary : 'HA transmits again unsolicited Mobile_Prefix_Advertisement after the

prolongation of the binding of the Mobile Node'

RQ ref  : RQ_001_1603

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1603_01

with {      QE1 away_from_home

and QE1 is registered to the EUT

and QE1 and the EUT configured to have a short binding_lifetime

-- (Suggest 30s)

}

ensure that

{ when {        QE1 is disconnected from the foreign_network

before the binding_lifetime expires between QE1 and the EUT

before QE1 is connected to another foreign_network }

then { QE1 and QE4 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1612_01

summary : 'When MN starts a transport-level connections at Home, it conserves

that connection away_from_home'

RQ ref  : RQ_001_1612

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1612_01

with {     EUT connected in home_network

and EUT having established a transport_connection to QE3

}

ensure that

{ when { EUT moves to a foreign_network }

then { EUT and QE3 are able to communicate

using the transport_connection }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1613_01

summary : 'When MN starts a transport-level connections in Foreign network,

it conserves this connection into another Foreign network'

RQ ref  : RQ_001_1613

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1613_01

with {      EUT away_from_home

and EUT registered to QE1

and EUT having established a transport_connection to QE3

}

ensure that

{ when { EUT moves to another foreign_network }

then { EUT and QE3 are able to communicate

using the transport_connection }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1413_01

summary : 'Correspondent Node drops packets containing Home Address

option (but no Binding Update) when there is no corresponding

Binding Cache entry'

RQ ref  : RQ_001_1413

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1413_01

with {      EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and EUT having no Binding_Cache_entry for QE4

and QE4 having a Binding_Cache_entry for EUT

}

ensure that

{ when { EUT receives a packet directly from QE4

indicating that a response is required }

then { EUT sends no response to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1413_02

summary : 'Correspondent Node drops packets containing Home Address

option (but no Binding Update) and send a Binding Error

message to the Mobile Node, when there is no corresponding

Binding Cache entry'

RQ ref  : RQ_001_1413

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1413_02

with {      EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and EUT having no Binding_Cache_entry for QE4

and QE4 having a Binding_Cache_entry for EUT

}

ensure that

{ when { EUT receives a packet directly from QE4

indicating that a response is required }

then {        EUT sends no response to QE4

before EUT and QE4 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1414_01

summary : 'When using Route Optimization, a Correspondent Node drops any

packet in which the Home Address option (but not Binding Update)

does not match the Home Address recorded in its Binding Cache'

RQ ref  : RQ_001_1414

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1414_01

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and QE4 having established a binding with EUT

}

ensure that

{ when { EUT receives a packet from QE4

containing a Home_Address_Option

not set to the Home_Address of QE4 }

then { EUT discards the packet }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1414_02

summary : 'When using Route Optimization, a Correspondent Node drops any

packet in which the Home Address option (but not Binding Update)

does not match the Home Address recorded in its Binding Cache and

send a Binding Error message to the Mobile Node'

RQ ref  : RQ_001_1414

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1414_02

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and QE4 having established a binding with EUT

}

ensure that

{ when {        EUT receives a packet from QE4

containing a Home_Address_Option

not set to the Home_Address of QE4 }

then {        EUT discards the packet

before EUT and QE4 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1415_01

summary : 'A Correspondent Node drops packets in which the Source Address does

not match the care-of address recorded in the corresponding

Binding Cache Entry'

RQ ref  : RQ_001_1415

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1415_01

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and QE4 having established a binding with EUT

}

ensure that

{ when { EUT receives a packet from QE4

containing a Home_Address_Option

set to the Home_Address of QE4

and containing a Source_Address

not set to the Care_Of_Address of QE4 }

then { EUT discards the packet }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1415_02

summary : 'A Correspondent Node drops packets in which the Source Address does

not match the care-of address recorded in the corresponding

Binding Cache Entry and sends a Binding Error message to the

Mobile Node'

RQ ref  : RQ_001_1415

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1415_02

with {     EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE4 away_from_home

and QE4 registered to QE1

and QE4 having established a binding with EUT

}

ensure that

{ when {        EUT receives a packet from QE4

containing a Home_Address_Option

set to the Home_Address of QE4

and containing a Source_Address

not set to the Care_Of_Address of QE4 }

then {        EUT discards the packet

before QE4 and the EUT are able communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1384_01

summary : 'MN reconfigures its home address according to the prefix information

in a Mobile_Prefix_Advertisement'

RQ ref  : RQ_001_1384

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1384_01

with { EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when { QE1 is requested to modify its home_network prefix }

then { QE4 and the EUT are able to communicate

using the new home_address }

}

End Group -- Group C

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

Group 1.4 'Group D'

Group 1.4.2

TP id   : TP_MOB_1574_01

summary : 'Home Agent supports the protection of Home Test and

Home Test Init messages'

RQ ref  : RQ_001_1574

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1574_01

with {     QE4 configured to perform route_optimization

and QE1 configured to perform route_optimization

and QE1 away_from_home

and QE1 registered to EUT

and QE1 configured to protect return_routability_packets

}

ensure that

{ when { QE1 receives a packet from QE4

indicating that a response is required }

then { QE1 sends the response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1371_01

summary : 'Home Agent supports ESP protection of Home Test and

Home Test Init messages'

RQ ref  : RQ_001_1371

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1371_01

with {     QE4 configured to perform route_optimization

and QE1 configured to perform route_optimization

and QE1 configured to protect return_routability_packets

using ESP

}

ensure that

{ when {        QE1 moves to a Foreign_Network

before QE4 sends a packet to QE1

indicating that a response is required }

then {        QE4 indicates receipt of the response directly from QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1082_01

summary : 'Home Agent uses a Security Association to protect integrity and

authenticity of Mobile_Prefix_Solicitations and Advertisements'

RQ ref  : RQ_001_1082 , RQ_001_1014 , RQ_001_1607

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1082_01

with {     QE1 at_home

and QE1 configured to protect

Mobile_Prefix_Solicitations

and QE1 configured to accept only secured

Mobile_Prefix_Advertisements

and QE1 configured to have a short prefix_lifetime --(suggest 30s)

}

ensure that

{ when {        QE1 moves to a foreign_network

before its prefix_lifetime expires

before QE4 sends a packet to QE1

indicating that a response is required }

then {        QE4 indicates receipt of the response from QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1082_02

summary : 'Mobile Node uses a Security Association to protect integrity and

authenticity of Mobile Prefix Solicitaions and Advertisements'

RQ ref  : RQ_001_1082 , RQ_001_1014 , RQ_001_1663 , RQ_001_1664

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1082_02

with {     EUT at_home

and QE1 configured to accept only secured

Mobile_Prefix_Solicitations

and QE1 configured to protect Mobile_Prefix_Advertisements

and EUT configured to have a short prefix_lifetime (--suggest 30s)'

}

ensure that

{ when {        EUT moves to a foreign_network

before its prefix_lifetime expires

before QE4 sends a packet to the EUT

indicating that response is required }

then {        QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1385_01

summary : 'Mobile Node supports Dynamic Home Agent Address Discovery'

RQ ref  : RQ_001_1385

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1385_01

with {     EUT registered to QE1

and EUT disconnected

and EUT configured not to perform Route_Optimization

and QE4 configured not to perform Route_Optimization

}

ensure that

{ when {            QE1 is requested to modify its IP_address

before the EUT is connected to a foreign_network }

then {            QE4 and the EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1657_01

summary : 'Mobile Node attemps Dynamic Home Agent Address Discovery

if it cannot contact its current Home Agent'

RQ ref  : RQ_001_1657

Role    : Mobile_Node

config  : CF_MOB_06

TD ref  : TD_MOB_1657_01

with {     EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {     QE1 is disconnected from the Home_Network

and EUT moves to another foreign_network }

then {     QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1743_01

summary : 'Mobile Node goes on registering home addresses when

the registration of one of them fails'

RQ ref  : RQ_001_1743

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1743_01

with {     EUT disconnected

and EUT configured to have 2 home_addresses

and QE3 configured to use the first home_address of EUT

}

ensure that

{ when {     EUT is connected to a foreign_network

and EUT receives a packet from QE4

containing a destination_address

set to EUT home_address 2

and indicating that a response is required }

then {     QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1727_01

summary : 'Mobile Node registers its new primary Care-Of Address

after changing it'

RQ ref  : RQ_001_1727

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1727_01

with {     EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {     EUT moves to another foreign_network

and EUT receives a packet from QE4

indicating that a response is required }

then { QE4 indicates receipt of the response from the EUT }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1742_01

summary : 'Mobile Node does not attempt to use its home address

if registration with Home Agent fails due to DAD'

RQ ref  : RQ_001_1742

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1742_01

with { QE3 configured to have the home_address of EUT }

ensure that

{ when { EUT moves to a foreign_network }

-- the registering of EUT has failed

then { EUT does not use its Home_Address to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1740_01

summary : 'Mobile Node attempts to register all of its home addresses'

RQ ref  : RQ_001_1740

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1740_01

with {     EUT disconnected

and EUT configured to have 2 home_addresses

}

ensure that

{ when {     EUT is connected to a foreign_network

and QE4 is requested to send a packet

indicating that a response is required

to the first home_address of EUT

and QE4 is requested to send a packet

indicating that a response is required

to the second home_address of EUT }

then {     QE4 indicates receipt of the first response

and QE4 indicates receipt of the second response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1016_01

summary : 'Home Agent supports transport_mode_ESP protection of

Binding Update messages'

RQ ref  : RQ_001_1016

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1016_01

with {     QE1 disconnected

and QE1 configured to protect any Binding_Update packet

using transport_mode_ESP

}

ensure that

{ when {     QE1 is connected to a foreign_network

and QE1 receives a packet from QE4

indicating that a response is required }

then { QE1 sends response directly to QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1017_01

summary : 'Mobile Node uses transport_mode_ESP to protect Binding Update

messages'

RQ ref  : RQ_001_1017

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1017_01

with { QE1 configured to accept only a Binding_Update

secured using transport_mode_ESP

}

ensure that

{ when {     EUT moves to a foreign_network

and QE4 is requested to send a packet to EUT

indicating that a response is required }

then { QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1655_01

summary : 'Mobile Node already registered to a Home Agent uses that

Home Agent for any new registrations'

RQ ref  : RQ_001_1655

Role    : Mobile_Node

config  : CF_MOB_06

TD ref  : TD_MOB_1655_01

with

{     EUT configured 'to use DHAAD'

and EUT away_from_home

and EUT registered to QE1

and QE2 disconnected from Home_Network 1

}

ensure that

{ when {     QE1 is disconnected from Home_Network 1

and QE2 is connected to Home_Network 1

and EUT moves to another foreign_network }

then {    QE4 and EUT are unable to communicate

within MAX_BINDACK_TIMEOUT

-- EUT tries to register with QE1

and QE4 is able to communicate after MAX_BINDACK_TIMEOUT }

-- EUT registered to QE2

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1366_01

summary : 'Home Agent returns a Binding_Acknowledgement message in response

to a Binding Update message'

RQ ref  : RQ_001_1366

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1366_01

with {     QE1 at_home

}

ensure that

{ when {     QE1 moves to a foreign_network

and QE1 receives a packet from QE4

indicating that a response is required }

then {     QE4 indicates receipt of the response}

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1804_01

summary : 'Home Agent is able to participate in

Dynamic Home Agent Address Discovery'

RQ ref  : RQ_001_1804 , RQ_001_1368

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1804_01

with {     QE1 at_home

and QE1 not configured to have its Home_Agent_address available

}

ensure that

{ when {     QE1 moves to a foreign_network

and QE4 is requested to send a packet to QE1

indicating that a response is required }

then {    QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1733_01

summary : 'Mobile Node sends Binding Update messages to its Home Agent

until it receives a matching Binding_Acknowledgement message,

before MAX_BINDACK_TIMEOUT seconds'

RQ ref  : RQ_001_1733

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1733_01

with {     EUT at_home

and EUT configured to have its Home_Agent_address available

and QE1 disconnected

}

ensure that

{ when {     EUT moves to a foreign_network

and QE1 is connected after 15 seconds

-- ~ MAX_BINDACK_TIMEOUT / 2

}

then {     QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1733_02

summary : 'If the Mobile Node knows just one Home Agent (no DHAAD),

it continues to send Binding Update messages to its

Home Agent after MAX_BINDACK_TIMEOUT seconds'

RQ ref  : RQ_001_1733

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1733_02

with {     EUT at_home

and EUT configured to have its Home_Agent_address available

and QE1 disconnected

}

ensure that

{ when {     EUT moves to a foreign_network

and QE1 is connected after MAX_BINDACK_TIMEOUT

}

then {     QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1734_01

summary : 'When Mobile Node knows several Home Agent (returned during DHAAD),

Mobile Node tries to register with other Home Agents when

registration fails with the first one'

RQ ref  : RQ_001_1734

Role    : Mobile_Node

config  : CF_MOB_06

TD ref  : TD_MOB_1734_01

with {     EUT not configured to have its Home_Agent_address available

and QE1 configured to have a Home_Agent_Preference greater than QE2

}

ensure that

{ when {     QE1 is disconnected

and EUT moves to a foreign_network }

then {     QE4 and EUT are able to communicate

after  MAX_BINDACK_TIMEOUT

}

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1814_01

summary : 'Mobile Node sends Binding Update messages to its Home Agent

until it receives a matching Binding_Acknowledgement message,

without time limit if it knows only one Home Agent'

RQ ref  : RQ_001_1814

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1814_01

with {     EUT at_home

and EUT configured to have its Home_Agent_address available

and QE1 disconnected

}

ensure that

{ when {     EUT moves to a foreign_network

and QE1 is connected after  MAX_BINDACK_TIMEOUT

and QE4 is requested to send a packet to QE1

indicating that a response is required }

then {     QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1013_01

summary : 'Home Agent supports the protection of Binding Update message'

RQ ref  : RQ_001_1013

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1013_01

with

{        QE1 at_home

and QE1 configured to protect any Binding_Update

}

ensure that

{ when {     QE1 moves to a foreign_network

and QE4 is requested to send a packet to QE1

indicating that a response is required }

then { QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1013_02

summary : 'Mobile Node supports the protection of Binding Update message'

RQ ref  : RQ_001_1013

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1013_02

with {     EUT at_home

and QE1 configured to accept only a secured Binding_Update

}

ensure that

{ when {     EUT moves to a foreign_network

and QE4 is requested to send a packet to EUT

indicating that a response is required }

then { QE4 indicates receipt of the response }

}

End Group

End Group

Group 1.5 'Group E'

TP id   : TP_MOB_1376_01

summary : 'Mobile Node is able to perform IPv6 encapsulation' -- miss decapsulation

RQ ref  : RQ_001_1376

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1376_01

with {    EUT away_from_home

and EUT registered to QE1

and EUT configured not to perform Route_Optimization

}

ensure that

{ when { QE4 is requested to send a packet to EUT

indicating that a response is required }

then { QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1536_01

summary : 'HA interceipts packets for registered mobile node on the home

network and uses reverse tunnel encapsulation'

RQ ref  : RQ_001_1536 , RQ_001_1551 , RQ_001_1568 , RQ_001_1364

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1536_01

with {    QE1 away_from_home

and QE1 registered to EUT

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { QE3 is requested to send a packet to QE1

indicating that a response is required }

then { QE3 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1537_01

summary : 'HA multicasts Neighbor Advertisement in Home network in order

to intercept packets for mobile node'

RQ ref  : RQ_001_1537

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1537_01

with {      QE1 at home

and QE1 having established communication to QE3

}

ensure that

{ when {      QE1 moves to a foreign_network

}

then { QE3 updates its Neighbor_Discovery_cache_entry

for the link_local_address of QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1547_01

summary : 'HA act as proxy for a registered mobile node and reply to any

received Neighbor Solicitations for it'

RQ ref  : RQ_001_1547

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1547_01

with {      QE3 'is disconnected'

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {      QE3 is connected to its home_network

and QE3 is requested to send a packet to QE1

indicating that a response is required }

then { QE3 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1557_01

summary : 'HA tunnels multicast packets with a global scope to the mobile node'

RQ ref  : RQ_001_1557 , RQ_001_1372

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1557_01

with {      QE1 subscribed to a global_multicast_group

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { QE3 is requested to send a packet to the global_multicast_group

indicating that a response is required }

then { QE3 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1552_01

summary : 'HA does not tunnel packets to the link_local_address of

mobile node'

RQ ref  : RQ_001_1552

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1552_01

with {     QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { QE3 is requested to send a packet

to the link_local_address of QE1

indicating that a response is required }

then { QE3 indicates no receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1803_01

summary : 'Home Agent discards packets received from

a non registered mobile node'

RQ ref  : RQ_001_1803

Role    : Home_Agent

config  : CF_MOB_05

TD ref  : TD_MOB_1803_01

with

{

EUT disconnected from home_network 1

and QE2 configured to use the same IP_address as EUT

and QE1 away_from_home

and QE1 registered to QE2

and QE1 configured to perform route_optimization

and QE4 configured to perform route_optimization

}

ensure that

{ when {     QE2 is disconnected from home_network

and EUT is connected to home_network

and QE1 is requested to send a packet to QE4

indicating that a response is required }

then {     QE3 indicates no receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1538_01

summary : 'HA multicast Neighbor Advertisement to intercept the packets

to the link_local_address of a registered mobile node'

RQ ref  : RQ_001_1538

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1538_01

with {      QE1 at_home

and QE1 using the same Interface_ID for its link_local_address

and its home_address

and QE3 having established communication

to the link_local_address of QE1

}

ensure that

{ when { QE1 moves to a foreign_network }

then { QE3 updates the Neighbor_Discovery_cache_entry

for the link_local_address of QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1555_01

summary : 'HA does not tunnel multicast packets with a scope smaller than

global to the mobile node '

RQ ref  : RQ_001_1555 , RQ_001_1556

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1555_01

with {     QE1 subscribed to a link_local_multicast_group

and QE1 subscribed to a organization_local_multicast_group

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {     QE3 is requested to send a packet

to the link_local_multicast_group

indicating that a response is required

and QE3 is requested to send a packet

to the organization_local_multicast_group

indicating that a response is required }

then { QE3 indicates no receipt of any response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1560_01

summary : 'if multicast forwarding is not supported, HA ignores muticast

group membership control messages'

RQ ref  : RQ_001_1560

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1560_01

with {      QE1 subscribed to a global_multicast_group

and EUT unable to support multicast_data_packet_forwarding

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { QE3 is requested to send a packet

to the global_multicast_group }

then { QE3 indicates no receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1810_01

summary : 'MN is able to receive tunneled multicast packets from HA'

RQ ref  : RQ_001_1810

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1810_01

with {      EUT subscribed to a global_multicast_group

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when { QE3 is requested to send a packet

to the global_multicast_group }

then { QE3 indicates no receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1817_01

summary : 'Correspondent Node registers the binding when it receives a BU

from Mobile Node'

RQ ref  : RQ_001_1817

Role    : Correspondent_Node

config  : CF_MOB_04

TD ref  : TD_MOB_1817_01

with { QE4 away_from_home

and QE4 registered to QE1

and QE4 configured to perform route_optimization

and EUT configured to perform route_optimization

}

ensure that

{ when { QE4 is requested to send a packet directly to EUT

indicating that a response is required

}

then { QE4 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1818_01

summary : 'A Binding Update contains a Home Address destination option.'

RQ ref  : RQ_001_1818

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1818_01

with

{ QE1 at_home

}

ensure that

{ when {     QE1 moves to a foreign_network

and QE1 sends a Binding_Update

containing no Home_Address_Destination_Option }

then { QE4 and QE1 are unable to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1820_01

summary : 'When Home Agent receives a packet from Mobile Node using reverse

tunneling, it forwards the encapsulated packet to Correspondent Node'

RQ ref  : RQ_001_1820

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1820_01

with {    QE1 away_from_home

and QE1 registered to EUT

and QE1 configured not to perform Route_Optimization

}

ensure that

{ when { EUT is disconnected }

then { QE1 and QE4 are unable to communicate with QE4 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1824_01

summary : 'When Mobile Node detects a L3 handover, it constructs a new

Care-of Address, it select a new default router and register

the new address to its Home Agent and the Correspondent Nodes

which it is performing route optimization'

RQ ref  : RQ_001_1824, RQ_001_1682

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_1824_01

with {    EUT away_from_home

and EUT registered to QE1

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

and EUT having established a binding to QE4

}

ensure that

{ when { EUT moves to another foreign_network }

then { QE4 and EUT are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1825_01

summary : 'When Home Agent processes a Binding Update secured by IPsec,

the contents of Home Address Option is not checked'

RQ ref  : RQ_001_1825

Role    : Home_Agent

config  : CF_MOB_05

TD ref  : TD_MOB_1825_01

with {     QE1 configured not to perform Route_Optimization

and QE1 away_from_home

and QE1 registered to EUT

and EUT configured to accept any secured Binding_Update from QE1

and QE1 configured to send only a secured Binding_Update to EUT

}

ensure that

{ when { QE1 sends a Binding_Update secured by IPsec

containing a Home_Address_Option

not indicating its Home_Address

}

then { EUT accepts the packet }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_1807_01

summary : 'If HA support the multicast group membership control protocols,

HA must be capable to determine which multicast data packets to

forward via the tunnel to MN'

RQ ref  : RQ_001_1807 , RQ_001_1561

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_1807_01

-- Config-HA

with {      QE1 connected to home_network

and QE1 subscribed to a global_multicast_group

and QE3 subscribed to another global_multicast_group

}

ensure that

{ when {     QE1 moves to a foreign_network

and QE1 registers to EUT }

then {     QE1 receives packets from its global_multicast_group }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

End Group -- Group E

End Group -- Group 1

--****************************************************--

--* RFC3776  -  Security for Mobility

--****************************************************--

Group 5

TP id   : TP_MOB_2013_01

summary : 'Mobile Node sends Binding Update secured using transport_mode_ESP

to its Home Agent'

RQ ref  : RQ_001_2013 , RQ_001_2031

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2013_01

with {     EUT configured to protect any Binding_Update to QE1

using transport_mode_ESP

and QE1 configured to accept only Binding_Update secured

using transport_mode_ESP from EUT

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and EUT moves to a foreign_network }

then { QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2013_02

summary : 'Home Agent sends Binding_Acknowledgement secured

using transport_mode_ESP to a Mobile Node'

RQ ref  : RQ_001_2013 , RQ_001_2031

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2013_02

with {     EUT configured to protect any Binding_Acknowledgement to QE1

using transport_mode_ESP

and QE1 configured to accept only a Binding_Acknowledgement secured

using transport_mode_ESP from EUT

}

ensure that

{ when {      a Security_Association is established between EUT and QE1

and QE1 moves to a foreign_network

}

then { QE4 is able to communicate with QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2014_01

summary : 'Home Agent supports Home Test Init secured using tunnel_mode_ESP'

RQ ref  :  RQ_001_2034, RQ_001_2035, RQ_001_1571

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2014_01

with {     QE1 configured to protect any Home_Test_Init to EUT

using tunnel_mode_ESP

and EUT configured to accept only Home_Test_Init secured

using tunnel_mode_ESP from QE1

and QE1 configured to perform route_optimization

and QE4 configured to perform route_optimization

and QE1 is away_from_home

and QE1 registered to EUT

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and QE1 moves to a foreign_network }

then { QE4 and QE1 are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2014_02

summary : 'Mobile Node supports Home Test secured using tunnel_mode_ESP'

RQ ref  : RQ_001_2034 , RQ_001_2035

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2014_02

with {     QE1 configured to protect any Home_Test to EUT

using tunnel_mode_ESP

and EUT configured to accept only a Home_Test secured

using tunnel_mode_ESP from QE1

and EUT configured to perform Route_Optimization

and QE4 configured to perform route_optimization

and EUT is away_from_home

and EUT registered to QE1

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and EUT moves to a foreign_network }

then {     QE4 and EUT are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2015_01

summary : 'Mobile Node sends Home Test Init secured

using tunnel_mode_ESP to its Home Agent'

RQ ref  : RQ_001_2034

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2015_01

with {     EUT configured to protect any Home_Test_Init to QE1

using tunnel_mode_ESP

and QE1 configured to accept only Home_Test_Init secured

using tunnel_mode_ESP from EUT

and EUT configured to perform route_optimization

and QE4 configured to perform route_optimization

}

ensure that

{ when {      a Security_Association is established between EUT and QE1

and EUT moves to a foreign_network }

then { QE4 and EUT are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2015_02

summary : 'Home Agent sends Home Test secured using tunnel_mode_ESP'

RQ ref  : RQ_001_2034

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2015_02

with {     EUT configured to protect any Home_Test to QE1

using tunnel_mode_ESP

and QE1 configured to accept only Home_Test secured

using tunnel_mode_ESP from EUT

and QE1 configured to perform Route_Optimization

and QE4 configured to perform Route_Optimization

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and QE1 moves to a foreign_network }

then { QE4 and QE1 are able to communicate directly }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2016_01

summary : 'Home Agent supports Mobile_Prefix_Solicitation secured

using transport_mode_ESP'

RQ ref  : RQ_001_2016 , RQ_001_2031

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2016_01

with {     QE1 configured to protect any Mobile_Prefix_Solicitation to EUT

using transport_mode_ESP

and EUT configured to accept only a Mobile_Prefix_Solicitation secured

using transport_mode_ESP from QE1

and QE6  configured to have a prefix_lifetime of 1 minute

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { a Security_Association is established between EUT and QE1 }

then { QE4 is able to communicate with QE1 after the prefix_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2016_02

summary : 'Mobile Node supports Mobile_Prefix_Advertisement secured

using transport_mode_ESP'

RQ ref  : RQ_001_2016 , RQ_001_2031

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2016_02

with {     QE1 configured to protect any Mobile_Prefix_Advertisement to EUT

using transport_mode_ESP

and EUT configured to accept only Mobile_Prefix_Advertisement

secured using transport_mode_ESP from QE1

and EUT away_from_home

and EUT registered to QE1

and QE6 configured to have a prefix_lifetime of 1 minute

}

ensure that

{ when { a Security_Association is established between EUT and QE1 }

then { QE4 and EUT are able to communicate after prefix_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2017_01

summary : 'Mobile Node sends Mobile_Prefix_Solicitation secured

using transport_mode_ESP to its Home Agent'

RQ ref  : RQ_001_2017 , RQ_001_2030

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2017_01

with {     EUT configured to protect any Mobile_Prefix_Solicitation to QE1

using transport_mode_ESP

and QE1 configured to accept only a Mobile_Prefix_Solicitation

secured using transport_mode_ESP from EUT

and QE6 configured to have a prefix_lifetime of 1 minute

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when { a Security_Association is established between EUT and QE1 }

then { QE4 and EUT are able to communicate after prefix_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2017_02

summary : 'Home Agent sends Mobile_Prefix_Advertisement secured

using transport_mode_ESP'

RQ ref  : RQ_001_2017 , RQ_001_2030

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2017_02

with {     EUT configured to protect any Mobile_Prefix_Advertisement to QE1

using transport_mode_ESP

and QE1 configured to accept only a Mobile_Prefix_Advertisement

secured using transport_mode_ESP from EUT

and QE1 away_from_home

and QE1 registered to EUT

and QE6 configured to have a prefix_lifetime of 1 minute

}

ensure that

{ when { a Security_Association is established between EUT and QE1 }

then { QE4 is able to communicate with QE1 after prefix_lifetime }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2018_01

summary : 'Mobile Node sends payload_packet tunneled to its Home Agent

secured using tunnel_mode_ESP'

RQ ref  : RQ_001_2018

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2018_01

with {     EUT configured to protect any payload_packet to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a payload_packet secured

using tunnel_mode_ESP from EUT

and EUT configured not to perform Route_Optimization

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {      a Security_Association is established between EUT and QE1

and EUT moves to a foreign_network

}

then { QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2018_02

summary : 'Home Agent sends payload_packet tunneled to Mobile Node secured

using tunnel_mode_ESP'

RQ ref  : RQ_001_2018

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2018_02

with {     EUT configured to protect any payload_packet to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a payload_packet secured

using tunnel_mode_ESP from EUT

and QE1 configured not to perform Route_Optimization

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and QE1 moves to a foreign_network }

then { QE4 and QE1 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2018_03

summary : 'Mobile Node supports payload_packet secured

using tunnel_mode_ESP'

RQ ref  : RQ_001_2018

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2018_03

with {     QE1 configured to protect any payload_packet to EUT

using tunnel_mode_ESP

and EUT configured to accept only a payload_packet secured

using tunnel_mode_ESP from QE1

and EUT configured not to perform Route_Optimization

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and EUT moves to a foreign_network }

then { QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2018_04

summary : 'Home Agent supports payload_packet tunneled from Mobile Node

and secured using tunnel_mode_ESP'

RQ ref  : RQ_001_2018

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2018_04

with {     QE1 configured to protect any payload_packet to EUT

using tunnel_mode_ESP

and EUT configured to accept only a payload_packet secured

using tunnel_mode_ESP from QE1

and QE1 configured not to perform Route_Optimization

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {   a Security_Association is established between EUT and QE1

and QE1 moves to a foreign_network }

then { QE4 is able to communicate with QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2025_01

summary : 'When Mobile Node returns home and uses Internet Key Exchange,

it mades inactive its Security_Policy protecting

tunneled traffic with its Home Agent'

RQ ref  : RQ_001_2025

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2025_01

with {     EUT configured to use IKEv2 to implement its Security_Policy

and EUT configured to protect any payload_packet to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a payload_packet secured

using tunnel_mode_ESP from EUT

and EUT configured not to perform Route_Optimization

and EUT away_from_home

and EUT registered to QE1

and EUT having established communication to QE4

}

ensure that

{ when { EUT returns home }

then { QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2025_02

summary : 'When Mobile Node returns home and uses Internet Key Exchange,

it mades inactive its Security_Policy protecting

tunneled traffic with its Home Agent'

RQ ref  : RQ_001_2025

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2025_02

with {     QE1 configured to use IKEv2 to implement its Security_Policy

and EUT configured to protect any payload_packet to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a payload_packet secured

using tunnel_mode_ESP from EUT by ESP

and QE1 configured not to perform Route_Optimization

and QE1 away_from_home

and QE1 registered to EUT

and QE1 having established communication to QE4

}

ensure that

{ when { QE1 returns home }

then { QE4 is able to communicate with QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2026_01

summary : 'When Mobile Node returns home and is configured with manualy

established Security Associations, it makes inactive security

policies concerning tunneled traffic with Home Agent without

deleting Security Associations'

RQ ref  : RQ_001_2026

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2026_01

with {     EUT configured 'with manually established Security Associations

and Policies'

and EUT configured to protect packets to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a packets secured

using tunnel_mode_ESP

and EUT configured not to perform Route_Optimization

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when {       EUT moves to another foreign_network

after EUT returns home }

then {       QE4 and EUT are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2026_02

summary : 'When Mobile Node returns home and is configured with manualy

established Security Associations, Home Agent makes inactive

security policies concerning tunneled traffic with Mobile Node

without deleting Security Associations'

RQ ref  : RQ_001_2026

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2026_02

with {     EUT configured 'with manually established Security Associations

and Policies'

and EUT configured to protect packets to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a packets secured

using tunnel_mode_ESP

and QE1 configured not to perform Route_Optimization

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when {       QE1 moves to another foreign_network

after QE1 returns home }

then {       QE4 is able to communicate with QE1 }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2019_01

summary : 'Mobile Node supports multicast group membership control packets

tunneled from its Home Agent proctected by ESP with the tunnel mode'

RQ ref  : RQ_001_2019

Role    : Mobile_Node

config  : CF_MOB_03

TD ref  : TD_MOB_2019_01

with {     QE1 configured to protect any

multicast_group_membership_control_packet to EUT

using tunnel_mode_ESP

and EUT configured to accept only a

multicast_group_membership_control_packet from QE1

secured using tunnel_mode_ESP

and EUT configured to subscribed to a global_multicast_group

and EUT away_from_home

and EUT registered to QE1

}

ensure that

{ when { QE3 sends a packet to the global_multicast_group

indicating that a response is required }

then { QE3 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2019_02

summary : 'Home Agent supports multicast group membership control packets

tunneled from Mobile Node proctected by ESP with the tunnel mode'

RQ ref  : RQ_001_2019

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2019_02

with {     QE1 configured to protect any

multicast_group_membership_control_packet to EUT

using tunnel_mode_ESP

and EUT configured to accept only

a multicast_group_membership_control_packet from QE1

secured using tunnel_mode_ESP

and QE1 configured to subscribed to a global_multicast_group

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { EUT sends a packet to the global_multicast_group

indicating that a response is requested }

then { QE3 indicates receipt of the response }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2039_01

summary : 'Home Agent update its security association entries when the

Mobile Node change of foreign network'

RQ ref  : RQ_001_2039

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2039_01

with {     EUT configured to protect any Binding_Acknowledgement to QE1

using tunnel_mode_ESP

and QE1 configured to accept only a Binding_Acknowledgement

secured using tunnel_mode_ESP from EUT

and QE1 away_from_home

and QE1 registered to EUT

}

ensure that

{ when { QE1 moves to another foreign_network }

then { QE4 and QE1 are able to communicate }

}

--xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx--

TP id   : TP_MOB_2040_01

summary : 'Home Agent does not take into account a Binding Update not

secured'

RQ ref  : RQ_001_2040

Role    : Home_Agent

config  : CF_MOB_02

TD ref  : TD_MOB_2040_01

with { and EUT configured to accept only a Binding_Update

secured using tunnel_mode_ESP

and QE1 configured to send any Binding_Update not secured

}

ensure that

{ when { QE1 moves to a foreign_network }

then { QE4 and QE1 are unable to communicate }

}

End Group 5

# History

| Document history |
| --- |
| V0.0.1 | December 2006 | Stable Draft |
| V0.0.2 | March 2007 | Final Draft |