## Slide 1: Current status of WI DES/MTS-202790
TTCN-3 language extensions: Support for security testing

## Slide 2: Current status
Meeting during wk35 with STF460
Issues
  Problematic introduction of new keyword
  Lazy evaluation has wider scope than security testing
  Seed operation related to random function
Proposals
  Introduction of a "modifier" concept in the Core Language (CL)
  Introduction of a "@lazy" modifier in CL instead of "fuzz" in Security Extension
  Introduction of getseed/setseed in CL
  Conclusion

## Slide 3: "modifier" concept (CL)
to avoid extending the list of keywords in the future, modifiers can be introduced to any declaration
to avoid possible name clashes the modifiers will have e.g. the "@" prefix
  e.g. @special function MySpecialFunction () return Random {...}

## Slide 4: "@lazy" modifier (CL)
fuzz function concept in the proposed Security Extension is rather a lazy evaluation of the expression
  concept has a wider range than just security testing
  Introduce to Core Language
"@lazy" could be used for several issues, for templates, functions, functions parameters, etc.
  e.g. template @lazy MyMessage t_message := { field1 := f1(), field2 := t_ field2, field3 := t_ field3 (f3()), ...} function f_MyFunction (in @lazy MyType pl_mypar) { p.send(t_INIT); p.receive (t_MESSAGE) -> value v_mymessage { if (v_mymessage.field2==42) { p.send(t_ACK0(pl_mypar))} // pl_mypar is evaluated here only else { p.send(t_ACK1)} }

## Slide 5: getseed/setseed (CL)
getseed/setseed related to the random function in CL
  Allow access to internal random seed
  Useful for reproducibility of testcases using the „rnd“ function
Move seed functions from Security Extension to CL as predefined functions

## Slide 6: Conclusion
All proposed functionalities of the existing draft for the Security Extension can be added to the Core Language
  WI to be closed/put on hold?
CRs will be created for the proposed features for the current TTCN-3 Evolution STF