Final draft ES 203 119-4 V1.1.2 (2015-01)

Methods for Testing and Specification (MTS);

The Test Description Language (TDL);

Part 4: Structured Test Objective Specification (Extension)

<

ETSI SPECIFICATION

Reference

DES/MTS-203119-4

Keywords

language, MBT, methodology, testing, 
TSS&TP, TTCN-3, UML

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

The present document can be downloaded from:
http://www.etsi.org

The present document may be made available in electronic versions and/or in print. The content of any electronic and/or print versions of the present document shall not be modified without the prior written authorization of ETSI. In case of any existing or perceived difference in contents between such versions and/or in print, the only prevailing document is the print of the Portable Document Format (PDF) version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm except as authorized by written permission of ETSI.

The content of the PDF version shall not be modified without the written authorization of ETSI.

The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2014.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# Contents

Contents	3

Intellectual Property Rights	5

Foreword	5

Introduction	5

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Definitions and abbreviations	7

3.1	Definitions	7

3.2	Abbreviations	7

4	Basic principles	7

4.1	Structured Test Objective Specification	7

4.2	Document Structure	8

4.3	Notational Conventions	8

4.4 	Conformance	8

5	Meta-Model Extensions	9

5.1	Overview	9

5.2	Foundation Abstract Syntax and Classifier Description	9

5.2.1	Entity	9

5.2.2	Event	10

5.2.3	PICS	10

5.3	Test Objective Abstract Syntax and Classifier Description	11

5.3.1	StructuredTestObjective	11

5.3.2	PICSReference	12

5.3.3	InitialConditions	12

5.3.4	ExpectedBehaviour	12

5.3.5	FinalConditions	13

5.4	Events Abstract Syntax and Classifier Description	14

5.4.1	EventSequence	14

5.4.2	EventOccurrence	14

5.4.3	EntityReference	15

5.4.4	EventReference	16

5.5	Data Abstract Syntax and Classifier Description	16

5.5.1	Value	16

5.5.2	LiteralValue	17

5.5.3	Content	17

5.5.4	LiteralValueReference	18

5.5.5	ContentReference	18

5.5.6	DataReference	18

6	Graphical Syntax Extensions	19

6.1	Foundation	19

6.1.1	Entity	19

6.1.2	Event	19

6.1.3	PICS	20

6.1.4	Comment	20

6.2	Test Objective	22

6.2.1	StructuredTestObjective	22

6.3	Events	24

6.3.1	EventSequence	24

6.3.2	EventOccurrence	24

6.3.3	EntityReference	25

6.3.4	EventReference	26

6.4	Data	26

6.4.1	Value	26

6.4.2	LiteralValue	27

6.4.3	Content	27

6.4.4	LiteralValueReference	28

6.4.5	ContentReference	28

6.4.6	DataReference	29

6.4.7	StaticDataUse	29

6.4.8	AnyValue	30

6.4.9	AnyValueOrOmit	30

6.4.10	OmitValue	31

6.4.11	DataInstanceUse	31

6.4.11	ArgumentSpecification	31

6.5	Time	32

6.5.1	TimeLabel	32

6.5.2	TimeConstraint	32

7	Exchange Format Extensions	33

Annex A (informative): Textual Syntax	34

A.1	A 3GPP Test Objective in Textual Syntax	34

A.2	An IMS Test Objective in Textual Syntax	35

Annex B (informative): Textual Syntax BNF Production Rules	36

B.1	Overview and Conventions	36

B.1	Production Rules	36

History	40

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This ETSI Standard (ES) has been produced by the ETSI Technical Committee Methods for Testing and Specification (MTS).

The present document is Part 4 of a multi-part deliverable on the Test Description Language as detailed below:

Part 1: Abstract Syntax and Associated Semantics [1]

Part 2: Graphical Syntax [2]

Part 3: Exchange Format [3]

Part 4: Structured Test Objective Specification

# Introduction

Test purposes play an essential role in test specification processes at ETSI. Currently, TDL treats test purposes, and test objectives in general as informal text without any additional structural constraints. This extension package for TDL refines and formalises test objective specification within TDL by introducing relevant meta-model concepts and a corresponding syntactical notation, both of which are related to TPLan [i.1] and TPLan-like notations already established at ETSI. This enables test purpose specification to enter the modelling world and paves the way for improved tool support and better structured test objectives, as well as additional formal verification and validation facilities down the road by integrating and unifying the means for the specification of test purposes and test descriptions, while relying on the same underlying meta-model and benefiting from other related technologies built around this meta-model.

The present document describes the relevant abstract syntax (meta-model) extensions as well as the corresponding concrete syntactical notation.

# 1	Scope

The present document specifies an extension of the Test Description Language (TDL) enabling the specification of structured test objectives. The extension covers the necessary additional constructs in the abstract syntax, their semantics, as well as the concrete syntactical notation for the added constructs. The intended use of the present document is to serve both as a foundation for TDL tools implementing support for the specification of structured test objectives, as well as a reference for end users applying the standardised syntax for the specification of structured test objectives with TDL.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication, ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	ETSI ES 203 119-1 (V1.2.1.): "Methods for Testing and Specification (MTS); The Test Description Language (TDL); Part 1: Abstract Syntax and Associated Semantics"

[2]	ETSI ES 203 119-2 (V1.1.1.): "Methods for Testing and Specification (MTS); The Test Description Language (TDL); Part 2: Graphical Syntax"

[3]	ETSI ES 203 119-3 (V1.1.1.): "Methods for Testing and Specification (MTS); The Test Description Language (TDL); Part 3: Exchange Format"

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	ETSI ES 202 553 (V1.2.1.): "Methods for Testing and Specification (MTS); TPLan: A notation for expressing Test Purposes "

[i.1]	ETSI TS 136 523-1 (V10.2.0): "LTE; Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Packet Core (EPC); User Equipment (UE) conformance specification; Part 1: Protocol conformance specification (3GPP TS 36.523-1 version 10.2.0 Release 10)".

[i.2]	ETSI TS 186 011-2: "Technical Committee for IMS Network Testing (INT); IMS NNI Interoperability Test Specifications; Part 2: Test descriptions for IMS NNI Interoperability".

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [1] and the following apply:

context: a set of circumstances related to the occurrence of an event

entity: an object that may be involved in the occurrence of an event as part of a specific context

entity type: an alias for additional meta-information that may be used to describe one or more entities

event: an observable phenomenon or state that may occur in a specific context

NOTE:	Related to a term of the same name defined in [i.1].

event occurrence: a description of the occurrence of an event in a specific context

event type: an alias for additional meta-information that may be used to describe one or more events

## 3.2	Abbreviations

For the purposes of the present document, thefollowing abbreviations apply:

EBNF	Extended Backus-Naur Form

IMS	IP Multimedia Subsystem

PICS	Protocol Implementation Conformance Statement

TPLan	Test Purpose Notation

# 4	Basic principles

## 4.1	Structured Test Objective Specification

This document defines an extension for TDL enabling the specification of structured test objectives. Rather than rely on external documents or informal text provided by the default test objective specification facilities of TDL, this extension enables users to describe test objectives in a more structured and formalised manner which can enable subsequent generation of test description skeletons and consistency checking against test descriptions realising a given test objective. In addition, the structured approach to test objective specification also enables syntactical and semantical consistency checking of the test objectives themselves.

The abstract concepts and the concrete syntax are based on TPLan [i.1] to a large extent, as they also reflect concepts and practices already established at ETSI. The fundamental concept in the specification of a structured test objectives is the event occurrence which describes the occurrence of an abstract event in a specific context, comprising one or more involved entities, an event argument, as well as a time label and/or a time constraint.

Events and entities referenced in an event occurrence need to be defined in advance as part of a domain description which can then be reused across all structured test objective specifications in that domain. An entity is an abstract representation of an object involved in an event occurrence that may be realised as a component instance or a gate instance within a test description realising the structured test objective.

An event argument may either refer to a data instance for data already defined with the facilities provided by TDL, or, following a more light weight approach, describe data inline without the need to define all data types and instances in advance. Pre-defined data and inline data can be integrated to a certain degree in that inline data may refer to pre-defined data, but not the other way around.

Event occurrence specifications are organised in the different compartments of a structured test objective, including initial conditions, expected behaviour, and final conditions. Multiple event occurrences are combined by means of an 'and' or 'or' operand indicating how subsequent event occurrences are related to each other (as a sequence or as alternatives, respectively).

Structured test objectives may also include references to PICS which may be used as selection criteria for the concrete realisation of the test objectives. The PICS need to be defined in advance as part of the domain description. Multiple PICS references within the same structured test objective are combined by means of 'and' or 'or' operands.

## 4.2	Document Structure

The present document defines the structured test objective specification extension for TDL comprising:

Meta-model extension describing additional concepts required for the specification of structured test objectives (clause 5).

Concrete syntax extension describing corresponding shapes for the representation of the additional concepts (clause 6).

An informative annex with examples in a textual concrete syntax (annex A)

An informative annex with production rules for the example textual syntax (annex B).

## 4.3	Notational Conventions

The present document inherits the notational conventions defined in [1] and [2].

The abstract syntax specification and the classifier descriptions follow the notational conventions defined in Clause 4.5 of Abstract Syntax and Associated Semantics [1]. The concrete syntax notation specification follows the notational conventions described in Clause 4.5 of the Graphical Syntax [2].

## 4.4 	Conformance

For an implementation claiming to conform to this extension of TDL meta-model, all concepts specified in the present document and in [1], as well as the concrete syntax representation specified in the present document shall be implemented consistently with the requirements given in the present document and the referenced documents. The electronic attachement from Annex A in [1] can serve as a starting point for a TDL meta-model implementation conforming to the present document and the overall abstract syntax of TDL [1].

# 5	Meta-Model Extensions

The following clauses specify extensions to the abstract syntax for TDL that enable the support for structured test objective specification.

## 5.1	Overview

The structured test objective specification is defined within a single package in the TDL meta-model. It relies on several concepts from the 'Foundation', 'Data', and 'Time' packages of the TDL meta-model.

## 5.2	Foundation Abstract Syntax and Classifier Description

Figure 5.1: Structured Test Objective Specification Foundation Concepts

### 5.2.1	Entity

Semantics

An 'Entity' is a 'PackageableElement' that describes a participant in an 'EventOccurrence'. User defined entities, such as IUT, SUT, Tester, etc. may be referenced by means of an 'EntityReference' within an 'EventOccurrence' as the source and/or target of an 'Event' referenced in a corresponding 'EventReference'. Whether an 'Entity' corresponds a 'ComponentInstance' or a 'GateInstance' is not specified in advance. 'Annotation's may be used to provide an indication for the type and role of the 'Entity'.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

### 5.2.2	Event

Semantics

An 'Event' is a 'PackageableElement' that describes a user defined event or activity that may be referenced in an 'EventOccurrence'. The direction of an 'Event' with respect to the 'Entity' or 'Entity's referenced in the 'EventOccurrence' depends on the interpretation of the 'Event', where 'Annotation's may be used to provide additional information as an indication of the intended interpretation.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

### 5.2.3	PICS

Semantics

A 'PICS' is a 'PackageableElement' that may be referenced in 'StructuredTestObjective's to indicate selection criteria for the 'StructuredTestObjective' based on features required for and/or tested with the realisation of the 'StructuredTestObjective'.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

## 5.3	Test Objective Abstract Syntax and Classifier Description

Figure 5.2: Structured Test Objective Concepts

### 5.3.1	StructuredTestObjective

Semantics

A 'StructuredTestObjective' is a refinement of 'TestObjective' that enables the use of additional constructs in order to formalise the description of 'TestObjective's. In addition to the 'description' and 'objectiveURI' properties inherited from 'TestObjective', a 'StructuredTestObjective' includes 'PICSReferences', 'InitialConditions', 'ExpectedBehaviour', and 'FinalConditions'.

Generalizations

TestObjective

Properties

picsReference : PICSReference [*] {ordered}
An ordered set of 'PICSReferences' to 'PICS'.

initialConditions : InitialConditions [0..1]
Initial conditions description for the 'StructuredTestObjective'.

expectedBehaviour : ExpectedBehaviour [0..1]
Expected behaviour description for the 'StructuredTestObjective'.

finalConditions : FinalConditions [0..1]
Final conditions description for the 'StructuredTestObjective'.

Constraints

There are no constraints specified.

### 5.3.2	PICSReference

Semantics

A 'PICSReference' is an 'Element' that enables the referencing of 'PICS' within a 'StructuredTestObjective'. A 'Comment' with body containing an 'and' or 'or' shall be used as a Boolean opearand if there are two or more 'PICSReference's specified within a 'StructuredTestObjective', starting with the second 'PICSReference' to indicate how the referenced 'PICS' shall be interpreted with regard to the other referenced 'PICS' within the same 'StructuredTestObjective'.

Generalizations

Element

Properties

pics : PICS [1] 
The referenced 'PICS'.

Constraints

Combining Multiple 'PICSReference's 
A 'Comment' with body containing an 'and' or 'or' shall be attached to the 'PICSReference' as a Boolean opearand if there are two or more 'PICSReference's and it is not the first 'PICSReference'.

### 5.3.3	InitialConditions

Semantics

'InitialConditions' is an 'Element' containing an 'EventSequence' describing the initial conditions of a 'StructuredTestObjective'.

Generalizations

Element

Properties

conditions : EventSequence [1] 
An 'EventSequence' containing the 'EventOccurrence's describing the initial conditions for the 'StructuredTestObjective'.

Constraints

There are no constraints specified.

### 5.3.4	ExpectedBehaviour

Semantics

'ExpectedBehaviour' is an 'Element' containing an 'EventSequence' describing the expected behaviour specified in a 'StructuredTestObjective'.

Generalizations

Element

Properties

whenClause : EventSequence [0..1] 
An 'EventSequence' containing the 'EventOccurrence's describing the stimuli for the 'ExpectedBehaviour' of the 'StructuredTestObjective'.

thenClause : EventSequence [1] 
An 'EventSequence' containing the 'EventOccurrence's describing the expected reaction for the 'ExpectedBehaviour' of the 'StructuredTestObjective' or the resulting expected state.

Constraints

There are no constraints specified.

### 5.3.5	FinalConditions

Semantics

'FinalConditions' is an 'Element' containing an 'EventSequence' describing the final conditions of a 'StructuredTestObjective'.

Generalizations

Element

Properties

conditions : EventSequence [1] 
An 'EventSequence' containing the 'EventOccurrence's describing the final conditions for the 'StructuredTestObjective'.

Constraints

There are no constraints specified.

## 5.4	Events Abstract Syntax and Classifier Description

Figure 5.3: Events Concepts

### 5.4.1	EventSequence

Semantics

'EventSequence' is an 'Element' containing 'EventOccurrence's.

Generalizations

Element

Properties

events : EventOccurrence [1..*] {ordered} 
A sequence of 'EventOccurrence's.

Constraints

There are no constraints specified.

### 5.4.2	EventOccurrence

Semantics

An 'EventOccurrence' is an 'Element' describing a concrete occurrence of an 'Event', including qualified references to the 'Event', to the 'Entity' related to the occurrence of the 'Event' and to any other 'Entity's involved in the 'EventOccurrence'. It also includes a 'Value' as an argument describing the details of the 'EventOccurrence' such as the data being sent or received, or a state an involved 'Entity' is in. The 'EventOccurrence' also includes an optional 'TimeLabel' and/or a 'TimeConstraint' for the specification of temporal relationships between 'EventOccurrence's. In case there is more than one 'EventOccurrence' within an 'EventSequence', a 'Comment' with body containing an 'and' or 'or' shall be used as an opearand, starting with the second 'EventOccurrence' to indicate how the 'EventOccurrence' shall be related to the previous 'EventOccurrence' within the same 'EventSequence', i.e. whether both 'EventOccurrence's are required or whether only one of the 'EventOccurrence's shall take place. The 'or' operand takes precedence, thus given an 'EventSequence' EO1 and EO2 or EO3, the intended interpretation is that EO1 takes place followed by EO2 or EO3 taking place. While this is opposite to conventional logical operator precedence (i.e. 'and' takes precedence over 'or'), conventional logical operator precedence is not applicable in the context of 'EventOccurrence's as the intended interpretation shall be implementable by means of an 'AlternativeBehaviour' or a 'ConditionalBehaviour' in TDL.

Additional 'Comment's may be added to describe the 'EventOccurrence'.

Generalizations

Element

Properties

entityReference : EntityReference [0..1] 
An 'EntityReference' to the 'Entity' related to the occurrence of the 'Event'.

oppositeEntityReference : EntityReference [0..*] 
'EntityReference's to other 'Entity's involved in the 'EventOccurrence'.

eventReference : EventReference [1] 
An 'EventReference' to the occurring 'Event'.

eventArgument : Value [0..1] 
A 'Value' describing the details of the 'EventOccurrence'.

timeLabel : TimeLabel [0..1] 
A 'TimeLabel' that may be added to the 'EventOccurrence' in order to be able to specify 'TimeConstraint's for subsequent 'EventOccurrence's with relation to the 'EventOccurrence'.

timeConstraint : TimeConstraint [0..1] 
A 'TimeConstraint' that may be added to the 'EventOccurrence' to describe temporal relationships to previous 'EventOccurrence's.

Constraints

Combining Multiple 'EventOccurrence's 
A 'Comment' with body containing an 'and' or 'or' shall be attached to the 'EventOccurrence' as an opearand if there are two or more 'EventOccurrence's and it is not the first 'EventOccurrence'.

'TimeConstraint' expression restriction
Only a 'DataInstanceUse' referring to a 'TimeLabel' may be used in 'TimeConstraint's contained in 'EventOccurrence's.

### 5.4.3	EntityReference

Semantics

An 'EntityReference' is an 'Element' that enables the referencing of 'Entity's within 'EventOccurrence's. 'Comment's may be used to add qualifiers describing peculiarities of the referenced 'Entity' related to the specific 'EventOccurrence'.

Generalizations

Element

Properties

entity : Entity [1] 
The referenced 'Entity'.

Constraints

There are no constraints specified.

### 5.4.4	EventReference

Semantics

An 'EventReference' is an 'Element' that enables the referencing of 'Events' within 'EventOccurrence's. 'Comment's may be used to add qualifiers describing peculiarities of the referenced 'Event' related to the specific 'EventOccurrence'.

Generalizations

Element

Properties

event : Event [1] 
The referenced 'Event'.

Constraints

There are no constraints specified.

## 5.5	Data Abstract Syntax and Classifier Description

Figure 5.4: Data Concepts

### 5.5.1	Value

Semantics

A 'Value' is an abstract 'Element' that is refined into 'DataReference', 'LiteralValue', 'LiteralValueReference' and 'ContentReference'. A 'DataReference' enables the referencing of 'DataInstance's defined in advance, as well as the corresponding 'AnyValue', 'AnyValueOrOmit', and 'OmitValue' specifications for a predefined 'DataType'. The remaining 'Value' refinements enable the inline description of data content and data structures, without the requirement of defining 'DataType's and 'DataInstance's in advance. 'DataInstance's and inline data descriptions may be combined to the extent that inline data descriptions may contain 'DataReference's to 'DataInstance's, but 'DataInstance's relying on declared 'DataType's may not reference inline data descriptions. 'Comment's may be used to add qualifiers describing further details related to the 'Value' with regard to the specific context of its usage. With the exception of 'DataInstance's, all inline descriptions are only visible within the containing 'StructuredTestObjective' and may only be referenced within the same 'StructuredTestObjective', where only 'LiteralValue's and 'Content' used in previous 'EventOccurrence's may be referenced in subsequent 'EventOccurrence's.

Generalizations

Element

Properties

There are no properties specified.

Constraints

There are no constraints specified.

### 5.5.2	LiteralValue

Semantics

A 'LiteralValue' is a 'Value' that represents any literal label used as an argument of an 'EventOccurrence' or as a value of 'Content'. 'Comment's may be used to provide additional information related to the the type and semantics of the 'LiteralValue'. A 'LiteralValue' may contain 'Content's enabling the definition of a substructure of the 'LiteralValue' that describes the details of the 'LiteralValue'.

Generalizations

Value

Properties

content : Content [0..*] {ordered} 
The 'Content's of the 'LiteralValue'.

Constraints

There are no constraints specified.

### 5.5.3	Content

Semantics

A 'Content' is an 'Element' that enables the specification of composite 'LiteralValue's which contain additional 'Value's assigned to the 'Content'. Alternatively, 'Content' may contain nested 'Content' without specifying a 'Value' enabling the specification of relevant sub-structures without full details of the 'Values' assigned to each structural feature.

Generalizations

Element

Properties

content : Content [0..*] {ordered} 
Nested contents of the 'Content'.

value : Value [0..1] 
A 'Value' assigned to the 'Content'.

Constraints

No nested 'Content's if 'Value' is provided 
Either nested 'Content's or 'Value' may be specified within 'Content', but not both.

### 5.5.4	LiteralValueReference

Semantics

A 'LiteralValueReference' is a 'Value' that enables the referencing of 'LiteralValues' from previous 'EventOccurrence's within the containing 'StructuredTestObjective' as an argument of an 'EventOccurrence' or as a value of 'Content'.

Generalizations

Value

Properties

content : LiteralValue [1] 
The referenced 'LiteralValue'.

Constraints

Referenced 'LiteralValue' visibility
Only 'LiteralValue's defined within previous 'EventOccurrence's of the containing 'StructuredTestObjective' may be referenced.

### 5.5.5	ContentReference

Semantics

A 'ContentReference' is a 'Value' that enables the referencing of the 'Content' of 'LiteralValues' from previous 'EventOccurrence's within the containing 'StructuredTestObjective' as an argument of an 'EventOccurrence' or as a value of 'Content'.

Generalizations

Value

Properties

content : Content [1] 
The referenced 'Content'.

Constraints

Referenced 'Content' visibility
Only 'Content' defined within previous 'EventOccurrence's of the containing 'StructuredTestObjective' may be referenced.

### 5.5.6	DataReference

Semantics

A 'DataReference' is a 'Value' that enables the referencing of 'DataInstance's by means of a 'DataInstanceUse', as well as the use of 'AnyValue', 'AnyValueOrOmit', and 'OmitValue' specifications for a predefined 'DataType' as an argument of 'EventOccurrence's or as a value of 'Content'.

Generalizations

Value

Properties

content : StaticDataUse [1] 
Specification of the referenced 'DataInstance'.

Constraints

'DataInstanceUse' restrictions within 'DataReference'
Only simple and structured data instances may be referenced directly or indirectly in 'ParameterBinding's of the 'StaticDataUse' within a 'DataReference'.

No 'reduction' within 'DataReference'
The 'reduction' property of 'StaticDataUse' inherited from 'DataUse' shall not be used within a 'DataReference'.

# 6	Graphical Syntax Extensions

The following clauses specify the graphical syntax extensions for TDL related to the additional concepts specified in Clause 5.

## 6.1	Foundation

### 6.1.1	Entity

Concrete Graphical Notation

Formal Description

context Entity

EntityLabel ::= self.name

Constraints

There are no constraints specified.

Comments

Example

### 6.1.2	Event

Concrete Graphical Notation

Formal Description

context Event

EventLabel ::= self.name

Constraints

There are no constraints specified.

Comments

Example

### 6.1.3	PICS

Concrete Graphical Notation

Formal Description

context PICS

PICSLabel ::= self.name

Constraints

There are no constraints specified.

Comments

Example

### 6.1.4	Comment

Concrete Graphical Notation

Inherited from [2] for 'Comment's not contained in a 'StructuredTestObjective', overridden for 'Comment's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context Comment

Qualifier ::= self.body

AndOrQualifier ::= 	if self.body = 'and'

or self.body = 'or'

then

self.body

endif

ArticleQualifier ::= 	if self.body = 'a'

or self.body = 'an'

or self.body = 'the'

then

self.body

endif

AssignmentQualifier ::= 	if self.body = 'indicating value'

or self.body = 'set to'

then

self.body

endif

CommonWordQualifier ::= 	if self.body = 'after'

or self.body = 'before'

or self.body = 'from'

or self.body = 'of'

or self.body = 'to'

then

self.body

endif

DirectionQualifier ::=		if self.body = 'by'

or self.body = 'for'

or self.body = 'from'

or self.body = 'in'

or self.body = 'into'

or self.body = 'to'

then

self.body

endif

QuantifiedQualifier ::=	if self.body = 'all'

or self.body = 'any'

or self.body = 'few'

or self.body = 'multiple'

or self.body = 'no'

or self.body = 'only'

or self.body = 'several'

or self.body = 'some'

then

self.body

endif

ReferenceQualifier ::=		if self.body = 'associated with'

or self.body = 'carrying'

or self.body = 'contained in'

or self.body = 'corresponding to'

or self.body = 'derived from'

then

self.body

endif

TimeConstraintQualifier ::=	if self.body = 'after'

or self.body = 'before'

or self.body = 'during'

or self.body = 'within'

then

self.body

endif

NoteLabel ::= '(' 'Note' self.name ':' self.body ')'

Constraints

Default comment label
The Qualifier label only applies to 'Comment's that do not match the conditions for any of the other qualifier labels.

Comments

Example

## 6.2	Test Objective

### 6.2.1	StructuredTestObjective

Concrete Graphical Notation

Formal Description

context StructuredTestObjective

TestObjectiveNameLabel ::=	self.name

DescriptionLabel ::= 	self.description

URIofObjectiveLabel ::=	self.objectiveURI->newline()

PICSSelectionLabel ::= foreach p:PICSReference in self.picsReferences p as context in <PICSReferenceLabel> end

PICSReferenceLabel ::=	[p.comment->first() as context in <AndOrQualifier>] p.pics.name

InitialConditionsLabel ::=	'with' '{'

self.initialConditions.conditions as context in <EventSequenceLabel>

'}'

ExpectedBehaviourLabel ::= 'ensure' 'that' '{'

if self.expectedBehaviour.whenClause.oclIsUndefined() then

self.expectedBehaviour.thenClause as context in <EventSequenceLabel>

else

'when' '{'

self.expectedBehaviour.whenClause as context in <EventSequenceLabel>

'}'

'then' '{'

self.expectedBehaviour.thenClause as context in <EventSequenceLabel>

'}'

endif

'}'

FinalConditionsLabel ::= 	'with' '{'

self.finalConditions.conditions as context in <EventSequenceLabel>

'}'

Constraints

Spaces in the 'name' of an 'Element' and the 'body' of a 'Comment' 
A 'name' of an 'Element' or a 'body' of a 'Comment' shall be enclosed in single or double quotes when the corresponding 'Element' or 'Comment' is contained within a 'PICSReference' or an 'EventSequence'.

Comments

The labels for the DescriptionLabel, URIofObjectiveLabel, and PICSSelectionLabel are optional and displayed only if the respective model elements are defined. The corresponding compartments are always displayed.

The compartments containing the InitialConditionsLabel, the ExpectedBehaviourLabel, and the FinalConditionsLabel are optional and displayed only if the respective model elements are defined. The corresponding headings containing the keywords Initial Conditions, Expected Behaviour, and Final Conditions are always displayed.

In the alternate notation shown above, all compartments except the TestObjective compartment are optional and only displayed if the respective model elements are defined.

Example

## 6.3	Events

### 6.3.1	EventSequence

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context EventSequence

EventSequenceLabel ::= 	foreach e:EventOccurrence in self.events newline() e as context in <EventOccurrenceLabel> end

Constraints

There are no constraints specified.

Comments

Example

the IUT entity being in the initial state and

the IUT entity using a "CBF algorithm" and

the IUT entity having received a "Beacon information" from the ItsNodeB or

the IUT entity having received any message from the ItsNodeD

### 6.3.2	EventOccurrence

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context EventOccurrence

EventOccurrenceLabel ::= 	[self.comment->first() as context in <AndOrQualifier>]

if self.timeLabel.oclIsUndefined() then

if not self.timeConstraint.oclIsUndefined() then

self.timeConstraint as context in <TimeConstraintLabel>

endif

else

self.timeLabel as context in <TimeLabelLabel>

if self.timeConstraint.oclIsUndefined() then

':'

else

',' self.timeConstraint as context in <TimeConstraintLabel>

endif

endif

[self.entityReference as context in <EntityReferenceLabel>]

self.eventReference as context in <EventReferenceLabel>

[self.eventArgument as context in <EventArgumentLabel>]

[foreach e:EntityReference in self.oppositeEntityReference separator(',') e as context in <OppositeEntityLabel> end]

[foreach c:Comment in self.comment separator(',') e as context in <NoteLabel> end]

Constraints

There are no constraints specified.

Comments

Example

the IUT entity having received a "Beacon information" from the ItsNodeB

(Note 1: "Beacon information may be incomplete")

at time point t the IUT entity receives a "message"

at time point t2, 3s after t : the IUT entity sends an invitation to the ItsNodeD

1s after t : the IUT entity receives a confirmation from the ItsNodeD

### 6.3.3	EntityReference

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context EntityReference

EntityReferenceLabel ::=  	self.comment->first() as context in <ArticleQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.entity.name

'entity'

OppositeEntityLabel ::=  	self.comment->first() as context in <DirectionQualifier>

self.comment->at(1) as context in <ArticleQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.entity.name

Constraints

There are no constraints specified.

Comments

Example

the IUT entity

from the ItsNodeB

in the location service buffer, for ItsNodeB

### 6.3.4	EventReference

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context EventReference

EventReferenceLabel ::=  	[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.event.name

Constraints

There are no constraints specified.

Comments

Example

being in

having automatically received

sends

## 6.4	Data

### 6.4.1	Value

Concrete Graphical Notation

There is no shape associated with this element as it is abstract.

Formal Description

context Value

EventArgumentLabel ::= 	if self.oclIsTypeOf(DataReference) then self as context in <DataReferenceArgumentLabel>

else if self.oclIsTypeOf(LiteralValue) then self as context in <LiteralValueArgumentLabel>

else if self.oclIsTypeOf(LiteralValueReference) then self as context in <LiteralValueReferenceArgumentLabel>

else if self.oclIsTypeOf(ContentReference) then self as context in <ContentReferenceArgumentLabel>

endif

Constraints

There are no constraints specified.

Comments

Example

### 6.4.2	LiteralValue

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context LiteralValue

LiteralValueArgumentLabel ::=		self.comment->first() as context in <ArticleQualifier>

| self.comment->first() as context in <QuantifiedQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.name

['containing' foreach c:Content in self.content separator(',') c as context in <ContentLabel> end ';']

LiteralValueLabel ::=	self.comment->first() as context in <AssignmentQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.name

['containing' foreach c:Content in self.content separator(',') c as context in <ContentLabel> end ';']

Constraints

There are no constraints specified.

Comments

Example

the "GUC packet"

a GUC packet

several GUC packets

indicating value itsGnProtocolVersion "MIB parameter" ,

set to itsGnDefaultHopLimit MIB parameter

### 6.4.3	Content

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context Content

ContentLabel ::=	[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.name

if self.value.oclIsUndefined() then

['containing' foreach c:Content in self.content separator(',') c as context in <ContentLabel> end ';']

else

self.value as context in <Value>

endif

Constraints

There are no constraints specified.

Comments

Example

a "GUC packet" containing

BasicHeader containing

"version field" indicating value "itsGnProtocolVersion MIB parameter" ,

"RHL field" indicating value "itsGnDefaultHopLimit MIB parameter"

;

;

### 6.4.4	LiteralValueReference

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context LiteralValueReference

LiteralValueReferenceArgumentLabel ::=	'the' 'value' 'of'

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content.name

LiteralValueReferenceLabel ::=	self.comment->first() as context in <ReferenceQualifier>

'the' 'value' 'of'

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content.name

Constraints

There are no constraints specified.

Comments

Example

the value of itsGnDefaultHopLimit MIB parameter

corresponding to the value of itsGnDefaultHopLimit MIB parameter

derived from the value of itsGnDefaultHopLimit MIB parameter

### 6.4.5	ContentReference

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context ContentReference

ContentReferenceArgumentLabel ::=	'the' 'value' 'contained' 'in'

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content.name

ContentReferenceLabel ::=		self.comment ->first() as context in <ReferenceQualifier>

'the' 'value' 'contained' 'in'

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content.name

Constraints

There are no constraints specified.

Comments

Example

the value contained in "RHL field"

corresponding to the value contained in "version field"

derived from the value contained in "BasicHeader"

### 6.4.6	DataReference

Concrete Graphical Notation

There is no shape associated with this element. Instead, it is represented as a label within the context of a 'StructuredTestObjective'.

Formal Description

context DataReference

DataReferenceArgumentLabel ::=	self.comment->first() as context in <ArticleQualifier>

| self.comment->first() as context in <QuantifiedQualifier>

'(predefined)'

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content as context in <StaticDataUseLabel>

DataReferenceLabel ::=	[self.name]

self.comment->first() as context in <ReferenceQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.content as context in <StaticDataUseLabel>

Constraints

There are no constraints specified.

Comments

Example

the (predefined) FullHeader

the (predefined) FullHeader containing

RHLField indicating value itGnDefaultHopLimit

;

### 6.4.7	StaticDataUse

Concrete Graphical Notation

Inherited from [2] for 'StaticDataUse's not contained in a 'StructuredTestObjective', overridden for 'StaticDataUse's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context StaticDataUse

StaticDataUseLabel ::= 	if self.oclIsTypeOf(DataInstanceUSe) then self as context in <DataInstanceUseLabel>

else if self.oclIsTypeOf(AnyValue) then self as context in <AnyValueLabel>

else if self.oclIsTypeOf(AnyValueOrOmitValue) then self as context in <AnyValueOrOmitLabel>

else if self.oclIsTypeOf(OmitValue) then self as context in <OmitValueLabel>

endif

Constraints

There are no constraints specified.

Comments

Example

FullHeader

any Header

any or no Header

no Header

### 6.4.8	AnyValue

Concrete Graphical Notation

Inherited from [2] for 'AnyValue's not contained in a 'StructuredTestObjective', overridden for 'AnyValue's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context AnyValue

AnyValueLabel ::= 'any' self.dataType.name

Constraints

There are no constraints specified.

Comments

Example

any Header

### 6.4.9	AnyValueOrOmit

Concrete Graphical Notation

Inherited from [2] for 'AnyValueOrOmit's not contained in a 'StructuredTestObjective', overridden for 'AnyValueOrOmit's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context AnyValueOrOmit

AnyValueOrOmitLabel ::= 'any' 'or' 'no' self.dataType.name

Constraints

There are no constraints specified.

Comments

Example

any or no Header

### 6.4.10	OmitValue

Concrete Graphical Notation

Inherited from [2] for 'OmitValue's not contained in a 'StructuredTestObjective', overridden for 'OmitValue's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context OmitValue

OmitValueLabel ::= 'no' self.dataType.name

Constraints

There are no constraints specified.

Comments

Example

no Header

### 6.4.11	DataInstanceUse

Concrete Graphical Notation

Inherited from [2] for 'DataInstanceUse's not contained in a 'StructuredTestObjective', overridden for 'DataInstanceUse's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context DataInstanceUse

DataInstanceUseLabel ::=	self.dataInstance.name

['containing'

foreach a:ArgumentSpecification in self.argument separator(', ') c as context in <ArgumentSpecificationLabel> end

';']

Constraints

There are no constraints specified.

Comments

Example

FullHeader

FullHeader containing

RHLField indicating value itGnDefaultHopLimit

;

### 6.4.11	ArgumentSpecification

Concrete Graphical Notation

Inherited from [2] for 'ArgumentSpecification's not contained in a 'StructuredTestObjective', overridden for 'ArgumentSpecification's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context ArgumentSpecification

ArgumentSpecificationLabel ::=		self.member.name

self.comment->first() as context in <AssignmentQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier> end]

self.dataUse as context in <StaticDataUseLabel>

Constraints

There are no constraints specified.

Comments

Example

RHLField indicating value itGnDefaultHopLimit

RHLField indicating value itGnDefaultHopLimit containing

VersionField indicating value baseVersion

;

## 6.5	Time

### 6.5.1	TimeLabel

Concrete Graphical Notation

Inherited from [2] for 'TimeLabel's not contained in a 'StructuredTestObjective', overridden for 'TimeLabel's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context TimeLabel

TimeLabelLabel ::=	'at' 'time' 'point' self.name

Constraints

There are no constraints specified.

Comments

Example

at time point t

### 6.5.2	TimeConstraint

Concrete Graphical Notation

Inherited from [2] for 'TimeConstraint's not contained in a 'StructuredTestObjective', overridden for ' TimeConstraint 's directly or indirectly contained in a 'StructuredTestObjective'.

Formal Description

context TimeConstraint

TimeConstraintLabel ::= 	[foreach c:Comment in self.comment as context in <Qualifier> end]

self.comment as context in <TimeConstraintQualifier>

[foreach c:Comment in self.comment c as context in <Qualifier|CommonWordQualifier|ArticleQualifier> end]

self.timeConstraintExpression.dataInstance.name

Constraints

There are no constraints specified.

Comments

Example

30s after t

within 5s of t

during the 5s after t

# 7	Exchange Format Extensions

The exchange format for the extension is fully governed by the exchange format for TDL as specified in [3]. No additional specification is provided.

Annex A (informative):
Textual Syntax

This annex specifies a textual syntax for the additional concepts and the minimal set of required TDL concepts to facilitate the specification and representation of 'StructuredTestObjective's in pure text. The syntax for the constituents of the 'StructuredTestObjective's, such as 'InitialConditions', 'ExpectedBehaviour', and 'FinalConditions' shall be identical to the corresponding compartment specifications in Clause 6.1. The complete BNF production rules are specified in Annex B.

## A.1	A 3GPP Test Objective in Textual Syntax

This example describes one possible way to translate the test objectives in clause 7.1.3.1 from TS 136 523-1 [i.1] into the proposed textual syntax for the structured test objective specification with TDL, by mapping the concepts from the representation in the source document to the corresponding concepts for the structured test objective specification with TDL described in the present document. The example has been reformulated and interpolated where applicable to fit into the framework of the present document.

Package "3GPP, Clause 7.1.3.1" {

//a possible specification of the test objectives from Clause 7.1.3.1 in [i.2]

//some interpolation has been applied to fit into the overall framework and concrete syntax

//of the present document

Domain{

entities:

- UE

- UE_A

- UE_B

- IMS_B

- "HSS of IMS_A"

- IUT

- buffer

;

events :

- "in"

- sends

- receives

- performs

- send

;

}

Test Purpose {

TP Id TP_7_1_3_1_1

Test objective ""

Reference "3GPP TS 36.321 clause 5.3.1"

PICS Selection

Initial conditions

with {

the UE entity "in" the "E-UTRA RRC_CONNECTED state"

}

Expected behaviour

ensure that {

when {

the UE entity receives a "downlink assignment on the PDCCH for the UE’s C-RNTI" and

the UE entity receives a "data in the associated subframe" and

the UE entity performs a HARQ operation

}

then {

the UE entity sends a "HARQ feedback on the HARQ process"

}

}

}

Test Purpose {

TP Id TP_7_1_3_1_2

Test objective ""

Reference "3GPP TS 36.321 clause 5.3.1"

PICS Selection

Initial conditions

with {

the UE entity "in" the "E-UTRA RRC_CONNECTED state"

}

Expected behaviour

ensure that {

when {

the UE entity receives a "downlink assignment on the PDCCH unknown by the UE" and

the UE entity receives a "data in the associated subframe"

}

then {

the UE entity does not send any "HARQ feedback on the HARQ process"

}

}

}

}

## A.2	An IMS Test Objective in Textual Syntax

This example describes one possible way to translate the test objective clause 4.5.1 from TS 186 011-2 [i.2] into the proposed textual syntax for the structured test objective specification with TDL, by mapping the concepts from the representation in the source document to the corresponding concepts for the structured test objective specification with TDL described in the present document. The example has been reformulated and interpolated where applicable to fit into the framework of the present document.

Package "3GPP_7_1_3_1" {

//a possible specification of the test objectives from Clause 7.1.3.1 in [i.2]

//some interpolation has been applied to fit into the overall framework and concrete syntax

//of the present document

Domain{

entities:

- UE

- UE_A

- UE_B

- IMS_B

- "HSS of IMS_A"

- IUT

- buffer

;

events :

- "in"

- sends

- receives

- performs

- send

;

}

Test Purpose {

TP Id TP_7_1_3_1_1

Test objective ""

Reference "3GPP TS 36.321 clause 5.3.1"

PICS Selection

Initial conditions

with {

the UE entity "in" the "E-UTRA RRC_CONNECTED state"

}

Expected behaviour

ensure that {

when {

the UE entity receives a "downlink assignment on the PDCCH for the UE’s C-RNTI" and

the UE entity receives a "data in the associated subframe" and

the UE entity performs a HARQ operation

}

then {

the UE entity sends a "HARQ feedback on the HARQ process"

}

}

}

Test Purpose {

TP Id TP_7_1_3_1_2

Test objective ""

Reference "3GPP TS 36.321 clause 5.3.1"

PICS Selection

Initial conditions

with {

the UE entity "in" the "E-UTRA RRC_CONNECTED state"

}

Expected behaviour

ensure that {

when {

the UE entity receives a "downlink assignment on the PDCCH unknown by the UE" and

the UE entity receives a "data in the associated subframe"

}

then {

the UE entity does not send any "HARQ feedback on the HARQ process"

}

}

}

}

Annex B (informative):
Textual Syntax BNF Production Rules

This annex describes the grammar for the representation of structured test objectives in pure text. It covers the additional concepts and the minimal set of required TDL concepts to facilitate the specification and representation of 'StructuredTestObjective's.

## B.1	Overview and Conventions

The notations is based on the Extended Backus-Naur Form (EBNF) notation. The EBNF representation may be used either as a concrete syntax reference for Structured Test Objective Specification with TDL for end users or as input to a parser generator tool. Table B.1 defines the syntactic conventions that are to be applied when reading the EBNF rules.

| Table B.1: Syntax definition conventions used |
| --- |
| ::= | is defined to be |
| abc | the non-terminal symbol abc |
| abc xyz | abc followed by xyz |
| abc ¦ xyz | alternative (abc or xyz) |
| [abc] | 0 or 1 instance of abc |
| {abc}+ | 1 or more instances of abc |
| {abc} | 0 or more instances of abc |
| 'a'-'z' | all characters from a to z |
| (...) | denotes a textual grouping |
| 'abc' | the terminal symbol abc |
| ; | production terminator |
| \ | the escape character |

## B.1	Production Rules

| Package | ::= | 'Package' Identifier '{' { ElementImport } [ 'Domain' '{' [ 'pics' ':' { PICS }+ ';' ] [ 'entity' 'types' ':' { EntityType }+ ';' ] [ 'entities' ':' { Entity }+ ';' ] [ 'event' 'types' ':' { EventType }+ ';' ] [ 'events' ':' { Event }+ ';' ] '}' ] [ 'Data' '{' { StructuredDataType } { StructuredDataInstance } '}' ] { StructuredTestObjective } { Group } '}' ; |
| --- | --- | --- |
| ElementImport | ::= | 'import' ( 'all' ¦ ( Identifier ¦ { ',' Identifier } ) ) 'from' Identifier ';' ; |
| Group | ::= | 'Group' Identifier '{' { StructuredTestObjective } { Group } '}' ; |
| PICS | ::= | '-' Identifier [ '(' Qualifier ')' ] ; |
| PICSReference | ::= | [ AndOrQualifier ] Identifier ; |
| EntityType | ::= | '-' Identifier ; |
| Entity | ::= | '-' Identifier [ '(' Annotation { ',' Annotation } ')' ] ; |
| EventType | ::= | '-' Identifier ; |
| Annotation | ::= | Identifier ; |
| Event | ::= | '-' Identifier [ '(' Annotation { ',' Annotation } ')' ] ; |
| StructuredTestObjective | ::= | 'Test Purpose' '{' 'TP Id' Identifier 'Test objective' Identifier 'Reference' [ Identifier { ',' Identifier } ] 'PICS Selection' { PICSReference } InitialConditions ExpectedBehaviour FinalConditions '}' ; |
| InitialConditions | ::= | 'Initial conditions' 'with' '{' EventSequence '}' ; |
| ExpectedBehaviour | ::= | FullExpectedBehaviour ¦ PartialExpectedBehaviour ; |
| FullExpectedBehaviour | ::= | 'Expected behaviour' 'ensure that' '{' 'when' '{' EventSequence '}' 'then' '{' EventSequence '}' '}' ; |
| PartialExpectedBehaviour | ::= | 'Expected behaviour' 'ensure that' '{' EventSequence '}' ; |
| FinalConditions | ::= | 'Final conditions' 'with' '{' EventSequence '}' ; |
| EventSequence | ::= | FirstEventOccurrence { EventOccurrence } ; |
| FirstEventOccurrence | ::= | [ ( TimeLabel ( ( ',' TimeConstraint ) ¦ ':' ) ) ¦ TimeConstraint ] EntityReference EventReference Argument [ OppositeEntityReference { ',' OppositeEntityReference } ] { Note } ; |
| Note | ::= | '(' 'Note' NumberAsIdentifier ':' Identifier ')' ; |
| EventOccurrence | ::= | AndOrQualifier [ ( TimeLabel ( ( ',' TimeConstraint ) ¦ ':' ) ) ¦ TimeConstraint ] EntityReference EventReference Argument [ OppositeEntityReference { ',' OppositeEntityReference } ] { Note } ; |
| TimeLabel | ::= | 'at' 'time' 'point' Identifier ; |
| TimeConstraint | ::= | { Qualifier } TimeConstraintQualifier { Qualifier ¦ CommonWordQualifier ¦ ArticleQualifier } TimeConstraintExpression ':' ; |
| TimeConstraintExpression | ::= | Identifier ; |
| TimeConstraintQualifier | ::= | ( 'before' ¦ 'after' ¦ 'during' ¦ 'within' ) ; |
| EntityReference | ::= | ArticleQualifier { Qualifier } Identifier 'entity' ; |
| OppositeEntityReference | ::= | DirectionQualifier ArticleQualifier { Qualifier } Identifier ; |
| EventReference | ::= | { Qualifier ¦ CommonWordQualifier } Identifier ; |
| Argument | ::= | LiteralValueAsArgument |
|  |  | ¦ DataReferenceAsArgument |
|  |  | ¦ ContentReferenceAsArgument |
|  |  | ¦ LiteralValueReferenceArgument ; |
| Value | ::= | LiteralValue |
|  |  | ¦ DataReference |
|  |  | ¦ ContentReference |
|  |  | ¦ LiteralValueReference ; |
| LiteralValueAsArgument | ::= | ( ArticleQualifier ¦ QuantifiedQualifier ) { Qualifier } ( Identifier ¦ NumberAsIdentifier ) [ 'containing' DataContent { ',' DataContent } ';' ] ; |
| LiteralValue | ::= | AssignmentQualifier { Qualifier } ( Identifier ¦ NumberAsIdentifier ) [ 'containing' DataContent { ',' DataContent } ';' ] ; |
| DataContent | ::= | { Qualifier } ( Identifier ¦ NumberAsIdentifier ) [ ( 'containing' ¦ DataContent ¦ { ',' DataContent } ¦ ';' ) ¦ Value ] ; |
| Identifier | ::= | STRING ¦ ID ; |
| Qualifier | ::= | Identifier ¦ NumberAsIdentifier ; |
| CommonWordQualifier | ::= | 'before' |
|  |  | ¦ 'after' |
|  |  | ¦ 'from' |
|  |  | ¦ 'to' |
|  |  | ¦ 'of' ; |
| ArticleQualifier | ::= | 'a' |
|  |  | ¦ 'an' |
|  |  | ¦ 'the' ; |
| QuantifiedQualifier | ::= | 'all' |
|  |  | ¦ 'any' |
|  |  | ¦ 'few' |
|  |  | ¦ 'multiple' |
|  |  | ¦ 'no' |
|  |  | ¦ 'only' |
|  |  | ¦ 'several' |
|  |  | ¦ 'some' ; |
| AssignmentQualifier | ::= | 'indicating value' ¦ 'set to' ; |
| AndOrQualifier | ::= | 'and' ¦ 'or' ; |
| DirectionQualifier | ::= | 'by' |
|  |  | ¦ 'in' |
|  |  | ¦ 'into' |
|  |  | ¦ 'for' |
|  |  | ¦ 'from' |
|  |  | ¦ 'to' ; |
| ReferenceQualifier | ::= | 'corresponding to' |
|  |  | ¦ 'derived from' |
|  |  | ¦ 'carrying' |
|  |  | ¦ 'contained in' |
|  |  | ¦ 'associated with' ; |
| DataInstanceUse | ::= | ( Identifier ¦ NumberAsIdentifier ) [ 'containing' ArgumentSpecification { ',' ArgumentSpecification } ';' ] ; |
| StaticDataUse | ::= | DataInstanceUse |
|  |  | ¦ AnyValue |
|  |  | ¦ AnyValueOrOmit |
|  |  | ¦ OmitValue ; |
| AnyValue | ::= | 'any' Identifier ; |
| AnyValueOrOmit | ::= | 'any' 'or' 'no' Identifier ; |
| OmitValue | ::= | 'no' Identifier ; |
| ArgumentSpecification | ::= | Identifier AssignmentQualifier { Qualifier } StaticDataUse ; |
| ContentReference | ::= | ReferenceQualifier 'the' 'value' 'contained in' { Qualifier } Identifier ; |
| LiteralValueReference | ::= | ReferenceQualifier 'the' 'value' 'of' { Qualifier } Identifier ; |
| ContentReferenceAsArgument | ::= | 'the' 'value' 'contained in' { Qualifier } Identifier ; |
| LiteralValueReferenceArgument | ::= | 'the' 'value' 'of' { Qualifier } Identifier ; |
| DataReference | ::= | Identifier ReferenceQualifier { Qualifier } StaticDataUse ; |
| DataReferenceAsArgument | ::= | ( ArticleQualifier ¦ QuantifiedQualifier ) '(predefined)' { Qualifier } StaticDataUse ; |
| NumberAsIdentifier | ::= | ['-'] INT [ '.' INT ] ; |
| StructuredDataType | ::= | 'type' Identifier [ 'with' Member { ',' Member } ] ';' ; |
| Member | ::= | Optional Identifier 'of' 'type' Identifier ; |
| Optional | ::= | 'optional' ; |
| StructuredDataInstance | ::= | Identifier ( Identifier ¦ NumberAsIdentifier ) [ 'containing' MemberAssignment { ',' MemberAssignment } ] ';' ; |
| MemberAssignment | ::= | Identifier AssignmentQualifier StaticDataUse ; |
| ID | ::= | ( ['^'] ( 'a'-'z' ¦ 'A'-'Z' ¦ '_' ) { 'a'-'z' ¦ 'A'-'Z' ¦ '_' ¦ '0'-'9' ¦ '/' } ) ; |
| INT | ::= | '0'-'9' ; |
| SQ | ::= | '"' ; |
| DQ | ::= | "'" ; |
| STRING | ::= | ( ( DQ ¦ { ( '\\' ¦ ( 'b' ¦ 't' ¦ 'n' ¦ 'f' ¦ 'r' ¦ 'u' ¦ '"' ¦ "'" ¦ '\\' ) ) ¦ ( '\\' ¦ DQ ) } ¦ DQ ) ¦ ( SQ ¦ { ( '\\' ¦ ( 'b' ¦ 't' ¦ 'n' ¦ 'f' ¦ 'r' ¦ 'u' ¦ '"' ¦ "'" ¦ '\\' ) ) ¦ ( '\\' ¦ SQ ) } ¦ SQ ) ) ; |
| ML_COMMENT | ::= | ( '/*' '*/') ; |
| SL_COMMENT | ::= | ( '//' ( '\\n' ¦ '\\r' ) [ ['\\r'] '\\n' ] ) ; |
| WS | ::= | { ' ' |
|  |  | ¦ '\\t' |
|  |  | ¦ '\\r' |
|  |  | ¦ '\\n' }+ ; |

# History

| Document history |
| --- |
| V 1.1.2 | January 2015 | Revised final draft implementing changes approved during MTS#64 and associated Technical Session |
| V1.1.1 | December 2014 | Final draft submitted for approval |