## Slide 1
Joint MTS-TST Meeting
NFV#26
NFVTST(19)000134r1

## Slide 2: ETSI NFV TST Landscape and Collaboration
NFV Testing
Reports
Conformance
3rd Party

## Slide 3: TST001 – Report on Validation of NFV Environments and Services
Target audience:
  All companies wanting to validate new SW, SW updates
  CI/CD pipeline
Content summary
  Definition of SUTs
  Test methods for pre-deployment validation of SUTs
  Pre-deployment validation of NFV Infrastructure
  Pre-deployment validation of VNFs
  Pre-deployment validation of Network Services

## Slide 4: TST001 Highlights
Impact of virtualization on test methods
  How to isolate the System Under Test (SUT)
  HW vs SW test units
Workload type impacts: control vs data plane testing
VNF and NS validation
  Lifecycle, control & data plane, autoscaling
NFVI validation
Examples!

## Slide 5: SUT Examples

## Slide 6: TST002 – Interop Test Methodology
Target audience
  Anyone concerned about interop of different NFV architecture components
Content summary
  Basic concepts
    Definitions
  Test specifications
    Specifics about how the test specs should look like
  SUT architecture
    Diagrams with SUT/FUT, test inputs, environment, etc
  Interop features
    Series of features covered in the report

## Slide 7: TST007 - Guidelines on Interoperability Testing for VIM/VNFM
Focus on features applicable directly for interoperability with and within MANO
Focus:
  VNF Performance Management
  VNF Fault Management;
  VNF Lifecycle management and Software Image Management.
Based on IFA013 and IFA008 for stimulus and monitoring
This WI is a follow-on to NFV TST WG (TST002).
The WI is applicable for all implementations aligned with ETSI NFV architecture; references to open source implementations are included.

## Slide 8: TST009 – NFVI Network Benchmarks and Measurement Methods
Expands the Requirements and Methods of RFC2544
  New reality of NFVI platforms are different than dedicated “boxes” of the past
Benchmark definition
Test setups
Test tool requirements
Methods of Measurement
Rapporteur: Al Morton (AT&T Labs)

## Slide 9: Benchmarks
Throughput
  Offered Load Frame Size
  Offered Load Step Size
  Min Trial Repetition Interval
  Trial Duration
  Max X% Loss Ratio
  Max # of Trials
Latency
Delay Variation
Loss
Background
Name
Parameters
Scope
Units of Measure
Definition
Units of Measure
Sources of Error
Discussion
Reporting Format
}
For each Benchmark:

## Slide 10: Methods of Measurement: Core Procedures
64 oct
128 oct
.256 oct
512 oct
Method (iterate over multiple frame sizes)
Rep #1
Rep #2
Set (multiple repetitions of the same settings from Method)
Meas Goal
30 Mfps
45 Mfps
37 Mfps
41 Mfps
43 Mfps
44 Mfps
Test (multiple Trials searching for a Measurement Goal)
Trials at different Offered Load levels
1024oct
1280 oct
1518 oct
Meas Goal
Method
Set
Test
Trial

## Slide 11: Mitigating Background Processes that Cause Errors (Loss)
Andrzej Pelc, "Searching games with errors— fifty years of coping with liars ", Theoretical Computer Science 270 (2002) 71–109. Available from https://www.gwern.net/docs/statistics/comparison/2002-pelc.pdf
1 Mfps
2 Mfps
....
11 Mfps
12 Mfps
12 Mfps
0 Mfps
False
False
....
True
True
Resource Exhaust, or Loss
Questioner
Responder / DUT
~
Resource Limit Exceeded
Messages:
TRUE or FALSE
Background Process Errors
Events per
Unit Time
Error converts FALSE -> TRUE
Error retains TRUE -> TRUE (half-lies)
Traffic
Generator
RCVR
Traffic
Receiver
Error-Free
Because of the nature of NFVI platform

## Slide 12: Binary Search with Loss Verification
Goal
  Separate resource exhaustion and loss due to transient processes
  They are dealt with in separate ways
Solution
  If a trial fails because of loss (< z), run the trial again with the same stimulus (Max (r) = 2)
  Keep trials short to avoid transients
  Isolate loss due to transients
    Run long duration tests to characterize effects and frequency
Prototyped with OPNFV
Showed marked success in repeatability

## Slide 13: TST010 – MANO API Conformance Test Suite
For 3 Reference Points:
  Os-Ma-Nfvo - ETSI GS NFV-SOL 005
  Or-Vnfm - ETSI GS NFV-SOL 003
  Ve-Vnfm - ETSI GS NFV-SOL 002
Document + Automatable Test Descriptions
  OpenAPIs developed by the SOL WG
  Using the open source Robot Framework
Rapporteur: Pierre Lynch (Keysight)

## Slide 14: Sample Test Description

## Slide 15: TST011 – Test Domain and Description Language Recommendations
NFV Test Domain with automation ecosystem
Recommendations for a DSL (Domain Specific Language)
Rapporteur: Frank Massoudian (Huawei)

## Slide 16: TST012 - VIM & NFVI Control and Management Performance Evaluation
Focus on the control plane performance of VIM + NFVI
Based on functional requirements in ETSI GS NFV-IFA010
Potential Metrics:
  Virtualization container instantiation
  Scaling
  Migration
Delicate!
  VNFs can impact these metrics
  Care will be taken to define the metrics and methods to be independent of VNF (maybe use standard samples)
Rapporteur: Huang Cheng (Huawei)