NOTE:	The relationship between BTF and RCEF as well as BTF and BGF is considered to be an internal relationship within the same physical node and will not be standardized as part of the current release.

Figure 1: RACS Security Functional Architecture

Exposed reference points: e4; Gq'; Ri'; Re; Ia.

### 6.3.2	e4 reference point (A-RACF - NASS)

This is the reference point between the A-RACF and the Customer Location Function (CLF) of the network attachment subsystem (NASS). The reference point e4 is described in ETSI TS 282 004 [6].

### 6.3.3	Ia Reference Point (SPDF -BGF)

The information elements for the Ia reference point are not described in ES 282 004. Further information is available in the Stage 3 documentation.

### 6.3.4	Gq’ Reference Point (AF - SPDF)

Resource reservation requests over Gq’ shall be expressed using the same information elements as those over the Rq and Ia with the exceptions listed in Table 11.

Table 11: Information Elements with specific meaning in Gq’

| Service Class | Service class requested by the AF. It reflects the service relationship between the AF and SPDF owners. The set of Service Classes that are offered to an AF is an administrative matter. |
| --- | --- |
| Resource Bundle-Id | Not transported over Gq’. |

### 6.3.5	Ri’ Reference Point (SPDF-SPDF inter-domain)

The information exchange over the Ri' reference point is not standardized in the current release.

### 6.3.6	Rd’ Reference Point (SPDF-SPDF intra-domain)

The Rd' reference point is not standardized in the current release.

### 6.3.7	Re Reference Point (A-RACF - RCEF)

The information elements for the Re reference point are not described in the present document. Further information is available in the Stage 3 documentation.

# Text boxes

AF

RACF

-

x

Rr

(Note 1)

(Note 1)

Rr

x

-

RACF

BTF

RACS

Functions

Processing

Transport

e4

Rq

’

Ri

,

’

Rd

’

Gq

Ia

Re

NASS

RCEF

BGF

SPDF

Ia

Gq

’

Rd

’

,

Ri

’

Rq

e4

Transport

Processing

Functions

RACS

BTF

AF

SPDF

BGF

RCEF

NASS

Re