TD <>

Draft ETSI TR 102 763 V<0.0.2> (2008-12)

Technical Report

Electromagnetic compatibility and

Radio spectrum Matters (ERM);

Short Range Devices (SRD);

Technical characteristics of Detect-And-Avoid (DAA)

mitigation techniques for SRD equipment using

Ultra Wideband (UWB) technology

Reference

<Workitem>

Keywords

<keyword>

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2009.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM, TIPHONTM, the TIPHON logo and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

# Contents

Contents	3

Intellectual Property Rights	5

Foreword	5

Introduction	6

1	Scope	7

2	References	7

2.1	Normative references	7

2.2	Informative references	7

3	Definitions, symbols and abbreviations	8

3.1	Definitions	8

3.2	Symbols	8

3.3	Abbreviations	9

4	Recommended Applicability of Test Descriptions	10

5	Test Configurations	12

5.1	Introduction	12

5.2	General Test conditions	13

5.2.1	Test conditions	13

5.2.2	Power sources	13

5.2.2.1	Power sources for stand-alone equipment	13

5.2.2.2	Power sources for plug-in radio devices	13

5.2.3	Normal test conditions	14

5.2.3.1	Normal temperature and humidity	14

5.2.3.2	Normal power source	14

5.2.3.2.1	Mains voltage	14

5.2.3.2.2	Lead-acid battery power sources used on vehicles	14

5.2.3.2.3	Other power sources	14

5.3	Choice of equipment for test suites	14

5.3.1	Choice of model	14

5.3.2	Presentation	15

5.4	Testing of host connected equipment and plug-in radio devices	15

5.4.1	The use of a host or test fixture for testing plug-In radio devices	15

5.5	UWB Test conditions	15

5.5.1	UWB configuration	15

5.5.2	UWB operational Frequencies	15

5.5.3	UWB operational modes during test	16

6	Test Procedure for the radio location systems DAA test	17

6.1 	Introduction	17

6.2 	Start-up test	17

6.2.1	Test without a radiolocation test signal during the Minimum Initial Channel Availability Check Time, Tavail_time	17

6.2.2	Tests with a radiolocation test signal at the beginning of the Minimum Initial Channel Availability Check Time, Tavail_time	18

6.2.3	Tests with radiolocation test signal at the end of the Minimum Initial Channel Availability Check Time, Tavail_time	19

6.3.1	In-operation test procedure with constant radio location test signal level	22

6.3.2	In-operation test procedure with increasing radio location test signal level	23

6.4	Test patterns for the radio location DAA test	24

7	Test Procedure for BWA systems in the band 3.4 GHz to 3.8 GHz	26

7.1 	Introduction	26

7.1.1	In service operating modes of BWA	26

7.2 	Initial start-up test	28

7.2.1	Test without a BWA test signal during the Minimum Initial Channel Availability Check Time, Tavail_time	28

7.2.2	Tests with a BWA test signal at the beginning of the Minimum Initial Channel Availability Check Time, Tavail_time	29

7.2.3	Tests with a BWA test signal at the end of the Minimum Initial Channel Availability Check Time, Tavail_time	30

7.3	In-operation test	31

7.4	Test Patterns for BWA Testing	33

Annex A (normative)	Radio location services in the band 3,1 GHz to 3,4 GHz	34

Annex B (normative)	Broadband wireless access services in the band 3,4 GHz to 3,8 GHz	35

Annex C (normative)	Radio location services in the band 8,5 GHz to 9,0 GHz	36

Annex D (normative)	LDC limits	37

Annex E (normative)	Requirements Catalogue	38

E.1	Definitions	38

E.2	Non Interference Mode requirements	38

E.2.1	General Requirements	38

E.2.3	NIM power levels	39

E.3	Normal operational mode	40

E.4	Detection requirements	41

E.5	Avoidance requirement	42

Annex F (normative)	ICS Proforma for DAA device	45

F.1	Identification of the protocol	45

F.2	ICS proforma tables	45

F.2.1	Avoidance Modes	45

History	45

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Report (TR) has been produced by ETSI ERM TG31a and the related Special Task Force 350 (STF-350) on DAA enabled UWB devices.

# Introduction

This Technical Report (TR) has been produced by ETSI Technical Committee Electromagnetic compatibility and Radio spectrum Matters (ERM). It describes a set of tests to evaluate the response of UWB devices equipped with Detect and Avoid algorithms in the presence of Radar signals in the range 3.1 to 3.4 and 8.5 to 9 GHz and BWA systems in the range 3.4 to 3.8 GHz.

This report identifies the general test criterion and operational states of the UWB device under test as well as the Radar and BWA systems. This test report will be used as input to the Walter project and the output of these tests will be used to guide the preparation of an EN.  This future EN, together with EN302065 will be used to demonstrate compliance with the essential requirements of the R&TTE Directive

# 1	Scope

The present document provides the description of the test setups and test procedures for the compliance of DAA (“Detect and Avoid”) enabled UWB (“Ultra wideband”) devices based on the ECC regulatory framework for DAA enabled UWB devices.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

For a specific reference, subsequent revisions do not apply.

Non-specific reference may be made only to a complete document or a part thereof and only in the following cases:

if it is accepted that it will be possible to use all future changes of the referenced document for the purposes of the referring document;

for informative references.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

For online referenced documents, information sufficient to identify and locate the source shall be provided. Preferably, the primary source of the referenced document should be cited, in order to ensure traceability. Furthermore, the reference should, as far as possible, remain valid for the expected life of the document. The reference shall include the method of access to the referenced document and the full network address, with the same punctuation and use of upper case and lower case letters.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are indispensable for the application of the present document. For dated references, only the edition cited applies. For non-specific references, the latest edition of the referenced document (including any amendments) applies.

## 2.2	Informative references

The following referenced documents are not essential to the use of the present document but they assist the user with regard to a particular subject area. For non-specific references, the latest version of the referenced document (including any amendments) applies.

[i.1]	ECC DEC(06)04: "ECC Decision of 24 March 2006 amended 6 July 2007 at Constanta on the harmonized conditions for devices using Ultra-Wideband (UWB) technology in bands below 10.6 GHz" (2007/131/EC).

[i.2]	Draft amended ECC DEC(06)12: "ECC Decision of [1 December 2006] on supplementary regulatory provisions to ECC/DEC/(06)04 for UWB devices using mitigation techniques".

[i.3]	ECC Report 120 (March 2008): "ECC Report on Technical requirements for UWB DAA (Detect and avoid) devices to ensure the protection of radiolocation in the bands 3.1-3.4 GHz and 8.5-9 GHz and BWA terminals in the band 3.4 - 4.2 GHz.

[i.4]	ECC TG3#18-18R0: "Flexible DAA mechanism based on "isolation criteria" between victim service and UWB devices", ECC TG3 Meeting 18, Mainz, March 2007.

[i.5]	ETSI TS 102 754 V1.2.1: “Electromagnetic compatibility and Radio spectrum Matters (ERM); Short Range Devices (SRD); Technical characteristics of Detect-And-Avoid (DAA) mitigation techniques for SRD equipment using Ultra Wideband (UWB) technology”

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

avoid implementation time: maximum time taken to adjust to a new TX parameter set following signal level measurement and identification, Parameter: Tavoid impl

avoidance level: maximum amplitude to which the UWB transmit power is set for the relevant protection zone

channel availability check interval: maximum time between two consecutive detect operations, Parameter: Tavail

detect and avoid time: time duration between a change of the external RF environmental conditions and adaptation of the corresponding UWB operational parameters

detection probability: probability that the DAA enabled UWB device reacts appropriately to a signal detection threshold crossing within the detect and avoid time

in operation channel availability check time: minimum time the UWB device spends searching for victim signals during normal operation, Parameter: Tin op avail

maximum avoidance power level: UWB transmit power assuring the equivalent protection of the victim service

minimum avoidance bandwidth: portion of the victim service bandwidth requiring protection

default avoidance bandwidth: portion of the victim service bandwidth to be protected if no enhanced service bandwidth identification mechanisms are implemented in the DAA enabled devices

minimum initial channel availability check time: minimum time the UWB device spends searching for victim signals after power on, Parameter: Tavail, Time

Non-Interference mode operation (NIM): operational mode that allows the use of the radio spectrum on a non-interference basis without active mitigation techniques

signal detection threshold: amplitude of the victim signal which defines the transition between adjacent protection zones, Parameter: Dthresh

signal detection threshold set: set of amplitudes of the victim signal which defines the transition between adjacent protection zones

victim signal: signal(s) of the service to be detected and protected by the DAA mitigation technique

## 3.2	Symbols

For the purposes of the present document, the following symbols apply:

T	time

f	frequency

D	detection threshold

I	Isolation in dB

P	Power in dBm

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

BPSK	Binary Phase Shift Keying

BWA	Broadband Wireless Access

DAA	Detect And Avoid

CEPT	European Conference of Postal and Telecommunications Administrations

CON	Conformance test results

CPC	Cognitive Pilot Channels

CW	Continuous Wave

dBm	deciBel relative to 1 mW

ECC	Electronic Communications Committee

e.i.r.p.	equivalent isotropically radiated power

ERM	Electromagnetic compatibility and Radio spectrum Matters

ICS	Implementation conformancestatement

LDC	Low Duty Cycle

LFM	Linear Frequency Modulation

NIM	Non Interference Mode

RF	Radio Frequency

SRD	Short Range Device

TPC	Transmit Power Control

UWB	Ultra WideBand

# 4	Recommended Applicability of Test Descriptions

The test descriptions are derived from the requirement catalogue based on the technical specification ETSI TS 102754. The essential elements of this requirment catalogue have been recorded in Annex E of this document.

The applicability of each individual test description is identified in table 1 and cross referenced to the requirements catalogue. The applicability of test descriptions is formally expressed by the use of Boolean expression that are based on (ICS) parameters included in annex F of the present document. Note:The applicability is just a recommendation based on the purpose for which the test description was written.

The columns in table 1 have the following meaning:

TD Id:	The TD Id column indicates the test description identifier.

RQ Id:	The RQ Id column gives the reqirement catalogue cross reference.

Summary:	The Summary column is the summary field of the test description.

Applicability:	The following notations are used for the applicability column:

M	mandatory - the test case is mandatory

O	optional – the test case is optional

N/A	not applicable - in the given context, the test case is not recommended.

O.i	qualified optional – for mutually exclusive or selectable options from a set. “i” is an integer which identifies an unique group of related optional items.

C.i	conditional - the test is recommended ("R") or not ("N/A") depending on the support of other items. "i" is an integer identifying an unique conditional status expression which is defined immediately following the table. For nested conditional expressions, the syntax "IF ... THEN (IF ... THEN ... ELSE...) ELSE ..." is used to avoid ambiguities.

Comments:	This column contains a verbal description of the condition included in the applicability column.

| TD Id | RQ Id | Summary | Applicability | Comments |
| --- | --- | --- | --- | --- |
| Radio Location System DAA |
| TD_RADAR_001 | RQ_NM_001, 002, 003 | Verify the NIM operation for at least Minimum Initial Channel Availability Check Time in the radio location bands when no radio location system is present | Mandatory |  |
| TD_RADAR_002 | RQ_Detect_008, 009, 010 | Verify the radio location signal detection capability and avoidance for the selected UWB operational frequency when a radio location signal occurs at the beginning of the Minimum Initial Channel Availability Check Time. | Mandatory |  |
| TD_RADAR_003 | RQ_Detect_008, 009, 010 | Verify the radio location detection capability and avoidance for the selected UWB operational frequency when a radio location signal occurs at the end of the Minimum Initial Channel Availability Check Time. | Mandatory |  |
| TD_RADAR_004 | RQ_Detect_008, 009, 010 | Verify the radio location detection and avoidance capability for the selected UWB operational frequency in normal UWB operation using a constant radio location test signal | Mandatory |  |
| TD_RADAR_005 | RQ_Detect_008, 009, 010 | Verify the radio location detection and avoidance capability for the selected UWB operational frequency in normal UWB operation using a increasing radio location test signal | Mandatory |  |

| BWA System DAA |
| --- |
| TD_BWA_006 | RQ_NM_001, 002, 003 | Verify the NIM operation for at least Minimum Initial Channel Availability Check Time in the BWA bands when no BWA system is present | Mandatory |  |
| TD_BWA_007 | RQ_Detect_008, 009, 010 | Verify the BWA signal detection capability and avoidance for the selected UWB operational frequency when a BWA signal occurs at the beginning of the Minimum Initial Channel Availability Check Time. Without the capability of a victim bandwidth identification | Mandatory |  |
| TD_BWA_008 | RQ_Detect_008, 009, 010 | Verify the BWA signal detection capability and avoidance for the selected UWB operational frequency when a BWA signal occurs at the end of the Minimum Initial Channel Availability Check Time. Without the capability of a victim bandwidth identification | Mandatory |  |
| TD_BWA_009 | RQ_Detect_008, 009, 010 | Verify the BWA signal detection and avoidance capability for the selected UWB operational frequency in normal UWB operation using a constant BWA test signal | Mandatory |  |
| TD_BWA_011 | RQ_Detect_008, 009, 010 | Verify the BWA signal detection capability and avoidance for the selected UWB operational frequency when a BWA signal occurs at the beginning of the Minimum Initial Channel Availability Check Time. With the capability of a victim bandwidth identification | C.1 |  |
| TD_BWA_012 | RQ_Detect_008, 009, 010 | Verify the BWA signal detection capability and avoidance for the selected UWB operational frequency when a BWA signal occurs at the end of the Minimum Initial Channel Availability Check Time. With the capability of a victim bandwidth identification | C.2 |  |
| C.1: IF F.1/1 = Y THEN M else N/A. C.2: IF F.1/1 = Y THEN M else N/A. |

Table 1: Applicability of tests

# 5	Test Configurations

## 5.1	Introduction

In this section the two basic test configurations will be presented and described. The test setup can be split into a conducted and a radiated test setup. A general example for the test set-up for the conducted test is given in figure 1 and for the raditated test in figure 2.

Due to the very low levels to be measured the conducted test setup is the preferred setup up. Nevertheless, a radiated setup will be needed in case of devices with integrated antennas, non accessable antenna connectors and devices deploying antenna techniques as an avoidance technique.

Figure 1: Proposed test configuration for a conducted DAA test setup [REF: WALTER]

Figure 2: Proposed test configuration for a radiated DAA test setup [REF: WALTER]

## 5.2	General Test conditions

This section covers the general laboratory requirements for power supply, environmental conditions, as well as the operational requirements for the UWB devices undertest.

### 5.2.1	Test conditions

Testing shall be performed under normal test conditions.

The test conditions and procedures shall be performed as specified in the following clauses.

### 5.2.2	Power sources

#### 5.2.2.1	Power sources for stand-alone equipment

During testing, the power source of the equipment shall be replaced by a test power source capable of producing normal and extreme test voltages as specified in clauses 5.2.3.2. The internal impedance of the test power source shall be low enough for its effect on the test results to be negligible. For the purpose of tests, the voltage of the power source shall be measured at the input terminals of the equipment.

For battery operated equipment the battery shall be removed and the test power source shall be applied as close to the battery terminals as practicable.

During tests the power source voltages shall be maintained within a tolerance of ±1 % relative to the voltage at the beginning of each test. The value of this tolerance is critical to power measurements; using a smaller tolerance will provide better measurement uncertainty values.

#### 5.2.2.2	Power sources for plug-in radio devices

The power source for testing plug-in radio devices shall be provided by a test fixture or host equipment.

Where the host equipment and/or the plug-in radio device is battery powered, the battery may be removed and the test power source applied as close to the battery terminals as practicable.

### 5.2.3	Normal test conditions

#### 5.2.3.1	Normal temperature and humidity

The normal temperature and humidity conditions for tests shall be any convenient combination of temperature and humidity within the following ranges:

temperature:	+15°C to +35°C;

relative humidity:	20 % to 75 %.

When it is impracticable to carry out the tests under these conditions, a note to this effect, stating the ambient temperature and relative humidity during the tests, shall be recorded.

The actual values during the tests shall be recorded.

#### 5.2.3.2	Normal power source

##### 5.2.3.2.1	Mains voltage

The normal test voltage for equipment to be connected to the mains shall be the nominal mains voltage. For the purpose of the present document, the nominal voltage shall be the voltage(s) for which the equipment was designed.

The frequency of the test power source corresponding to the AC mains shall be between 49 Hz and 51 Hz.

##### 5.2.3.2.2	Lead-acid battery power sources used on vehicles

When radio equipment is intended for operation from the usual, alternator fed lead-acid battery power source used on vehicles, then the normal test voltage shall be 1,1 times the nominal voltage of the battery (6 V, 12 V, etc.).

##### 5.2.3.2.3	Other power sources

For operation from other power sources or types of battery (primary or secondary), the nominal test voltage shall be as stated by the equipment manufacturer. This shall be recorded.

## 5.3	Choice of equipment for test suites

### 5.3.1	Choice of model

The tests shall be carried out on one or more production models or equivalent preliminary models, as appropriate. If testing is performed on (a) preliminary model(s), then the corresponding production models shall be identical to the tested models in all respects relevant for the purposes of the present document.

If an equipment has several optional features that are considered to affect directly the RF parameters then tests need only be performed on the equipment configured with the considered worst case combination of features as declared by the manufacturer.

Some radiated RF power measurements are difficult to carry out at the limits described in the present document, and therefore conducted measurements may be used in accordance with the specified test procedures. Equipment used for testing may be provided with a suitable 50 ohm connector for conducted RF power measurements. If a 50 ohm impedance cannot be provided at the test point for conducted testing then the test shall be performed as a radiated test using the radiated test procedure presented in the relevant test procedure in the following clauses.

### 5.3.2	Presentation

Stand-alone equipment shall be tested complete with any ancillary equipment.

Plug-in radio devices may be tested together with a suitable test fixture and/or typical host equipment (see clause 5.5).

## 5.4	Testing of host connected equipment and plug-in radio devices

For combined equipment and for radio parts for which connection to or integration with host equipment is required to offer functionality to the radio, different alternative test approaches are permitted. Where more than one such combination is intended, testing shall not be repeated for combinations of the radio part and various host equipment where the latter are substantially similar.

Where more than one such combination is intended and the combinations are not substantially similar, one combination shall be tested against all requirements of the present document and all other combinations shall be tested separately for radiated spurious emissions only.

### 5.4.1	The use of a host or test fixture for testing plug-In radio devices

Where the radio part is a plug-in radio device which is intended to be used within a variety of combinations, a suitable test configuration consisting of either a test fixture or a typical host equipment shall be used. This shall be representative for the range of combinations in which the device may be used. The test fixture shall allow the radio equipment part to be powered and stimulated as if connected to or inserted into host or combined equipment. Measurements shall be made to all requirements of the present document.

NOTE: For further information on this topic, see ETSI document ETSI TR 102 070-2: “Electromagnetic compatibility and Radio spectrum Matters (ERM); Guide to the application of harmonized standards to multi-radio and combined radio and non-radio equipment; Part 2: Effective use of the radio frequency spectrum” [7].

## 5.5	UWB Test conditions

### 5.5.1	UWB configuration

The preferred test set-up shall be a radiated test set-up. The UWB devices under test will be configured as a master-slave pair or equivalent where at least one of the devices has a DAA capability.  The separation of these devices will be such that a good link between the two devices can be assured at all times. Only the DAA equipped device need be illuminated in the Victim service field.  If this is not possible and where both devices are DAA enabled,  then care should be taken to prevent false triggering.

### 5.5.2	UWB operational Frequencies

The required UWB operational frequencies are defined by the victim services. The width of a UWB frequency band such that, below the lower and above the upper frequency limits, the mean powers emitted are each equal to a percentage of 0,5 % of the total mean power of a given emission.  For the purposes of the present document the measurements are made at the -23 dBc points.

The operational frequency bands required are given in Table 2. The UWB system bandwidth as defined by the –23dBc points shall at least partly include the victim service. Where the frequency span of the UWB device is insufficient to cover the victim service’s bandwidth, the frequency range shall be split into two bands and tests repeated for the higher and lower frequency ranges.

| Victim Service | Bandwidth | Comments |
| --- | --- | --- |
| S-band Radiolocation | 3.1 to 3.4 GHz | NIM power level: -70dBm/MHz mean -36dBm peak in 50MHz |
| BWA | 3.4 to 3.8GHz | NIM power level: -80dBm/MHz mean -40dBm in 50MHz peak |
| X-Band Radio location | 8.5 to 9GHz | NIM power level: -65dBm/MHz mean -25dBm in 50MHz peak |

Table 2: UWB System bandwidth for test

### 5.5.3	UWB operational modes during test

To assure repeatability of the tests it will be necessary to ensure that all UWB devices under test follow a predefined start up and enter a known status following the start up.  The condition at the end of the start up shall be dependent upon the test being undertaken.  The suggested status is given in  Table 3 below:

| Test ID | UWB Status after start-up | Comments |
| --- | --- | --- |
| TD_Radar_001 & BWA_006 | NIM operation: LDC NIM power level | The UWB DAA device should be set into a operational state where it intend to operate in a non NIM operation after the Minimum Initial Channel Availability Check Time |
| TD_Radar_002, 003 and BWA_007, 008 | NIM operation: LDC NIM power level | The UWB DAA device should be set into a operational state where it intend to operate in a non NIM operation after the Minimum Initial Channel Availability Check Time |
| TD_Radar_004, 005 and BWA_009, 010 | Transmitting/Receiving data at Payload levels identified in the relevant test section at max permitted mean power level | Payload shall be 50% For a two zone system, the max mean power level will normally be –41.3dBm/MHz. |

Table 3: UWB device status during test

# 6	Test Procedure for the radio location systems DAA test

## 6.1 	Introduction

In the present clause the test procedure for the radio location DAA test is depicted. The UWB DAA device under test shall be verified under normal operational conditions.

The DAA test is split into two main test conditions:

start-up test with and without radio location test signal and;

in-operation test.

The start-up test verifies the operation of the UWB DAA device during the initial start-up when the DAA UWB device intends to operate directly in a non NIM. Thus the UWB DAA device need to be set in an operational condition in which this is guaranteed. The test verifies that the UWB DAA device respects the defined Minimum Initial Channel availability Check Time.

The in-operation test is intended to verify the dynamic behaviour of the UWB DAA device under test. During this test the UWB DAA device under test shall operate in a normal dynamic operational mode. The manufacturer has to declare this normal operational mode taking into account the zone model.

## 6.2 	Start-up test

The clauses below define the procedure to verify the Minimum Initial Channel Availability Check by ensuring that the UWB DAA device is capable of detecting radar pulses at the beginning and at the end of the Minimum Channel Availability Check Time.

### 6.2.1	Test without a radiolocation test signal during the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify  the UWB DAA device will not start transmitting in a non NIM operation before the end of the Minimum Initial Channel Availability Check Time when no radio location test signal is present. This is illustrated in figure 3

Test description identifier: TD_Radar_001

Requirement Reference: See table 1

Pre-test Condition:

- Two UWB devices at least one supporting DAA

- Both UWB devices switched off

Test Sequence:

a)	The UWB DAA device will be switched off. No signal generator is connected to the test setup or the signal generator is switched off.

b)	The UWB DAA device is powered on at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up) , enters into the operational mode defined in Table 3 and is ready to start the radar detection.

CON-1: The UWB DAA device shall not switch into a mode other than a NIM before the end of T1 + Tavail_time after switch on of the device, where the NIM operation is either the LDC mode or the power level defined in]Annex A for the relevant victim band.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

CON-2: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded.

Figure 3: Example of timing for radio location testing of the Minimum Initial Channel Availability Check Time Tavail_time, UWB DAA devive intent to operate in a non NIM mode.

### 6.2.2	Tests with a radiolocation test signal at the beginning of the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify the radar detection and avoidance capability for the selected UWB operational frequency when a radar burst occurs at the beginning of the Minimum Initial Channel Availability Check Time. This is illustrated in figure 4.

Test description identifier: TD_Radar_002

Requirement Reference: See table 1

Pre-test Condition:

- Two UWB devices at least one supporting DAA

- Both UWB devices switched off

Test Sequence:

a)	The UWB DAA device will be switched off. The signal generator used to generate the test patterns in Table 4 will be connected to an antenna of suitable characteristics to permit the UWB DAA device to be illuminated with a field equal to the threshold detection limit or connected to the corresponding connectors in the case of a conducted measurement setup.

b)	The UWB DAA device is powered on at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up) , enters into the operational mode defined in Table 3 and is ready to start the radar detection. 
CON-1: The Minimum initial Channel Availability Check is expected to commence at T1 and is expected to end no sooner than T1 + Tavail_time unless a radio location signal is detected sooner.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

- A radar burst is generated in the relevant radio location frequency band using the radar test frequency and radar test signal #1 defined in Table 4 at a level of 10 dB above the level defined in annexes [A and C] and at exactly the threshold levels as defined in annexes A and C.  This single-burst radar test signal shall commence within 2 sec after time T1.

CON-2: It shall be recorded if the radio location test signal was detected. This can be done by verifying that the UWB DAA device is switched into a NIM operation in the relevant operational band using the default avoidance bandwidth of the regarded radio location service.

- Repeat b) and c) for each of the relevant radar test signals for the UWB operational frequency range as defined in  Table 4 at a level of 10 dB above the defined threshold level as defined in Annex A and C and at exactly the threshold levels as defined in annexes A and C.

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded.

- Repeat c) and d) for each of the identified radar frequencies.

Figure 4: Example of timing for radio location testing at the beginning of the Minimum Initial Channel Availability Check Time, UWB DAA device intent to operate in a non-NIM mode.

### 6.2.3	Tests with radiolocation test signal at the end of the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify the radar detection capability for the selected UWB operational frequency when a radar burst occurs at the end of the Minimum Initial Channel Availability Check Time. This is illustrated in figure 5.

Test description identifier: TD_Radar_003

Requirement Reference:  See table 1

Pre-test Condition:

- UWB device supporting DAA

- UWB device switched off

Test Sequence:

- The UWB DAA device will be switched off. The signal generator used to generate the test patterns in Table 4  will be connected to an antenna of suitable characteristics to permit the UUT to be illuminated with a field equal to the threshold detection limit or connected to the corresponding connectors in the case of a conducted measurement setup.

- The UWB DAA device is powered up at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up), enters into the operational mode defined in Table 3  and is ready to start the radar detection.
CON-1: The Minimum Initial Channel Availability Check Tavail_time is expected to commence at instant T1 and is expected to end no sooner than T1 + Tavail_time unless a radar is detected sooner.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

- A radar burst is generated in the relevant radio location frequency band using the radar test frequency and radar test signal #1 defined in Table 4  at a level of 10 dB above the level defined in Annexes A and C. This single-burst radar test signal shall commence towards the end of the minimum required Minimum Initial Channel Availability Check Time but not before time T1 +10 sec.

CON-2: It shall be recorded if the radar test signal was detected. This can be done by verifying that the UWB DAA device is switched into a NIM operation in the relevant operational band using the default avoidance bandwidth of the regarded radio location service.

- Repeat b) and c) for each of the relevant radar test signals for the UWB operational frequency range as defined in Table 4 at a level of 10 dB above the defined threshold level as defined in Annex A and C and at exactly the threshold levels as defined in annexes A and C.

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded.

- Repeat c) and d) for each of the identified radar frequencies.

Figure 5: Example of timing for radar testing towards the end of the Minimum initial Channel Availability Check Time

6.3 	In-operation test

The clauses below define the procedure to verify the Detect and Avoid Time, Tavoid by ensuring that the UWB DAA device is capable of detecting radiolocation system pulses during the normal operation of the UWB DAA device using a maximum mean EIRP power of -41.3dBm/MHz which corresponds to a Zone 2 operation in the Radio location bands. This test should represent the relative movement of an UBW DAA device in relation to a potential victim radiolocation device. In figure 6 an example of signal diagram for the in-operation test is depicted for a constant radio location test signal above the detection threshold given in table [Reference]. After the first appearance of the radio location test signal the UWB DAA devices shall switch into a NIM operation not later than Tavoid. In figure 7 a similar diagram is depicted for the case of an increasing radio location test signal level. After the reach of the detection threshold level given in table [Reference] the UWB DAA device shall switch into a NIM operation not later than Tavoid.

Figure 6: Example of timing for radiolocation signal in-operation testing of the Detect and Avoid Time, here with constant Radiolocation test signal level larger than the threshold.

Figure 7: Example of timing for radio location signal in-operation testing of the Detect and Avoid Time, here with increasing Radio location test signal level larger than the threshold.

### 6.3.1	In-operation test procedure with constant radio location test signal level

Summary:

Verify the radio location detection and avoidance capability for the selected UWB operational frequency in normal UWB operation using a constant radio location test signal. In this test the Detect and Avoid time and verifies that the UWB DAA device switches into a NIM operation in the default avoidance bandwidth. This is illustrated in figure 5.

Test description identifier: TD_Radar_004

Requirement Reference:  See table 1

Pre-test Condition:

- Two UWB devices at least one supporting DAA

- Both UWB devices switched on

- UWB device in communication mode with a channel load of 50%

Test Sequence:

  - The UWB DAA device shall be switched on, enter the correct operational frequency band table 2, and in a stable operational mode as defined in table 3. The signal generator used to generate the test patterns in table 4 will be connected to an antenna of suitable characteristics to permit the UUT to be illuminated with a field equal to the threshold detection limit or connected to the corresponding connectors in the case of a conducted measurement setup.

  - The radio location test signal will be switched on at an arbitrary time Tarb after the UWB pair has reached operational stability with a signal level equal to the threshold level given in Annex A and C.

CON-1: The Maximum Detect and Avoid Time Tavoid  is expected to commence at instant Tarb and is expected to end no later than  Tarb + Tavoid unless a radar is detected sooner.

CON-2: It shall be recorded if the radar test signal was detected. This can be done by verifying that the UWB DAA device is switched into a NIM operation in the relevant operational band using the default avoidance bandwidth of the regarded radio location service.

  - Repeat b)  for each of the relevant radar test signals for the UWB operational frequency range as defined in Table 4 at the threshold levels as defined in annexes [A and C].

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded.

  - Repeat b) and c) for each of the radar frequencies.

### 6.3.2	In-operation test procedure with increasing radio location test signal level

Summary:

The procedure below verifies the radio location detection and avoidance capability for the selected UWB operational frequency in normal UWB operation using an increasing radio location test signal level. In this test the Detect and Avoid time and the corresponding avoidance operation will be verified. This is illustrated in figure 6.

Test description identifier: TD_Radar_005

Requirement Reference:  See table 1

Pre-test Condition:

- Two UWB devices at least one supporting DAA

- Both UWB devices switched on

- UWB device in normal communication mode with a channel load of 50%

Test Sequence:

  - The UWB DAA device shall be switched on, enter the correct operational frequency band table 2, and in a stable operational mode as defined in table 3. The signal generator used to generate the test patterns in table 4 will be connected to an antenna of suitable characteristics to permit the UUT to be illuminated with a field equal to the threshold detection limit or connected to the corresponding connectors in the case of a conducted measurement setup.

  - The radio location test signal will be switched on at T0  with the test pattern an accordance with table 4 at a power level 20dB below the threshold identified in Annex A and will be increased progressively to reach the threshold value at T0 +105 seconds Insert by SE

CON-1: The Maximum Detect and Avoid Time Tavoid is expected to commence at instant T0 + 105sec and is expected to end no later than T0  + 105sec + Tavoid unless a radar is detected sooner.

CON-2: It shall be recorded if the radar test signal was detected. This can be done by verifying that the UWB DAA device is switched into a NIM operation in the relevant operational band using the default avoidance bandwidth of the regarded radio location service.

  - Repeat b) for each of the relevant radar test signals for the UWB operational frequency range as defined in  Table 4 at the threshold levels as defined in annexes [A and C].

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded.

  - Repeat b) and c) for each of the radar frequencies.

## 6.4	Test patterns for the radio location DAA test

The general structure of radiolocation bursts is given in Figure 8. The test patterns to be used throughout testing, together with the relevant radar frequencies of operation are given in Table 4.

Table 4: Parameters of radio location test signals

| Radar Test Frequencies (note 11) | Radar test signal | Pulse width W [µs] (see note 5) | Pulse repetition frequency fPRF [pps] | Pulses per burst [PPB] (see note 1) | Burst repetition frequency fBRF [bps] | Detection probability with 50 % channel load |
| --- | --- | --- | --- | --- | --- | --- |
| f1= 3.1GHz f1 < f2 < f3 f3= 3.4 GHz | 1 – Variable | 20, 30, 40 | 400 – 1 400 (see note 6) | 10 – 60 | 0.2 – 0.08 | Pd > 90 % |
| f1= 3.GHz f1 < f2 < f3 f3= 3.4 GHz | 2 – Variable | 10, 20, 40, 60, 100 | 100 – 500 (see note 6) | 2 – 5 | 0.2 – 0.08 | Pd > 90 % |
| f1= 8.55GHz f1 < f2 < f3 f3= 8.95GHz | 3 – Variable | 1, 2, 5, 10, 15 | 5000 – 15 000 | 20 – 560 | 2.0 – 0.22 | Pd > 90 % |

NOTE 1: This represents the number of pulses seen at the UWB DAA device per radar scan: N = [{antenna beamwidth (deg)} × {pulse repetition rate (pps)}] / [{scan rate (deg/s)}]. Chose randomly a number of pulses in the given limits. L = PPB*1/fPRF, Burst length in seconds. NOTE 2: The test signals above only contain a single burst of pulses. See figure D.4. NOTE 3: The number of pulses per burst given in this table simulates real radar systems and takes into account the effects of pulse repetition rate and pulse width on the detection probability for a single burst. NOTE 4: Pd gives the probability of detection per simulated radar burst and represents a minimum level of detection performance under defined conditions - in this case a 50 % traffic load. Therefore Pd does not represent the overall detection probability for any particular radar under real life conditions. In general 2 sequential bursts are needed to achieve a real life detection rate of better that 99 % for any radar that falls within the scope of this table. NOTE 5: The pulse width used in these tests is assumed to be representative of real radar systems with different pulse widths and different modulations. The pulse width is assumed to have an accuracy of ± 10 %. NOTE 6: Chose PRF randomly in the given range. NOTE 7: The burst repetition frequency fBRF is used in the In-Service Monitoring test setup. NOTE 8: The radar test signals 1 and 2 are to be used for the DAA device test in the band 3,1GHz to 3,4GHz NOTE 9: The radar test signals 3 are to be used for the DAA device test in the 8,5 GHz to 9 GHz NOTE 10: Pulses have instantaneous bandwidth of 0.5, 1, 2 or 5 MHz. Modulation types can be CW, LFM, BPSK. NOTE 11: The Radar Test Frequency f2 shall be arbitrarily chosen between the f1 and f3

Figure 8: General structure of the bursts for DAA radio location test transmissions

# 7	Test Procedure for BWA systems in the band 3.4 GHz to 3.8 GHz

## 7.1 	Introduction

The series of tests described in this section emulates the operational conditions of a WiMax base station communicating with a WiMax subscriber collocated with a UWB enabled device.  The possible range of performance evaluation tests might include assessment during preamble, data exchange and call termination between the two devices.  In all cases the tests undertaken would establish that the minimum threshold detection levels, identified in the ECC decision and reproduced in Annex B of ETSI TS 101754 v1.2.1, can be met.

The current BWA systems deployed in Europe are all Time Division Duplex (TDD) however more recent developments have introduced Frequency Division Duplex (FDD) systems where the separation of carriers is approximately 200 MHz.  The presently deployed BWA systems are fixed in nature although mobile systems are available these do not have significant market penetration.  Nonetheless these further developments are anticipated in this document and are tested for through the selective use of common bandwidth sizes and modulation schemes.

In both configurations, fixed or mobile, using either FDD or TDD in general the base station to subscriber link will present the lower power level to the UWB device and the nature of the signal, particularly the payload density, will correspond to the traffic type being carried. In the case of a collocated subscriber waking from idle and entering the start-up negotiation, the levels to be detected will be very much higher and, until data transfer begins, the signals periodic with no payload.

### 7.1.1	In service operating modes of BWA

The deployed BWA systems will support different classes of service representing different payload types and the bandwidth and modulation scheme of the traffic will depend on the distance between the base station and terminal.  At the BWA cell perimeter the bandwidth/modulation will be the smallest/lowest to assure a stable link.  This minimum bandwidth/modulation will be analagous to a terminal seeking a base station at wake up before operational parameters are negotiated however in this case the amplitude of the signal falling on the UUWB device will be larger .  The other extreme of operation will be when the base station and terminal are in close proximity and the bandwidth modulation scheme will be at its maximum.  These conditions can be summarised in the table 5.

| Operating Condition | Terminal / Base Station proximity | B/W – Modulation / coding scheme | Amplitude of Signal falling on the UWB device |
| --- | --- | --- | --- |
| Normal Data Exchange | Close | High / High | High |
| Normal Data Exchange | Remote | Low / Low | Low |
| Start-Up | Undefined | Low / Low | High |

Table 5: Summary of operating conditions

However, at the physical layer where the measurements are to be made the only parameters which can be observed are the payload and power levels.  These two parameters are for the moment assumed to be mutually exclusive.

For each type of payload, different response times will be required of the detect and avoid performance of the UWB device; these are identified in Annex B.  The ability of the UWB device to detect the presence of a BWA signal is likely to be determined not only by the signal strength and bandwidth of the BWA signal but also the activity of the UWB devices. These UWB devices will also carry different traffic types and can reasonably be expected to have different payloads. Although UWB devices will generally have power control implemented to simplify testing it is assumed that all UWB transmissions will be at the maximum permitted mean value.

The UWB payload figure is drawn from the ECC report 120 where 50% was found to be a realistic loading for the UWB link and studies showed the onset of interference betweeen UWB and BWA devices. This 50% payload figure has been retained from these tests. The BWA payload is defined by the service supported.

The range of tests required for verification is thus a combination of BWA, power level bandwidth and modulation, and payload and UWB payload. This range of tests is summmarised in table 6.

| Services | BWA Signal Level at UWB Device | BWA B/W - Mod | BWA Payload | UWB Payload |
| --- | --- | --- | --- | --- |
| VoIP | Web Surfing | Broadcast | -41dBm/MHz | 14MHz/64QAM | As specified for each service in Table 7 | 50% at max mean power level of –41 dBm/MHz |
|  |  |  | -65dBm/MHz | 7MHz/16QAM |  |  |
|  |  |  | -80dBm/MHz | 3.5MHz/QPSK |  |  |

Table 6 : Matrix of tests for each BWA / UWB Payload

This range of tests identified in table 6, shall be used for the in-operation tests of 7.3.

    - UWB devices with and without victim service identification

To enhance spectrum utilisation, manufacturers may chose to implement victim service identification.  Such a scheme allows the use of an extended range of optional avoidance mechanisms which will permit enhanced performance of the UWB device whilst assuring the victim service operation.  The manufacturer will identify at the time of test whether the UWB device is equipped with victim service identification and the associated avoidance mechanisms implemented.  These associated avoidance mechanisms will be evaluated.

    - UWB responses to the detection of a victim signal

For each detection of a victim signal , there is a mandated reponse identified in Annex B. However, alternative responses, are permitted provided they offer an equivalent level of protection. A non-exhaustive selection of these is given in Annex E. Where implemented these shall be identified, and justified by the manufacturer, before testing begins, together with the method to demonstrate the successful execution of the avoidance mechanism.  Where this assessment relies on measurement of parameters other than those at the physical layer, then the manufacturer must provide the necessary tools to access this data at the time of test.

The range of avoidance mechanisms to be evaluated can be determined from Figure 9. These shall be identified in Table F.1 of the manufacturer’s ICS file, the key elements of which are shown in Annex F.

Figure 9: Determination of Conformance tests

## 7.2 Initial start-up test

The clauses below define the procedure to verify that the Minimum Initial Channel Availability Check time is met and that  the UWB DAA device is capable of detecting BWA systems at the beginning and at the end of the Minimum Channel Availability Check Time. Thus the UWB DAA devices need to be set in a typical operational mode where a non NIM operation is required. Following the power up procedure the UWB device will enter the state identified in Table 3. The startup test needs to be performed using all defined thresholds and optionally with a downlink signal deployed.

### 7.2.1	Test without a BWA test signal during the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify that the UWB DAA device will not start transmitting in a non NIM operation before the end of the Minimum Initial Channel Availability Check Time under the condition that no BWA test signal is present.

Test description identifier: TD_BWA_006

Requirement Reference:  See table 1

Pre-test Condition:

- Two UWB devices with at least one supporting DAA

- Both UWB devices switched off

Test Sequence:

a)	The UWB DAA devices will be switched off. No signal generator is connected to the test setup or the signal generator is switched off.

b)	The UWB DAA devices are powered on at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up), has entered the correct operational frequency band shown in table 2 is in a known state, identified in table 3 and is ready to start the BWA detection.

CON-1: The UWB DAA device shall not switch into a mode other than a NIM before the end of T1 + Tavail_time after switch on of the device, where the NIM operation is either the LDC mode or the power level defined in Annex B for the relevant victim band.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

CON-2: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded. An example is shown in Figure 3.

### 7.2.2	Tests with a BWA test signal at the beginning of the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify the BWA detection and avoidance capability for the selected UWB operational frequency when a BWA signal occurs at the beginning of the Minimum Initial Channel Availability Check Time.

The UWB DAA device shall protect the complete default avoidance bandwidth as defined in Annex B; this is a mandatory test for all UWB DAA devices. Where the UWB device is equipped with victim service identification, the associated victim service identification avoidance mechanisms and any other optional avoidance mechanisms identified by the manufacturer drawn from the avoidance RQ shall be specified and conformance established.

Test description identifier: TD_BWA_007

Requirement Reference:  See table 1

Pre-test Condition:

- Two UWB devices with at least one supporting DAA

- Both UWB devices switched off

Test Sequence:

a)	The UWB DAA device will be switched off. The signal generator used to generate the test patterns in table 7 will be connected to an antenna of suitable characteristics to permit the UWB DAA device to be illuminated with a field intensity quantified below or connected to the corresponding connectors in the case of a conducted measurement setup deploying the same threshold limits defined in Annex B.

- The UWB DAA device is powered on at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up), has entered the correct operational frequency band table 2 and in a predefined state table 3 and is ready to start the BWA detection.

CON-1: The Minimum initial Channel Availability Check is expected to commence at T1 and is expected to end no sooner than T1 + Tavail_time unless a BWA signal is detected sooner.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

- A BWA signal is generated in the relevant BWA frequency band using the web surfing test pattern defined in table 7 at a level of 10 dB above each of the threshold levels defined in annexe B. This BWA test signal shall commence within 1 sec after time T1 and repeat for a maximum of 5.1 seconds.

CON-2: It shall be recorded if the BWA test signal was detected. This can be done by verifying that the UWB DAA device is switched into an avoid operation corresponding to the investigated threshold level in the relevant operational band. The following avoid operations shall be verified:

    - default avoidance bandwidth for the BWA service identified and where relevant

    - optional avoidance mechanisms identified by the manufacturer for the BWA service identified

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded for each avoidance mechanism.  An example is shown in Figure 4

- Repeat a) to c) at each of the threshold levels in Annex B.

- Repeat a) to d) for each BWA operating frequency identified

- If the UWB device has optional avoidance mechanisms, repeat a) to e) for each optional avoidance mechanism identified.

- If the UWB devices have Victim Service Identification implemented, re-establish the victim service as an Up-link down-link pair as identified in table 7 and repeat steps a) to f) for each of the associated victim service identification avoidance mechanisms.

### 7.2.3	Tests with a BWA test signal at the end of the Minimum Initial Channel Availability Check Time, Tavail_time

Summary:

Verify the BWA detection and avoidance capability for the selected UWB operational frequency when a BWA signal occurs at the end of the Minimum Initial Channel Availability Check Time.

The UWB DAA device shall protect the complete default avoidance bandwidth as defined in Annex B; this is a mandatory test for all UWB DAA devices. Where the UWB device is equipped with victim service identification, the associated victim service identification avoidance mechanisms and any other optional avoidance mechanisms identified by the manufacturer drawn from the avoidance RQ shall be specified and conformance established.

Test description identifier: TD_BWA_008

Requirement Reference: See table 1

Pre-test Condition:

- Two UWB devices with at least one supporting DAA

- Both UWB devices switched off

Test Sequence:

a)	The UWB DAA device will be switched off. The signal generator used to generate the test patterns in table 7 will be connected to an antenna of suitable characteristics to permit the UWB DAA device to be illuminated with a field intensity quantified below or connected to the corresponding connectors in the case of a conducted measurement setup deploying the same threshold limits defined in Annex B

- The UWB DAA device is powered on at T0. T1 denotes the instant when the UWB DAA device has completed its power-up sequence (Tpower_up), has entered the correct operational frequency band (table 2) and in a predefined state (table 3) and is ready to start the BWA detection

CON-1: The Minimum initial Channel Availability Check is expected to commence at T1 and is expected to end no sooner than T1 + Tavail_time unless a BWA  signal is detected sooner.

NOTE:	Additional verification may be needed to define T1 in case it is not exactly known or indicated by the UWB DAA device.

- A BWA signal is generated in the relevant BWA frequency band using the web surfing test pattern defined in table 7 a level of 10 dB above each of the threshold levels defined in annex B. This BWA test signal shall commence towards the end of the minimum required Minimum Initial Channel Availability Check Time but not before time T1 +3 sec and repeat for a maximum of 2.1 seconds.

CON-2: It shall be recorded if the BWA test signal was detected. This can be done by verifying that the UWB DAA device is switched into an avoid operation corresponding to the investigated threshold level in the relevant operational band. The following avoid operations shall be verified:

    - default avoidance bandwidth for the BWA service identified and where relevant

    - optional avoidance mechanisms identified by the manufacturer for the BWA service identified

CON-3: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded for each avoidance mechanism. An example is shown in figure 5

- Repeat a) to c) at each of the threshold levels in Annex B.

- Repeat a) to d) for each BWA operating frequency identified.

- If the UWB device has optional avoidance mechanisms, repeat a) to e) for each optional avoidance mechanism identified.

- If the UWB devices have Victim Service Identification implemented, re-establish the victim service as an Up-link down-link pair as identified in table 7 and repeat steps a) to f) for each of the associated victim service identification avoidance mechanisms.

## 7.3	In-operation test

This series of tests evaluates the UWB device’s response to the presence of different payload types which the victim service may carry.  The range of services was defined by the ECC and is reproduced in Annex B.  Each service requires a different response time from the UWB device and these are also recorded in Annex B.

The in-operation is different from the start-up tests previously identified only in as much as the UWB pair will be actively exchanging data and the victim signal will also be an established transmission. In this test the Detect and Avoid time will be recorded and the corresponding avoidance operation will be verified.

Summary:

Verify the BWA detection and avoidance capability for the selected UWB operational frequency when a BWA signal occurs during the normal exchange of data between two active UWB devices.

The UWB DAA device shall protect the complete default avoidance bandwidth as defined in Annex B; this is a mandatory test for all UWB DAA devices. Where the UWB device is equipped with victim service identification, the associated victim service identification avoidance mechanisms and any other optional avoidance mechanisms identified by the manufacturer drawn from the avoidance RQ shall be specified and conformance established.

Test description identifier: TD_BWA_009

Requirement Reference: See table 1

Pre-test Condition:

- Two UWB devices with at least one supporting DAA

- Both UWB devices switched on and exchanging data

Test Sequence:

  - The UWB DAA device shall be switched on, enter the correct operational frequency band table 2 and in a stable operational mode and the payload defined in Table 3. The signal generator used to generate the test patterns in table 7 will be connected to an antenna of suitable characteristics to permit the UUT to be illuminated with a field intensity defined below or connected to the corresponding connectors in the case of a conducted measurement setup.

  - The BWA service will be established with the test pattern in accordance with table 7 at a power level 20dB below the lowest threshold identified in Annex B.

  - The amplitude of the BWA test signal will be raised to the first of the thresholds to be tested in not less than 20 seconds, at an arbitrary time Tarb after the UWB pair has reached operational stability.

CON-1: The Maximum Detect and Avoid Time Tavoid  is expected to commence at instant Tarb  and detection shall occur no later than Tarb + Tavoid. It shall be recorded when the BWA test signal was detected, and the avoidance operation executed. The following avoid operations shall be verified:

    - default avoidance bandwidth for the BWA service identified and where relevant

    - optional avoidance mechanisms identified by the manufacturer for the BWA service identified

CON-2: A timing trace or description of the observed timing and behaviour of the UWB DAA device shall be recorded for each test case. An example is shown in Figure 7

  - Repeat c) for each threshold in Annex B

  - Repeat b) and c) for each service identified in table 7

  - Repeat c) to e) for each BWA operating frequency identified

  - If the UWB device has optional avoidance mechanisms, repeat c) to f) for each optional avoidance mechanism identified.

  - If the UWB devices have Victim Service Identification implemented, re-establish the victim service as an Up-link down-link pair as identified in table 7 and repeat steps c) to f) for each of the associated victim service identification avoidance mechanisms.

## 7.4	Test Patterns for BWA Testing

The test patterns to be used throughout testing for the services identified in Annex B, will display the periodicity of signals given in figure 10. The details of each burst for each service is given are given in table 7.

Table 7: Test patterns for BWA testing

|  |  | Test Pattern |
| --- | --- | --- |
| Service/Operational Status | Operational Frequencies See Note 1 | BW 14MHz / 64 QAM (5/6) | BW 7MHz / 16 QAM (3/4) | BW 3.5MHz / QPSK (3/4) |
| VoIP | 3.41, 3.5, 3.459, 3.61, 3.7, 3.79GHz | 8 OFDM symbols frame each at intervals identified in Figure 10 |
| Web Surfing |  |  |
| Broadcast |  |  |

Note 1: Where Up-link down-link pairs are required these shall be centred symmetrically around the frequencies 3.5 and 3.7GHz. The down link level shall be at each of the threshold levels.

Figure 10: Periodicity of BWA test signals

# Annex A (normative)	Radio location services in the band 3,1 GHz to 3,4 GHz

Table A.1: Band 3,1 GHz to 3,4 GHz: Radio Location systems Detect and avoid parameter set

| Parameter |  | Zone 1 | Zone 2 |
| --- | --- | --- | --- |
| Minimum Initial channel availability Check time | Tavail | 14 s |
| Detect and Avoid time |  | 150 s |
| Detection probability |  | 99% |
| Detection probability in Continuous detection operation during UWB device operation |  | 97 % |
| Signal detection threshold (Peak Detector) | Dthresh | Dthresh_1 = -38 dBm |  |
| Avoidance Level (UWB maximum mean Tx Power density) |  | -70 dBm/MHz | -41,3 dBm/MHz |
| Default Avoidance Bandwidth |  | 3,1GHz to 3,4GHz (300 MHz) |
| Possible Avoidance Options |  | All |

Additional requirement for operation in the band 3.1 – 4.8 GHz

UWB DAA devices shall be capable of selecting an operating channel anywhere within the band 3.1 – 4.8 GHz.

# Annex B (normative)	Broadband wireless access services in the band 3,4 GHz to 3,8 GHz

Table B.1: BWA Detect and avoid parameter set

| Parameter |  | Zone 1 | Zone 2 | Zone 3 |
| --- | --- | --- | --- | --- |
| Minimum Initial channel availability Check time | Tavail, Time | 5,1 s |
| Detection Probability for initial detect operation after UWB device power on |  | 99 % |
| Signal detection threshold (UL) | Dthresh(UL) | Dthresh_1 = -38 dBm | Dthresh_2 = -61 dBm |  |
| Avoidance Level (UWB Maximum mean Tx Power density) |  | -80 dBm/MHz in the frequency range from 3,4 GHz to 3,8 GHz and | -65 dBm/MHz | -41,3 dBm/MHz |
| Default Avoidance Bandwidth |  | 3,4GHz to 3,6GHz, 3,6GHz to 3,8GHz |
| Possible Avoidance Options |  | All |

Note 1: Detection mechanism needs to be validated to protect existing operation of victim stations of radio services such as BWA terminals in the band 3,4 GHz to 3,8 GHz

Table B.2: BWA Detect and avoid timings

| BWA system / mode | Detect and Avoid Time | Detection Probability (for continuous detect operation) |
| --- | --- | --- |
| VoIP | 2 s | 95 % |
| Web surfing | 15 s | 95 % |
| Sleep mode | 60 s | 95 % |
| Multimedia broadcasting | 15 s | 95 % |

Taking into account moving devices, the detect and avoid parameters in the table above shall provide an equivalent protection of the potential victim device. These test modes must be verified in the corresponding test setup for the harmonized ETSI standard.

Additional requirement for operation in the band 3.1 – 4.8 GHz

UWB DAA devices shall be capable of selecting an operating channel anywhere within the band 3.1 – 4.8 GHz.

# Annex C (normative)	Radio location services in the band 8,5 GHz to 9,0 GHz

Table C.1: Band 8,5 GHz to 9,0 GHz: Radio Location systems Detect and avoid parameter set

| Parameter |  | Zone 1 | Zone 2 |
| --- | --- | --- | --- |
| Minimum Initial channel availability Check time | Tavail | 14 s |
| Detect and Avoid time |  | 150 s |
| Detection probability g |  | 99% |
| Detection probability in Continuous detection operation during UWB device operation |  | 97 % |
| Signal detection threshold (Peak Detector) | Dthresh | Dthresh_1 = -61 dBm |  |
| Avoidance Level (UWB maximum mean Tx Power density) |  | -65 dBm/MHz | -41,3 dBm/MHz |
| Default Avoidance Bandwidth |  | 8,5GHz to 9,0GHz (500 MHz) |
| Possible Avoidance Options |  | All |

# Annex D (normative)	LDC limits

UWB devices having LDC and DAA implemented and operating in all or part of the frequency band from 3,1 GHz to 4,8 GHz may switch on the LDC parameter set to avoid interference to BWA services and radio navigation services as shown in table D.1.

Table D.1. LDC Limits

| LDC parameter | Value |
| --- | --- |
| Maximum Tx on | ≤ 5 ms |
| Minimum Mean Tx off | ≥ 38 ms (mean value averaged over one (1) second) |
| Accumulated minimum Tx off (Σ Tx off) | ≥ 950 ms in one (1) second |
| Maximum accumulated transmission time (Σ Tx on) | 18 s in one (1) hour |

# Annex E (normative)	Requirements Catalogue

## E.1	Definitions

The following terms and definitions apply:

conditionally mandatory: requirement that shall be supported by a standard conformant equipment if and only if the condition(s) stated within its requirement text are met

NOTE:	If one of these conditions is not met the requirement is considered to be not applicable.

EXAMPLE: 	Such a condition may be the support of an optional higher level requirement by the equipment.

conditionally optional: requirement that may be supported by a standard conformant equipment if and only if the condition(s) stated within its requirement text are met

NOTE:	If one of these conditions is not met the requirement is considered to be not applicable.

mandatory: requirement that shall be supported by a standard conformant equipment

optional: requirement that may be supported by a standard conformant equipment

not applicable: requirement that does not have to be met by a standard conformant equipment

## E.2	Non Interference Mode requirements

### E.2.1	General Requirements

RQ_NIM_001	General NIM

TS 102 754 V1.2.1	Clause: 4.3	Type: Mandatory

Applies to: 	All DAA enabled devices

Requirement: 	All UWB devices shall switch into a non interference mode at start-up

Specification Text: 	All UWB devices enter a non interference mode at start-up

RQ_NIM_002	General NIM

TS 102 754 V1.2.1	Clause: 4.3	Type: Mandatory

Applies to: 	All DAA enabled devices

Requirement: 	Remain in the non interference mode until a signal detect is undertaken.

Specification Text: 	This non-interference mode can only be changed after a signal detect, estimation and decision process has been performed.

RQ_NIM_003	General NIM

TS 102 754 V1.2.1	Clause: 4.3	Type: Mandatory

Applies to: 	All DAA enabled devices

Requirement: 	The switch into a higher avoidance zone shall only be allowed after a detection process.

Specification Text: 	This non-interference mode can only be changed after a signal detect, estimation and decision process has been performed. Estimations are done against threshold levels Dthresh_n , n = 1…N-1.

### E.2.3	NIM power levels

RQ_POWER_004	NIM power levels

TS 102 754 V1.2.1	Clause: 4.2	Type: Mandatory

Applies to: 	All DAA and all LDC enabled devices.

Requirement: 	All DAA enabled UWB devices shall be cabable of operting in one of the defined “Non Interference Modes” given by a power level and an activity pattern. The activity patterns might be a normal pattern or the LDC pattern.

Specification Text: 	See Table below

| Operational Frequency | NIM Power levels (e.i.r.p.) for normal pattern | NIM Power levels (e.i.r.p.) with LDC implemented |
| --- | --- | --- |
| 3,1 GHz to 3,4 GHz | - 70 dBm/MHz average. -36 dBm peak | - 41,3 dBm/MHz average. 0 dBm peak |
| 3,4 GHz to 3,8 GHz | - 80 dBm/MHz average. - 40 dBm peak | - 41,3 dBm/MHz average. 0 dBm peak |
| 3,8 GHz to 4,8 GHz | - 70 dBm/MHz average. -30 dBm peak | - 41,3 dBm/MHz average. 0 dBm peak |
| 6,0 GHz to 8,5 GHz | -41.3dBm/MHz average 0dBm peak | 41,3 dBm/MHz average. 0 dBm peak |
| 8,5 GHz to 9,0 GHz | - 65 dBm/MHz average. - 25 dBm peak | - 41,3 dBm/MHz average. 0 dBm peak |

## E.3	Normal operational mode

The normal operation mode of a DAA enabled UWB device is the mode where no avoidance operation is needed. These modes are addressed in the current EN 302065.  They are repeated here for completeness

RQ_normal_005	Normal operation mode

TS 102 754 V1.1.2	Clause: None	Type: Mandatory

Applies to: 	All DAA enabled devices

Requirement: 	All DAA enabled UWB devices shall not transmit more than -41.3dBm/MHz in the band 3.1GHz to 4.8GHz and 6.0 GHz to 9.0GHz.

Specification Text:	None

RQ_normal_006	Normal operation mode in road and rail vehicles

TS 102 754 V1.1.2	Clause: None	Type: Mandatory

Applies to: 	All DAA enabled devices operated in vehicles in non LDC mode.

Requirement: 	A DAA enabled UWB device operated in road or rail vehicles not deploying a LDC mode shall be capable of deploying a power control scheme with at least 12dB control range

Specification Text:	None

RQ_normal_007	Normal operation mode in road and rail vehicles

TS 102 754 V1.1.2	Clause:None	Type: Mandatory

Applies to: 	All DAA enabled devices operated in road and rail vehicles without LDC and power control.

Requirement: 	A DAA enabled UWB device operated in road or rail vehicles not deploying LDC mode and without the capability of a power control scheme with at least 12dB control range shall not tranmit more than -53.3dBm/MHz in the band 3.1GHz to 4.8GHz and 6.0 GHz to 9.0GHz.

Specification Text: 	None

## E.4	Detection requirements

RQ_Detect_008	Detection Requirements ( Initial channel availability check time)

TS 102 754 V1.2.1	Clause: 5.3.1	Type: Mandatory

Applies to: 	All DAA & LDC enabled devices.

Requirement: 	All DAA & LDC devices shall be able to detect victim system signals.

Specification Text: 		The UWB device shall perform victim system monitoring and shall be required to detect any actively operating victim system signals within a minimum time given by Minimum Initial Channel Availability Check Time, Tavail, Time.

RQ_Detect_009	Detection Requirements ( Max detect and avoid)

TS 102 754 V1.2.1	Clause: 5.3.2	Type: Mandatory

Applies to: 	All DAA enabled devices.

Requirement: 	All DAA devices shall have maximum detect and avoid  time not exceeding that identified in the relevant annex of TS 102 754.

Specification Text:	The combined detect and avoid time shall include a number of parameters which are not accessible from the physical layer. These include;

- Channel availability check Periodicity,

- In Operation Channel Availability Check Time and

- Avoid implementation time

RQ_Detect_010	Detection Requirements ( Signal detection threshold)

TS 102 754 V1.2.1	Clause: 5.3.3	Type: Mandatory

Applies to: 	All DAA enabled devices.

Requirement: 	All DAA devices shall have adequate discrimination to accurately measure the Detection threshold, Dthresh defined in the relevant annex of TS 012 754.

Specification Text: 	This function shall be able to detect victim service signals and measure if the power level is above or below the Signal Detection Threshold, Dthresh in any of the relevant frequency bands. See table below

| Operational frequency | 3.1 to 3.4 GHz | 3.4 to 4.8 GHz | 8.5 to 9 GHz |
| --- | --- | --- | --- |
| Signal Detection threshold A | -38 dBm | -38 dBm | -61 dBm |
| Signal Detection threshold B | - | -61 dBm | - |

RQ_Detect_011	Detection Requirements ( Detection probability)

TS 102 754 V1.2.1	Clause: 5.3.4	Type: Mandatory

Applies to: 	All DAA enabled devices.

Requirement: 	All DAA enabled devices must respond correctly to a signal detection threshold.

Specification Text: 	Where multiple detection thresholds or detection probabilities are defined a test shall be undertaken for each relevant threshold/probability combination.

## E.5	Avoidance requirement

Following the detection and identification of a victim system the selected avoidance option shall ensure the required protection level at the victim receiver.

RQ_avoid_012	Avoidance Requirements (General Requiremet for Avoidance operation)

TS 102 754 V1.2.1	Clause: 6	Type: Mandatory

Applies to: 	All DAA enabled devices.

Requirement: 	A DAA enabled UWB device shall be capable of deploying at least one of the avoidance methods defined in the RQ_Avoid_010 to RQ_Avoid_017

Specification Text: 	The avoidance options fall into four major categories:

power reduction;

spatial avoidance;

frequency avoidance;

time sharing.

Any of these techniques may be used individually or in combination to protect the victim services provided that the avoidance levels given in the victim service related annexes are met.

RQ_Avoid_013	Avoidance Requirements (Transmit Power Management)

TS 102 754 V1.2.1	Clause: 6.2	Type: Optional

Applies to: 	All DAA enabled devices.

Requirement: 	A DAA enabled UWB device shall be capable of reducing power over the UWB operational band.

Specification Text: 	Transmit  power management is the reduction of the UWB transmission power over the complete UWB operational band to the required level.

RQ_Avoid_014	Avoidance Requirements (Transmit Power Management in vehicles)

TS 102 754 V1.2.1	Clause: 6.2	Type: Conditionally Mandatory Optional

Applies to: 	All DAA enabled devices operated in vehicles.

Requirement: 	A DAA enabled UWB device operated in road or rail vehicles shall be capable of deploying a power control scheme with at least 12dB control range.

Specification Text: 	Transmit  power management is the reduction of the UWB transmission power over the complete UWB operational band to the required level.

RQ_Avoid_015	Avoidance Requirements (Transmit Power Management in vehicles)

TS 102 754 V1.2.1	Clause: 6.2	Type: Conditionally Mandatory Optional

Applies to: 	All DAA enabled devices in vehicles.

Requirement: 	A DAA enabled UWB device operated in road or rail vehicles without a power control scheme  shall be capable of reducing power over the UWB operational band.

Specification Text: 	Transmit  power management is the reduction of the UWB transmission power over the complete UWB operational band to the required level.

RQ_Avoid_016	Avoidance Requirements (Band relocation)

TS 102 754 V1	Clause: 6.3.1.2	Type: Optional

Applies to: 	All DAA enabled devices.

Requirement: 	A DAA enabled UWB device shall be capable of band relocation.

Specification Text:	This protection may either be done by band shifting or band switching.

RQ_Avoid_017	Avoidance Requirements (Frequency band notching)

TS 102 754 V1.2.1	Clause: 6.4	Type: Optional

Applies to: 	All DAA enabled devices using frequency band notching.

Requirement: 	All DAA enabled devices using frequency band notching shall be capable of generating a notch adequate to protect the intended service.

Specification Text: 	 This is a frequency dependent transmit power management technique which protects the victim service.

RQ_Avoid_018	Avoidance Requirements (LDC)

TS 102 754 V1.2.1	Clause: 6.5	Type: Optional

Applies to: 	All DAA enabled devices using LDC

Requirement: 	A DAA enabled UWB device shall be capable of switching into the LDC  in the event of a victim service detection in the required frequency band.

Specification Text: 	Low duty cycle techniques decrease the total transmitted energy integrated over a period of time. This is achieved by transmitting at the maximum power for the given frequency band but restricting the transmission in duration.

RQ_Avoid_019	Avoidance Requirements (Antenna techniques)

TS 102 754 V1.2.1	Clause: 6.6	Type: Optional

Applies to: 	All DAA enabled devices using antenna techniques.

Requirement: 	A DAA enabled using antenna techniques shall be capable of  using techniques  such as beam forming or antenna switching to reduce the interference potential to a victim system

Specification Text: 	Antenna techniques in general rely on the spatial distribution of the transmitted UWB signal. The spatial distribution of the signal may be controlled by the directivity of the antenna used. Possible examples include: switching, re-orientation, phased arrays.

RQ_Avoid_020	Avoidance Requirements (Future techniques)

TS 102 754 V1.2.1	Clause: 6.1	Type: Optional

Applies to: 	All DAA enabled devices using future techniques.

Requirement: 	A DAA enabled UWB devices shall be capable of using an avoidnce method that provides an equivalent level of protection of a potential victim system to the non interference mode.

Specification Text: 	The currently qualified techniques for use with UWB devices are given in clauses 6.2 to 6.7 of TS 102 754 however, other techniques may be used where equivalent protection can be demonstrated.

RQ_Avoid_021	Avoidance Parameters

TS 102 754 V1.2.1	Clause: 6.8.2	Type: Conditionally mandatory

Applies to: 	All DAA enabled devices without victim service bandwidth identification.

Requirement:	If a DAA device is not capable of identifying the victim services bandwidth to be protected it shall protect the default avoidance bandwidth for the service to be protected.

Specification Text: 	The default avoidance bandwidths are given in annexes A,B &C.

RQ_Avoid_022	Avoidance Parameters ( Maximum avoidance power level)

TS 102 754 V1.2.1	Clause: 6.8.3	Type: Conditionally mandatory

Applies to: 	All DAA enabled devices using power control techniques for the avoidance.

Requirement: 	If a DAA enabled UWB devices use power reduction for the avoidance operation it shall have adequate attenutation to achieve the identified thresholds between the maximum permitted power level of –41.3dBm./MHz and the NIM level.

Specification Text: 	The maximum avoidance power level is the UWB transmit power assuring the equivalent protection of the victim service.  In the multizone model there is be a hierarchy of avoidance power levels associated with each zone where the lowest maximum avoidance power level in the hierarchy equals the NIM power level.

RQ_Avoid_022	Avoidance Parameters

TS 102 754 V1.2.1	Clause: 6.9	Type: Conditionally mandatory

Applies to: 	LDC enabled devices

Requirement: 	The LDC limits are given in the table below

| LDC parameter | Value |
| --- | --- |
| Maximum Tx on | ≤ 5 ms |
| Minimum Mean Tx off | ≥ 38 ms (mean value averaged over one (1) second) |
| Accumulated minimum Tx off (Σ Tx off) | ≥ 950 ms in one (1) second |
| Maximum accumulated transmission time (Σ Tx on) | 18 s in one (1) hour |

LDC Limits

Specification Text: 	UWB devices having LDC and DAA implemented and operating in all or part of the frequency band from 3,1 GHz to 4,8 GHz may also switch on the LDC parameter set to avoid interference to BWA services and radio navigation services.

# Annex F (normative)	ICS Proforma for DAA device

## F.1	Identification of the protocol

This ICS proforma applies to the DAA standard listed in the normative references clause of the present

document.

## F.2	ICS proforma tables

### F.2.1	Avoidance Modes

These are detailed in table F.1

Table F.1: Avoidance Modes for Radar and BWA operation

| Item | Avoidance Mode | Ref Clauses | Support (Y/N) | Values supported |
| --- | --- | --- | --- | --- |
| 1 | Does the UWB device support a victim service ID ? | [i.5] clause 5.2.2 |  | - |
| 2 | Does the UWB device support optional avoidance mechanisms ? | [i.5] clause 6 |  |  |

# History

| Document history |
| --- |
| V0.0.1internal | October 2008 | Initial Version developed by FB |
| V0.0.9internal | October 2008 | BWA test section, general test conditions, UWB & operating conditions added by SE. |
| V0.0.1 | November 2009 | First complete draft |