TR 101 569 V0.0.6 (2012-04)

Access, Terminals, Transmission, Multiplexing (ATTM) –
Integrated Broadband Cable and Television Networks –
Cable Network Transition to IPv6

<

TECHNICAL REPORT

Reference

DTR/ATTM-003018

Keywords

Cable, DOCSIS, HFC, IPv6

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

Reproduction is only permitted for the purpose of standardization work undertaken within ETSI.
No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2012.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# Contents

Contents	3

Intellectual Property Rights	5

Foreword	5

Introduction	5

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Definitions, symbols and abbreviations	8

3.1	Definitions	8

3.2	Symbols	8

3.3	Abbreviations	8

4	Background and Concept of Transition	10

4.1	History of Internet Protocol	10

4.2	Cable Networks as Broadband Service Providers	10

4.3	IP-Connectivity in Cable Networks	10

4.3.1	Customer Host	11

4.3.2	Home Network	11

4.3.3	Access Gateway	11

4.3.4	Access Network	11

4.3.5	Headend	12

4.3.6	Internet	12

5	Analysis of Present Cable Industry Network Deployments	12

5. 1	Introduction	12

5.2	End-user CPE	13

5.2.1	Stand-alone cable modem	13

5.2.2	Home Router	14

5.2.3	eRouter	14

5.2.4	Set-top box	15

5.2.5	Consumer Equipment	15

5.2.6	E-MTA	15

5.3	Access Network	15

5.3.1	DHCP	15

5.3.2	TFTP	16

5.3.3	ToD	16

5.3.4	CMTS	16

5.4	Core network	17

5.5	Datacentre	17

5.5.1	DNS	17

5.5.1.1	Authoritative	18

5.5.1.2	Recursive	18

5.5.2	Email	18

5.5.3	Web portals	18

5.6	OSS	18

5.6.1	Lawful Intercept / Data Retention	18

5.7	Other functions	18

6	Support of IPv6 on the networks within the cable deployments	19

6.1	Introduction	19

6.2	Peering	20

6.3	Routing & CORE	21

6.4	Access Aggregation PE & Intermediate	21

6.5	CMTS	21

6.6	DOCSIS 2/3	22

6.7	CPE & HFC	22

6.8	OSS & BSS	22

6.9	DHCP & DNS	23

6.10	Firewalls & Load Balancers	23

6.11	Backend Support Services	24

6.12	Web Services	24

6.13	DTV	25

6.14	NMS	25

6.15	DR & LI	25

6.16	Home Services	25

7	IPv6 Standards	26

Proforma copyright release text block	29

Annexes	29

Annex 1: Bibliography	30

History	30

A few examples:	30

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Report (TR) has been produced by ETSI Technical Committee Access, Terminals, Transmission and Multiplexing (ATTM).

# Introduction

This clause is optional. If it exists, it is always the third unnumbered clause.

This Technical Report accommodates an urgent need in the industry to assess the current status of Cable equipment standards that are implemented and deployed in the components that are comprising integrated broadband cable and television networks with regard to their readiness for IPv6. Considering the depletion of IPv4 addresses, transition to IPv6 is required in order to enable continued growth of the customer base connected to Cable Networks and ensure service continuity for existing and new customers. High-quality connectivity to all kinds of IP-based services and networks is essential in today’s business and private life.

A plethora of transition technologies have been proposed in IETF, other standardization organizations and by manufacturers of IP technology to allow coexistence of IPv4 and IPv6 hosts, access and core networks as well as services. Each of these technology options is specified, implemented and deployed in various forms and stages. This report analyses the transition technologies, provides technical summaries and derives recommendations for one or more technologies depending on demographic and cable network architecture requirements. The results of the technical analysis can be used for further standardization of cable IPv6 transition.

# 1	Scope

The TR (ETSI Technical Report) is the default deliverable when the document contains only informative elements.

The scope shall always be clause 1 of each ETSI deliverable and shall start on a new page (more details can be found in clause 11 of the EDRs).

No text block identified. Forms of expression such as the following should be used:

The present document assesses the current status of Cable equipment standards that are implemented and deployed in the components that are comprising integrated broadband cable and television networks and the approaches for their transition to IPv6. Since the time-to-market is a factor considering the depletion of IPv4 addresses, this report accommodates an urgent need in the industry and provides the fundamental analysis for further standardization work.

The Scope shall not contain requirements.

# 2	References

The following text block applies. More details can be found in clause 12 of the EDRs.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

## 2.1	Normative references

As the ETSI Technical Report (SR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

Use the EX style, add the letter "i" (for informative) before the number (which shall be in square brackets) and separate this from the title with a tab (you may use sequence fields for automatically numbering references, see clause A.4: "Sequence numbering") (see example).

EXAMPLE:

[i.1]	ETSI TR 102 881: "Access, Terminals, Transmission and Multiplexing (ATTM); Cable Network Handbook". V1.1.1 (2010-06)

[i.2]	DOCSIS/EuroDOCSIS 3.0:  ETSI EN 302 878-x v1.1.1, Access, Terminals, Transmission and Multiplexing (ATTM);Third Generation Transmission Systems for Interactive Cable Television Services - IP Cable Modems, November 2011

[i.3]	ETSI TS 103 161: “Access, Terminals, Transmission and Multiplexing (ATTM); Integrated Broadband Cable and Television Networks; IPCablecom 1.5”. Parts 1-21

[i.4]	IEEE 802.11a: IEEE Standard for Telecommunications and Information Exchange Between Systems - LAN/MAN Specific Requirements - Part 11: Wireless Medium Access Control (MAC) and physical layer (PHY) specifications: High Speed Physical Layer in the 5 GHz band, 1999

[i.5]	IEEE 802.11b: IEEE Standard for Information Technology - Telecommunications and information exchange between systems - Local and Metropolitan networks - Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications: Higher Speed Physical Layer (PHY) Extension in the 2.4 GHz band, 1999

[i.6]	IEEE 802.11g: IEEE Standard for Information technology - Local and metropolitan area networks -  Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications: Further Higher Data Rate Extension in the 2.4 GHz Band, 2003

[i.7]	IEEE 802.11n: IEEE Standard for Information technology - Local and metropolitan area networks-- Specific requirements -  Part 11: Wireless LAN Medium Access Control (MAC)and Physical Layer (PHY) Specifications Amendment 5: Enhancements for Higher Throughput, 2009

[i.8]	IETF RFC 1918: Address Allocation for Private Internets, February 1996, http://tools.ietf.org/html/rfc1918.txt

[i.9]	IETF RFC 2131: Dynamic Host Configuration Protocol March 1997, http://www.ietf.org/rfc/rfc2131.txt

[i.10]	IETF RFC1350: Trivial File Transfer Protocol July 1992, http://www.ietf.org/rfc/rfc1350.txt

[i.11]	IETF RFC868: Time Protocol May 1983, http://www.ietf.org/rfc/rfc868

[i12]	DOCSIS/EuroDOCSIS 1.0: ETSI ES 201 488 v1.1.1,  Data-Over-Cable Service Interface Specifications Radio Frequency Interface Specification, November 2000

[i.13]	DOCSIS/EuroDOCSIS 1.1: ETSI ES 201 488-x v1.2.2, Access and Terminals (AT); Data Over Cable Systems, October 2003

[i.14]	DOCSIS/EuroDOCSIS 2.0:  ETSI ES 202 488-x v1.1.1, Access and Terminals (AT);Second Generation Transmission Systems for Interactive Cable Television Services - IP Cable Modems, September 2003

[i.15]	IETF RFC1912: Common DNS Operational and Configuration Errors Feb 1996, http://www.ietf.org/rfc/rfc1912.txt

[i.16]	CPE WAN Management Protocol, TR-069 Issue 1 Amendment 4, the Broadband Forum, http://www.broadband-forum.org/technical/download/TR-069_Amendment-4.pdf

[i.17]	IETF RFC 1142: IS-IS protocol specification Feb 1990, http://www.ietf.org/rfc/rfc1142.txt

[i.18]	IETF RFC2178: OSPF version 2 April 1998, http://www.ietf.org/rfc/rfc2178.txt

[i.19]	IETF RFC2453: RIP version 2 Nov 1998, http://www.ietf.org/rfc/rfc2453.txt

[i.20]	IETF RFC 2462: IPv6 Stateless Address Autoconfiguration, December 1998, http://tools.ietf.org/html/rfc2462

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable, (see clauses 13 and 14 of EDRs).

Definitions and abbreviations extracted from ETSI deliverables can be useful when drafting documents and can be consulted via the Terms and Definitions Interactive Database (TEDDI) (http://webapp.etsi.org/Teddi/).

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

BSSID	Basic Service Set Identifier

CE	Consumer Equipment

CMTS	Cable Modem Termination System

CPE	Customer Premises Equipment

DHCP 	Dynamic Host Configuration Protocol

DNS 	Domain Name System

DOCSIS	Data Over Cable Service Interface Specification

E-MTA	Embedded Multimedia Terminal Adapter

HE	Headend

HFC	Hybrid fiber-coaxial

HTML	HyperText Markup Language

IANA	Internet Assigned Numbers Authority

IPv4	Internet Protocol version 4

IPv6	Internet Protocol version 6

LAN	Local Area Network

MPLS	MultiProtocol Label Switching

NAT	Network Address Translator

OSS	Operational Support Systems

QAM	Quadrature Amplitude Modulation

QoS	Quality of Service

PTR	Pointer Record

RIPE	Réseaux IP Européens

RIPE NCC	RIPE Network Coordination Centre

SMTP	Simple Mail Transfer Protocol

TFTP	Trivial File Transfer Protocol

ToD	Time of Day protocol

VoIP	Voice over IP

VPN	Virtual Private Network

WAN	Wide Area Network

WEP	Wired Equivalent Privacy

WPA	Wi-Fi Protected Access

WPA2	Wi-Fi Protected Access version 2

# 4	Background and Concept of Transition

IPv6 transition is critical to the long-term sustainability of European and global networks. As more and more services and industries come to rely on the global Internet as a fundamental platform, the need for ubiquitous connectivity of devices and services becomes very urgent. Such near-term strategic areas like Mobile Internet and Smart Grids as well as the continued growth in residential and business broadband access services are poised to introduce massive numbers of devices that require network connectivity, which may not easily be provided by the current Internet (IPv4) networks. with its depleting address space.

Widespread adoption of IPv6 has been identified as the best way forward to address the exhaustion of the IPv4 address space. Prompt and efficient adoption offered potential for innovation and leadership in advancing the Internet, and that delayed adoption of IPv6 would lead to disadvantages for all users and a weaker competitive position of the industry. In the meantime, we have seen the exhaustion of the IANA Unallocated IPv4 Address Pool on 3 February 2011, and the current prediction for the exhaustion of the RIPE NCC IPv4 Address Pool is early-to-mid 2012. The urgency to transition broadband Internet networks to IPv6 is becoming critical.

While device manufacturers, software developers and network operators are adopting IPv6, the vision of an Internet running IPv6 only will not become reality any time soon. For a considerable period of time, significant number of devices and services will exist that customers want to use and that require IPv4 connectivity. An immediate replacement of these IPv4 hosts and networks may not be feasible or not desirable for various technical and economic reasons. It is particularly the task of access network operators and broadband service providers to ensure customer choice in terms of technology and services. Appropriate transition technologies enable the coexistence of IPv6 and IPv4 in various parts of the end-to-end network allowing services to be consumed and customer premises equipment to be used transparently while fostering a smooth transition to the required extended address space provided by IPv6.

## 4.1	History of Internet Protocol

Why is IPv6 not backward compatible?

## 4.2	Cable Networks as Broadband Service Providers

As of 2009, integrated broadband cable and television networks go into the home of 67 million customers in the European Union, providing Digital TV, Broadband Internet and Telephony services. Broadband Internet provided by Cable Networks utilizing DOCSIS cable modem technology provide services to 20.9 million subscribers in Europe (2009) with access speeds of currently up to 200 Mbit/s. This figure has grown by at least 12% annually. As such Cable Networks provide the platform to satisfy fundamental entertainment, communication and information needs to consumers. Furthermore, the industry is anticipating a transition to delivery of digital television using broadband cable modem technology, which will dramatically increase the number of broadband connected households.

Cable Networks are recognised as a key enabler in supporting Europe’s Digital Agenda. To continue to meet the demand of accelerating connectivity of digital devices, a standardised approach for the cable eco-system to rapidly transition to IPv6 is required. A failure for an effective standards driven transition would impair the ability to achieve cost effective solutions on a large scale.

## 4.3	IP-Connectivity in Cable Networks

Integrated broadband cable and television networks are built against various international and ETSI standards. Figure 1 depicts the fundamental architecture of a Cable Network as it is currently deployed with a hybrid fibre-coax approach. [i.1] provides a complete overview on Cable Network architectures and services. The IP communication system in Cable Networks is based on the series of ETSI DOCSIS [i.2] and PacketCable standards [i.3]. Since 2006, the current version of the DOCSIS technology (DOCSIS 3.0) has natively supported IPv6. For various technical reasons, service providers have not implemented IPv6 support for their customers.

Figure 1: Principle architecture of a hybrid fiber-coax (HFC) Cable Network

In order to achieve end-to-end connectivity, the Cable Network is interconnected at the Headend (HE) with a backbone network and the Internet. The backbone network may or may not be operated and managed by the same entity as the access network. The home network within the customers’ premises is typically installed, configured and operated by the customer.

For the purposes of the analysis in this report, the end-to-end network is subdivided into various parts, each of which supports IPv6 and/or IPv4 with various degrees of probability. The network parts also distinguish themselves by the number of times they occur globally and by the uniformity of their operation and management. Both aspects have an impact on how difficult it is to homogeneously transition to IPv6.

### 4.3.1	Customer Host

This is the device that the customer uses to consum an IP-based service. It is the final destination and the originating source of IP packets. As Customer Premises Equipment (CPE) it is typically owned and operated by the customer. Cable Network operators are unlikely to be able to support the wide variety of host devices that customers are deploying in their homes.

### 4.3.2	Home Network

The Home Network extends from the Customer Host to the Access Gateway. It may be constituted by a simple wired or wireless link between the two devices (in which case it becomes irrelevant for this analysis since it is not addressable and does not process protocol messages) or may consist of a complete infrastructure of routers, wireless access points etc. It may connect multiple Customer Hosts to the Access Gateway and it is typically owned, installed and operated by the customer. Cable Network operators may impact the capabilities of the Home Network up to a certain extent by customer information and/or delivery of devices.

### 4.3.3	Access Gateway

This device is installed at the customer location and constitutes the separation between the Home Network and the Access Network. While the device may be owned by the customer or the Cable Network operator it is typically authorized for usage by the latter. It terminates the Cable Network on the customer side.

### 4.3.4	Access Network

The Access Network extends from the Access Gateway to the Headend. It is operated and managed by the Cable Network operator. It typically uses DOCSIS technology to establish IP connectivity and packet transport.

### 4.3.5	Headend

This device separates the Access Network from the Backbone Network. It terminates the Cable Network. For the purposes of this report it also terminates the portion of the end-to-end IP connection that traverses the operator-managed network. As such it will be the location of devices that are providing transition technology services.

### 4.3.6	Internet

This is the Internet cloud that provides IP-based services. It is the final destination and the originating source of IP packets which may be delivered as IPv4 or IPv6. The actual delivery of the service or the path the packet has taken is irrelevant for this report, only the way of addressing is taken into account.

Due to the inherent incompatibility of IPv4 and IPv6 protocols and addressing schemes, special measures have to be taken (i.e. transition technologies have to be deployed) in order to ensure connectivity between equivalent network parts supporting different Internet protocols (e.g. IPv4 host talking to IPv6 service across IPv4 home network and IPv6 access network and backbone). Figure 1 summarizes the types of connectivity that are considered in this report.

- IPv4 Customer Host via IPv4 Access Network with IPv4 Internet

Editor’s note: This is out-of-scope of this TR as provided by native IPv4

- IPv6 Customer Host via IPv4 Access Network with IPv4 Internet

Editor’s note: This is out-of-scope of this TR as within customer responsibility

- IPv4 Customer Host via IPv6 Access Network with IPv4 Internet

- IPv6 Customer Host via IPv6 Access Network with IPv4 Internet

- IPv4 Customer Host via IPv6 Access Network with IPv6 Internet

- IPv6 Customer Host via IPv6 Access Network with IPv6 Internet

Editor’s note: This is out-of-scope of this TR out-of-scope as provided by native IPv6

- IPv4 Customer Host via IPv4 Access Network with IPv6 Internet

- IPv6 Customer Host via IPv4 Access Network with IPV6 Internet

# 5	Analysis of Present Cable Industry Network Deployments

## 5. 1	Introduction

In this clause, a high level view of the present IPv4 deployments for the cable industry   including the following technologies is provided:

- End-user CPE

- Access Network

- Core network

- Data centre

Whilst this list is not exhaustive, and does not cover irregular or bespoke components used by individual cable network oprators, it provides an overview of the main areas that can be mapped to individual operator deployments.

The Figure below shows the main component areas of a cable operator network, providing end-to-end Internet access.  There are a number of additional services that may be offered by the cable operator, including business

customer site-to-site Virtual Private Networks (VPNs). The detail of such configurations are beyond the scope of this

analysis.

Figure 2: Main component areas of a cable operator network for end-to-end Internet access

## 5.2	End-user CPE

The following Figure gives a view of the most common CPE installed at a customer site.

Figure 3: CPE installed at a customer side

### 5.2.1	Stand-alone cable modem

A stand-alone cable modem is a CPE device that provides connectivity to the cable operators HFC network, and has a single Ethernet interface on the customer-facing side. Stand-alone modems do not provide any routing facility, and it is either used for connecting a single host (eg PC), or for connecting to the WAN interface of a stand-alone home router. The customer equipment is assigned a  public IP address from the operators DHCP server.

### 5.2.2	Home Router

A stand-alone home router provides LAN functionality within the customer home. It has one Ethernet  WAN interface, which is connected to the cable modem, one or more wired Ethernet LAN interfaces, and generally includes Wireless using IEEE802.11a/b/g/n standards [i.4, i.5, i.6, i7].

The IP addressing of the LAN generally uses private [i.8] IP addresses, the most common in the class C range 192.168.x.x. There are an extensive range of home routers available, all with differing functionality, however the most common features found include:

- LAN DHCP server

- DNS (Domain Name System) forwarding

- Stateful Packet Inspection firewall

- Network Address Translation, with features to allow single or multiple port forwarding (manual or via uPnP)

- Wireless configuration to support one or more BSSIDs (Basic Service Set Identifiers), wireless security (WEP, WPA, WPA2).

### 5.2.3	eRouter

An eRouter is a combined cable modem and home gateway. These generally provide all of the services shown above, however are in a single unit, which requires a single power supply and takes up less space. Features and functionality vary widely between manufacturers. The CableLabs eRouter specification defines the minimum set of requirements for these devices.

### 5.2.4	Set-top box

#### A set-top box is used to receive and decode digital television signals from the cable operator. In addition, the set-top box may also provide interactive services and be able to retrieve content from the internet. The broadcast signal does not use IP, however interactive functions and access to the internet are provided using IP. Where the set-top box can is provisioned with a private IP address, access to the interactive functions either remain internal to the operator network, use web proxies, or operate behind a Network Address Translator, with NAT-44. A web proxy, or NAT hardware allows multiple privately addressed clients to access content from a single public IPv4 address. Interactive and internet connectivity on set-top boxes is generally limited to HTML based content.

### 5.2.5	Consumer Equipment

There is an ever-increasing wide range of equipment that is becoming ‘internet-ready’, by having either a wired Ethernet interface, or a built-in wireless IEEE 802.11a/b/g/n interface. This category includes Personal Computers and laptops, with a wide range of operating systems and versions, as well as tablet devices, eReaders, games consoles (static and handheld), network storage devices, printers, PDAs, televisions, smartphones etc.

### 5.2.6	E-MTA

An E-MTA (Embedded Multimedia Terminal Adapter) is used by cable operators to provide telephony services, using VoIP across the HFC network. The eMTA is provisioned with an IP address from the cable operators DHCP server. Additional options such as SIP (Session Initiation Protocol) gateway address are provided with the DHCP response. Some cable operators offer VoIP services using PacketCable to provide dedicated bandwidth for VoIP services.

## 5.3	Access Network

The access network provides the physical connectivity from the Cable Modem Termination System to the network core. This can be achieved using layer 2 (eg Metro Ethernet), Layer 3 routing, or directly from a CMTS into the MPLS backbone. IP addressing is also commonly provided from within the access network.

### 5.3.1	DHCP

DHCP (Dynamic Host Configuration Protocol) is used extensively in cable networks to provide IP addressing for both the cable device, and the public IP address for the customer LAN. The DHCP protocol is defined in [i.9].

The CMTS is used as a relay agent to receive broadcast DHCP messages from the HFC network, and forward them unicast to a DHCP server. The CMTS also inserts the following additional options into the DHCP message (Table 1):

| GIADDR | The IPv4 address of the interface of the CMTS on which the DHCP DISCOVER was received. |
| --- | --- |
| Option 82, suboption 1 | The MAC address of the cable device via which the DISCOVER was broadcast |
| Option 82, suboption 2 | The Circuit ID. This is generally a CMTS interface ID. |

Table 1: CMTS additional options into the DHCP message

The DHCP server is often used to authenticate the request using a database or directory, and assign a class of service. The service class is used to specify the reply options and their values. For example, to specify a DOCSIS configuration file to download, or to provide DNS server IP addresses.

An OFFER is made to the client, which it will then REQUEST, and the server ACKnowledge to complete the process.

Additional functionality on the CMTS can be used to improve security by intercepting the OFFER and encrypt the configuration file name.

A further security mechanism can be enabled on the CMTS to perform Source Address Verification. The client IP address is extracted from the DHCP OFFER and / or by sending LEASEQUERY messages to the DHCP server to confirm the MAC identity for the IP address.

DHCP resilience is generally provided by two or more DHCP servers being specified in the configuration of the CMTS. The CMTS will forward DHCP DISCOVER messages to all defined servers, and the client chooses which response to REQUEST. This is generally the first received response.

### 5.3.2	TFTP

Trivial File Transfer Protocol [i.10] is used in cable operator networks to provide DOCSIS configuration files to the cable modems and set-top boxes. As part of its initialisation process, a cable modem downloads the configuration file (specified in a DHCP option) from a TFTP server (also specified in a DHCP option). TFTP can also be used for downloading a new firmware revision to a cable modem.

### 5.3.3	ToD

Time of Day protocol [i.11] is used by cable devices during initialisation to acquire the current time. The time server IP address is provided as a DHCP reply option.

Regulatory requirements / enforcements

Under European guidelines, cable operators are required to provide real-time and historical data on which IP address has been assigned to a customer. This data is generally stored in a database, and is retained for the time specified by the local authority.

### 5.3.4	CMTS

The Cable Modem Termination System (CMTS) is a router that hosts the physical interface to the HFC network, and provides the routed IP connectivity to the service provider access network. The CMTS may be provided by a wide range of suppliers.

On the HFC interface, the following standards are supported:

DOCSIS1 / EuroDOCSIS1 [i.12]

This is the original DOCSIS cable transmission standard, which was originally developed in 1997. It supported upstream and downstream channels. The main difference between the North American DOCSIS standard, and the European EuroDOCSIS standard is the channel bandwidth. These are based on the original television standards for the bandwidth required to broadcast a single analogue television channel. The DOCSIS standard supports 6Mhz channels, whereas the EuroDOCSIS standard supports 8Mhz channels.

Using 256-QAM modulation, an 8Mhz channel allows for a maximum bandwidth of 55Mbps.

DOCSIS1 supports QPSK or 16-QAM modulation in the upstream, using a 3.2Mhz channel. This provides a maximum upstream bandwidth of 10.2Mbps.

The DOCSIS1.1 / EuroDOCSIS1.1 [i.13 enhancement was introduced in 1999, and added QoS functionality to the specification

DOCSIS2  / EuroDOCSIS2 [i.14]

This standard was introduced in 2001, to provide improvements in the  upstream bandwidth available over the HFC network. It supports the QPSK, 8-QAM, 16-QAM, 32-QAM or 64-QAM modulation, and provides a maximum upstream bandwidth of 30.72Mbps.

DOCSIS3  / EuroDOCSIS3 [i.2]

The DOCSIS3 standard, introduced in 2006 added several new features and enhancements to functionality. The primary ones being:

- support for multiple bonded channels in both the upstream and downstream.

- support for IPv6.

Whilst the maximum bandwidth for each channel has not changed from DOCSIS2, by combining multiple channels, and sharing the data across them, it is possible to increase the overall bandwidth available to the end user. There is no defined maximum number of bonded channels, although current technology provides up to 16 downstream channels, and 8 upstream.

These are fully defined in the relevant CableLabs specifications.

The DOCSIS or EuroDOCSIS standard(s) supported by each CMTS depends on the make and model of CMTS, HFC interface card, processor and router operating system.

## 5.4	Core network

The core network provides the physical connectivity between multiple access networks, datacentres and the transit / peering partners.

The topology is different for each service provider, but many use MPLS (Multiprotocol Label Switching) in a full-mesh configuration to ensure resilience and reliability across the network.

## 5.5	Datacentre

The datacentre infrastructure is generally used to host the cable service providers own, or third party network services. These include authoritative and recursive DNS servers, eMail servers, web portal services, provisioning systems, OSS platforms, data storage and backup.

### 5.5.1	DNS

DNS (Domain Name Service) is used in IP networks to resolve domain names into host IP addresses. There are two primary functions of DNS:

#### 5.5.1.1		Authoritative

This server holds the zone files that hold the mapping between IP address and host name. It is the IETF best practice [i15] to define a reverse mapping (PTR record) for every client. This is normally achieved by pre-populating the forward and reverse zones with unique names mapped to the IP addresses. The structure of the name is decided by the cable operator, but generally takes the form <customer_number>.<region>.<serviceprovider>.com.

Zone files will also exist for any other domains that the cable operator is responsible for, such as for hosting , and for its own email, web content etc.

#### 5.5.1.2	Recursive

Recursive servers are deployed in the cable operator network, and are used by the clients to resolve IP addresses and names from the internet. These generally also cache the results of lookups to improve performance and reduce overall DNS query rate.

Service providers generally provide additional services to customers, either from internal systems or via third-party agreements.

### 5.5.2	Email

An eMail service may be supplied to a customer using standard protocols PoP, SMTP and/or IMAP, as well as via a webmail portal over HTTP/S.

### 5.5.3	Web portals

The service provider may also allow for customer self-care functions including the ability to subscribe to, change service tier or profile, or subscribe to additional services offered by the service provider or an approved third party. These are generally provided via a web-based portal, using HTTP/S.

## 5.6	OSS

Within the cable service provider network, support for the cable modems is provided by a wide range of Operational Support Systems tools. These often use industry standard communication protocols, such as SNMPv1 or SNMP v2 and more recently CPE WAN Management Protocol [i.16].

Other OSS tools have been developed internally by the service provider.

### 5.6.1	Lawful Intercept / Data Retention

Lawful intercept is the lawfully authorized interception and monitoring of communications.  Cable service providers must comply with Cable service providers must comply with the legal and regulatory requirements for the interception of voice as well as data communications in IP networks.

The IP data must be retained by the cable service provider for a defined duration, and made available to the legal and regulatory authorities when requested. The defined data retention period varies from region to region.

## 5.7	Other functions

Other functions exist within many cable operator networks that are irregular or of a bespoke nature, and cannot all be identifued. These may include:

- Web content filtering: This is the blocking of illegal / immoral web content from a specified list of internet hosts. The specified list may be provided by the local legal or regulatory authority.

- Deep Packet Inspection: This can be used to enforce traffic restrictions on end users based on the type of traffic. One example is the rate-limiting of peer-to-peer file transfer. Restrictions can be imposed on overall network traffic, or to individual end users, based on policy rulesets.

In Summary, there is extensive use of IPv4 across every component within the cable service operator network. This includes a complex combination of:

- private, non-globally routable, IP addressing within the end-user LAN, which uses network address and port translation to a single globally routable IPv4 address

- private, non globally routable, IP addressing for ontrol and connectivity of the cable devices

- globally routable IPv4 addresses used in all of the core network components across the access and core networks, and within the data centre.

It is common to find a mixture of several routing protocols within the cable service provider network. Routing across the core network, and with transit and peering partners is generally achieved using BGPv4, however the access networks often use interior routing protocols such as IS-IS [i.17], , OSPFv2 [i.18], or RIPv2 [i.19] to provide routing between the CMTS to the core network, data centres or other networks.

# 6	Support of IPv6 on the networks within the cable deployments

## 6.1	 	Introduction

In this Clause, a high level view of the present IPv6 development for the cable industry including the following technologies is provided;

- Peering

- Routing & CORE

- Access Aggregation PE & Intermediate

- CMTS

- Headend

- CPE & HFC

- OSS & BSS

- DHCP & DNS

- Firewalls & Load Balancers

- Backend Support Services

- Web Services

- DTV Services

- NMS.

The document does not cover the following technologies;

- SIP services

- VoC

- Other technologies within the cable industry.

Note that the above technologies are not part of the IPv6 development analysis due to the lack of requirement in the present day MSOs for these to be provide over IPv6.

The following sub-clauses are based on the reasoning for transition technologies and the effect of the level of IPv6 deployments within the cable industry comparative to transitioning.  Also defines what restrictions, technical or logistical, that will force Cable MSOs into transitioning instead of deploying full dual stack from day one.

IPv6, the new Internet protocol, is a requirement based on the depletion of IPv4 addressing.  IANA, RIPE & all other registries, if they haven’t already, will run out of blocks shortly.  This presents the industry with a large issue of delivering services across a new protocol & how to transition across from IPv4 and IPv6.  The market is truly end-to-end for ISPs leaving them in a position of little to no control over the transition to IPv6 due to the dependency on OSEs, Application & Home Stack readiness.  No matter what we do to our network we will be forced into the final gap analysis and at some point the decision of service deprecation.  What devices are necessary to be IPv6 ready to allow for “no” IPv4 connectivity in the home?

Generally the market is doing well on the development of IPv6 and transitioning across their products & services but the issue is the gap that will be left & we are three years behind. This is mostly due to the industry cohesiveness not being apparent.  We don’t work well enough together for everyone to agree to complete on a date.  If this had been the consensus we could have moved to IPv6 native or dual stacked solutions instead of needing transition technologies.

So the problem with IPv6 is that it’s conducive to a gradual transition. By planning an IPv6 deployment early, one can minimize risks, costs and complexities, but unfortunately not the need for a transition technology of which most companies will be forced into.  Thus the most important standard today for networks in any arena, not just Cable MSOs, is the transition standard.

The requirements for MSO transition to IPv6 are these;

- You have run out, or will shortly, of global IPv4 addresses with no access to a new pool;

- IPv6 only services are being deployed so without IPv6 on your network those services to your customers do not exist unless Teredo is configured or some other tunneling potential;

- Doing an early transition even beyond any IPv4 depletion requirement will give a company time to settle into the new technology and find the gaps in deployment.

So the technologies that will effect the basis for this transition, where is the market on delivery of IPv6, and what restrictions will force into an IPv6 transitional technology are considered here.

Within the technologies section the separate & isolated categories within the Cable ISP MSO, the degree of their readiness & finally the effect on this readiness on the necessity for Ipv6 transition technologies to cover any gaps on business continuity with the depletion of IPv4 addressing are discussed.

## 6.2	Peering

When discussing peering from a Cable ISP viewpoint we are focusing on the ability for the customer to access the outside world from within our network.  Peering gives this connectivity so one must start here if one is going to provide an IPv6 service for your subscribers.  Now peering might not be considered a “hardware” based technology or a “feature” based technology as such but it is a fundamental technology in your transition to IPv6.  Whatever connectivity an MSO plans to do they will have to peer on IPv6 eventually during transition.

The present IPv6 routing table in eBGP is hitting 9k routes and increases per day.  IPv4 is however increasing by leaps & bounds to an even greater degree.  IPv4 now has hit 400k routes, which bring us to potential resource issues, and the impact this will have on transitional technologies & hardware requirements.  If we cogitate the potential increase that will be coming some time in the future on Ipv4 with broken Supernets, higher & higher prefixes being accepted by peers & the general displacement of subnets … the lack on contiguous prefixes in the IPv4 will increase exponentially the further into depletion we go.  As the IPv6 table erupts into the 100k marks so the IPv4 table may push into 500-600k routes.  Now the resource issue has been removed from memory but the convergence times & route-dampening implications start, and are already, to become extreme.

Most MSOs base their IPv6 peering on their present IPv4 peering except maybe in Hurricane Electric’s case which is the “master” Tier 1 in the world from an IPv6 routing table prospective.  So the rules haven’t changed much, the peering relationship policies are the same and usually duplicated with only the charging not being implemented at present due to the lack of IPv6 traffic. China is yet to open its peering points on IPv6, which should open up some 20,000 prefixes, & many gigs off traffic on IPv6.  So the days of free IPv6 transit are numbered but at least not for the coming year. Let’s consider why IPv6 will increase and gradient to the transition will be more prevalent than previously thought. With transition technologies, although designed well, with little or not impact generally, still provide a service deprecation and even latency in some flows, especially peer to peer.  Now considering this IPv6 native transport will be preferred to the private IPv4 solution provided by the cable ISPs to deliver an almost equivalent service but not quite.  So the mass use of the transition tech, also due to more services being placed on IPv6 out in the Internet Cloud, will be measurably shorter than we expected.

It should be noted that eBGP ingress & egress filtering changes dramatically with problems concerning allowing ICMPv6 (due to the nature of NDP) out through your interfaces.  There are also major issues with PMTU & the might be need to force the MTU value down to 1280 fixed to prevent blackholing as there is no fragmentation on IPv6 in transit and therefore when PMTU breaks due to incorrect filters or corporate security standards we are left with little other choice.

So, in summary, peering is IPv6 capable, it has issues, but in general it works well with workarounds where it doesn’t.

## 6.3		Routing & CORE

For IPv6-based networks, routing is the part of IPv6 that provides forwarding capabilities between hosts that are located on separate L3 networks; this can be defined in two areas for the Cable Operator.  Firstly the CORE (which is discussed in this section) and secondly the Access Layer, PE to CMTS.  Most MSOs tend to go for an MPLS core that, at present, has no native IPv6 implementation on RSVP or LDP.  They use instead a method of IPv6 “tunneling” across the MPLS using 6PE or 6VPE (use of VPNs) using the IPv4 FECs.

Routing is the primary function of IPv6 as it is a L3 protocol although does have intelligence of the onlink & L2 within NDP as this translates into a new ether-type and NDP using ICMPv6 for messaging.

Above the IPv6 layer, transport services on the source host pass data in the form of TCP segments or UDP messages down to the IPv6 layer which actually does not change so for the most part we are looking at applications that focus on the IP packet, L3 & local link functionality. This functionality in the most part is in hardware presenting a forwarding plane and same or quicker than IPv4.

At present there are 6PE & 6VPE & IPv4 IGPs for MPLS to deliver IPv6 through the network COREs.  This provides a good starting point and allows a provider to dual stack his BGP with both L3 protocols.  The only issue is the feature sets needs to be aligned.  For example, IPv4 CoPP & QoS are well defined and encompassing, whereas IPv6 has major gaps within these technologies already especially in tunneled topologies.

## 6.4		Access Aggregation PE & Intermediate

PE iBGP to the Access IGP is reasonably easy within the data-networking kingdom.  6PE and IPv6 ISIS/OSPFv3 give ample functionality for interconnecting to the CE cloud aggregation.   Route summarization & aggregation are fully configurable/implemented within most IGPs.  Intermediate L2/L3 switches are also generally well defined for IPv6 with profiling & forwarding done in hardware in most cases at both L3 and L2.

The Access Layer is still being heavily developed at present and cannot be considered stably defined & implemented by vendors in general on the CMTS.  However, as above in the PE CORE, the implementation of IPv6 function is mostly defined for most features, if a little minimal in some areas.   This is is constant development at present & should be, by the end of the year, a fully stable access aggregation topology from PE to CMTS running native IPv6 IGPs for transport with an extremely close proximity to IPv4 features.  Which means that cable transport through the CMTS on IPv6 on to the PE routers is controlled at present by the CMTS development, as this is the bottleneck in IPv6 feature progression, but is at present able to be deployed in a minimal manner within most vendor deployments.

It can be surmised then that the access aggregation will be in the next few months capable of a full, non-static, IPv6 topology environment on the PEs & intermediate switches if used.

## 6.5		CMTS

CMTSes have had a slow start but are now, in the most part, fully developed for IPv6.  The big four CMTS vendors do have excellent IPv6 support, although bugs are common, the features are there and able to be used and are live in some networks.

Native IGPs, at least ISIS, is ready for deployment in most topologies, with filtering, NDP & many interface standard being compliant to especially across the four heavy vendors in the market.   Native & dual stacked interfaces with PD & SLAAC capabilities are also fully compliant on most vendor deployments.

CMTSes are almost ready for most IPv6 native & dual stack topologies at least on ISIS as an IGP and bundles are fully functional for most vendors.

## 6.6		DOCSIS 2/3

Cablelabs published the 160 meg DOCSIS 3.0 IPv6-ready specifications for cable modems in August 2006.  This shows the prediction from cablelabs in general for the IPv6 deployment. The widely used DOCSIS 2.0, even today, did not fully support IPv6 until the new 'DOCSIS 2.0 + IPv6' standard was created.  However, most ISPs that support DOCSIS 3.0 have not deployed IPv6 across their networks at present and those that have are only looking at testing or TFT ro friendly customer validations.  We have very few full Ipv6 deployments in the cable world today.

It is considered that most networks, to bridge or develop into DOCSIS 3 with IPv6 or DOCSIS 2+IPv6, transitional requirements where needed or even when allow bridging where only the ether-type is required for transit traffic & management traffic will stay IPv4.  Most management will be considered the highest priority for the highest percentage of cable MSOs and therefore end up holding its IPv4 management addressing where possible.

DOCSIS is generally IPv6 complaint & compatible within certain boundaries to date & does not create a barrier to IPv6 deployments.

## 6.7		CPE & HFC

The CPE is the largest part of any cable ISP cost in equipment times that of CMTSes, CORE & backend device costs by 10 times if not more in some cases.  This is also the largest, numerically, hardware deployment in the network.

HFC distribution network, layer 1 physical transport on the RF, has little concern with IPv6.  It considers the IP data streams to be signals with no relation (in the most part) to its transport & unseen.  Multiplexers, ILAs & LXC 16:1s legacy cross connects on fiber or coax will not see the IPv6 transition & change.  So the CPE are the largest impacting device in this section and have proven to have a quite unpredicted development requirement for most cable L2 & L3 modem, EMTA & eRouter vendors.  The development has really been pushed since the beginning of 2011 towards an IPv6 capable CPE market.  Even the bridging modems requirement of pushing IPv6 forwarding (L2 only) with only knowledge of the frame and IPv6 ether type have had trouble pushing the mechanism into hardware.

We have seen since 2002 CPE vendors having some responsibility towards IPv6 but without actual native compatibility.   Tunneling was the optimal choice but Teredo pass through was the most valued choice within cable provided home devices and even this was at a minimum.  So the actual industry did not start to really consider native forwarding until late 2008 and then only a few vendors.  But with the issues and defined changes between the two protocols, IPv6 showed itself to be a rather difficult delivery, impacting almost every implementation within the CPE.

We now sit in 2012 with full-blown tunnel implementations, IPv6 friendly firewalls, DHCPv6 PD & SLAAC, IPv6 Accessible Web GUIs, RAs for RDNS & DNSSL, Prefix Suppression within the RA & finally UPnP support   We have come a long way and IPv6 deployment speeds will not slow due to development on the CPE or the L3 integration of IPv6 but the possibility of deployment on other factors.  The factors of logistics, mass swap outs, cost & confidence on the end-to-end delivery will be final reasons why IPv6 transitional technologies will be required for the next 3-8 years in the cable industry.

So one can consider CPEs to be almost completely developed for a basic dual stack or native IPv6 only implementation.

## 6.8		OSS & BSS

All cable ISPs these days provide advanced IP services– whether it is IP telephony, tiered data, home networking, or subscription media – cannot scale without tools to efficiently install, provision, and manage network devices, as well as activate and support subscriber services. In short, operations support systems (OSS) software is the oil that keeps the broadband IP infrastructure and services engine running smoothly. OSSes are by nature extremely valuable to the functionality of the service the ISP offers.

High-speed Internet access is now the dominant cable IP service offering. During the past five years, MSOs have made significant progress in improving cable modem installations and subscriber service activation. When done manually, the cable modem activation process requires a telephone call from the prospective customer to a cable company service center. However, MSOs are increasingly automating this progress through the use of Web-based tools that allow user self-registration. Additionally, many cable operators offer consumers self-installation options, so they can purchase and connect cable modems themselves.

During the service provisioning process over IPv4, services are linked to the subscriber's account, and then instantiated in the network through device provisioning processes. Service provisioning can either be done manually by a MSO CSR or directly by the consumer through a Website. The latter is obviously preferable as it provides a customer self-service option, reducing costs and time to service activation.

For high-speed data access, service options that must be provisioned include the customer's Internet service provider (ISP), service class (defined by access speed or other attributes), email addresses, and personal Web space. A home networking offering adds enhanced data features, such as a managed firewall or virus protection and end-device authentication for a wireless network. Content service provisioning may include enabling access to targeted video, audio, or gaming services. Telephone service provisioning is significantly more complex. In addition to provisioning the underlying data service, telephone lines and numbers must be assigned, along with enhanced services, such as voice mail, caller ID, call forwarding, and more.

Once services have been selected and assigned to the customer, devices on the network must be provisioned to deliver these services, typically via simple network management protocol (SNMP). For all cable IP services this includes configuring DNS, Dynamic Host Configuration Protocol (DHCP), Trivial File Transfer Protocol (TFTP), SYSLOG, and Time of Day (ToD) servers.

So considering the integration & complexity of these services IPv6 is a heavy requirement for such a valuable service.   The industry applications & network requirements for OSS is actually well advanced on IPv6 support & can be implemented today.

BSS is just as valuable as OSS, and at some points, more so.  Defining the requirements for BSS as a whole within the MSO is extremely difficult as the degree of topologies, applications & type of deployments out there today makes impossible to generalize.  BSS must be considered on a per MSO basis unfortunately.   But to estimate we can assume that the development is there in process or already complete to the point of delivery for certain topologies.

## 6.9		DHCP & DNS

DHCP is currently the standard host configuration protocol for the TCP/IP protocol suite for IPv4 with development work being done since the early 1990s on DHCPv6.  There are again are a few gaps which are being contained & changed but generally DHCPv6 alone is functional and deployable.

While most of the changes that IPv6 brings impact technologies at the lower layers of the TCP/IP architectural model, the significance of the modifications means that many other TCP/IP protocols are also affected which gets neglected. This is particularly true of protocols that work with addresses or configuration information, including DHCP.  For this reason, a new version of DHCP was created due to the nature of IPv6.

Two Methods for Autoconfiguration in IPv6

One of the many enhancements introduced in IPv6 is an overall strategy for easier administration of IP devices, including host configuration. There are two basic methods defined for autoconfiguration of IPv6 hosts:

- Stateless Autoconfiguration: A method defined to allow a host to configure itself without help from any other device.

- “Stateful” Autoconfiguration: A technique where configuration information is provided to a host by a server.

Which of these methods is used depends on the characteristics of the network. Stateless autoconfiguration is described in [i.20].  DHCPv6 provides “Stateful” autoconfiguration for IPv6. As with regular DHCP, DHCPv6 may be used to obtain an IP address and other configuration parameters, or just to get configuration parameters when the client already has an IP address.

## 6.10		Firewalls & Load Balancers

The main firewall vendors for cable (& generally other industries) are extremely forward on IPv6 deployment.  Full rule base, packet decryption (specific packet field integer rules) , acceptance of all lengths of prefix, NDP ICMPv6 separation, VRRP, all interface configurations & general policies all based on IPv6 & more is accepted.  Basically the firewall & ADC (load balancers) are completely IPv6 compliant.

DNS has a similar issue to CORE network routing tables, which is resources.  Being able to handle the requests for both quad A and single A records at the same time and then defining the priority if this is implemented.  We can though place DNS as a fully and proven IPv6 functional service worldwide with some security gaps & lacking white listing it is still a completely valid service on IPv6 and has been since the days of 6bone.

## 6.11	Backend Support Services

So we have dealt with OSS (Operational support systems) that cover the DHCP, CPE & CMTS backend requirements & BSS (Billing support systems) but there are backend infrastructure that require a company to continue to function and provide those services such as backup, data center services & general corporate applications to allow reporting, administration & management.  These systems tend to be neglected due to their unseen nature & lack of direct effect on MSO subscriber connectivity.

Now considering this categorization we can determine that OSes, backup software, corporate finance application clusters, as examples are actually extremely compliant with IPv6.

EMC, one of the largest backup solutions providers for the cable industry, has had IPv6 functional support & implementations since 2006.

“As part of our commitment to ongoing IPv6 support for our customers, EMC established a corporate IPv6 Program Office in 2006 to drive consistent implementations of IPv6 requirements and coordinate product plans, services, and sales.”

If we look at the BESS (Back-End Support Services) as a whole we find that this area is well covered for IPv6 with only a few holes in application awareness on IPv6, but the gap is small.

## 6.12	Web Services

When migrating the Web Services from IPv4 to IPv6 within an MSO, just making a Web server ready for IPv6 can raise serious problems. For example, users experience errors when they request services that have not yet supported IPv6. In addition, the solution requires that the organization network be protected from malicious IPv6 accesses, although there are no total security solutions for IPv6 unless a separate firewall.  Reverse proxy solutions have been implemented to handle this but generally the web services area is still a little shaky with IPv6.

The simplest solution to make the Web service IPv6-ready is a Web server that supports both IPv4 and IPv6, e.g., Apache with IPv6/IPv4 dual stack. Because the essence of Web service is to connect various services to each other, making a single server ready for IPv6 causes various errors by the services that have not yet supported IPv6 not including all of the DNS potential mismatches for double entries.

Another solution for deployment is duplicating the present IPv4 system for IPv6. With this solution, we can remove the errors by modifying links to the services that are not ready for IPv6. However, this solution pushes up the content management cost because the administrator has to manage double sets of Web contents consistently.

The most consistent topology unfortunately is not the IPv6 service that has been isolated not only logically but also physically from the current IPv4 services. Actually, IPv6 has been designed with much regard to peaceful coexistence with IPv4 in the sense that there is no integration, which would have created no extra need for transitional technologies if we were not running out of IPv4 addressing.  This brings up the ultimate issue that private or public IPv4 addressing cannot be “translated” into na IPv6 address within the protocol & technology and thus we need protocol translators/transitional devices/services on our networks.

To minimize the influence on the current IPv4 Web services if willing to implement separately, a reverse proxy server is currently the best solution for several reasons. First, a reverse proxy server does not require any modification in the IPv4 services working. Secondly, cache technologies can be applied on the proxy server to keep the number of the requests forwarded to the Web servers extremely low. Because the total volume of contents the reverse proxy server handles is relatively small (usually under several gigabytes), the reverse proxy server can achieve a high hit ratio. Lastly, we can preserve the security of the IPv4 world by setting up the proxy server outside the firewall of the IPv4 organization network. This prevents the IPv6 proxy server from being a backdoor host that breaks the security of the network.

So the vendor feature deployments & topologies are available for web services and are generally whichever deployment option you choose rather simple and easy to add on top of your current IPv4 setup.

## 6.13	DTV

Reasonably recently digital television networks are shifting from the mere transport of native MPEG-2 streams to the provision of IP-based services, either unidirectional or fully interactive. The inclusion of an IPv4/IPv6 stack in a DTV terminal requires configuration such as Host, Gateway and DNS IP addresses are configured either statically or dynamically.   DTV generally has an uncertain history concerning its IP stacks with set-top boxes being delivered with overlay IP stacks & ignoring the OS stack completely & bypassing it through the kernel, which means propriettry IP implementations that are hard to change.  Generally upgrading the firmware it is not possible to the degree required for IPv6 or even the nodes don’t have the capability to upgrade the on-node software even if you could get to it locally for IPv6.  The HFC/DTV industry is coming into alignment with the data networking kingdom however with more IP deployment options & integration with even considerations on removing DOCSIS from the equation altogether.   So we start on dangerous ground as it is especially considering the legacy DTV equipment still running in some cable MSO networks today.

For simplicity reasons the term “Digital Television Network” is assumed to refer to a single DTV downlink conveying a single MPEG-2 (or other services) to a certain coverage area across IP or not dependent.   IPv6 is not even heavily considered within this part of the MSO unless in new and upcoming kit.   This area is around two years behind almost all other MSO technologies for IPv6 if one removes the “new” technologies being developed at the moment such as Horizon.

## 6.14	NMS

NMS systems are fast becoming IPv6 compliant equal to that of IPv4.  There are generally things missing like MIBs within SNMP, Syslog events on NDP DAD, IPFIX/Netflowv9 IPv6 & IPv4 integrated templates & IPv6 DPI.  The NMS industry is huge but although there are great gaps generally we are capable of monitoring our IPv6 network well including in the RF with products like SAA.

Element management & IPSLA for 6PE v4 FECs are still an issue as monitoring an LSP for IPv6 forwarding capability when not being uses is almost impossible with single vendors on the network let alone multiple.  Saying this however one can assume from the present development of most NSM solutions used in the cable industry today we can monitor beyond the bare minimum of IPv6 deployments.

## 6.15	DR & LI

With Data Retention Acts being passed in most of Europe over the last few decades each ISP is required to track potential user activities & keep a long, detailed & reconciled history of traffic on the network.

IPv6 puts new challenges for network administrators in the context of user identification & traffic interception especially with the lack of security either employed or capable within the protocol.  Unlike IPv4, an IPv6 address no longer uniquely identifies a user or PC the IPv6 address can be randomly generated and can keep changing all the time dependent on the network configuration.  PCs with IPv6 stack can also communicate via predefined tunnels over IPv4 infrastructure without the ISP being able to DPI every single flow due to the capacity capabilities of most of the network equipment. So that tunneled traffic mostly bypasses network security implemented via firewalls, monitoring & LI. The solution for IPv6 requires an extended set of monitoring data to be collected from network devices with extended features without effecting neutrality on the network.   This new solution is either a duplicate of the present IPv4 structure or adds netflow in with “smart” logging like within some implementations of DS-lite.

IPv6 DR & LI are well covered in most cases both CMTS deployments & separately on other network devices.  The new deployments are being executed and the governments are being at little less ridged on the requirements during the IPv4 to IPv6 transition phases which helps a great deal.  We can say that there are deployments for both DR & LI on IPv6 but the full extent of the abilities and the differences in the topologies makes IPv6 still in early days for traffic inception & retention on IPv6.

## 6.16	Home Services

Unfortunately here we have the technology that causes us the most problem.  It is the largest part of the end-to-end market, although not owned or deployed by the ISP itself, the home content, applications & devices controlled by the customer provides the strongest challenge to IPv6 deployment worldwide.

So we have to consider here the degree of change within the industry from a device & home OS Application viewpoint.  What will be ready and what will not be ready on IPv6?  But then even this integer means little even if there are 95% of the applications & home devices are IPv6 ready will a marketing team for a large cable ISP really agree that the company ignore connectivity for the five year old IPTV that is only capable of an IPv4 stack?  Or what of the old smartphones that cannot be, or the vendor unwilling to, upgraded to support IPv6?  This is the major issue we face today in the cable ISP industry, the MSO is restricted, not by its own development, but by legacy home devices, even if new now, many do not have IPv6 stacks.

So although D-link and many other home router companies, plus Apple, Blackberry, PVRs and other such vendors & devices types are IPv6 ready or going to be we will always be limited by the legacy for many years to come.

However, with legacy in consideration, the development within the home & handheld device market of IPv6 native & dual stack is actually extremely good.  The only issue here is the 96,000 approved applications (approved & recommended – PC/workstations only – on Windows, Apple & Linux current OS releases.  Not including the 1.3 million approved handheld applications for the mobile market.  Software, especially on the PC side, does not have that great a turnover.  This then provides us with another requirement that falls short of pure IPv6 deployment.

We can then summarize that the home network, customer controlled devices, then restrict us to a full native deployment as a whole.  As we run out of IPv4 addressing to provide connectivity to these IPv4 only devices & applications we require an IPv4 gateway provided at home in some form & then to be able to transport this to the IPv4 service within or beyond our networks.

# 7	IPv6 Standards

In this Clause, the major standards within the industry that effect IPv6 deployment are considered.

While the IETF started working on IPv6 in 1990 limited IPv6 adoption to date in residential environments has been seen. Although governments/institutions have been pushing service providers to adopt IPv6, there has never been a real business driver for service providers to introduce IPv6. There were no new applications that required IPv6 and the cost of introducing IPv6 was perceived too high. All of this has resulted that service providers had very little focus on introducing IPv6 in the residential broadband networks to date. However with the Public IPv4 address exhaustion and the very rapid adoption of smart-phones and M2M devices people should realize that introducing IPv6 should be done as quickly as possible in order to sustain the growth and to provide customers a proper service.

Technically we see that IPv6 is incompatible with IPv4 and has introduced several new concepts that change the present mode of operation of broadband networks:

- IPv6 addressing schemes: unicast: LLA (link local addresses), GUA (Global unicast address) and ULA (Unique local address), multicast addressing, depreciation of broadcast addressing;

- IPv6 header changes Next Header, etc.;

- SLAAC: Stateless auto-configuration for IPv6 address assignment without consuming a DHCP server;

- Default router support using Route Advertisements (RA);

- DHCP PD: DHCP prefix delegation to assign prefixes to Home networks;

- Neighbor discovery (ND), MLD (Multicast Listener Discovery), etc supported through ICMP.

Although there have been many good reasons for these changes, these concepts have implications on how IPv6 can be offered to residential subscribers.

On top IPv6 posses multi-dimensional issues with requirements over which service providers have none/little control. IPv6 support has implication on multiple elements (Figure 4):

- End devices HW/Operating systems

  - PC: MAC OS, Linux, Windows Vista/7 have good IPv6 support while windows XP operates only in dual stack mode and Windows 98 has no IPv6 support

  - IPv6 support on mobile handsets are emerging (Symbian, Iphone, Android, etc)

  - VoIP OS have little IPv6 support to date

  - IPTV OS/STB have little IPv6 support to date

- CPE/RG

  - Support for IPv6 is emerging on xDSL/GPON/ETH/Cable residential GW

- Access nodes

  - DSL/GPON/ETH: most vendors start supporting certain architectures for IPv6.

  - CMTS: most vendors support IPv6

- Aggregation/Edge/Core network elements

  - Most of these devices support IPv6 since many years and have been deployed for a while.

- Fixed (BNG/BRAS), MGW (GGSN/PGW) Edge node

  - BNG/BRAS: Most vendors start supporting IPv6 for PPPoX, IPoE (DHCPv6/DHCPv6 PD), LNS

  - GGSN/PGW: Most vendors have support for R8 and R7 3GPP IPv6 architectures

- Applications

  - End-user application:

    - If they are supported on the proper OS

    - If they use the IPv6 API(s) to support the IPv6 network connectivity

  - Websites:

    - If they support IPv6 addressing/connectivity

  - CDN:

    - If they support IPv6 addressing/connectivity.

Figure 4: IPv6 introduction, the multi-dimensional problem

Some of the implications on these elements are dependent on the network design you choose for introducing IPv6. The following chapter highlights the implications of certain scenarios in a Telco/Cable/Mobile environment. The chapters below are focused on unicast IPv6 connectivity, since most multicast IPTV platforms are not ready yet to move to IPv6 and most IPTV solutions do not require public IPv4 address space.

Here is the list of some of the applicable standards;

| RFC no. | RFC Name | RFC Description (partially generated from the RFC introductions) |
| --- | --- | --- |
| RFC2460 | IPv6 architecture | IP version 6 (IPv6) is a new version of the Internet Protocol, designed as the successor to IP version 4 (IPv4) [RFC-791]. The changes from IPv4 to IPv6 fall primarily into the following categories: Expanded Addressing Capabilities IPv6 increases the IP address size from 32 bits to 128 bits, to support more levels of addressing hierarchy, a much greater number of addressable nodes, and simpler auto-configuration of addresses. The scalability of multicast routing is improved by adding a "scope" field to multicast addresses. And a new type of address called an "anycast address" is defined, used to send a packet to any one of a group of nodes. Header Format Simplification Some IPv4 header fields have been dropped or made optional, to reduce the common-case processing cost of packet handling and to limit the bandwidth cost of the IPv6 header. Improved Support for Extensions and Options Changes in the way IP header options are encoded allows for more efficient forwarding, less stringent limits on the length of options, and greater flexibility for introducing new options in the future. Flow Labeling Capability A new capability is added to enable the labeling of packets belonging to particular traffic "flows" for which the sender requests special handling, such as non-default quality of service or "real-time" service. |
| RFC4193 | ULA | This RFC defines an IPv6 unicast address format that is globally unique and is intended for local communications [IPV6]. These addresses are called Unique Local IPv6 Unicast Addresses and are abbreviated in this document as Local IPv6 addresses. They are not expected to be routable on the global Internet. They are routable inside of a more limited area such as a site. They may also be routed between a limited set of sites. Local IPv6 unicast addresses have the following characteristics: Globally unique prefix (with high probability of uniqueness). Well-known prefix to allow for easy filtering at site boundaries. Allow sites to be combined or privately interconnected without creating any address conflicts or requiring renumbering of interfaces that use these prefixes. Internet Service Provider independent and can be used for communications inside of a site without having any permanent or intermittent Internet connectivity. If accidentally leaked outside of a site via routing or DNS, there is no conflict with any other addresses. In practice, applications may treat these addresses like global scoped addresses. This document defines the format of Local IPv6 addresses, how to allocate them, and usage considerations including routing, site border routers, DNS, application support, VPN usage, and guidelines for how to use for local communication inside a site. |
| RFC5942 | IPv6 subnet model | IPv4 implementations typically associate a netmask with an address when an IPv4 address is assigned to an interface. That netmask together with the IPv4 address designates an on-link prefix. Nodes consider addresses covered by an on-link prefix to be directly attached to the same link as the sending node, i.e., they send traffic for such addresses directly rather than to a router. See Section 3.3.1 of [RFC1122]. Prior to the development of subnetting [RFC0950] and Classless Inter-Domain Routing (CIDR) [RFC4632], an address's netmask could be derived directly from the address simply by determining whether it was a Class A, B, or C address. Today, assigning an address to an interface also requires specifying a netmask to use. In the absence of specifying a specific netmask when assigning an address, some implementations would fall back to deriving the netmask from the class of the address. The behavior of IPv6 as specified in Neighbor Discovery (ND) [RFC4861] is quite different. The on-link determination is separate from the address assignment. A host can have IPv6 addresses without any related on-link prefixes or can have on-link prefixes that are not related to any IPv6 addresses that are assigned to the host. Any assigned address on an interface should initially be considered as having no internal structure as shown in [RFC4291]. In IPv6, by default, a host treats only the link-local prefix as on-link. The reception of a Prefix Information Option (PIO) with the L-bit set [RFC4861] and a non-zero valid lifetime creates (or updates) an entry in the Prefix List. All prefixes on a host's Prefix List (i.e., those prefixes that have not yet timed out) are considered to be on-link by that host. The on-link definition in the Terminology section of [RFC4861], as modified by this document, defines the complete list of cases in which a host considers an address to be on-link. Individual address entries can be expired by the Neighbor Unreachability Detection mechanism. IPv6 packets sent using the Conceptual Sending Algorithm as described in [RFC4861] only trigger address resolution for IPv6 addresses that the sender considers to be on-link. Packets to any other address are sent to a default router. If there is no default router, then the node should send an ICMPv6 Destination Unreachable indication as specified in [RFC4861] -- more details are provided in the "Host Behavior" and "Host Rules" sections of this document. (Note that [RFC4861] changed the behavior when the Default Router List is empty. In the old version of Neighbor Discovery [RFC2461], if the Default Router List is empty, rather than sending the ICMPv6 Destination Unreachable indication, the [RFC2461] node assumed that the destination was on-link.) Note that ND is scoped to a single link. All Neighbor Solicitation (NS) responses are assumed to be sent out the same interface on which the corresponding query was received without using the Conceptual Sending Algorithm. Failure of host implementations to correctly implement the IPv6 subnet model can result in lack of IPv6 connectivity. See the "Observed Incorrect Implementation Behavior" section for details. This document deprecates the last two bullets from the definition of "on-link" in [RFC4861] to address security concerns arising from particular ND implementations. Host behavior is clarified in the "Host Behavior" and "Host Rules" sections. |
| RFC4861 | Neighbor discovery | This specification defines the Neighbor Discovery (ND) protocol for Internet Protocol Version 6 (IPv6). Nodes (hosts and routers) use Neighbor Discovery to determine the link-layer addresses for neighbors known to reside on attached links and to quickly purge cached values that become invalid. Hosts also use Neighbor Discovery to find neighboring routers that are willing to forward packets on their behalf. Finally, nodes use the protocol to actively keep track of which neighbors are reachable and which are not, and to detect changed link-layer addresses. When a router or the path to a router fails, a host actively searches for functioning alternates. Unless specified otherwise (in a document that covers operating IP over a particular link type) this document applies to all link types. However, because ND uses link-layer multicast for some of its services, it is possible that on some link types (e.g., Non-Broadcast Multi-Access (NBMA) links), alternative protocols or mechanisms to implement those services will be specified (in the appropriate document covering the operation of IP over a particular link type). The services described in this document that are not directly dependent on multicast, such as Redirects, Next-hop determination, Neighbor Unreachability Detection, etc., are expected to be provided as specified in this document. The details of how one uses ND on NBMA links are addressed in [IPv6-NBMA]. In addition, [IPv6-3GPP] and[IPv6-CELL] discuss the use of this protocol over some cellular links, which are examples of NBMA links. |
| RFC4862 | SLAAC | This document specifies the steps a host takes in deciding how to autoconfigure its interfaces in IP version 6 (IPv6). The autoconfiguration process includes generating a link-local address, generating global addresses via stateless address autoconfiguration, and the Duplicate Address Detection procedure to verify the uniqueness of the addresses on a link. The IPv6 stateless autoconfiguration mechanism requires no manual configuration of hosts, minimal (if any) configuration of routers, and no additional servers. The stateless mechanism allows a host to generate its own addresses using a combination of locally available information and information advertised by routers. Routers advertise prefixes that identify the subnet(s) associated with a link, while hosts generate an "interface identifier" that uniquely identifies an interface on a subnet. An address is formed by combining the two. In the absence of routers, a host can only generate link-local addresses. However, link-local addresses are sufficient for allowing communication among nodes attached to the same link. The stateless approach is used when a site is not particularly concerned with the exact addresses hosts use, so long as they are unique and properly routable. On the other hand, Dynamic Host Configuration Protocol for IPv6 (DHCPv6) [RFC3315] is used when a site requires tighter control over exact address assignments. Both stateless address autoconfiguration and DHCPv6 may be used simultaneously. IPv6 addresses are leased to an interface for a fixed (possibly infinite) length of time. Each address has an associated lifetime that indicates how long the address is bound to an interface. When a lifetime expires, the binding (and address) become invalid and the address may be reassigned to another interface elsewhere in the Internet. To handle the expiration of address bindings gracefully, an address goes through two distinct phases while assigned to an interface. Initially, an address is "preferred", meaning that its use in arbitrary communication is unrestricted. Later, an address becomes "deprecated" in anticipation that its current interface binding will become invalid. While an address is in a deprecated state, its use is discouraged, but not strictly forbidden. New communication (e.g., the opening of a new TCP connection) should use a preferred address when possible. A deprecated address should be used only by applications that have been using it and would have difficulty switching to another address without a service disruption. |
| RFC3971 | SEND | IPv6 defines the Neighbor Discovery Protocol (NDP) in RFCs 2461and 2462. Nodes on the same link use NDP to discover each other's presence and link-layer addresses, to find routers, and to maintain reachability information about the paths to active neighbors. NDP is used by both hosts and routers. Its functions include Neighbor Discovery (ND), Router Discovery (RD), Address Autoconfiguration, Address Resolution, Neighbor Unreachability Detection (NUD), Duplicate Address Detection (DAD), and Redirection. The original NDP specifications called for the use of IPsec to protect NDP messages. However, the RFCs do not give detailed instructions for using IPsec to do this. In this particular application, IPsec can only be used with a manual configuration of security associations, due to bootstrapping problems in using IKE. Furthermore, the number of manually configured security associations needed for protecting NDP can be very large, making that approach impractical for most purposes. The SEND protocol is designed to counter the threats to NDP. These threats are described in detail in [22]. SEND is applicable in environments where physical security on the link is not assured (such as over wireless) and attacks on NDP are a concern. This document is organized as follows. Sections 2 and 3 define some terminology and present a brief review of NDP, respectively. Section 4 describes the overall approach to securing NDP. This approach involves the use of new NDP options to carry public key - based signatures. A zero-configuration mechanism is used for showing address ownership on individual nodes; routers are certified by a trust anchor [7]. The formats, procedures, and cryptographic mechanisms for the zero-configuration mechanism are described in a related specification [11]. The required new NDP options are discussed in Section 5. Section 6 describes the mechanism for distributing certification paths to establish an authorization delegation chain to a trust anchor. Finally, Section 8 discusses the co-existence of secured and unsecured NDP on the same link, and Section 9 discusses security considerations for SEcure Neighbor Discovery (SEND). The use of identity certificates provisioned on end hosts for authorizing address use is out of the scope for this document, as is the security of NDP when the entity defending an address is not the same as the entity claiming that address (also known as "proxy ND"). These are extensions of SEND that may be treated in separate documents, should the need arise. |
| RFC4443 | ICMPv6 | The Internet Protocol version 6 (IPv6) uses the Internet Control Message Protocol (ICMP) as defined for IPv4 [RFC-792], with a number of changes. The resulting protocol is called ICMPv6 and has an IPv6 Next Header value of 58. This document describes the format of a set of control messages used in ICMPv6. It does not describe the procedures for using these messages to achieve functions like Path MTU discovery; these procedures are described in other documents (e.g., [PMTU]). Other documents may also introduce additional ICMPv6 message types, such as Neighbor Discovery messages [IPv6-DISC], subject to the general rules for ICMPv6 messages given in Section 2 of this document. Terminology defined in the IPv6 specification [IPv6] and the IPv6 Routing and Addressing specification [IPv6-ADDR] applies to this document as well. |
| RFC4605 | IGMP/MLD proxy | This document applies spanning tree multicast routing [MCAST] to an Internet Group Management Protocol (IGMP) or Multicast Listener Discovery (MLD)-only environment. The topology is limited to a tree, since we specify no protocol to build a spanning tree over a more complex topology. The root of the tree is assumed to be connected to a wider multicast infrastructure. In a simple tree topology, it is not necessary to run a multicast routing protocol. It is sufficient to learn and proxy group membership information and simply forward multicast packets based upon that information. One typical example of such a tree topology can be found on an edge aggregation box such as a Digital Subscriber Line Access Multiplexer (DSLAM). In most deployment scenarios, an edge box has only one connection to the core network side and has many connections to the customer side. Using IGMP/MLD-based forwarding to replicate multicast traffic on devices such as the edge boxes can greatly simplify the design and implementation of those devices. By not supporting more complicated multicast routing protocols such as Protocol Independent Multicast (PIM) or Distance Vector Multicast Routing Protocol (DVMRP), it reduces not only the cost of the devices but also the operational overhead. Another advantage is that it makes the proxy devices independent of the multicast routing protocol used by the core network routers. Hence, proxy devices can be easily deployed in any multicast network. Robustness in an edge box is usually achieved by using a hot spare connection to the core network. When the first connection fails, the edge box fails over to the second connection. IGMP/MLD-based forwarding can benefit from such a mechanism and use the spare connection for its redundant or backup connection to multicast routers. When an edge box fails over to the second connection, the proxy upstream connection can also be updated to the new connection. |
| RFC4632 | CIDR | What is now known as the Internet started as a research project in the 1970s to design and develop a set of protocols that could be used with many different network technologies to provide a seamless, end- to-end facility for interconnecting a diverse set of end systems. When it was determined how the 32-bit address space would be used, certain assumptions were made about the number of organizations to be connected, the number of end systems per organization, and total number of end systems on the network. The end result was the establishment (see [RFC791]) of three classes of networks: Class A (most significant address bits '00'), with 128 possible networks each and 16777216 end systems (minus special bit values reserved for network/broadcast addresses); Class B (MSB '10'), with 16384 possible networks each with 65536 end systems (less reserved values); and Class C (MSB '110'), and 2097152 possible networks each and 254 end systems (256 bit combinations minus the reserved all-zeros and all- ones patterns). The set of addresses with MSB '111' was reserved for future use; parts of this were eventually defined (MSB '1110') for use with IPv4 multicast and parts are still reserved as of the writing of this document. In the late 1980s, the expansion and commercialization of the former research network resulted in the connection of many new organizations to the rapidly growing Internet, and each new organization required an address assignment according to the Class A/B/C addressing plan. As demand for new network numbers (particularly in the Class B space) took what appeared to be an exponential growth rate, some members of the operations and engineering community started to have concerns over the long-term scaling properties of the class A/B/C system and began thinking about how to modify network number assignment policy and routing protocols to accommodate the growth. In November, 1991, the Internet Engineering Task Force (IETF) created the ROAD (Routing and Addressing) group to examine the situation. This group met in January 1992 and identified three major problems: Exhaustion of the Class B network address space. One fundamental cause of this problem is the lack of a network class of a size that is appropriate for mid-sized organization. Class C, with a maximum of 254 host addresses, is too small, whereas Class B, which allows up to 65534 host addresses, is too large for most organizations but was the best fit available for use with subnetting. Growth of routing tables in Internet routers beyond the ability of current software, hardware, and people to effectively manage. Eventual exhaustion of the 32-bit IPv4 address space. It was clear that then-current rates of Internet growth would cause the first two problems to become critical sometime between 1993 and 1995. Work already in progress on topological assignment of addressing for Connectionless Network Service (CLNS), which was presented to the community at the Boulder IETF in December of 1990, led to thoughts on how to re-structure the 32-bit IPv4 address space to increase its lifespan. Work in the ROAD group followed and eventually resulted in the publication of [RFC1338], and later, [RFC1519]. The design and deployment of CIDR was intended to solve these problems by providing a mechanism to slow the growth of global routing tables and to reduce the rate of consumption of IPv4 address space. It did not and does not attempt to solve the third problem, which is of a more long-term nature; instead, it endeavors to ease enough of the short- to mid-term difficulties to allow the Internet to continue to function efficiently while progress is made on a longer-term solution. More historical background on this effort and on the ROAD group may be found in [RFC1380] and at [LWRD]. Classless Addressing as a Solution The solution that the community created was to deprecate the Class A/B/C network address assignment system in favor of using "classless", hierarchical blocks of IP addresses (referred to as prefixes). The assignment of prefixes is intended to roughly follow the underlying Internet topology so that aggregation can be used to facilitate scaling of the global routing system. One implication of this strategy is that prefix assignment and aggregation is generally done according to provider-subscriber relationships, since that is how the Internet topology is determined. When originally proposed in [RFC1338] and [RFC1519], this addressing plan was intended to be a relatively short-term response, lasting approximately three to five years, during which a more permanent addressing and routing architecture would be designed and implemented. As can be inferred from the dates on the original documents, CIDR has far outlasted its anticipated lifespan and has become the mid-term solution to the problems described above. Note that in the following text we describe the current policies and procedures that have been put in place to implement the allocation architecture discussed here. This description is not intended to be interpreted as direction to IANA. Coupled with address management strategies implemented by the Regional Internet Registries (see [NRO] for details), the deployment of CIDR-style addressing has also reduced the rate at which IPv4 address space has been consumed, thus providing short- to medium-term relief to problem #3, described above. Note that, as defined, this plan neither requires nor assumes the re-assignment of those parts of the legacy "Class C" space that are not amenable to aggregation (sometimes called "the swamp"). Doing so would somewhat reduce routing table sizes (current estimate is that "the swamp" contains approximately 15,000 entries), though at a significant renumbering cost. Similarly, there is no hard requirement that any end site renumber when changing transit service provider, but end sites are encouraged do so to eliminate the need for explicit advertisement of their prefixes into the global routing system. |
| RFC5308 | ISIS routing IPv6 | IS-IS is an extendible intra-domain routing protocol. Each router in the routing domain issues an Link State Protocol Data Unit (LSP) that contains information pertaining to that router. The LSP contains typed variable-length data, often referred to as TLVs (type-length- values). We extend the protocol with two new TLVs to carry information required to perform IPv6 routing. In [RFC1195], a method is described to route both OSI and IPv4. We utilize this same method with some minor changes to allow for IPv6. To do so, we must define two new TLVs, namely "IPv6 Reachability" and "IPv6 Interface Address", and a new IPv6 protocol identifier. In our new TLVs, we utilize the extended metrics and up/down semantics of [RFC5305]. |
| RFC2740 | OSPFv3 | This document describes the modifications to OSPF to support version 6 of the Internet Protocol (IPv6). The fundamental mechanisms of OSPF (flooding, DR election, area support, SPF calculations, etc.) remain unchanged. However, some changes have been necessary, either due to changes in protocol semantics between IPv4 and IPv6, or simply to handle the increased address size of IPv6. This document is organized as follows. Section 2 describes the differences between OSPF for IPv4 and OSPF for IPv6 in detail. Section 3 provides implementation details for the changes. Appendix A gives the OSPF for IPv6 packet and LSA formats. Appendix B lists the OSPF architectural constants. Appendix C describes configuration parameters. 1.1. Terminology This document attempts to use terms from both the OSPF for IPv4 specification ([Ref1]) and the IPv6 protocol specifications ([Ref14]). This has produced a mixed result. Most of the terms used both by OSPF and IPv6 have roughly the same meaning (e.g., interfaces). However, there are a few conflicts. IPv6 uses "link" similarly to IPv4 OSPF's "subnet" or "network". In this case, we have chosen to use IPv6's "link" terminology. "Link" replaces OSPF's "subnet" and "network" in most places in this document, although OSPF's Network-LSA remains unchanged (and possibly unfortunately, a new Link-LSA has also been created). The names of some of the OSPF LSAs have also changed. See Section 2.8 for details. |
| RFC4798 | 6PE | There are several approaches for providing IPv6 connectivity over an MPLS core network [RFC4029] including (i) requiring that MPLS networks support setting up IPv6-signaled Label Switched Paths (LSPs) and establish IPv6 connectivity by using those LSPs, (ii) use configured tunneling over IPv4-signaled LSPs, or (iii) use the IPv6 Provider Edge (6PE) approach defined in this document. The 6PE approach is required as an alternative to the use of standard tunnels. It provides a solution for an MPLS environment where all tunnels are established dynamically, thereby addressing environments where the effort to configure and maintain explicitly configured tunnels is not acceptable. This document specifies operations of the 6PE approach for interconnection of IPv6 islands over an IPv4 MPLS cloud. The approach requires that the edge routers connected to IPv6 islands be Dual Stack Multiprotocol-BGP-speaking routers [RFC4760], while the core routers are only required to run IPv4 MPLS. The approach uses MP-BGP over IPv4, relies on identification of the 6PE routers by their IPv4 address, and uses IPv4-signaled MPLS LSPs that do not require any explicit tunnel configuration. Throughout this document, the terminology of [RFC2460] and [RFC4364] is used. In this document an 'IPv6 island' is a network running native IPv6 as per [RFC2460]. A typical example of an IPv6 island would be a customer's IPv6 site connected via its IPv6 Customer Edge (CE) router to one (or more) Dual Stack Provider Edge router(s) of a Service Provider. These IPv6 Provider Edge routers (6PE) are connected to an IPv4 MPLS core network. +--------+ ¦site A CE---+ +-----------------+ +--------+ ¦ ¦ ¦ +--------+ 6PE-+ IPv4 MPLS core +-6PE--CE site C ¦ +--------+ ¦ ¦ ¦ +--------+ ¦site B CE---+ +-----------------+ +--------+ IPv6 islands IPv4 cloud IPv6 island <-------------><---------------------><--------------> Figure 1 The interconnection method described in this document typically applies to an Internet Service Provider (ISP) that has an IPv4 MPLS network, that is familiar with BGP (possibly already offering BGP/MPLS VPN services), and that wants to offer IPv6 services to some of its customers. However, the ISP may not (yet) want to upgrade its network core to IPv6, nor use only IPv6-over-IPv4 tunneling. With the 6PE approach described here, the provider only has to upgrade some Provider Edge (PE) routers to Dual Stack operations so that they behave as 6PE routers (and route reflectors if those are used for the exchange of IPv6 reachability among 6PE routers) while leaving the IPv4 MPLS core routers untouched. These 6PE routers provide connectivity to IPv6 islands. They may also provide other services simultaneously (IPv4 connectivity, IPv4 L3VPN services, L2VPN services, etc.). Also with the 6PE approach, no tunnels need to be explicitly configured, and no IPv4 headers need to be inserted in front of the IPv6 packets between the customer and provider edge. The ISP obtains IPv6 connectivity to its peers and upstreams using means outside of the scope of this document, and its 6PE routers readvertise it over the IPv4 MPLS core with MP-BGP. The interface between the edge router of the IPv6 island (Customer Edge (CE) router) and the 6PE router is a native IPv6 interface which can be physical or logical. A routing protocol (IGP or EGP) may run between the CE router and the 6PE router for the distribution of IPv6 reachability information. Alternatively, static routes and/or a default route may be used on the 6PE router and the CE router to control reachability. An IPv6 island may connect to the provider network over more than one interface. The 6PE approach described in this document can be used for customers that already have an IPv4 service from the network provider and additionally require an IPv6 service, as well as for customers that require only IPv6 connectivity. The scenario is also described in [RFC4029]. Note that the 6PE approach specified in this document provides global IPv6 reachability. Support of IPv6 VPNs is not within the scope of this document and is addressed in [RFC4659]. Deployment of the 6PE approach over an existing IPv4 MPLS cloud does not require an introduction of new mechanisms in the core (other than potentially those described at the end of Section 3 for dealing with dynamic MTU discovery). Configuration and operations of the 6PE approach have a lot of similarities with the configuration and operations of an IPv4 VPN service ([RFC4364]) or IPv6 VPN service ([RFC4659]) over an IPv4 MPLS core because they all use MP-BGP to distribute non-IPv4 reachability information for transport over an IPv4 MPLS Core. However, the configuration and operations of the 6PE approach is somewhat simpler, since it does not involve all the VPN concepts such as Virtual Routing and Forwarding (VRFs) tables. |
| RFC4659 | 6VPE | This document describes a method by which a Service Provider may useits packet-switched backbone to provide Virtual Private Network services for its IPv6 customers. This method reuses, and extends where necessary, the "BGP/MPLS IP VPN" method [BGP/MPLS-VPN] for support of IPv6. In particular, this method uses the same "peer model" as [BGP/MPLS-VPN], in which the customers' edge routers ("CE routers") send their IPv6 routes to the Service Provider's edge routers ("PE routers"). BGP ("Border Gateway Protocol", [BGP, BGP-MP]) is then used by the Service Provider to exchange the routes of a particular IPv6 VPN among the PE routers that are attached to that IPv6 VPN. Eventually, the PE routers distribute, to the CE routers in a particular VPN, the IPv6 routes from other CE routers in that VPN. As with IPv4 VPNs, a key characteristic of this "peer model" is that the (IPv6) CE routers within an (IPv6) VPN do not peer with each other; there is no "overlay" visible to the (IPv6) VPN's routing algorithm. This document adopts the definitions, acronyms, and mechanisms described in [BGP/MPLS-VPN]. Unless it is stated otherwise, the mechanisms of [BGP/MPLS-VPN] apply and will not be re-described here. A VPN is said to be an IPv6 VPN when each site of this VPN is IPv6 capable and is natively connected over an IPv6 interface or sub- interface to the Service Provider (SP) backbone via a Provider Edge device (PE). A site may be both IPv4 capable and IPv6 capable. The logical interface on which packets arrive at the PE may determine the IP version. Alternatively, the same logical interface may be used for both IPv4 and IPv6, in which case a per-packet lookup at the Version field of the IP packet header determines the IP version. This document only concerns itself with handling of IPv6 communication between IPv6 hosts located on IPv6-capable sites. Handling of IPv4 communication between IPv4 hosts located on IPv4- capable sites is outside the scope of this document and is covered in [BGP/MPLS-VPN]. Communication between an IPv4 host located in an IPv4- capable site and an IPv6 host located in an IPv6-capable site is outside the scope of this document. In a similar manner to how IPv4 VPN routes are distributed in [BGP/MPLS-VPN], BGP and its extensions are used to distribute routes from an IPv6 VPN site to all the other PE routers connected to a site of the same IPv6 VPN. PEs use "VPN Routing and Forwarding tables" (VRFs) to maintain the reachability information and forwarding information of each IPv6 VPN separately. As is done for IPv4 VPNs [BGP/MPLS-VPN], we allow each IPv6 VPN to have its own IPv6 address space, which means that a given address may denote different systems in different VPNs. This is achieved via a new address family, the VPN-IPv6 Address Family, in a fashion similar to that of the VPN-IPv4 address family, defined in [BGP/MPLS-VPN], which prepends a Route Distinguisher to the IP address. In addition to its operation over MPLS Label Switched Paths (LSPs), the IPv4 BGP/MPLS VPN solution has been extended to allow operation over other tunneling techniques, including GRE tunnels, IP-in-IP tunnels [2547-GRE/IP], L2TPv3 tunnels [MPLS-in-L2TPv3], and IPsec protected tunnels [2547-IPsec]. In a similar manner, this document allows support of an IPv6 VPN service over MPLS LSPs, as well as over other tunneling techniques. This document allows support for an IPv6 VPN service over an IPv4 backbone, as well as over an IPv6 backbone. The IPv6 VPN service supported is identical in both cases. The IPv6 VPN solution defined in this document offers the following benefits: From both the Service Provider perspective and the customer perspective, the VPN service that can be supported for IPv6 sites is identical to the one that can be supported for IPv4 sites. From the Service Provider perspective, operations of the IPv6 VPN service require the exact same skills, procedures, and mechanisms as those for the IPv4 VPN service. Where both IPv4 VPNs and IPv6 VPN services are supported over an IPv4 core, the same single set of MP-BGP peering relationships and the same single PE-PE tunnel mesh MAY be used for both. The IPv6 VPN service is independent of whether the core runs IPv4 or IPv6. This is so that the IPv6 VPN service supported before and after a migration of the core from IPv4 to IPv6 is undistinguishable to the VPN customer. Note that supporting IPv4 VPN services over an IPv6 core is not covered by this document. The VPN-IPv6 Address Family The BGP Multiprotocol Extensions [BGP-MP] allow BGP to carry routes from multiple "address families". We introduce the notion of the "VPN-IPv6 address family", which is similar to the VPN-IPv4 address family introduced in [BGP/MPLS-VPN]. A VPN-IPv6 address is a 24-octet quantity, beginning with an 8-octet "Route Distinguisher" (RD) and ending with a 16-octet IPv6 address. The purpose of the RD is solely to allow one to create distinct routes to a common IPv6 address prefix, which is similar to the purpose of the RD defined in [BGP/MPLS-VPN]. In the same way as it is possible per [BGP/MPLS-VPN], the RD can be used to create multiple different routes to the very same system. This can be achieved by creating two different VPN-IPv6 routes that have the same IPv6 part but different RDs. This allows the provider's BGP to install multiple different routes to the same system and allows policy to be used to decide which packets use which route. |
| RFC3315 | DHCPv6 | This document describes DHCP for IPv6 (DHCP), a client/server protocol that provides managed configuration of devices. DHCP can provide a device with addresses assigned by a DHCP server and other configuration information, which are carried in options. DHCP can be extended through the definition of new options to carry configuration information not specified in this document. DHCP is the "stateful address autoconfiguration protocol" and the "stateful autoconfiguration protocol" referred to in "IPv6 Stateless Address Autoconfiguration" [17]. The operational models and relevant configuration information for DHCPv4 [18][19] and DHCPv6 are sufficiently different that integration between the two services is not included in this document. If there is sufficient interest and demand, integration can be specified in a document that extends DHCPv6 to carry IPv4 addresses and configuration information. The remainder of this introduction summarizes DHCP, explaining the message exchange mechanisms and example message flows. The message flows in sections 1.2 and 1.3 are intended as illustrations of DHCP operation rather than an exhaustive list of all possible client-server interactions. Sections 17, 18, and 19 explain client and server operation in detail. Protocols and Addressing Clients and servers exchange DHCP messages using UDP [15]. The client uses a link-local address or addresses determined through other mechanisms for transmitting and receiving DHCP messages. DHCP servers receive messages from clients using a reserved, link-scoped multicast address. A DHCP client transmits most messages to this reserved multicast address, so that the client need not be configured with the address or addresses of DHCP servers. To allow a DHCP client to send a message to a DHCP server that is not attached to the same link, a DHCP relay agent on the client's link will relay messages between the client and server. The operation of the relay agent is transparent to the client and the discussion of message exchanges in the remainder of this section will omit the description of message relaying by relay agents. Once the client has determined the address of a server, it may under some circumstances send messages directly to the server using unicast. |
| RFC3633 | DHCPv6 prefix delegation | This document describes new options for Dynamic Host Configuration Protocol (DHCP) that provide a mechanism for the delegation of IPv6 prefixes [1]. Through these options, a delegating router can delegate prefixes to authorized requesting routers. The prefix delegation mechanism described in this document is intended for simple delegation of prefixes from a delegating router to requesting routers. It is appropriate for situations in which the delegating router does not have knowledge about the topology of the networks to which the requesting router is attached, and the delegating router does not require other information aside from the identity of the requesting router to choose a prefix for delegation. For example, these options would be used by a service provider to assign a prefix to a Customer Premise Equipment (CPE) device acting as a router between the subscriber's internal network and the service provider's core network. Many applications expect stable addresses. Even though this mechanism makes automatic renumbering easier, it is expected that prefixes have a long lifespan. During renumbering it is expected that the old and the new prefix co-exist for some time. The design of this prefix delegation mechanism meets the requirements for prefix delegation in Requirements for IPv6 prefix delegation [6]. Note that this use of DHCP is not bound to the assignment of IP addresses or other configuration information to hosts, and that no mechanism is currently available to communicate delegated prefixes to a DHCP server that serves such a function. This may be an item of future work, should usage warrant. DHCPv6 specification dependency This document describes new DHCPv6 options for IPv6 prefix delegation. This document should be read in conjunction with the DHCPv6 specification, RFC 3315 [2], for a complete specification of the Prefix Delegation options and mechanism. Definitions for terms and acronyms not specifically defined in this document are defined in RFC 3315. |
| RFC3646 | DNS for IPv6 | The DNS Recursive Name Server option provides a list of one or more IPv6 addresses of DNS recursive name servers to which a client's DNS resolver MAY send DNS queries [1]. The DNS servers are listed in the order of preference for use by the client resolver. The format of the DNS Recursive Name Server option is: 0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ OPTION_DNS_SERVERS ¦ option-len ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ¦ ¦ DNS-recursive-name-server (IPv6 address) ¦ ¦ ¦ ¦ ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ¦ ¦ DNS-recursive-name-server (IPv6 address) ¦ ¦ ¦ ¦ ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ... ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ option-code: OPTION_DNS_SERVERS (23) option-len: Length of the list of DNS recursive name servers in octets; must be a multiple of 16 DNS-recursive-name-server: IPv6 address of DNS recursive name server 4. Domain Search List option The Domain Search List option specifies the domain search list the client is to use when resolving hostnames with DNS. This option does not apply to other name resolution mechanisms. The format of the Domain Search List option is: 0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ OPTION_DOMAIN_LIST ¦ option-len ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ searchlist ¦ ¦ ... ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ option-code: OPTION_DOMAIN_LIST (24) option-len: Length of the 'searchlist' field in octets searchlist: The specification of the list of domain names in the Domain Search List The list of domain names in the 'searchlist' MUST be encoded as specified in section "Representation and use of domain names" of RFC 3315. 5. Appearance of these options The DNS Recursive Name Server option MUST NOT appear in any other than the following messages: Solicit, Advertise, Request, Renew, Rebind, Information-Request, and Reply. The Domain Search List option MUST NOT appear in any other than the following messages: Solicit, Advertise, Request, Renew, Rebind, Information-Request, and Reply. 6. Security Considerations The DNS Recursive Name Server option may be used by an intruder DHCP server to cause DHCP clients to send DNS queries to an intruder DNS recursive name server. The results of these misdirected DNS queries may be used to spoof DNS names. To avoid attacks through the DNS Recursive Name Server option, the DHCP client SHOULD require DHCP authentication (see section "Authentication of DHCP messages" in RFC 3315) before installing a list of DNS recursive name servers obtained through authenticated DHCP. The Domain Search List option may be used by an intruder DHCP server to cause DHCP clients to search through invalid domains for incompletely specified domain names. The results of these |
| RFC3736 | stateless DHCPv6 | This document assumes that a node using stateless DHCP configuration is not using DHCP for address assignment, and that a node has determined at least a link-local address as described in section 5.3 of RFC 2461 [4]. To obtain configuration parameters through stateless DHCP, a node uses the DHCP Information-request message. DHCP servers respond to the node's message with a Reply message that carries configuration parameters for the node. The Reply message from the server can carry configuration information, such as a list of DNS recursive name servers [3] and SIP servers [5]. This document does not apply to the function of DHCP relay agents as described in RFC 3315. A network element can provide both DHCP server and DHCP relay service. For example, a network element can provide stateless DHCP service to hosts requesting stateless DHCP service, while relaying messages from hosts requesting address assignment through DHCP to another DHCP server. 4. Basic Requirements for Implementation of DHCP Several sections of the DHCP specification provide background information or define parts of the specification that are common to all implementations: 1-4: give an introduction to DHCP and an overview of DHCP message flows 5: defines constants used throughout the protocol specification 6, 7: illustrate the format of DHCP messages 8: describes the representation of Domain Names 9: defines the "DHCP unique identifier" (DUID) 13-16: describe DHCP message transmission, retransmission, and validation 21: describes authentication for DHCP 5. Implementation of Stateless DHCP The client indicates that it is requesting configuration information by sending an Information-request message that includes an Option Request option specifying the options that it wishes to receive from the DHCP server. For example, if the client is attempting to obtain a list of DNS recursive name servers, it identifies the DNS Recursive Name Server option in the Information-request message. The server determines the appropriate configuration parameters for the client based on its configuration policies and responds with a Reply message containing the requested parameters. In this example, the server would respond with DNS configuration parameters. As described in section 18.1.5 of RFC 3315, a node may include a Client Identifier option in the Information-request message to identify itself to a server, because the server administrator may want to customize the server's response to each node, based on the node's identity. RFC 3315 does not define any mechanisms through which the time at which a host uses an Information-request message to obtain updated configuration parameters can be controlled. The DHC WG has undertaken the development of such a mechanism or mechanisms which will be published as Standards-track RFC(s). RFC 3315 also does not provide any guidance about when a host might use an Information-request message to obtain updated configuration parameters when the host has moved to a new link. The DHC WG is reviewing a related document, "Detection of Network Attachment (DNA) in IPv4" [8], which describes how a host using IPv4 can determine when to use DHCPv4. Either the DHC WG or a WG formed from the DNA BOF will undertake development of a similar document for IPv6. |
| RFC4191 | default router preferences | Neighbor Discovery [RFC2461] specifies a conceptual model for hosts that includes a Default Router List and a Prefix List. Hosts send Router Solicitation messages and receive Router Advertisement messages from routers. Hosts populate their Default Router List and Prefix List based on information in the Router Advertisement messages. A conceptual sending algorithm uses the Prefix List to determine if a destination address is on-link and uses the Default Router List to select a router for off-link destinations. In some network topologies where the host has multiple routers on its Default Router List, the choice of router for an off-link destination is important. In some situations, one router may provide much better performance than another for a destination. In other situations, choosing the wrong router may result in a failure to communicate. (Section 5 gives specific examples of these scenarios.) This document describes an optional extension to Neighbor Discovery Router Advertisement messages for communicating default router preferences and more-specific routes from routers to hosts. This improves the ability of hosts to pick an appropriate router for an off-link destination. Note that since these procedures are applicable to hosts only, the forwarding algorithm used by the routers (including hosts with enabled IP forwarding) is not affected. Neighbor Discovery provides a Redirect message that routers can use to correct a host's choice of router. A router can send a Redirect message to a host, telling it to use a different router for a specific destination. However, the Redirect functionality is limited to a single link. A router on one link cannot redirect a host to a router on another link. Hence, Redirect messages do not help multi- homed (through multiple interfaces) hosts select an appropriate router. Multi-homed hosts are an increasingly important scenario, especially with IPv6. In addition to a wired network connection, like Ethernet, hosts may have one or more wireless connections, like 802.11 or Bluetooth. In addition to physical network connections, hosts may have virtual or tunnel network connections. For example, in addition to a direct connection to the public Internet, a host may have a tunnel into a private corporate network. Some IPv6 transition scenarios can add additional tunnels. For example, hosts may have 6to4 [RFC3056] or configured tunnel [RFC2893] network connections. This document requires that the preference values and specific routes advertised to hosts require explicit administrative configuration. They are not automatically derived from routing tables. In particular, the preference values are not routing metrics and it is not recommended that routers "dump out" their entire routing tables to hosts. We use Router Advertisement messages, instead of some other protocol like RIP [RFC2080], because Router Advertisements are an existing standard, stable protocol for router-to-host communication. Piggybacking this information on existing message traffic from routers to hosts reduces network overhead. Neighbor Discovery shares with Multicast Listener Discovery the property that they both define host-to-router interactions, while shielding the host from having to participate in more general router-to-router interactions. In addition, RIP is unsuitable because it does not carry route lifetimes so it requires frequent message traffic with greater processing overheads. The mechanisms specified here are backwards-compatible, so that hosts that do not implement them continue to function as well as they did previously. |
| RFC4075 | sNTP | The Simple Network Time Protocol servers option provides a list of one or more IPv6 addresses of SNTP [3] servers available to the client for synchronization. The clients use these SNTP servers to synchronize their system time to that of the standard time servers. Clients MUST treat the list of SNTP servers as an ordered list. The server MAY list the SNTP servers in decreasing order of preference. The option defined in this document can only be used to configure information about SNTP servers that can be reached using IPv6. The DHCP option to configure information about IPv4 SNTP servers can be found in RFC 2132 [4]. Mechanisms for configuring IPv4/IPv6 dual- stack applications are being considered, but are not specified in this document. The format of the Simple Network Time Protocol servers option is as shown below: 0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ OPTION_SNTP_SERVERS ¦ option-len ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ¦ ¦ SNTP server (IPv6 address) ¦ ¦ ¦ ¦ ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ¦ ¦ SNTP server (IPv6 address) ¦ ¦ ¦ ¦ ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ ... ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ option-code: OPTION_SNTP_SERVERS (31) option-len: Length of the 'SNTP server' fields, in octets; it must be a multiple of 16 SNTP server: IPv6 address of SNTP server 5. Appearance of This Option The SNTP servers option MUST NOT appear in messages other than the following: Solicit, Advertise, Request, Renew, Rebind, Information- Request, and Reply. If this option appears in messages other than those specified above, the receiver SHOULD ignore it. The option number for this option MAY appear in the Option Request Option [1] in the following messages: Solicit, Request, Renew, Rebind, Information-Request, and Reconfigure. If this option number appears in the Option Request Option in messages other than those specified above, the receiver SHOULD ignore it. |
| RFC3596 | DNS IPv6 | Current support for the storage of Internet addresses in the Domain Name System (DNS) [1,2] cannot easily be extended to support IPv6 addresses [3] since applications assume that address queries return 32-bit IPv4 addresses only. To support the storage of IPv6 addresses in the DNS, this document defines the following extensions: o A resource record type is defined to map a domain name to an IPv6 address. o A domain is defined to support lookups based on address. o Existing queries that perform additional section processing to locate IPv4 addresses are redefined to perform additional section processing on both IPv4 and IPv6 addresses. The changes are designed to be compatible with existing software. The existing support for IPv4 addresses is retained. Transition issues related to the co-existence of both IPv4 and IPv6 addresses in the DNS are discussed in [4]. The IP protocol version used for querying resource records is independent of the protocol version of the resource records; e.g., IPv4 transport can be used to query IPv6 records and vice versa. This document combines RFC 1886 [5] and changes to RFC 1886 made by RFC 3152 [6], obsoleting both. Changes mainly consist in replacing the IP6.INT domain by IP6.ARPA as defined in RFC 3152. 2. New resource record definition and domain A record type is defined to store a host's IPv6 address. A host that has more than one IPv6 address must have more than one such record. 2.1 AAAA record type The AAAA resource record type is a record specific to the Internet class that stores a single IPv6 address. The IANA assigned value of the type is 28 (decimal). 2.2 AAAA data format A 128 bit IPv6 address is encoded in the data portion of an AAAA resource record in network byte order (high-order byte first). 2.3 AAAA query An AAAA query for a specified domain name in the Internet class returns all associated AAAA resource records in the answer section of a response. A type AAAA query does not trigger additional section processing. 2.4 Textual format of AAAA records The textual representation of the data portion of the AAAA resource record used in a master database file is the textual representation of an IPv6 address as defined in [3]. 2.5 IP6.ARPA Domain A special domain is defined to look up a record given an IPv6 address. The intent of this domain is to provide a way of mapping an IPv6 address to a host name, although it may be used for other purposes as well. The domain is rooted at IP6.ARPA. An IPv6 address is represented as a name in the IP6.ARPA domain by a sequence of nibbles separated by dots with the suffix ".IP6.ARPA". The sequence of nibbles is encoded in reverse order, i.e., the low-order nibble is encoded first, followed by the next low-order nibble and so on. Each nibble is represented by a hexadecimal digit. For example, the reverse lookup domain name corresponding to the address 4321:0:1:2:3:4:567:89ab would be b.a.9.8.7.6.5.0.4.0.0.0.3.0.0.0.2.0.0.0.1.0.0.0.0.0.0.0.1.2.3.4.IP6. ARPA. 3. Modifications to existing query types All existing query types that perform type A additional section processing, i.e., name server (NS), location of services (SRV) and mail exchange (MX) query types, must be redefined to perform both type A and type AAAA additional section processing. These definitions mean that a name server must add any relevant IPv4 addresses and any relevant IPv6 addresses available locally to the additional section of a response when processing any one of the above queries. |
| RFC6434 | IPv6 node requirements | This document defines common functionality required from both IPv6 hosts and routers. Many IPv6 nodes will implement optional or additional features, but this document collects and summarizes requirements from other published Standards Track documents in one place. This document tries to avoid discussion of protocol details and references RFCs for this purpose. This document is intended to be an applicability statement and to provide guidance as to which IPv6 specifications should be implemented in the general case and which specifications may be of interest to specific deployment scenarios. This document does not update any individual protocol document RFCs. Although this document points to different specifications, it should be noted that in many cases, the granularity of a particular requirement will be smaller than a single specification, as many specifications define multiple, independent pieces, some of which may not be mandatory. In addition, most specifications define both client and server behavior in the same specification, while many implementations will be focused on only one of those roles. This document defines a minimal level of requirement needed for a device to provide useful internet service and considers a broad range of device types and deployment scenarios. Because of the wide range of deployment scenarios, the minimal requirements specified in this document may not be sufficient for all deployment scenarios. It is perfectly reasonable (and indeed expected) for other profiles to define additional or stricter requirements appropriate for specific usage and deployment environments. For example, this document does not mandate that all clients support DHCP, but some deployment scenarios may deem it appropriate to make such a requirement. For example, government agencies in the USA have defined profiles for specialized requirements for IPv6 in target environments (see [DODv6] and [USGv6]). As it is not always possible for an implementer to know the exact usage of IPv6 in a node, an overriding requirement for IPv6 nodes is that they should adhere to Jon Postel's Robustness Principle: "Be conservative in what you do, be liberal in what you accept from others" [RFC0793]. 1.1. Scope of This Document IPv6 covers many specifications. It is intended that IPv6 will be deployed in many different situations and environments. Therefore, it is important to develop requirements for IPv6 nodes to ensure interoperability. This document assumes that all IPv6 nodes meet the minimum requirements specified here. 1.2. Description of IPv6 Nodes From the Internet Protocol, Version 6 (IPv6) Specification [RFC2460], we have the following definitions: IPv6 node - a device that implements IPv6. IPv6 router - a node that forwards IPv6 packets not explicitly addressed to itself. IPv6 host - any node that is not a router. 4. Sub-IP Layer An IPv6 node must include support for one or more IPv6 link-layer specifications. Which link-layer specifications an implementation should include will depend upon what link-layers are supported by the hardware available on the system. It is possible for a conformant IPv6 node to support IPv6 on some of its interfaces and not on others. As IPv6 is run over new layer 2 technologies, it is expected that new specifications will be issued. In the following, we list some of the layer 2 technologies for which an IPv6 specification has been developed. It is provided for informational purposes only and may not be complete. - Transmission of IPv6 Packets over Ethernet Networks [RFC2464] - IPv6 over ATM Networks [RFC2492] - Transmission of IPv6 Packets over Frame Relay Networks Specification [RFC2590] - Transmission of IPv6 Packets over IEEE 1394 Networks [RFC3146] - Transmission of IPv6, IPv4, and Address Resolution Protocol (ARP) Packets over Fibre Channel [RFC4338] - Transmission of IPv6 Packets over IEEE 802.15.4 Networks [RFC4944] - Transmission of IPv6 via the IPv6 Convergence Sublayer over IEEE 802.16 Networks [RFC5121] - IP version 6 over PPP [RFC5072] In addition to traditional physical link-layers, it is also possible to tunnel IPv6 over other protocols. Examples include: - Teredo: Tunneling IPv6 over UDP through Network Address Translations (NATs) [RFC4380] - Section 3 of "Basic Transition Mechanisms for IPv6 Hosts and Routers" [RFC4213] 5. IP Layer 5.1. Internet Protocol Version 6 - RFC 2460 The Internet Protocol Version 6 is specified in [RFC2460]. This specification MUST be supported. Any unrecognized extension headers or options MUST be processed as described in RFC 2460. The node MUST follow the packet transmission rules in RFC 2460. Nodes MUST always be able to send, receive, and process fragment headers. All conformant IPv6 implementations MUST be capable of sending and receiving IPv6 packets; the forwarding functionality MAY be supported. Overlapping fragments MUST be handled as described in [RFC5722]. RFC 2460 specifies extension headers and the processing for these headers. An IPv6 node MUST be able to process these headers. An exception is Routing Header type 0 (RH0), which was deprecated by [RFC5095] due to security concerns and which MUST be treated as an unrecognized routing type. All nodes SHOULD support the setting and use of the IPv6 Flow Label field as defined in the IPv6 Flow Label specification [RFC6437]. Forwarding nodes such as routers and load distributors MUST NOT depend only on Flow Label values being uniformly distributed. It is RECOMMENDED that source hosts support the flow label by setting the Flow Label field for all packets of a given flow to the same value chosen from an approximation to a discrete uniform distribution. 5.2. Neighbor Discovery for IPv6 - RFC 4861 Neighbor Discovery is defined in [RFC4861]; the definition was updated by [RFC5942]. Neighbor Discovery SHOULD be supported. RFC 4861 states: Unless specified otherwise (in a document that covers operating IP over a particular link type) this document applies to all link types. However, because ND uses link-layer multicast for some of its services, it is possible that on some link types (e.g., Non- Broadcast Multi-Access (NBMA) links), alternative protocols or mechanisms to implement those services will be specified (in the appropriate document covering the operation of IP over a particular link type). The services described in this document that are not directly dependent on multicast, such as Redirects, next-hop determination, Neighbor Unreachability Detection, etc., are expected to be provided as specified in this document. The details of how one uses ND on NBMA links are addressed in [RFC2491]. Some detailed analysis of Neighbor Discovery follows: Router Discovery is how hosts locate routers that reside on an attached link. Hosts MUST support Router Discovery functionality. Prefix Discovery is how hosts discover the set of address prefixes that define which destinations are on-link for an attached link. Hosts MUST support Prefix Discovery. Hosts MUST also implement Neighbor Unreachability Detection (NUD) for all paths between hosts and neighboring nodes. NUD is not required for paths between routers. However, all nodes MUST respond to unicast Neighbor Solicitation (NS) messages. Hosts MUST support the sending of Router Solicitations and the receiving of Router Advertisements. The ability to understand individual Router Advertisement options is dependent on supporting the functionality making use of the particular option. All nodes MUST support the sending and receiving of Neighbor Solicitation (NS) and Neighbor Advertisement (NA) messages. NS and NA messages are required for Duplicate Address Detection (DAD). Hosts SHOULD support the processing of Redirect functionality. Routers MUST support the sending of Redirects, though not necessarily for every individual packet (e.g., due to rate limiting). Redirects are only useful on networks supporting hosts. In core networks dominated by routers, Redirects are typically disabled. The sending of Redirects SHOULD be disabled by default on backbone routers. They MAY be enabled by default on routers intended to support hosts on edge networks. "IPv6 Host-to-Router Load Sharing" [RFC4311] includes additional recommendations on how to select from a set of available routers. [RFC4311] SHOULD be supported. 5.3. Default Router Preferences and More-Specific Routes - RFC 4191 "Default Router Preferences and More-Specific Routes" [RFC4191] provides support for nodes attached to multiple (different) networks, each providing routers that advertise themselves as default routers via Router Advertisements. In some scenarios, one router may provide connectivity to destinations the other router does not, and choosing the "wrong" default router can result in reachability failures. In such cases, RFC 4191 can help. Small Office/Home Office (SOHO) deployments supported by routers adhering to [RFC6204] use RFC 4191 to advertise routes to certain local destinations. Consequently, nodes that will be deployed in SOHO environments SHOULD implement RFC 4191. 5.4. SEcure Neighbor Discovery (SEND) - RFC 3971 SEND [RFC3971] and Cryptographically Generated Address (CGA) [RFC3972] provide a way to secure the message exchanges of Neighbor Discovery. SEND is a new technology in that it has no IPv4 counterpart, but it has significant potential to address certain classes of spoofing attacks. While there have been some implementations of SEND, there has been only limited deployment experience to date in using the technology. In addition, the IETF working group Cga & Send maIntenance (csi) is currently working on additional extensions intended to make SEND more attractive for deployment. At this time, SEND is considered optional, and IPv6 nodes MAY provide SEND functionality. 5.5. IPv6 Router Advertisement Flags Option - RFC 5175 Router Advertisements include an 8-bit field of single-bit Router Advertisement flags. The Router Advertisement Flags Option extends the number of available flag bits by 48 bits. At the time of this writing, 6 of the original 8 single-bit flags have been assigned, while 2 remain available for future assignment. No flags have been defined that make use of the new option, and thus, strictly speaking, there is no requirement to implement the option today. However, implementations that are able to pass unrecognized options to a higher-level entity that may be able to understand them (e.g., a user-level process using a "raw socket" facility) MAY take steps to handle the option in anticipation of a future usage. 5.6. Path MTU Discovery and Packet Size 5.6.1. Path MTU Discovery - RFC 1981 "Path MTU Discovery for IP version 6" [RFC1981] SHOULD be supported. From [RFC2460]: It is strongly recommended that IPv6 nodes implement Path MTU Discovery [RFC1981], in order to discover and take advantage of path MTUs greater than 1280 octets. However, a minimal IPv6 implementation (e.g., in a boot ROM) may simply restrict itself to sending packets no larger than 1280 octets, and omit implementation of Path MTU Discovery. The rules in [RFC2460] and [RFC5722] MUST be followed for packet fragmentation and reassembly. One operational issue with Path MTU Discovery occurs when firewalls block ICMP Packet Too Big messages. Path MTU Discovery relies on such messages to determine what size messages can be successfully sent. "Packetization Layer Path MTU Discovery" [RFC4821] avoids having a dependency on Packet Too Big messages. 5.7. IPv6 Jumbograms - RFC 2675 IPv6 Jumbograms [RFC2675] are an optional extension that allow the sending of IP datagrams larger than 65.535 bytes. IPv6 Jumbograms make use of IPv6 hop-by-hop options and are only suitable on paths in which every hop and link are capable of supporting Jumbograms (e.g., within a campus or datacenter). To date, few implementations exist, and there is essentially no reported experience from usage. Consequently, IPv6 Jumbograms [RFC2675] remain optional at this time. 5.8. ICMP for the Internet Protocol Version 6 (IPv6) - RFC 4443 ICMPv6 [RFC4443] MUST be supported. "Extended ICMP to Support Multi- Part Messages" [RFC4884] MAY be supported. 5.9. Addressing 5.9.1. IP Version 6 Addressing Architecture - RFC 4291 The IPv6 Addressing Architecture [RFC4291] MUST be supported. 5.9.2. IPv6 Stateless Address Autoconfiguration - RFC 4862 Hosts MUST support IPv6 Stateless Address Autoconfiguration as defined in [RFC4862]. Configuration of static address(es) may be supported as well. Nodes that are routers MUST be able to generate link-local addresses as described in [RFC4862]. From RFC 4862: The autoconfiguration process specified in this document applies only to hosts and not routers. Since host autoconfiguration uses information advertised by routers, routers will need to be configured by some other means. However, it is expected that routers will generate link-local addresses using the mechanism described in this document. In addition, routers are expected to successfully pass the Duplicate Address Detection procedure described in this document on all addresses prior to assigning them to an interface. All nodes MUST implement Duplicate Address Detection. Quoting from Section 5.4 of RFC 4862: Duplicate Address Detection MUST be performed on all unicast addresses prior to assigning them to an interface, regardless of whether they are obtained through stateless autoconfiguration, DHCPv6, or manual configuration, with the following [exceptions noted therein]. "Optimistic Duplicate Address Detection (DAD) for IPv6" [RFC4429] specifies a mechanism to reduce delays associated with generating addresses via Stateless Address Autoconfiguration [RFC4862]. RFC 4429 was developed in conjunction with Mobile IPv6 in order to reduce the time needed to acquire and configure addresses as devices quickly move from one network to another, and it is desirable to minimize transition delays. For general purpose devices, RFC 4429 remains optional at this time. 5.9.3. Privacy Extensions for Address Configuration in IPv6 - RFC 4941 Privacy Extensions for Stateless Address Autoconfiguration [RFC4941] addresses a specific problem involving a client device whose user is concerned about its activity or location being tracked. The problem arises both for a static client and for one that regularly changes its point of attachment to the Internet. When using Stateless Address Autoconfiguration [RFC4862], the Interface Identifier portion of formed addresses stays constant and is globally unique. Thus, although a node's global IPv6 address will change if it changes its point of attachment, the Interface Identifier portion of those addresses remains the same, making it possible for servers to track the location of an individual device as it moves around or its pattern of activity if it remains in one place. This may raise privacy concerns as described in [RFC4862]. In such situations, RFC 4941 SHOULD be implemented. In other cases, such as with dedicated servers in a data center, RFC 4941 provides limited or no benefit. Implementers of RFC 4941 should be aware that certain addresses are reserved and should not be chosen for use as temporary addresses. Consult "Reserved IPv6 Interface Identifiers" [RFC5453] for more details. 5.9.4. Default Address Selection for IPv6 - RFC 3484 The rules specified in the Default Address Selection for IPv6 [RFC3484] document MUST be implemented. IPv6 nodes will need to deal with multiple addresses configured simultaneously. 5.9.5. Stateful Address Autoconfiguration (DHCPv6) - RFC 3315 DHCPv6 [RFC3315] can be used to obtain and configure addresses. In general, a network may provide for the configuration of addresses through Router Advertisements, DHCPv6, or both. There will be a wide range of IPv6 deployment models and differences in address assignment requirements, some of which may require DHCPv6 for address assignment. Consequently, all hosts SHOULD implement address configuration via DHCPv6. In the absence of a router, IPv6 nodes using DHCP for address assignment MAY initiate DHCP to obtain IPv6 addresses and other configuration information, as described in Section 5.5.2 of [RFC4862]. 5.10. Multicast Listener Discovery (MLD) for IPv6 Nodes that need to join multicast groups MUST support MLDv1 [RFC2710]. MLDv1 is needed by any node that is expected to receive and process multicast traffic. Note that Neighbor Discovery (as used on most link types -- see Section 5.2) depends on multicast and requires that nodes join Solicited Node multicast addresses. MLDv2 [RFC3810] extends the functionality of MLDv1 by supporting Source-Specific Multicast. The original MLDv2 protocol [RFC3810] supporting Source-Specific Multicast [RFC4607] supports two types of "filter modes". Using an INCLUDE filter, a node indicates a multicast group along with a list of senders for the group from which it wishes to receive traffic. Using an EXCLUDE filter, a node indicates a multicast group along with a list of senders from which it wishes to exclude receiving traffic. In practice, operations to block source(s) using EXCLUDE mode are rarely used but add considerable implementation complexity to MLDv2. Lightweight MLDv2 [RFC5790] is a simplified subset of the original MLDv2 specification that omits EXCLUDE filter mode to specify undesired source(s). Nodes SHOULD implement either MLDv2 [RFC3810] or Lightweight MLDv2 [RFC5790]. Specifically, nodes supporting applications using Source- Specific Multicast that expect to take advantage of MLDv2's EXCLUDE functionality [RFC3810] MUST support MLDv2 as defined in [RFC3810], [RFC4604], and [RFC4607]. Nodes supporting applications that expect to only take advantage of MLDv2's INCLUDE functionality as well as Any-Source Multicast will find it sufficient to support MLDv2 as defined in [RFC5790]. If a node only supports applications that use Any-Source Multicast (i.e, they do not use Source-Specific Multicast), implementing MLDv1 [RFC2710] is sufficient. In all cases, however, nodes are strongly encouraged to implement MLDv2 or Lightweight MLDv2 rather than MLDv1, as the presence of a single MLDv1 participant on a link requires that all other nodes on the link operate in version 1 compatibility mode. When MLDv1 is used, the rules in the Source Address Selection for the Multicast Listener Discovery (MLD) Protocol [RFC3590] MUST be followed. 6. DHCP versus Router Advertisement Options for Host Configuration In IPv6, there are two main protocol mechanisms for propagating configuration information to hosts: Router Advertisements (RAs) and DHCP. Historically, RA options have been restricted to those deemed essential for basic network functioning and for which all nodes are configured with exactly the same information. Examples include the Prefix Information Options, the MTU option, etc. On the other hand, DHCP has generally been preferred for configuration of more general parameters and for parameters that may be client-specific. That said, identifying the exact line on whether a particular option should be configured via DHCP versus an RA option has not always been easy. Generally speaking, however, there has been a desire to define only one mechanism for configuring a given option, rather than defining multiple (different) ways of configuring the same information. One issue with having multiple ways of configuring the same information is that interoperability suffers if a host chooses one mechanism but the network operator chooses a different mechanism. For "closed" environments, where the network operator has significant influence over what devices connect to the network and thus what configuration mechanisms they support, the operator may be able to ensure that a particular mechanism is supported by all connected hosts. In more open environments, however, where arbitrary devices may connect (e.g., a WIFI hotspot), problems can arise. To maximize interoperability in such environments, hosts would need to implement multiple configuration mechanisms to ensure interoperability. Originally, in IPv6, configuring information about DNS servers was performed exclusively via DHCP. In 2007, an RA option was defined but was published as Experimental [RFC5006]. In 2010, "IPv6 Router Advertisement Options for DNS Configuration" [RFC6106] was published as a Standards Track document. Consequently, DNS configuration information can now be learned either through DHCP or through RAs. Hosts will need to decide which mechanism (or whether both) should be implemented. Specific guidance regarding DNS server discovery is discussed in Section 7. 7. DNS and DHCP 7.1. DNS DNS is described in [RFC1034], [RFC1035], [RFC3363], and [RFC3596]. Not all nodes will need to resolve names; those that will never need to resolve DNS names do not need to implement resolver functionality. However, the ability to resolve names is a basic infrastructure capability on which applications rely, and most nodes will need to provide support. All nodes SHOULD implement stub-resolver [RFC1034] functionality, as in [RFC1034], Section 5.3.1, with support for: - AAAA type Resource Records [RFC3596]; - reverse addressing in ip6.arpa using PTR records [RFC3596]; - Extension Mechanisms for DNS (EDNS0) [RFC2671] to allow for DNS packet sizes larger than 512 octets. Those nodes are RECOMMENDED to support DNS security extensions [RFC4033] [RFC4034] [RFC4035]. Those nodes are NOT RECOMMENDED to support the experimental A6 Resource Records [RFC3363]. 7.2. Dynamic Host Configuration Protocol for IPv6 (DHCPv6) - RFC 3315 7.2.1. Other Configuration Information IPv6 nodes use DHCP [RFC3315] to obtain address configuration information (see Section 5.9.5) and to obtain additional (non- address) configuration. If a host implementation supports applications or other protocols that require configuration that is only available via DHCP, hosts SHOULD implement DHCP. For specialized devices on which no such configuration need is present, DHCP may not be necessary. An IPv6 node can use the subset of DHCP (described in [RFC3736]) to obtain other configuration information. 7.2.2. Use of Router Advertisements in Managed Environments Nodes using the Dynamic Host Configuration Protocol for IPv6 (DHCPv6) are expected to determine their default router information and on- link prefix information from received Router Advertisements. 7.3. IPv6 Router Advertisement Options for DNS Configuration - RFC 6106 Router Advertisements have historically limited options to those that are critical to basic IPv6 functioning. Originally, DNS configuration was not included as an RA option, and DHCP was the recommended way to obtain DNS configuration information. Over time, the thinking surrounding such an option has evolved. It is now generally recognized that few nodes can function adequately without having access to a working DNS resolver. [RFC5006] was published as an Experimental document in 2007, and recently, a revised version was placed on the Standards Track [RFC6106]. Implementations SHOULD implement the DNS RA option [RFC6106]. 8. IPv4 Support and Transition IPv6 nodes MAY support IPv4. 8.1. Transition Mechanisms 8.1.1. Basic Transition Mechanisms for IPv6 Hosts and Routers - RFC 4213 If an IPv6 node implements dual stack and tunneling, then [RFC4213] MUST be supported. 9. Application Support 9.1. Textual Representation of IPv6 Addresses - RFC 5952 Software that allows users and operators to input IPv6 addresses in text form SHOULD support "A Recommendation for IPv6 Address Text Representation" [RFC5952]. 9.2. Application Programming Interfaces (APIs) There are a number of IPv6-related APIs. This document does not mandate the use of any, because the choice of API does not directly relate to on-the-wire behavior of protocols. Implementers, however, would be advised to consider providing a common API or reviewing existing APIs for the type of functionality they provide to applications. "Basic Socket Interface Extensions for IPv6" [RFC3493] provides IPv6 functionality used by typical applications. Implementers should note that RFC3493 has been picked up and further standardized by the Portable Operating System Interface (POSIX) [POSIX]. "Advanced Sockets Application Program Interface (API) for IPv6" [RFC3542] provides access to advanced IPv6 features needed by diagnostic and other more specialized applications. "IPv6 Socket API for Source Address Selection" [RFC5014] provides facilities that allow an application to override the default Source Address Selection rules of [RFC3484]. "Socket Interface Extensions for Multicast Source Filters" [RFC3678] provides support for expressing source filters on multicast group memberships. "Extension to Sockets API for Mobile IPv6" [RFC4584] provides application support for accessing and enabling Mobile IPv6 [RFC6275] features. 10. Mobility Mobile IPv6 [RFC6275] and associated specifications [RFC3776] [RFC4877] allow a node to change its point of attachment within the Internet, while maintaining (and using) a permanent address. All communication using the permanent address continues to proceed as expected even as the node moves around. The definition of Mobile IP includes requirements for the following types of nodes: - mobile nodes - correspondent nodes with support for route optimization - home agents - all IPv6 routers At the present time, Mobile IP has seen only limited implementation and no significant deployment, partly because it originally assumed an IPv6-only environment rather than a mixed IPv4/IPv6 Internet. Recently, additional work has been done to support mobility in mixed- mode IPv4 and IPv6 networks [RFC5555]. More usage and deployment experience is needed with mobility before any specific approach can be recommended for broad implementation in all hosts and routers. Consequently, [RFC6275], [RFC5555], and associated standards such as [RFC4877] are considered a MAY at this time. 11. Security This section describes the specification for security for IPv6 nodes. Achieving security in practice is a complex undertaking. Operational procedures, protocols, key distribution mechanisms, certificate management approaches, etc., are all components that impact the level of security actually achieved in practice. More importantly, deficiencies or a poor fit in any one individual component can significantly reduce the overall effectiveness of a particular security approach. IPsec provides channel security at the Internet layer, making it possible to provide secure communication for all (or a subset of) communication flows at the IP layer between pairs of internet nodes. IPsec provides sufficient flexibility and granularity that individual TCP connections can (selectively) be protected, etc. Although IPsec can be used with manual keying in some cases, such usage has limited applicability and is not recommended. A range of security technologies and approaches proliferate today (e.g., IPsec, Transport Layer Security (TLS), Secure SHell (SSH), etc.) No one approach has emerged as an ideal technology for all needs and environments. Moreover, IPsec is not viewed as the ideal security technology in all cases and is unlikely to displace the others. Previously, IPv6 mandated implementation of IPsec and recommended the key management approach of IKE. This document updates that recommendation by making support of the IPsec Architecture [RFC4301] a SHOULD for all IPv6 nodes. Note that the IPsec Architecture requires (e.g., Section 4.5 of RFC 4301) the implementation of both manual and automatic key management. Currently, the default automated key management protocol to implement is IKEv2 [RFC5996]. This document recognizes that there exists a range of device types and environments where approaches to security other than IPsec can be justified. For example, special-purpose devices may support only a very limited number or type of applications, and an application- specific security approach may be sufficient for limited management or configuration capabilities. Alternatively, some devices may run on extremely constrained hardware (e.g., sensors) where the full IPsec Architecture is not justified. |
| RFC2464 | IPv6 over Ethernet | This document specifies the frame format for transmission of IPv6 packets and the method of forming IPv6 link-local addresses and statelessly autoconfigured addresses on Ethernet networks. It also specifies the content of the Source/Target Link-layer Address option used in Router Solicitation, Router Advertisement, Neighbor Solicitation, Neighbor Advertisement and Redirect messages when those messages are transmitted on an Ethernet. This document replaces RFC 1972, "A Method for the Transmission of IPv6 Packets over Ethernet Networks", which will become historic. The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in [RFC 2119]. 2. Maximum Transmission Unit The default MTU size for IPv6 [IPV6] packets on an Ethernet is 1500 octets. This size may be reduced by a Router Advertisement [DISC] containing an MTU option which specifies a smaller MTU, or by manual configuration of each node. If a Router Advertisement received on an Ethernet interface has an MTU option specifying an MTU larger than 1500, or larger than a manually configured value, that MTU option may be logged to system management but must be otherwise ignored. For purposes of this document, information received from DHCP is considered "manually configured" and the term Ethernet includes CSMA/CD and full-duplex subnetworks based on ISO/IEC 8802-3, with various data rates. 3. Frame Format IPv6 packets are transmitted in standard Ethernet frames. The Ethernet header contains the Destination and Source Ethernet addresses and the Ethernet type code, which must contain the value 86DD hexadecimal. The data field contains the IPv6 header followed immediately by the payload, and possibly padding octets to meet the minimum frame size for the Ethernet link. 0 1 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ Destination ¦ +- -+ ¦ Ethernet ¦ +- -+ ¦ Address ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ Source ¦ +- -+ ¦ Ethernet ¦ +- -+ ¦ Address ¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦1 0 0 0 0 1 1 0 1 1 0 1 1 1 0 1¦ +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ ¦ IPv6 ¦ +- -+ ¦ header ¦ +- -+ ¦ and ¦ +- -+ / payload ... / +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ (Each tic mark represents one bit.) 4. Stateless Autoconfiguration The Interface Identifier [AARCH] for an Ethernet interface is based on the EUI-64 identifier [EUI64] derived from the interface's built- in 48-bit IEEE 802 address. The EUI-64 is formed as follows. (Canonical bit order is assumed throughout.) The OUI of the Ethernet address (the first three octets) becomes the company_id of the EUI-64 (the first three octets). The fourth and fifth octets of the EUI are set to the fixed value FFFE hexadecimal. The last three octets of the Ethernet address become the last three octets of the EUI-64. The Interface Identifier is then formed from the EUI-64 by complementing the "Universal/Local" (U/L) bit, which is the next-to- lowest order bit of the first octet of the EUI-64. Complementing this bit will generally change a 0 value to a 1, since an interface's built-in address is expected to be from a universally administered address space and hence have a globally unique value. A universally administered IEEE 802 address or an EUI-64 is signified by a 0 in the U/L bit position, while a globally unique IPv6 Interface Identifier is signified by a 1 in the corresponding position. For further discussion on this point, see [AARCH]. For example, the Interface Identifier for an Ethernet interface whose built-in address is, in hexadecimal, 34-56-78-9A-BC-DE would be 36-56-78-FF-FE-9A-BC-DE. A different MAC address set manually or by software should not be used to derive the Interface Identifier. If such a MAC address must be used, its global uniqueness property should be reflected in the value of the U/L bit. An IPv6 address prefix used for stateless autoconfiguration [ACONF] of an Ethernet interface must have a length of 64 bits. 5. Link-Local Addresses The IPv6 link-local address [AARCH] for an Ethernet interface is formed by appending the Interface Identifier, as defined above, to the prefix FE80::/64. 10 bits 54 bits 64 bits +----------+-----------------------+----------------------------+ ¦1111111010¦ (zeros) ¦ Interface Identifier ¦ +----------+-----------------------+----------------------------+ 6. Address Mapping -- Unicast The procedure for mapping IPv6 unicast addresses into Ethernet link- layer addresses is described in [DISC]. The Source/Target Link-layer Address option has the following form when the link layer is Ethernet. |
| RFC2827 | Network ingress filtering | A resurgence of Denial of Service Attacks [1] aimed at various targets in the Internet have produced new challenges within the Internet Service Provider (ISP) and network security communities to find new and innovative methods to mitigate these types of attacks. The difficulties in reaching this goal are numerous; some simple tools already exist to limit the effectiveness and scope of these attacks, but they have not been widely implemented. This method of attack has been known for some time. Defending against it, however, has been an ongoing concern. Bill Cheswick is quoted in [2] as saying that he pulled a chapter from his book, "Firewalls and Internet Security" [3], at the last minute because there was no way for an administrator of the system under attack to effectively defend the system. By mentioning the method, he was concerned about encouraging it's use. While the filtering method discussed in this document does absolutely nothing to protect against flooding attacks which originate from valid prefixes (IP addresses), it will prohibit an attacker within the originating network from launching an attack of this nature using forged source addresses that do not conform to ingress filtering rules. All providers of Internet connectivity are urged to implement filtering described in this document to prohibit attackers from using forged source addresses which do not reside within a range of legitimately advertised prefixes. In other words, if an ISP is aggregating routing announcements for multiple downstream networks, strict traffic filtering should be used to prohibit traffic which claims to have originated from outside of these aggregated announcements. An additional benefit of implementing this type of filtering is that it enables the originator to be easily traced to it's true source, since the attacker would have to use a valid, and legitimately reachable, source address. 2. Background A simplified diagram of the TCP SYN flooding problem is depicted below: 204.69.207.0/24 host <----- router <--- Internet <----- router <-- attacker TCP/SYN <--------------------------------------------- Source: 192.168.0.4/32 SYN/ACK no route TCP/SYN <--------------------------------------------- Source: 10.0.0.13/32 SYN/ACK no route TCP/SYN <--------------------------------------------- Source: 172.16.0.2/32 SYN/ACK no route [etc.] Assume: o The "host" is the targeted machine. o The attacker resides within the "valid" prefix, 204.69.207.0/24. o The attacker launches the attack using randomly changing source addresses; in this example, the source addresses are depicted as from within [4], which are not generally present in the global Internet routing tables, and therefore, unreachable. However, any unreachable prefix could be used to perpetrate this attack method. Also worthy of mention is a case wherein the source address is forged to appear to have originated from within another legitimate network which appears in the global routing table(s). For example, an attacker using a valid network address could wreak havoc by making the attack appear to come from an organization which did not, in fact, originate the attack and was completely innocent. In such cases, the administrator of a system under attack may be inclined to filter all traffic coming from the apparent attack source. Adding such a filter would then result in a denial of service to legitimate, non-hostile end-systems. In this case, the administrator of the system under attack unwittingly becomes an accomplice of the attacker. Further complicating matters, TCP SYN flood attacks will result in SYN-ACK packets being sent to one or many hosts which have no involvement in the attack, but which become secondary victims. This allows the attacker to abuse two or more systems at once. Similar attacks have been attempted using UDP and ICMP flooding. The former attack (UDP flooding) uses forged packets to try and connect the chargen UDP service to the echo UDP service at another site. Systems administrators should NEVER allow UDP packets destined for system diagnostic ports from outside of their administrative domain to reach their systems. The latter attack (ICMP flooding), uses an insidious feature in IP subnet broadcast replication mechanics. This attack relies on a router serving a large multi- access broadcast network to frame an IP broadcast address (such as one destined for 10.255.255.255) into a Layer 2 broadcast frame (for ethernet, FF:FF:FF:FF:FF:FF). Ethernet NIC hardware (MAC-layer hardware, specifically) will only listen to a select number of addresses in normal operation. The one MAC address that all devices share in common in normal operation is the media broadcast, or FF:FF:FF:FF:FF:FF. In this case, a device will take the packet and send an interrupt for processing. Thus, a flood of these broadcast frames will consume all available resources on an end-system [9]. It is perhaps prudent that system administrators should consider ensuring that their border routers do not allow directed broadcast packets to be forwarded through their routers as a default. When an TCP SYN attack is launched using unreachable source address, the target host attempts to reserve resources waiting for a response. The attacker repeatedly changes the bogus source address on each new packet sent, thus exhausting additional host resources. Alternatively, if the attacker uses someone else's valid host address as the source address, the system under attack will send a large number of SYN/ACK packets to what it believes is the originator of the connection establishment sequence. In this fashion, the attacker does damage to two systems: the destination target system, as well as the system which is actually using the spoofed address in the global routing system. The result of both attack methods is extremely degraded performance, or worse, a system crash. |
| RFC2460 | IPv6 Addressing Arhcitecture | This specification defines the addressing architecture of the IP Version 6 (IPv6) protocol. It includes the basic formats for the various types of IPv6 addresses (unicast, anycast, and multicast). The authors would like to acknowledge the contributions of Paul Francis, Scott Bradner, Jim Bound, Brian Carpenter, Matt Crawford, Deborah Estrin, Roger Fajman, Bob Fink, Peter Ford, Bob Gilligan, Dimitry Haskin, Tom Harsch, Christian Huitema, Tony Li, Greg Minshall, Thomas Narten, Erik Nordmark, Yakov Rekhter, Bill Simpson, Sue Thomson, Markku Savela, and Larry Masinter. 2. IPv6 Addressing IPv6 addresses are 128-bit identifiers for interfaces and sets of interfaces (where "interface" is as defined in section 2 of [IPV6]). There are three types of addresses: Unicast: An identifier for a single interface. A packet sent to a unicast address is delivered to the interface identified by that address. Anycast: An identifier for a set of interfaces (typically belonging to different nodes). A packet sent to an anycast address is delivered to one of the interfaces identified by that address (the "nearest" one, according to the routing protocols' measure of distance). Multicast: An identifier for a set of interfaces (typically belonging to different nodes). A packet sent to a multicast address is delivered to all interfaces identified by that address. There are no broadcast addresses in IPv6, their function being superseded by multicast addresses. In this document, fields in addresses are given a specific name, for example "subnet". When this name is used with the term "ID" for identifier after the name (e.g., "subnet ID"), it refers to the contents of the named field. When it is used with the term "prefix" (e.g., "subnet prefix") it refers to all of the address from the left up to and including this field. In IPv6, all zeros and all ones are legal values for any field, unless specifically excluded. Specifically, prefixes may contain, or end with, zero-valued fields. 2.1 Addressing Model IPv6 addresses of all types are assigned to interfaces, not nodes. An IPv6 unicast address refers to a single interface. Since each interface belongs to a single node, any of that node's interfaces' unicast addresses may be used as an identifier for the node. All interfaces are required to have at least one link-local unicast address (see section 2.8 for additional required addresses). A single interface may also have multiple IPv6 addresses of any type (unicast, anycast, and multicast) or scope. Unicast addresses with scope greater than link-scope are not needed for interfaces that are not used as the origin or destination of any IPv6 packets to or from non-neighbors. This is sometimes convenient for point-to-point interfaces. There is one exception to this addressing model: A unicast address or a set of unicast addresses may be assigned to multiple physical interfaces if the implementation treats the multiple physical interfaces as one interface when presenting it to the internet layer. This is useful for load-sharing over multiple physical interfaces. Currently IPv6 continues the IPv4 model that a subnet prefix is associated with one link. Multiple subnet prefixes may be assigned to the same link. |
| RFC 2185 | Routing aspects of Ipv6 Transiton | This document gives an overview of the routing aspects of IPv4 to IPv6 transition. The approach outlined here is designed to be compatible with the existing mechanisms for IPv6 transition [1]. During an extended IPv4-to-IPv6 transition period, IPv6-based systems must coexist with the installed base of IPv4 systems. In such a dual internetworking protocol environment, both IPv4 and IPv6 routing infrastructure will be present. Initially, deployed IPv6-capable domains might not be globally interconnected via IPv6-capable internet infrastructure and therefore may need to communicate across IPv4-only routing regions. In order to achieve dynamic routing in such a mixed environment, there need to be mechanisms to globally distribute IPv6 network layer reachability information between dispersed IPv6 routing regions. The same techniques can be used in later stages of IPv4-to-IPv6 transition to route IPv4 packets between isolated IPv4-only routing region over IPv6 infrastructure. Callon & Haskin Informational [Page 2] RFC 2185 Routing Aspects Of IPv6 Transition September 1997 The IPng transition provides a dual-IP-layer transition, augmented by use of encapsulation where necessary and appropriate. Routing issues related to this transition include: (1) Routing for IPv4 packets (2) Routing for IPv6 packets (2a) IPv6 packets with IPv6-native addresses (2b) IPv6 packets with IPv4-compatible addresses (3) Operation of manually configured static tunnels (4) Operation of automatic encapsulation (4a) Locating encapsulators (4b) Ensuring that routing is consist with encapsulation Basic mechanisms required to accomplish these goals include: (i) Dual-IP-layer Route Computation; (ii) Manual configuration of point- to-point tunnels; and (iii) Route leaking to support automatic encapsulation. The basic mechanism for routing of IPv4 and IPv6 involves dual-IP- layer routing. This implies that routes are separately calculated for IPv4 addresses and for IPv6 addressing. This is discussed in more detail in section 3.1. Tunnels (either IPv4 over IPv6, or IPv6 over IPv4) may be manually configured. For example, in the early stages of transition this may be used to allow two IPv6 domains to interact over an IPv4 infrastructure. Manually configured static tunnels are treated as if they were a normal data link. This is discussed in more detail in section 3.2. Use of automatic encapsulation, where the IPv4 tunnel endpoint address is determined from the IPv4 address embedded in the IPv4- compatible destination address of IPv6 packet, requires consistency of routes between IPv4 and IPv6 routing domains for destinations using IPv4-compatible addresses. For example, consider a packet which starts off as an IPv6 packet, but then is encapsulated in an IPv4 packet in the middle of its path from source to destination. This packet must locate an encapsulator at the correct part of its path. Also, this packet has to follow a consistent route for the entire path from source to destination. This is discussed in more detail in section 3.3. The mechanisms for tunneling IPv6 over IPv4 are defined in the transition mechanisms specification [1]. |
| RFC 3053 | IPv67 Tunnel Broker | The growth of IPv6 networks started mainly using the transport facilities offered by the current Internet. This led to the development of several techniques to manage IPv6 over IPv4 tunnels. At present most of the 6bone network is built using manually configured tunnels over the Internet. The main drawback of this approach is the overwhelming management load for network administrators, who have to perform extensive manual configuration for each tunnel. Several attempts to reduce this management overhead have already been proposed and each of them presents interesting advantages but also solves different problems than the Tunnel Broker, or poses drawbacks not present in the Tunnel Broker: - the use of automatic tunnels with IPv4 compatible addresses [1] is a simple mechanism to establish early IPv6 connectivity among isolated dual-stack hosts and/or routers. The problem with this approach is that it does not solve the address exhaustion problem of IPv4. Also there is a great fear to include the complete IPv4 routing table into the IPv6 world because this would worsen the routing table size problem multiplying it by 5; - 6over4 [2] is a site local transition mechanism based on the use of IPv4 multicast as a virtual link layer. It does not solve the problem of connecting an isolated user to the global IPv6 Internet; - 6to4 [3] has been designed to allow isolated IPv6 domains, attached to a wide area network with no native IPv6 support (e.g., the IPv4 Internet), to communicate with other such IPv6 domains with minimal manual configuration. The idea is to embed IPv4 tunnel addresses into the IPv6 prefixes so that any domain border router can automatically discover tunnel endpoints for outbound IPv6 traffic. The Tunnel Broker idea is an alternative approach based on the provision of dedicated servers, called Tunnel Brokers, to automatically manage tunnel requests coming from the users. This approach is expected to be useful to stimulate the growth of IPv6 interconnected hosts and to allow early IPv6 network providers to provide easy access to their IPv6 networks. The main difference between the Tunnel Broker and the 6to4 mechanisms is that the they serve a different segment of the IPv6 community: - the Tunnel Broker fits well for small isolated IPv6 sites, and especially isolated IPv6 hosts on the IPv4 Internet, that want to easily connect to an existing IPv6 network; - the 6to4 approach has been designed to allow isolated IPv6 sites to easily connect together without having to wait for their IPv4 ISPs to deliver native IPv6 services. This is very well suited for extranet and virtual private networks. Using 6to4 relays, 6to4 sites can also reach sites on the IPv6 Internet. In addition, the Tunnel Broker approach allows IPv6 ISPs to easily perform access control on the users enforcing their own policies on network resources utilization. This document is intended to present a framework describing the guidelines for the provision of a Tunnel Broker service within the Internet. It does not specify any protocol but details the general architecture of the proposed approach. It also outlines a set of viable alternatives for implementing it. Section 2 provides an overall description of the Tunnel Broker model; Section 3 reports known limitations to the model; Section 4 briefly outlines other possible applications of the Tunnel Broker approach; Section 5 addresses security issues. 2. Tunnel Broker Model Tunnel brokers can be seen as virtual IPv6 ISPs, providing IPv6 connectivity to users already connected to the IPv4 Internet. In the emerging IPv6 Internet it is expected that many tunnel brokers will be available so that the user will just have to pick one. The list of the tunnel brokers should be referenced on a "well known" web page (e.g. on http://www.ipv6.org) to allow users to choose the "closest" one, the "cheapest" one, or any other one. The tunnel broker model is based on the set of functional elements depicted in figure 1. +------+ /¦tunnel¦ / ¦server¦ / ¦ ¦ / +------+ +----------+ +------+/ +------+ ¦dual-stack¦ ¦tunnel¦ ¦tunnel¦ ¦ node ¦<--->¦broker¦<--->¦server¦ ¦ (user) ¦ ¦ ¦ ¦ ¦ +----------+ +------+\ +------+ ¦ \ +------+ tunnel end-point v \ ¦tunnel¦ /\ +---+ \ ¦server¦ ¦¦ ¦DNS¦ \¦ ¦ ¦¦ +---+ +------+ ¦¦ ¦¦ tunnel end-point ¦¦ /\ ¦¦ ¦¦ ¦+---------------------------+¦ +-----------------------------+ IPv6 over IPv4 tunnel Figure 1: the Tunnel Broker model 2.1 Tunnel Broker (TB) The TB is the place where the user connects to register and activate tunnels. The TB manages tunnel creation, modification and deletion on behalf of the user. For scalability reasons the tunnel broker can share the load of network side tunnel end-points among several tunnel servers. It sends configuration orders to the relevant tunnel server whenever a tunnel has to be created, modified or deleted. The TB may also register the user IPv6 address and name in the DNS. A TB must be IPv4 addressable. It may also be IPv6 addressable, but this is not mandatory. Communications between the broker and the servers can take place either with IPv4 or IPv6. |
| RFC 4213 | Basic Transition Mechanisms for IPv6 Hosts & Routers | The key to a successful IPv6 transition is compatibility with the large installed base of IPv4 hosts and routers. Maintaining compatibility with IPv4 while deploying IPv6 will streamline the task of transitioning the Internet to IPv6. This specification defines two mechanisms that IPv6 hosts and routers may implement in order to be compatible with IPv4 hosts and routers. The mechanisms in this document are designed to be employed by IPv6 hosts and routers that need to interoperate with IPv4 hosts and utilize IPv4 routing infrastructures. We expect that most nodes in the Internet will need such compatibility for a long time to come, and perhaps even indefinitely. The mechanisms specified here are: - Dual IP layer (also known as dual stack): A technique for providing complete support for both Internet protocols -- IPv4 and IPv6 -- in hosts and routers. - Configured tunneling of IPv6 over IPv4: A technique for establishing point-to-point tunnels by encapsulating IPv6 packets within IPv4 headers to carry them over IPv4 routing infrastructures. The mechanisms defined here are intended to be the core of a "transition toolbox" -- a growing collection of techniques that implementations and users may employ to ease the transition. The tools may be used as needed. Implementations and sites decide which techniques are appropriate to their specific needs. This document defines the basic set of transition mechanisms, but these are not the only tools available. Additional transition and compatibility mechanisms are specified in other documents. 1.1. Terminology The following terms are used in this document: Types of Nodes IPv4-only node: A host or router that implements only IPv4. An IPv4-only node does not understand IPv6. The installed base of IPv4 hosts and routers existing before the transition begins are IPv4-only nodes. IPv6/IPv4 node: A host or router that implements both IPv4 and IPv6. IPv6-only node: A host or router that implements IPv6 and does not implement IPv4. The operation of IPv6-only nodes is not addressed in this memo. IPv6 node: Any host or router that implements IPv6. IPv6/IPv4 and IPv6- only nodes are both IPv6 nodes. IPv4 node: Any host or router that implements IPv4. IPv6/IPv4 and IPv4- only nodes are both IPv4 nodes. Techniques Used in the Transition IPv6-over-IPv4 tunneling: The technique of encapsulating IPv6 packets within IPv4 so that they can be carried across IPv4 routing infrastructures. Configured tunneling: IPv6-over-IPv4 tunneling where the IPv4 tunnel endpoint address(es) are determined by configuration information on tunnel endpoints. All tunnels are assumed to be bidirectional. The tunnel provides a (virtual) point-to-point link to the IPv6 layer, using the configured IPv4 addresses as the lower-layer endpoint addresses. Other transition mechanisms, including other tunneling mechanisms, are outside the scope of this document. The key words MUST, MUST NOT, REQUIRED, SHALL, SHALL NOT, SHOULD, SHOULD NOT, RECOMMENDED, MAY, and OPTIONAL, when they appear in this document, are to be interpreted as described in [RFC2119]. 2. Dual IP Layer Operation The most straightforward way for IPv6 nodes to remain compatible with IPv4-only nodes is by providing a complete IPv4 implementation. IPv6 nodes that provide complete IPv4 and IPv6 implementations are called "IPv6/IPv4 nodes". IPv6/IPv4 nodes have the ability to send and receive both IPv4 and IPv6 packets. They can directly interoperate with IPv4 nodes using IPv4 packets, and also directly interoperate with IPv6 nodes using IPv6 packets. Even though a node may be equipped to support both protocols, one or the other stack may be disabled for operational reasons. Here we use a rather loose notion of "stack". A stack being enabled has IP addresses assigned, but whether or not any particular application is available on the stacks is explicitly not defined. Thus, IPv6/IPv4 nodes may be operated in one of three modes: - With their IPv4 stack enabled and their IPv6 stack disabled. - With their IPv6 stack enabled and their IPv4 stack disabled. - With both stacks enabled. IPv6/IPv4 nodes with their IPv6 stack disabled will operate like IPv4-only nodes. Similarly, IPv6/IPv4 nodes with their IPv4 stacks disabled will operate like IPv6-only nodes. IPv6/IPv4 nodes MAY provide a configuration switch to disable either their IPv4 or IPv6 stack. The configured tunneling technique, which is described in Section 3, may or may not be used in addition to the dual IP layer operation. 2.1. Address Configuration Because the nodes support both protocols, IPv6/IPv4 nodes may be configured with both IPv4 and IPv6 addresses. IPv6/IPv4 nodes use IPv4 mechanisms (e.g., DHCP) to acquire their IPv4 addresses, and IPv6 protocol mechanisms (e.g., stateless address autoconfiguration [RFC2462] and/or DHCPv6) to acquire their IPv6 addresses. |

In summary it can can be said that most technologies are on the way or nearly there with IPv6 deployments and those that aren’t do not hold back the dual stack topology for MSO execution for IPv6.  What does restrict us however is the home network with legacy equipment, non-willing application owners to upgrade to support IPv6, old OSes & the potential for many IPv4 Internet Services not to move to IPv6.  This then limits the Cable ISP to keep an IPv4 address within the home and therefore we are forced into transition technologies once the MSO has depleted its IPv4 pool, which will happen to everyone within the next 5-8 years.  No ISP will be exempt form this migration & use of a transition technology.

The following text is to be used when appropriate:

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, ETSI grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (informative):
Title of normative annex (style H9)

<Text>

<PAGE BREAK>

Annex <B> (informative):
Title of informative annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/Files/other/EDRs_navigator.chm).

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Document history |
| --- |
| <Version> | <Date> | <Milestone> |

## A few examples:

| Document history |
| --- |
| V1.1.1 | April 2001 | Publication |
| V1.3.1 | June 2011 | Pre-processed by the ETSI Secretariat editHelp! e-mail: mailto:edithelp@etsi.org |

2011-08-09

# Comments

The list of abbreviations to be completed.

ME comment: What does this suppose to suggest, that we take IPv6, or we don´t?

To be re-phrased , to be web services specific - Phil

ME comment: What they wanted to say with this?

To be re-phrased – Phil

To be decided if the table stays here or moves to Annex.

This Table should be re-elaborated. It should contain just a brief summary of RFCs, not a copy of the whole parts of a text including the page numbers ;-)

Is this really needed?

If the Figure is kept here, it has to be re-drawn. Microsoft Visio 2003 and 2007 are accepted formats.

If the Figure is kept here, it has to be re-drawn.

If the Figure is kept here, it has to be re-drawn.

# Text boxes

IPv6

End devices
- PC OS
- Mobile OS
- VoIP OS
- IPTV OS
- etc

Access Nodes
- DSLAM
- GPON
- CMTS
- ETH switches
- WIFI Hotspots
- NB

CPE
- DSL RG/CPE
- GPON EG/CPE
- ETH RG/CPE
- Cable RG/CPE

IP Nodes
- Edge
- Aggregation
- Core

BNG/BRAS
- PPPoX
- IPoE (DHCPv6/DHCPv6 PD)

Applications
- End-User applications
- CDN
- WebSites
- etc