ETSI TR 103 099 V1.1.1 (2012-11)

Intelligent Transport Systems (ITS);

Architecture of conformance validation framework

<

Technical Report

Reference

DTR/ITS-0030038

Keywords

architecture, conformance, ITS, testing

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2012.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

Contents

Intellectual Property Rights	5

Foreword	5

Introduction	5

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Abbreviations	7

4	Test platform overview	8

4.1	Constraints and requirements	8

4.2	General architecture	8

5	Hardware equipment	9

5.1	PC	9

5.2	G5 adapter box	10

6	Codecs	10

6.1	Advanced details of implementation	12

7	Test Adapter	12

7.1	Lower Tester	13

7.1.1	Overview	13

7.1.2	Advanced details of implementation	15

7.1.3	Extensibility of the test adapter	17

7.1.4	Adapter Control primitives	17

7.2	Platform Adapter	17

7.3	Upper Tester	17

Annex A:	Codecs source code	19

Annex B:	Test Adapter source code	20

Annex C:	Upper Tester message format	21

C.1	CAM Upper Tester Primitives	21

C.1.1	CamInitialize	21

C.1.2	ChangeHeading	22

C.1.3	ChangePosition	22

C.1.4	ChangeSpeed	22

C.1.5	SetCrashSignal	23

C.1.6	SetDangerousGoodsStatus	23

C.1.7	SetLengthWidthPrecision	23

C.1.8	SetDistanceToStopLine	23

C.1.9	SetTurnAdvice	24

C.1.10	SetCurvature	24

C.1.11	SetOccupancy	24

C.1.12	SetDoorStatus	25

C.1.13	SetLightBarStatus	25

C.1.14	SetSireneStatus	25

C.1.15	SetTrafficLightPriority	26

C.1.16	SetScheduleDeviation	26

C.1.17	SetPtLineDescription	26

C.1.18	SetExteriorLightsStatus	27

C.1.19	CheckCam	27

C.2	DENM Upper Tester Primitives	27

C.2.1	DenmInitialize	27

C.2.2	GenerateDenmEvent	28

C.2.3	CancelDenmEvent	28

C.2.4	NegateDenmEvent	29

C.2.5	UpdateDenmEvent	29

C.2.6	CheckDenm	29

C.3	GeoNetworking Upper Tester Primitives	30

C.3.1	GnInitialize	30

C.3.2	GenerateGeoUnicast	30

C.3.3	GenerateGeoAnycast	30

C.3.4	GenerateGeoBroadcast	31

C.3.5	GenerateSHB	31

C.3.6	GenerateTSB	32

C.3.7	CheckPacket	32

Annex D:	MK2 bridge application	33

Annex E:	Example of Test Platform implementation	34

Annex F:	Complete Test Adapter class diagram	38

Annex G:	Validated ATS in TTCN-3 and ASN.1 modules	39

Annex H:	Bibliography	40

History	42

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Report (TR) has been produced by ETSI Technical Committee Intelligent Transport System (ITS).

# Introduction

In response to EC mandate M/453, ETSI Technical Committee (TC) ITS has standardized base and test specifications for ITS protocols. In a next step a prototype TTCN-3 test system was built and validated. The present document and its related TR 103 061 series, describe the design and validation of the prototype TTCN-3 test system.

The action described in the present document has supported the implementation of ITS standards by:

Making available validated and standardized test specifications and thus enabling the application of reliable certification schemes.

Executing conformance validation framework against real Implementations Under Test (IUTs) from industry and thus providing these companies a conformance assessment of their implementations. During the lifetime of this action, the conformance validation framework was as well provided at ITS Cooperative Mobility Services Interoperability events.

Releasing all software as open source and thus allowing industry to build and run their own conformance validation framework.

# 1	Scope

The present document provides a description of the architecture of the ITS conformance validation framework, including definition of the test environment, codec and test adapter. It provides, as well, all the necessary source code to build and run the ITS conformance validation framework.

The ITS conformance validation framework integrates the CAM, DENM, BTP and GeoNetworking abstract test suites (ATS) ([i.10] to [i.13]). The results of the validation are described in the TR 103 061 series [i.4] to [i.8].

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication, ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	ETSI ES 201 873-5 (V4.2.1): "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 5: TTCN-3 Runtime Interface (TRI)".

[i.2]	ETSI ES 201 873-6 (V4.2.1): "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 6: TTCN-3 Control Interface (TCI)".

[i.3]	ETSI EG 201 015 (V2.1.1): "Methods for Testing and Specification (MTS); Standards engineering process; A handbook of validation methods".

[i.4]	ETSI TR 103 061-1 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Co-operative Awareness Messages (CAM); CAM validation report".

[i.5]	ETSI TR 103 061-2 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Decentralized Environmental Notification basic Service Message (DENM); DENM validation report".

[i.6]	ETSI TR 103 061-3 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Geographical addressing and forwarding for point-to-point and point-to-multipoint communications; GeoNetworking validation report".

[i.7]	ETSI TR 103 061-4 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for GeoNetworking Basic Transport Protocol (BTP); GeoNetworking BTP validation report".

[i.8]	ETSI TR 103 061-5 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; IPv6 over GeoNetworking validation report".

[i.9]	IEEE 802.11p: "IEEE Standard for Local and Metropolitan Area Networks - Specific requirements; Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications; Amendment 6: Wireless Access in Vehicular Environments".

[i.10]	ETSI TS 102 859-3 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Transmission of IP packets over GeoNetworking; Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT)".

[i.11]	ETSI TS 102 868-3 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Co-operative Awareness Messages (CAM); Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT)".

[i.12]	ETSI TS 102 869-3 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Of Decentralized Environmental Notification basic Service (DENM); Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT)".

[i.13]	ETSI TS 102 870-3 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specifications for Geonetworking Basic Transport Protocol (BTP); Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT)".

# 3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

AC	Adapter Control

API	Application Programming Interface

ASN	Abstract Syntax Notation

ATS	Abstract Test Suite

BTP	Basic Transport Protocol

CAM	Cooperative Awareness Message

CT	Causer Type

DENM	Decentralized Environmental Notification Message

ETH	Ethernet

GN	GeoNetworking

HB	High Beam

IP	Internet Protocol

ITS	Intelligent Transportation Systems

IUT	Implementation Under Test

JDK	Java Development Kit

LB	Low Beam

LDM	Local Dynamic Map

LT	Left Turn

MAC	Media Access Control

OS	Operating System

OSI	Open Systems Interconnection model

PC	Personal Computer

Pcap	Packet Capture

PDU	Protocol Data Unit

RT	Right Turn

SHB	Single Hop Broadcast

SUT	System Under Test

TA	Test Adapter

TC	Test Cases

TCI	TTCN-3 Control Interface

TP	Test Purposes

TRI	TTCN-3 Runtime Interface

TSB	Topology Scoped Broadcast

TTCN-3	Testing and Test Control Notation 3

UDP	User Datagram Protocol

UT	Upper Tester

# 4	Test platform overview

## 4.1	Constraints and requirements

The purpose of the ITS test platform is to provide a reliable set of software and hardware equipments that can be used to validate TTCN-3 abstract test suites (ATS) developed in ETSI.

The architecture of this test platform has been designed with respect to the following constraints:

to be compatible with the requirements expressed in the validation handbook (EG 201 015 [i.3]);

to be independent of the platform used to implement the test system;

to be independent of the TTCN-3 tool provider;

to be configurable and customizable;

to provide tools and well defined interfaces to system under test (SUT), allowing test automation;

to be easily extensible for future ITS protocols;

to provide generic components that can be reused in other test platforms.

In order to ensure independence of hardware platforms, all software pieces running on the test platform have been implemented using Java™ language, using generic and widely used libraries.

Test tool independence has been achieved by isolating the tool specific interfaces from core functionalities of the platform. Adapting the current platform to a different test tool would only require the implementation of a very simple piece of software mapping tool-specific functions to generic functions defined in this project.

In addition, great care has been taken to separate ITS specific functionalities from generic test platform tasks in order to provide a maximum number of reusable components for future test platforms.

## 4.2	General architecture

Typically a TTCN-3 test platform is composed of four different components:

The TTCN-3 test tool providing necessary software to execute the abstract test suites.

The hardware equipment supporting TTCN-3 test execution and adaptation to SUTs.

The codecs which convert protocol messages into their abstract TTCN-3 representation.

The Test Adapter (TA) implementing interfaces with the device under test.

The interaction of these components is described in figure 1.

Figure 1: General architecture

The TTCN-3 test tools are usually provided by commercial companies and their description is out of the scope of the present document. The implementation details of the other components are described in the following clauses.

# 5	Hardware equipment

The ITS test platform is composed of two hardware equipments, a standard PC and a G5 adapter box.

## 5.1	PC

The main hardware component of the ITS test platform is a standard PC. Its role is to host the execution of the test suites using a commercial TTCN-3 test tool.

Whatever operating system is installed on the computer, it is necessary to ensure that the following points are taken into account:

No firewall interference with traffic generated by the Test System and/or SUT.

Excellent time synchronisation between the SUT and the test system.

Test system processes (especially the test adapter) have to be granted unrestricted control to telecommunication hardware.

Time synchronisation is maybe the most critical point to be checked before starting any test session, as it can be the source of strange SUT behaviour and generate incoherent results. Indeed, most ITS protocol messages feature a time tag used by the receiver to determine if the information it carries is still valid; if the test system is ahead in time, all messages it sends will be considered either as coming from the future or from a very old date, and be discarded.

This PC is equipped with two network cards, one being used for ITS communication with SUT (lower layers link), the other one being used for exchanging upper tester messages (upper tester transport link). Separating these two communications on different hardware interfaces is not an absolute necessity, but it is a good practice and it ensures that there will be no interaction between the flows.

The communication between the SUT and the test system is achieved through Ethernet if the SUT supports it or using a G5 adaptation box.

Figure 2: Communication via G5 adaptation box

Figure 3: Communication via Ethernet

## 5.2	G5 adapter box

The ITS protocol stack makes use of G5 radio protocol in order to establish communication between ITS devices. To achieve G5 connectivity, a dedicated hardware equipment needs to be added to the test platform. The role of this adaptation box is to handle all radio-related tasks transparently and to act as a bridge for the test system.

Cohda WirelessTM MK2 has been chosen to fulfil this task. This device is fully IEEE 802.11p [i.9] compliant and provides as well an Ethernet interface so that it can be used as a transparent bridge between the test system and the SUT, as depicted in figure 2.

To transfer frames received on the Ethernet interface to the radio interface and vice versa, it is necessary to install and execute a small bridge application on the MK2. Only the frame featuring a specific ethertype (0x0707 by default) will be transferred from one interface to the other, so that only desired traffic will cross the bridge. The source code of this program and its configuration file are provided in annex D.

# 6	Codecs

The codec entity is responsible for the encoding and decoding of TTCN-3 abstract values into bitstrings suitable to be sent to the System Under Test (SUT).

In order simplify implementation and to ease the maintenance, coding and decoding tasks are handled by several codecs:

One independent codec per ITS protocol.

One codec for TTCN-3 types that do not correspond to real protocol messages. It includes for example all auxiliary types used to carry information to/from Test Adapter, like the ones defined in TestSystem modules (GeoNetworkingInd, GeoNetworkingReq, etc.).

For protocol messages defined in ASN.1 (CAM and DENM protocols), usage of dedicated commercial ASN.1 tools is recommended.

Figure 4: Codec package organisation

Selection of correct codec for encoding a message at runtime is dictated by means of the "with encode" statement within TTCN-3 modules. For instance the following statement:

with {

encode "LibItsGeoNetworking_TypesAndValues"

}

will cause org.etsi.its.codec.ttcn.LibItsGeoNetworking_TypesAndValuesCodec to be invoked.

## 6.1	Advanced details of implementation

Figure 5 gives an overview of the relations between the different java classes implementing the codec. The structure is relatively simple. Connection with the tool-dependent classes is realized through the ICodec interface and is not depicted in figure 5.

Figure 5: Codec class diagram

Each codec implements the standard TCI interface TciCDProvided as described in ES 201 873-6 [i.2]. In addition codecs have to implement the ICodec interface, which is providing a tool-independent instantiation API to TTCN-3 tools.

The BaseCodecImpl class implements the minimal functionalities of a codec and is used as a base class for further codec development. For extensibility purpose, this class is not ITS-specific, and it can be used as-is in other platform projects.

The ItsCodecImpl class directly extends BaseCodecImpl and provides ITS common codec functionalities. Each ITS codec derives from this class.

# 7	Test Adapter

The test adapter conceptually splits into three parts:

a lower test adapter;

a TTCN-3 platform adapter implementing timers;

an upper test adapter.

## 7.1	Lower Tester

### 7.1.1	Overview

TTCN-3 test suites are usually focusing on a single protocol layer and designed to be executed against real implementations (IUT). However it is unusual to find standalone implementations as they are commonly integrated as an internal component of a physical device (SUT).

The purpose of a lower test adapter is to prepare and adapt the protocol messages used by TTCN-3 test suites so that they can be transmitted successfully to the SUT. One way to achieve this goal is for example to implement lower layers and encapsulate protocol messages accordingly. For instance, CAM and DENM messages need to be encapsulated in BTP datagrams, themselves encapsulated into GeoNetworking packets, and transmitted over G5 radio link. The higher up the IUT is located in the OSI stack, the more complex is the test adapter.

TTCN-3 test suites send and receive protocol messages via TTCN-3 communication ports. For each of these ports defined in the test suites, a corresponding port entity needs to be implemented in the test adapter using standardised TRI interface (ES 201 873-5 [i.1]). To provide maximum flexibility and allow for extensibility, the test adapter ports of the ITS test platform have been designed with the following constraints:

For each port family, the lower stack can be configured using test adapter parameters (see annex E). As a consequence it is possible to dynamically define what will be the lower layers used to communicate with SUT, and how protocol messages will be encapsulated.

All the instances of ports are independent.

Behaviour of ports and lower layers can be dynamically modified by using predefined AC (Adapter Control) primitives directly sent from TTCN-3 script using dedicated port AcPort. For example the AC primitive 'startBeaconing' requests the test adapter to start sending beacons.

The test adapter implementation mainly features Port and Layer objects. The relationship and interactions between these objects will be further detailed in the next section, but it is important to notice the main differences between these objects, as misunderstanding their roles can lead to confusion:

Port objects are the counterpart of TTCN-3 communication ports.

Layer objects implement the minimal functionalities of a protocol layer and provide facilities for encapsulating or decapsulating packets.

Port objects are configured with a lower stack composed of cascading Layer objects.

For a same protocol layer, Layer objects usually implement more functionalities than Port objects.

Figures 6 and 7 show an example of interactions between these objects respectively when sending and receiving a message. The port described in this example is a CAM port configured with a BTP/GN/G5 lower stack.

Figure 6: Message sending sequence diagram

Figure 7: Message reception sequence diagram

### 7.1.2	Advanced details of implementation

Figure 8 presents the simplified class diagram of the test adapter. For better readability, auxiliary classes such as factories are not represented. The complete class diagram, also featuring design pattern indications, can be found in annex F.

Figure 8: Test Adapter class diagram

The main class of this implementation is the TestAdapter class. It implements the standardised interface TriCommunicationSA and uses the ITERequired interface implemented by test tool providers. These interfaces are part of the TRI API defined in ES 201 873-5 [i.1]. All other classes of this implementation are completely TRI-agnostic. The main purpose of the TestAdapter class is to instantiate and manage the different ports.

There are two different kinds of ports:

Protocol ports realising communication between TTCN-3 and SUT.

Adapter ports which are used for test adapter configuration and upper tester communication.

Upon protocol port initialisation, lower layers are instanciated in cascade and chained as depicted in figure 9, base on lower stack description. This picture also illustrate the usage of "Factory" design patterns for instanciating Layer and Port objects. Each Layer is responsible for encapsulating/decapsulating packets and transmitting result to lower/upper layer using send()/receive() methods.

Figure 9: Port initialisation sequence diagram

Currently the following layers have been implemented:

GnLayer: basic functionalities of GeoNetworking layer, including beaconing.

BtpLayer.

EthernetLayer. Important: this class requires the usage of the external library JnetPcap for capturing and injecting Ethernet frames.

G5Layer.

The Management class, implementing IManagementTA and IManagementLayers interfaces is used for handling the dynamic configuration of Layer objects. It is directly linked to the AdapterControlPort and implements the AC primitives defined in the TTCN-3 test suites. "It is important to notice that this class is implemented using a "Multiton or Multiple Singleton" design pattern: one single instance of this class can be instanciated per TTCN-3 component.

### 7.1.3	Extensibility of the test adapter

The test adapter can be extended in several ways. The first option is to add new protocol layers by adding new classes inheriting from the Layer class. These new layers have then to be assigned a short name and registered in the LayerFactory.

It is also possible to define new protocol ports. To do so, it is necessary to implement new classes inheriting from the ProtocolPort class. These new ports have then to be assigned a short name and registered in the ProtocolPortFactory.

Furthermore it is also possible to extend AC primitives. This requires to enrich IManagementLayers and IManagementTA interfaces and to implement new functionalities in the Management class.

### 7.1.4	Adapter Control primitives

The following AC primitives are used to control the dynamic configuration of the various layers:

| AC Primitive | Description |
| --- | --- |
| startBeaconing | Requests Test Adapter to start sending periodic beacons for the current component |
| stopBeaconing | Requests Test Adapter to stop sending periodic beacons for the current component |
| startEnqueueingBeacons | Requests Test Adapter to start enqueueing beacon messages on the current component GN port |
| stopEnqueueingBeacons | Requests Test Adapter to stop enqueueing beacon messages on the current component GN port |
| startMultipleBeaconing | Requests Test Adapter to start simulating neighbour presence by sending multiple periodic beacons for the current component |
| stopMultipleBeaconing | Requests Test Adapter to stop simulating neighbour presence |
| getLongPositionVector | Gets the long position vector of a neighbour given its GN_Address |

## 7.2	Platform Adapter

All TTCN-3 commercial tools provide generic Platform Adapter implementations for managing TTCN-3 timers. These implementations are well tested and usually accurate enough for most usages. In the case of ITS protocols, e.g. DENM re-broadcasting, GN beacon interval etc., the protocol timer value is in the order of magnitude of hundreds of milliseconds. This order of magnitude can be handled well with the built in test system timers. As a consequence no specific development is required for this component.

## 7.3	Upper Tester

The upper tester is used to interact with the upper interface of the implementation under test (IUT). It is typically implemented as an upper tester module executing in the test adapter and as a small module executing on the SUT and acts as an upper layer for the IUT. It is particularly useful for:

Triggering events in SUT.

Triggering messages.

Checking that payload are transmitted correctly to upper layers.

The communication between the two upper tester module is performed in accordance with the upper tester message format described in annex C.

As it interacts with potentially proprietary APIs, it is usually the responsibility of IUT vendors to implement module located within SUT.

Figure 10: Upper Tester architecture

: This upper tester module implements the upper tester message based API described in annex C.

The source code of the test system side of the upper tester module is provided in annex B as part of the test adapter source code.

Annex A:
Codecs source code

The software modules are contained in archive AnnexA_Codec.zip which is included in archive tr_103099v010101p0.zip which accompanies the present document.

Annex B:
Test Adapter source code

The software modules are contained in archive AnnexB_Adapter.zip which is included in archive tr_103099v010101p0.zip which accompanies the present document.

Annex C:
Upper Tester message format

The messages defined in the present annex are exchanged between the Test System and Upper Tester using a UDP connection.

All integer values are encoded in big-endian byte order (most significant byte first).

Two  different message exchange can occur.

- The first one is initiated by the test system and consists in a request – response exchange as described below. The UpperTester result message is specific to each primitive and may be used to indicate the success of the request or to report some values.

| TestSystem |  | UT |
| --- | --- | --- |
|  |  | UpperTester primitive |  |  |
|  |  | ==============================> |  |  |
|  |  | UpperTester result |  |  |
|  |  | <=============================== |  |  |

In this case the UDP destination port of the response shall be identical to the UDP source port of the request. When receiving UtInitialize primitive from Test System, the UDP source port of this request shall be saved as 'defaultUTPort' and used for unsolicited indications.

- The second communication exchange is initiated by the Upper Tester. It consists in unsolicited indications sent each time a packet is transmitted to upper layers, as described below. The Test System never replies to such messages (one way communication)

| TestSystem |  | UT |  |
| --- | --- | --- | --- |
|  |  |  |  |  | Message received |
|  |  |  |  |  | <================ |
|  |  | UpperTester indication |  |  |  |
|  |  | <=============================== |  |  |  |

In this case, the UDP destination port of the indication shall be set to the 'defaultUTPort', which corresponds to the UDP source port of the UTInitialize request.

Format of UtResult:

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x24 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x24 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

# C.1	Common Upper Tester Primitives

## C.1.1	UtInitialize

This message is used to request initialization of IUT implementation. As a result, IUT shall perform a soft reset, i.e. discard all buffered messages and flush all Location Table entries.

Request (UtInitialize TS->UT):

| 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x00 |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x00 |

Response (UtInitializeResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x01 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x01 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.1.2	ChangePosition

This message is used to change the position of the ITS station. The latitude, longitude and elevation parameters are relative to the current position of IUT. They are NOT absolute position.

Request (UtChangePosition TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x02 | DeltaLatitude |
| ... | DeltaLatitude |
| ... | DeltaElevation |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x02 |
| DeltaLatitude | 4 bytes | Latitude offset (multiples of 0.1 microdegree) |
| DeltaLongitude | 4 bytes | Longitude offset (multiples of 0.1 microdegree) |
| DeltaElevation | 1 byte | Elevation offset (meter) |

Response (UtChangePositionResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x03 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x03 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

# C.2	CAM Upper Tester Primitives

C.2.1	ChangeCurvature

This message is used to set the curvature of the ITS station.

Request (UtCamTrigger_changeCurvature TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |
| MessageType = 0x30 | Curvature |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x30 |
| Curvature | 2 bytes | Signed integer. Curvature change from -30000 to 30001 |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.2	ChangeSpeed

This message is used to change the speed of the ITS station. The vehicle speed  is increased by the value of 'SpeedVariation' field.

For instance, if the current speed of the ITS station is 10 m/s and received SpeedVariation is +300, then the new vehicle speed will be 10 + 0,01 × 300 = 13 m/s.

Request (UtCamTrigger_changeSpeed TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |
| MessageType = 0x31 | SpeedVariation |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x31 |
| SpeedVariation | 2 bytes | Signed integer. Speed variation in units of cm/s |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.3	SetAccelerationControlStatus

brakePedalActive (0),

gasPedalActive (1),

emergencyBrakeActive (2),

collisionWarningActive (3),

accActive (4),

cruiseControl (5),

speedLimiterActive (6)

This message is used to set acceleration control status of the ITS station.

Request (UtCamTrigger_ SetAccelerationControlStatus TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x32 | B | G | E | C | A | CC | L | X |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x32 |
| B | 1 bit | 0: brake pedal inactive 1: brake pedal active |
| G | 1 bit | 0: gas pedal inactive 1: gas pedal active |
| E | 1 bit | 0: emergency brake inactive 1: emergency brake active |
| C | 1 bit | 0: collision warining inactive 1: collision warning active |
| A | 1 bit | 0: ACC inactive 1: ACC active |
| CC | 1 bit | 0: cruise control inactive 1: cruise control active |
| L | 1 bit | 0: speed limiter inactive 1: speed limiter active |
| X | 1 bit | Reserved |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.4	SetExteriorLightsStatus

This message is used to set exterior lights status of the ITS station.

Request (UtCamTrigger_setExteriorLightsStatus TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x33 | LB | HB | LT | RT | D | R | F | P |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x33 |
| LB | 1 bit | 0: low beam headlights off 1: low beam headlights on |
| HB | 1 bit | 0: high beam off 1: high beam headlights on |
| LT | 1 bit | 0: left turn signal off 1: left turn signal on |
| RT | 1 bit | 0: right turn signal off 1: right turn signal on |
| D | 1 bit | 0: daytime running lights off 1: daytime running lights on |
| R | 1 bit | 0: reverse light off 1: reverse lights on |
| F | 1 bit | 0: fog light off 1: fog light on |
| P | 1 bit | 0: parking lights off 1: parking lights on |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.5	ChangeHeading

This message is used to change the heading of the ITS station. The new heading of the ITS station is reflect Direction parameter.

Request (UtCamTrigger_changeHeading TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |
| MessageType = 0x34 | Direction |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x34 |
| Direction | 2 bytes | Integer value from 0 to 3600 0: North 900: East 1800: South 2700: West 3600: Unavailable |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.6	SetDriveDirection

This message is used to change the direction of the ITS station.

Request (UtCamTrigger_setDriveDirection TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x35 | Direction |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x35 |
| Direction | 1 byte | 0x00: Forward 0x01: Backward 0x02: Unaivailable |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.7	ChangeYawRate

This message is used to change the yaw rate of the ITS station.

Request (UtCamTrigger_changeYawRate TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |
| MessageType = 0x36 | YawRate |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x36 |
| YawRate | 2 bytes | Signed integer. Curvature change from -32768 to +32767 |

Response (UtCamTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x21 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x21 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.2.8	CamEventIndication

This message is used to indicate reception of CAM information by IUT.

Indication (UtCamEventInd UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x23 | CamPduLength | CamPdu |
|  | ... |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x23 |
| CamPduLength | 2 bytes | Length of 'CamPdu' field |
| CamPdu | Variable | Received CAM |

# C.3	DENM Upper Tester Primitives

## C.3.1	GenerateDenmEvent

This message is used to create a new DENM event.

Request (UtDenmTrigger TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x10 | V | R | X | I | X | DetectionTime |
| … |
| ValidityDuration | RepetitionDuration |
| … | InfoQuality | Cause |
| SubCause | RelevanceDistance | TrafficDirection | TransmissionInterval |
| … | KAF |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x10 |
| V | 1 bit | 0: validityDuration to be ignored 1: validityDuration to be used |
| R | 1 bit | 0: RepetitionDuration to be ignored 1: RepetitionDuration to be used |
| X | 3 bits | reserved |
| I | 1 bit | 0: TransmissionInterval to be ignored 1: TransmissionInterval to be used |
| X | 2 bits | reserved |
| DetectionTime | 6 bytes | Unsigned integer. From 0 to 3153600000000 |
| ValidityDuration | 3 bytes | Unsigned integer. From 0 to 86400 (s) |
| RepetitionDuration | 3 bytes | Unsigned integer. From 0 to 86400 (s) |
| InfoQuality | 1 byte | 0x00: Unavailable 0x01: Lowest … 0x07: Highest |
| Cause | 1 byte | Event cause ID |
| Subcause | 1 byte | Event sub-cause ID |
| RelevanceDistance | 1 byte | 0x00: less than 50m 0x01: less than 100m 0x02: less than 200m 0x03: less than 500m 0x04: less than 1000m 0x05: less than 5km 0x06: less than 10km 0x07: over 10km |
| TrafficDirection | 1 byte | 0x00: unavailable 0x01: upstream traffic 0x02: downstream traffic 0x03: all traffic direction |
| TransmissionInterval | 2 bytes | From 1 to 10000 (ms) |
| KAF | 1 byte | 0x00: No Keep-Alive Forwarding 0x01: Keep-Alive Forwarding |

Response (UtDenmTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x11 | Result | StationID |
| ... | SequenceNo |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x11 |
| Result | 1 byte | 0x00: Failure 0x01: Success |
| StationId | 4 bytes | Station ID |
| SequenceNo | 2 bytes | Event sequence number |

## C.3.2	UpdateDenmEvent

This message is used to update expiration time of an existing DENM event.

Request (UtDenmUpdate TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x12 | V | S | D | T | C | I | X | StationId |
| … | SequenceNo |
| DetectionTime |
| … | ValidityDuration |
| … | InfoQuality | Cause | SubCause |
| RelevanceDistance | TrafficDirection | TransmissionInterval |
| KAF |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x12 |
| V | 1 bit | 0: validityDuration to be ignored 1: validityDuration to be used |
| S | 1 bit | 0: InfoQuality, CauseCaude SubCauseCode to be ignored 1: InfoQuality, CauseCaude SubCauseCode to be used |
| D | 1 bit | 0: relevanceDistance to be ignored 1: relevanceDistance to be used |
| T | 1 bit | 0: TrafficDirection to be ignored 1: TrafficDirection to be used |
| C | 1 bit | 0: TrafficClass to be ignored 1: TrafficClass to be used |
| I | 1 bit | 0: TransmissionInterval to be ignored 1: TransmissionInterval to be used |
| X | 2 bits | reserved |
| StationId | 4 bytes | Original event’s station ID |
| SequenceNo | 2 bytes | Original event’s sequence number |
| DetectionTime | 6 bytes | Unsigned integer. From 0 to 3153600000000 |
| ValidityDuration | 3 bytes | Unsigned integer. From 0 to 86400 (s) |
| InfoQuality | 1 byte | 0x00: Unavailable 0x01: Lowest … 0x07: Highest |
| Cause | 1 byte | Event cause ID |
| Subcause | 1 byte | Event sub-cause ID |
| RelevanceDistance | 1 byte | 0x00: less than 50m 0x01: less than 100m 0x02: less than 200m 0x03: less than 500m 0x04: less than 1000m 0x05: less than 5km 0x06: less than 10km 0x07: over 10km |
| TrafficDirection | 1 byte | 0x00: unavailable 0x01: upstream traffic 0x02: downstream traffic 0x03: all traffic direction |
| TransmissionInterval | 2 bytes | From 1 to 10000 (ms) |
| KAF | 1 byte | 0x00: No Keep-Alive Forwarding 0x01: Keep-Alive Forwarding |

Response (UtDenmUpdateResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x13 | Result | StationID |
| ... | SequenceNo |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x13 |
| Result | 1 byte | 0x00: Failure 0x01: Success |
| StationId | 4 bytes | Station ID |
| SequenceNo | 2 bytes | Event sequence number |

## C.3.3	TerminateDenmEvent

This message is used to terminate an existing DENM event.

Request (UtDenmTermination TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x14 | StationId |
| ... | SequenceNo |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x14 |
| StationId | 4 bytes | Original Station ID |
| SequenceNo | 2 bytes | Event sequence number |

Response (UtDenmTerminationResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x15 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x15 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.3.4	DenmEventIndication

This message is used to indicate reception of DENM information by IUT.

Indication (UtDenmEventInd UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x17 | DenmPduLength | DenmPdu |
|  | ... |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x17 |
| DenmPduLength | 2 bytes | Length of 'DenmPdu' field |
| DenmPdu | Variable | Received DENM |

# C.4	GeoNetworking Upper Tester Primitives

## C.4.1	GenerateGeoUnicast

This message is used to trigger a GeoUnicast message.

Request (UtGnTrigger_geoUnicast TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x50 | DstGnAddress |
| ... |
| ... | Lifetime | TrafficClass |
| PayloadLength | Payload |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x50 |
| DstGnAddr | 8 bytes | Destination GN Address |
| Lifetime | 2 bytes | Packet lifetime in miliseconds |
| TrafficClass | 1 byte | Traffic Class value |
| PayloadLength | 2 bytes | Length of 'Payload' field |
| Payload | Variable | Packet's final payload |

Response (UtGnTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x41 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x41 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.4.2	GenerateGeoBroadcast

This message is used to trigger a GeoBroadcast message.

Request (UtGnTrigger_geoBroadcast TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x51 | Shape | Lifetime |
| TrafficClass | Latitude |
|  | Longitude |
|  | DistanceA | DistanceB |
|  | Angle | PayloadLength |
|  | Payload |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x51 |
| Shape | 1 byte | 0: Circle 1: Rectangle 2: Ellipse |
| Lifetime | 2 bytes | Packet lifetime in miliseconds |
| TrafficClass | 1 byte | Traffic Class value |
| Latitude | 4 bytes | Destination area latitude (1/10 degrees) |
| Longitude | 4 bytes | Destination area longitude (1/10 degrees) |
| DistanceA | 2 bytes | Destination area distance A |
| DistanceB | 2 bytes | Destination area distance B |
| Angle | 2 bytes | Destination area angle |
| PayloadLength | 2 bytes | Length of 'Payload' field |
| Payload | Variable | Packet's final payload |

Response (UtGnTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x41 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x41 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.4.3	GenerateGeoAnycast

This message is used to trigger a GeoAnycast message.

Request (UtGnTrigger_geoAnycast TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x52 | Shape | Lifetime |
| TrafficClass | Latitude |
|  | Longitude |
|  | DistanceA | DistanceB |
|  | Angle | PayloadLength |
|  | Payload |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x52 |
| Shape | 1 byte | 0: Circle 1: Rectangle 2: Ellipse |
| Lifetime | 2 bytes | Packet lifetime in miliseconds |
| TrafficClass | 1 byte | Traffic Class value |
| Latitude | 4 bytes | Destination area latitude (1/10 degrees) |
| Longitude | 4 bytes | Destination area longitude (1/10 degrees) |
| DistanceA | 2 bytes | Destination area distance A |
| DistanceB | 2 bytes | Destination area distance B |
| Angle | 2 bytes | Destination area angle |
| PayloadLength | 2 bytes | Length of 'Payload' field |
| Payload | Variable | Packet's final payload |

Response (UtGnTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x41 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x41 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.4.4	GenerateSHB

This message is used to trigger a SHB message.

Request (UtGnTrigger_shb TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x53 | TrafficClass | PayloadLength |
| Payload |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x53 |
| TrafficClass | 1 byte | Traffic Class value |
| PayloadLength | 2 bytes | Length of 'Payload' field |
| Payload | Variable | Packet's final payload |

Response (UtGnTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x41 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x41 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.4.5	GenerateTSB

This message is used to trigger a TSB message.

Request (UtGnTrigger_tsb TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x54 | NbHops | TrafficClass | PayloadLength |
|  | Payload |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x54 |
| NbHops | 1 byte | Number of hops |
| TrafficClass | 1 byte | Traffic Class value |
| PayloadLength | 2 bytes | Length of 'Payload' field |
| Payload | Variable | Packet's final payload |

Response (UtGnTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x41 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x41 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.4.6	GnEventIndication

This message is used to check whether payload contained in GeoNetworking PDU has been transmitted to upper layer (CAM/DENM/IPv6).

Indication (UtGnEventInd UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x17 | PacketLength | Packet |
|  | ... |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x17 |
| PacketLength | 2 bytes | Length of 'Packet' field |
| Packet | Variable | Packet's final payload |

# C.5	IPv6OverGeoNetworking Upper Tester Primitives

## C.5.1	SendIPv6Message

This message is used to trigger the sending of an IPv6 message on a specified network interface.

Request (UtGn6Trigger TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x80 | InterfaceLength | InterfaceName | … |  |
| SrcMacAddress |
| … | DestMacAddress |
| … |
| PacketLength | IPv6Packet | … |  |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x80 |
| InterfaceLength | 1 byte | Length of “InterfaceName” field |
| InterfaceName | InterfaceLength x 1byte | Name of the interface on which to send the IPv6 packet |
| SrcMacAddress | 6 bytes | Source MAC address |
| DestMacAddress | 6 bytes | Destination MAC address |
| PacketLength | 2 bytes | Length of the “IPv6Packet” field |
| IPv6Packet | Variable | IPv6 packet to be sent |

Response (UtGn6TriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x81 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x81 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.5.2	GetInterfaceInfos

This message is used by the Test System to retrieve the configuration of network interfaces on IUT.

Request (UtGn6GetInterfaceInfo TS->UT):

| 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x84 |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x84 |

Response (UtGn6GetInterfaceInfoResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x85 | InterfaceCount | InterfaceLength[0] | InterfaceName[1] |
| … | AddressCount[0] | Addresses[0][0] |
| … |
| … |
| … |
| … | Addresses[0][1] |
| … | InterfaceLength[1] | InterfaceName[1] |
| … | … |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x85 |
| InterfaceCount | 1 byte | Number of interface descriptors |
| Interface Descriptor | InterfaceLength | 1 byte | Length of “InterfaceName” field |
|  | InterfaceName | InterfaceLength x 1byte | Name of the interface |
|  | AddressCount | 1 byte | Number of configured IPv6 address on the interface |
|  | Addresses | AddressCount x 16 bytes | IPv6 addresses configured on interface |

## C.5.3	Gn6EventIndication

This message is used to check whether payload contained in GeoNetworking PDU has been transmitted to upper layer (CAM/DENM/IPv6).

Indication (UtGnEventInd UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x83 | InterfaceLength | InterfaceName | … |  |
| PacketLength | IPv6Packet |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x83 |
| InterfaceLength | 1 byte | Length of “InterfaceName” field |
| InterfaceName | InterfaceLength x 1byte | Name of the interface on the IPv6 packet has been received |
| PacketLength | 2 bytes | Length of ' IPv6Packet' field |
| IPv6Packet | Variable | Received IPv6 packet |

# C.6	BTP Upper Tester Primitives

## C.6.1	GenerateBtpA

This message is used to trigger a BTP-A message.

Request (UtBtpTrigger_A TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x70 | DestPort | SrcPort |
| … |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x70 |
| DestPort | 2 bytes | Destination port |
| SrcPort | 2 bytes | Source port |

Response (UtBtpTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x61 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x61 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.6.2	GenerateBtpB

This message is used to trigger a BTP-B message.

Request (UtBtpTrigger_B TS->UT):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x71 | DestPort | DestPortInfo |
| … |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x71 |
| DestPort | 2 bytes | Destination port |
| DestPortInfo | 2 bytes | Destination port info |

Response (UtBtpTriggerResult UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MessageType = 0x61 | Result |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x61 |
| Result | 1 byte | 0x00: Failure 0x01: Success |

## C.6.3	BtpEventIndication

This message is used to check whether payload contained in BTP PDU has been transmitted to upper layer.

Indication (UtBtpEventInd UT->TS):

| 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| MessageType = 0x63 | PacketLength | Packet |
|  | ... |

| Name | Length | Value |
| --- | --- | --- |
| MessageType | 1 byte | 0x63 |
| PacketLength | 2 bytes | Length of 'Packet' field |
| Packet | Variable | Packet's final payload |

Annex D:
MK2 bridge application

The software modules are contained in archive AnnexD_MK2_Bridge_Application.zip which is included in archive tr_103099v010101p0.zip which accompanies the present document.

Annex E:
Example of Test Platform implementation

The test platform used by ETSI STF424 for validating ITS conformance test suites has been developed using the following tools and components:

Standard PC equipped with two Ethernet network cards (It is possible to use the same single network card for both tasks, but it is less practical and gives less flexibility).
One network card (Mac address: 00-A0-24-AD-56-FF) is used to communicate with G5 device.
The second one (Mac address: 00-50-56-C0-00-08) is used to establish upper tester link with SUT and is configured with IP address 192.168.56.1/24.

Windows XP Professional operating system (32 bits)
No special requirement concerning operating system. Theorically the platform can be used above Linux based operating system, as it is OS independent.

Testing Technologies TTworkbench Basic v13 with ASN.1 plugins
ASN.1 plugins are necessary for CAM and DENM codecs. Any other TTCN-3 test tool would be suitable with minimum adaptation as the test platform is tool independent.

Java™ JDK 1.6.0-24
All the software used in the test platform have been developed using Java™ language.

JnetPcap 1.3.0
This library is used for capturing and injecting raw Ethernet packets. It is a direct dependency of EthernetLayer module. For easy setup the jnetpcap.dll file has to be installed in C:\Windows\System32\ folder and the jnetpcap.jar has to be installed in C:\Windows\Sun\Java\lib\ext\ folder or equivalent. By doing this, no specific setting will be required to include JnetPcap library when building Test Adapter.

Cohda WirelessTM MK2
This device provides G5 connectivity to the test platform. This device features a G5 radion interface used to communicate with SUT and Ethernet interface that is connect to the test platform PC in order to transfer G5 packets to be sent/received via the radio interface.

Before running successfully any test, a certain number of settings have to be verified in TTworkbench:

Project has to be set for using Java™ JDK 1.6.0 as indicating in the following picture. Please note that JnetPcap should automatically appear in the library list:

Test Adapter and Codecs source folders have to be declared in project's Java Build Path:

Test Adapter and Codecs will then be automatically compiled if "Build automatically" option is set:

Alternatively, Test Adapter and Codecs precompiled libraries have to be referenced as external libraries

TTCN-3 test suites and ASN.1 definitions have to be copied to the project and declared as TTCN-3 source folders:

The test suites need to be compiled using the "Rebuild All" button:

TT3 plugins have to be configured using the provided xml files:

Test adapter parameters have to be adjusted in taconfig.xml file:

<parameter id="taParams">
      <parameter id="DEBUG_ENABLED" value="ALL"/>
      <parameter id="camPort" value="BTP/GN/ETH"/>
      <parameter id="denmPort" value="BTP/GN/ETH"/>
      <parameter id="btpPort" value="GN/ETH"/>
      <parameter id="geoNetworkingPort" value="ETH"/>
      <parameter id="ipv6OverGeoNetworkingPort" value="Debug"/>
      <parameter id="CamUpperTester" value="Operator"/>
      <parameter id="CamUpperTesterSettings" value=""/>
      <parameter id="DenmUpperTester" value="Operator"/>
      <parameter id="DenmUpperTesterSettings" value=""/>
      <parameter id="BtpUpperTester" value="Operator"/>
      <parameter id="BtpUpperTesterSettings" value=""/>
      <parameter id="GnUpperTester" value="Generic"/>
      <parameter id="GnUpperTesterSettings" 
            value="NwtaTrigger:192.168.56.10:1600:1601"/>
      <parameter id="LocalEthernetMAC" value="00A024AD56FF"/>
      <parameter id="IutEthernetTypeValue" value="0x0707"/>
      <parameter id="LinkLayer_MTC" value="BABEBABE0000"/>
      <parameter id="LinkLayer_NodeA" value="BABEBABE0001"/>
      <parameter id="LinkLayer_NodeB" value="BABEBABE0002"/>
      <parameter id="LinkLayer_NodeC" value="BABEBABE0003"/>
      <parameter id="LinkLayer_NodeD" value="BABEBABE0004"/>
      <parameter id="Gn6RemoteAdapterIp" value="192.168.56.10"/>
      <parameter id="Gn6RemoteAdapterPort" value="42000"/>
</parameter>

Table E.1 summarizes the authorised values for these parameters.

Table E.1: Test Adapter Parameters

| Parameter | Description | Allowed values |
| --- | --- | --- |
| DEBUG_ENABLED | Indicates whether Codecs and Test Adapter produce debugging logs | ALL, NONE, OFF |
| camPort | Defines the lower stack of CamPort | Any combinaison of valid layer identifier separated by "/" symbol: ETH BTP GN UdpIp Debug (pseudo layer that dumps packet to console) Loopback (pseudo layer that reinjects the packets) |
| denmPort | Defines the lower stack of CamPort |  |
| btpPort | Defines the lower stack of CamPort |  |
| geoNetworkingPort | Defines the lower stack of CamPort |  |
| ipv6OverGeoNetworkingPort | Defines the lower stack of CamPort |  |
| CamUpperTester DenmUpperTester BtpUpperTester GnUpperTester | Selects the type of Upper tester to be used for each test suite | Operator, Yes, Generic |
| CamUpperTesterSettings DenmUpperTesterSettings BtpUpperTesterSettings GnUpperTesterSettings | Defines Upper Tester specific settings like remote IP addresses, UDP ports, etc. | Upper tester specific |
| LocalEthernetMAC | MAC Address of the Ethernet card used to communicate with G5 equipment | Hexstring representation of Mac Address without separator |
| IutEthernetTypeValue | Ethertype value to be used for sending and capturing packets | Integer 0 to 65 635. Should be 0x0707 |
| LinkLayer_MTC LinkLayer_NodeA LinkLayer_NodeB LinkLayer_NodeC LinkLayer_NodeD | MAC addresses used by simulated ITS nodes | Hexstring representation of Mac Address without separator |
| Gn6RemoteAdapterIp | IP Address of GN6 Remote Adapter | Standard IP address notation |
| Gn6RemoteAdapterPort | UDP port of GN6 Remote Adapter | Integer 0 to 65 635. |

Annex F:
Complete Test Adapter class diagram

Figure F.1: Test adapter complete class diagram

Annex G:
Validated ATS in TTCN-3 and ASN.1 modules

During the validation a number of issues were fixed in the ATSs of the different modules (refer to the appropriate reports TR 103 061-1 [i.4], -2 [i.5], -3 [i.6], -4 [i.7] and -5 [i.8]).

The software modules are contained in archive AnnexG_Validated_TTCN.zip which is included in archive tr_103099v010101p0.zip which accompanies the present document.

Annex H:
Bibliography

This annex lists all test specifications which were integrated with the Conformance Validation Framework:

ETSI TS 102 868-1 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Co-operative Awareness Messages (CAM); Part 1: Test requirements and Protocol Implementation Conformance Statement (PICS) proforma".

ETSI TS 102 868-2 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Co-operative Awareness Messages (CAM); Part 2: Test Suite Structure and Test Purposes (TSS&TP)".

ETSI TS 102 869-1 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Of Decentralized Environmental Notification basic Service (DENM); Part 1: Test requirements and Protocol Implementation Conformance Statement (PICS) proforma".

ETSI TS 102 869-2 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specification for Of Decentralized Environmental Notification basic Service (DENM); Part 2: Test Suite Structure and Test Purposes (TSS&TP)".

ETSI TS 102 870-1 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specifications for Geonetworking Basic Transport Protocol (BTP); Part 1: Test requirements and Protocol Implementation Conformance Statement (PICS) proforma".

ETSI TS 102 870-2 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specifications for Geonetworking Basic Transport Protocol (BTP); Part 2: Test Suite Structure and Test Purposes (TSS&TP)".

ETSI TS 102 859-1 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specifications for Transmission of IP packets over GeoNetworking; Part 1: Test requirements and Protocol Implementation Conformance Statement (PICS) proforma".

ETSI TS 102 859-2 (V.1.1.1): "Intelligent Transport Systems (ITS); Testing; Conformance test specifications for Transmission of IP packets over GeoNetworking; Part 2: Test Suite Structure and Test Purposes (TSS&TP)".

ETSI ES 201 873-1 (V4.2.1): "Methods for Testing and Specification (MTS); The Testing and Test Control Notation version 3; Part 1: TTCN-3 Core Language".

ETSI EG 202 798 (V1.1.1): "Intelligent Transport Systems (ITS); Testing; Framework for conformance and interoperability testing".

JNetPcap library: "http://jnetpcap.com/".

List of figures

Figure 1: General architecture	9

Figure 2: Communication via G5 adaptation box	10

Figure 3: Communication via Ethernet	10

Figure 4: Codec package organisation	11

Figure 5: Codec class diagram	12

Figure 6: Message sending sequence diagram	14

Figure 7: Message reception sequence diagram	14

Figure 8: Test Adapter class diagram	15

Figure 9: Port initialisation sequence diagram	16

Figure 10: Upper Tester architecture	18

Figure F.1: Test adapter complete class diagram	38

# History

| Document history |
| --- |
| V1.1.1 | November 2012 | Publication |