TS 103 260-1 V0.0.6 (2014-04)

Satellite Earth Stations and Systems (SES);

Reference scenario for the deployment of emergency communications;

Part 1: Earthquake

TECHNICAL SPECIFICATION

Reference

DTS/SES-00341-1

Keywords

Emergency, satellite, telecommunications, earthquake

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# Contents

Contents	3

Intellectual Property Rights	5

Foreword	5

Introduction	5

1	Scope	6

2	References	6

2.1	Normative references	6

2.2	Informative references	6

3	Definitions and abbreviations	7

3.1	Definitions	7

3.2	Abbreviations	7

4	Disaster Scenario	9

4.1	Scenario Definition	9

4.1.1	Physical Effects	9

4.1.1.1	Collapse of buildings	9

4.1.1.2	Fire (F)	9

4.1.1.3	Chemical Accident (CA)	9

4.1.1.4	Disruption infrastructure	10

4.1.1.4.1	Power	10

4.1.1.4.2	Transport facilities	10

4.1.1.4.3	Water supply	10

4.1.1.4.4	Sanitation	10

4.1.1.4.5	Telecommunication	10

4.1.1.5	Disruption of services	10

4.1.2	Disaster Response Actions	10

4.1.2.1	General	10

4.1.2.2	Situation assessment	10

4.1.2.3	Search and Rescue	11

4.1.2.4	Triage/ First Aid	11

4.1.2.5	Fire-fighting/ Chemical incidents	11

4.1.2.6	Command and control structures	12

4.1.2.7	Logistics	12

4.1.2.8	Evacuation of population	12

4.1.2.9	Emergency shelters	12

4.1.2.10	Information	13

4.1.3	Entities involved	13

4.1.4	Quantitative timeline	14

5	Information Exchanges	14

5.1	Characteristics of Information Exchanges	15

5.1.1	Communications services requirements	15

5.1.2	Speech services	15

5.1.2.1	Point To Point Speech Services	15

5.1.2.2	Group Speech Services	15

5.1.2.3	Push To Talk (PoC)/Command and Control (C&C) features	15

5.1.2.4	Video Tele-Conferencing	16

5.1.2.5	Data services	16

5.1.2.6	Paging (short message) Services	16

5.1.2.7	Status Monitoring and Location Services	17

5.1.2.8	FRs – FRs	18

5.1.2.9	FRs – corresponding CP	18

5.1.2.10	CP – CP	18

5.1.2.11	CP – EATF	18

5.1.2.12	CPs – External entities	18

5.1.2.13	CPs – External information	18

5.1.3	User requirements for Information Exchange	21

6	Topology Model	21

Annex A (informative): Major Recent Earthquakes	22

Annex B (informative): Fictive example scenario timeline	22

Annex <X> (informative): Bibliography	25

7	History	26

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Specification (TS) has been produced by ETSI Technical Committee Satellite Earth Stations and Systems (SES).

The present document is part 1 of a two-part deliverable.

# Introduction

Major emergencies or disasters may result in a need for additional resources in local telecommunications networks, especially if they are damaged or overloaded, in order to maintain or enhance the ability of rescue workers to respond and coordinate their activities effectively. Satellites can play a role in replacing or supplementing other telecommunications links in these scenarios. For example satellite systems can provide:

broadband and secure communication facilities anywhere/anytime in locations where no other facilities are available, and

temporary replacement of broken/saturated infrastructures by means of backhauling

fast deployment of temporary communication networks in emergency situations.

Hence a set of requirements for such links needs to be established in emergency situations.

The work is also a response to EC mandate M/496, specifically dossier 9 "Disaster Management" part 2: “Emergency Telecommunication Services” which aims to support standardization for the optimal needs of the emergency responders.

# Scope

The present document defines a reference scenario for an earthquake which is relevant for the evaluation and dimensioning of satellite-based emergency telecommunications.

This scenario includes potential roles for satellite systems for the telecommunication services identified.

The services defined for these scenarios are limited to safety services (i.e. not security such as law enforcement).

This document defines firstly a disaster scenario. It then defines the gross communication needs of the actors involved. Finally the more detailed results of topology modelling of these communications requirements is provided.

# References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication, ETSI cannot guarantee their long term validity.

## Normative references

The following referenced documents are necessary for the application of the present document.

## Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

- ETSI TR 102 180: "Emergency Communications (EMTEL); Basis of requirements for communication of individuals with authorities/organizations in case of distress (Emergency call handling)".

- ETSI TS 102 181: "Emergency Communications (EMTEL); Requirements for communication between authorities/organizations during emergencies".

- ETSI TS 102 182: “Emergency Communications (EMTEL); Requirements for cimmunications from authorities/organizations to individuals, groups or the general public during emergencies”.

- ETSI TR 102 299: "Emergency Communications (EMTEL); Collection of European Regulatory Texts and orientations".

- ETSI TR 102 410: "Emergency Communications (EMTEL); Basis of requirements for communications between individuals and between individuals and authorities whilst emergencies are in progress".

- ETSI TR 102 476: "Emergency Communications (EMTEL); Emergency calls and VoIP: possible short and long term solutions and standardization activities".

- ETSI TR 102 641: “Satellite Earth Stations and Systems (SES); Overview of present satellite emergency communications resources”.

- ETSI TR 103 166: "Satellite Earth Stations and Systems (SES); Satellite Emergency Communications (SatEC); Emergency Communication Cell over Satellite (ECCS)".

- ETSI TS 103 260-2: “Satellite Earth Stations and Systems (SES); Reference scenario for the deployment of emergency communications; Part 2: Mass Casualty Incident in Public Transportation”

- Mandates from the European Commission?????

- ITU-T Recommendation G.1010: End-user multimedia QoS categories

- ITU-R Resolution 647: Space services emergency database

- Report ITU-R S.2151-1: “Use and examples of systems in the fixed satellite service in the event of natural disasters and similar emergencies for warning and relief operations”

- “Environmental health in emergencies and disasters: a practical guide”. 
Edited by B. Wisner and J. Adams, World Health Organization, 2003.

- European Union Handbook on assistance intervention in the Frame of community mechanism for the cooperation of civil protection

# Definitions and abbreviations

N.B. All of this clause will be updated when the document is stable.

## Definitions

For the purposes of the present document, the following terms and definitions apply:

Aftershocks: Smaller earthquakes over the days/ weeks following the main earthquake. These may be sufficiently strong to cause substantial added damage.

Emergency: an event or situation which threatens serious damage to human welfare or to the environment.

Emergency Control Centre (ECC): facilities used by emergency organizations to handle rescue actions in answer to an emergency calls (

Emergency service: service, recognized as such by the Member State, that provides immediate and rapid assistance in situations where there is a direct risk to life or limb, individual or public health or safety, to private or public property, or the environment but not necessarily limited to these situations

Field emergency control centre (FECC): facilities used by emergency organizations to handle rescue actions in the field

Flash flood: A rapid flooding of low-lying areas; washes, rivers, dry lakes and basins. (http://en.wikipedia.org/wiki/Flash_flood)

Incident area: area where the incident occurred, and/or the area which needs communication coverage to manage the response implemented

Public Safety Answering Point (PSAP): physical location where emergency calls are received under the responsibility of a public authority

## Abbreviations

For the purposes of the present document, the following abbreviations apply:

CAP	Common Alerting Protocol

CEPT	Conférence Européenne des Postes et Télécommunications

ECA	European Common Allocation

ECC	European Communications Committee

ECC	Emergency Control Centre

ELT	Emergency Locator Transmitter

EMTEL	EMergency TELecommunications

EPIRB	Emergency Position Indicating Radio Beacon

ETSI	European Telecommunications Standards Institute

FECC 	Field emergency control centre

FSS	Fixed Satellite Service

GNSS	Global Navigation Satellite System

GOES	Geostationary Operational Environmental Satellite

GPS	Global Positioning System

GSO	Geostationary Orbit

ICT	Information and Communication Technology

IPR	Intellectual Property Right

ISO	International Standardization Organization

ITU	International Telecommunication Union

ITU-R	International Telecommunication Union Radiocommunications Sector

ITU-T	International Telecommunication Union Telecommunications Sector

LEO	Low Earth Orbit

MSS	Mobile Satellite Service

NRBC	Nuclear, Radiological, Bacteriological, Chemical

OASIS	Organization for the Advancement of Structured Information Standards

PAMR	Public Access Mobile Radio

PLB	Personal Locator Beacon

PLMN	Public Land Mobile Network

PMR	Private Mobile Radio

PPDR	Public Protection and Disaster Relief

PSAP	Public Safety Answering Point

PSTN	Public Switched Telephony Network

RCC	Rescue Coordination Centre

RDSS	Radio Determination Satellite Service

SARSAT	Search And Rescue Satellite-Aided Tracking

SatEC	Satellite Emergency Communications Working Group

SCN	Satellite Communications and Navigation Working Group

SG	Study Group

SES	Satellite Earth Station and Systems

TC	Technical Committee

TETRA	Terrestrial Trunked Radio

TR	Technical Report

TS	Technical Specification

# Disaster Scenario

This clause firstly defines an earthquake scenario in terms of its main constituent events and secondly by its physical consequences. Subsequently the response actions by emergency forces to this scenario are defined in terms of the casualties involved, the actors and organisations, overall operating modes, duration and dimensioning factors etc..

This scenario is chosen to be sufficiently generic to be considered representative of many potential future earthquakes, and thus to allow relevant communication characteristics for current and future needs to be established.

## Scenario Definition

A summary of recent earthquakes and their effects is given in Annex A as examples of the scale of events being considered.

The main assumption is that the earthquake affects an urban area.

The Earthquake is assumed to be of a magnitude sufficient to cause a multitude of physical effects, such as collapsed buildings, flash-floods/tsunamis, disruption of infrastructure with resulting traffic accidents, lack of power, lack of telecommunications, fires, risks of chemical accidents etc. Each of these incidents may not differ much from isolated similar incidents of this nature, but the added challenge is that the incidents happen at the same time, thus reinforcing the effects and strains on available resources.

### Physical Effects

The effects of the earthquake on the population and on local infrastructure can last for an appreciable time, even many years, but the focus here will be on the period for which emergency communications are needed. The nature of these consequences is as follows.

#### Collapse of buildings

Domestic and commercial buildings in varying state of collapse.

#### Fire (F)

Incident goes on and spreads till successfully combatted by services

Fire-fighters and smoke-divers at forefront

Other rescue workers start work when fire is under control

Added risks (chemicals etc.)

#### Chemical Accident (CA)

Different effects:

Pollution of water etc

Visible/ invisible cloud (high level of scare-factor)

May have effects in a wide geographical area

Information and specification on substances often not available

Effects can be immediate and/ or delayed

#### Disruption infrastructure

##### Power

Major earthquakes invariably lead to loss of power. This may be caused by power plants being hit. In addition the supply lines will be broken, typically in several areas. Some critical facilities, e.g. hospitals, may have separate emergency power supply, but all other facilities will be without power, probably for an extended period of time.

##### Transport facilities

Transport facilities, such as roads, railway lines, harbours etc. will be disrupted/ destroyed. This will lead to challenges both for the rescue activities in terms of access to incident sites, evacuation of the victims, and broken lines of supply.

##### Water supply

The effects on water supplies are partly due to the distribution network (pipes) being destroyed. In addition, water sources or distribution systems may be polluted due to protective barriers breaking down.

##### Sanitation

Sewage systems, garbage collection etc. may be rendered non-functional by an earthquake. Combined with lack of housing, evacuation of victims to temporary shelters, difficulties with supply of clean water, this constitutes a serious risk for epidemics.

##### Telecommunication

A major earthquake may influence both telecommunication systems based on fixed lines and terrestrial systems. The effect may vary from large areas being completely without any means of telecommunication to coverage and capacity being reduced in parts of the disaster area. Over time (hours) lack of power supply will also lead to terminals not functioning. The latter will obviously also affect satellite communication systems.

#### Disruption of services

Emergency services (police, fire services, health services): In disaster situations the demands on emergency services are substantial. In addition, the services themselves may be struck by the disaster.

Supplies: The broken infrastructure will mean that supply chains will be broken. The immediate effect is on rescue work itself, which will be delayed due to reduced access.

In addition, Basic supplies, such as water, food, clothing, facilities for basic hygiene (latrines etc) will have to be organised.

### Disaster Response Actions

#### General

A major earthquake in an urban setting will have multiple effects. Collapse of buildings and broken infrastructure, such as roads, water supply and telecommunication systems will be universally present. These will obviously represent challenges for all the rescue work, but are not repeated for each of the responses listed below.

#### Situation assessment

Initially done by members of public who witness the incident.

Contact authorities (PSAP, local representatives, e.g. hospitals, police stations, fire departments)

Contact media (newspapers, radio stations)

Contact other members of the public (family/ relatives, friends)

PSAP/ ECC

Structured interview of caller

Active fact-finding

Emergency resources

Initial assessment upon arrival, reporting to ECC

In-depth assessments and monitoring as incident/ disaster, reporting to ECC

Sensors, e.g. water level monitors in rivers, automatic fire alarms, gas alarms

#### Search and Rescue

Preparation (ECC/ Site management)

Maps/ drawings

Estimated number of persons to be found/ rescued

Estimated need of resources

Activating/ recruiting resources

Implementation (Site management)

Allocation SAR teams

Reporting on progress/ sitreps ??????   to ECC

#### Triage/ First Aid

Preparation (Site management/ ECC)

Needs assessment personnel

Needs assessment special resources (e.g. IV fluids, technical equipment)

Implementation (Health care team)

Prioritization

First aid/ temporary treatment

Referral/ medical evacuation

Documentation and reporting

#### Fire-fighting/ Chemical incidents

Preparation (Site management/ ECC)

Risk assessment (dangerous substances, risks for explosion, further flooding) (S

Needs assessment and mobilization special resources (e.g. technical equipment, specialists etc)

Implementation (Fire-fighting team)

Fire-fighting including smoke-diving

Containing/ measuring hazardous material/ dangerous substances

Assessing and reporting progress/ risk development

#### Command and control structures

set-up of FECCs for involved disciplines

coordination of working/arriving rescue forces and resources

mapping of patients to transport vehicles and destinations

coordination of interim care centre

coordination among involved FECCs and ECC

reporting and demand notification to ECC

#### Logistics

Initial phase (ECC)

Assessment needed resources based on limited information

Primary allocation and mobilization of resources

Later phases (ECC/ Site management)

Maintaining inventory missing/ dead/ injured/ sheltered/ evacuated individuals

Disaster resource recruitment and allocation

General supplies (Food, shelter, equipment for sanitation etc.)

Non-medical evacuation

#### Evacuation of population

Initial phase (Hours/ Days)

Evacuation to safe haven close to the site: Emergency services/ Rescue personnel

Later phases

Evacuation to temporary dwellings: Emergency services/ Rescue Personnel/ Local Authorities

#### Emergency shelters

Immediate (Hours/ Days)

Tents, pit-latrines, mobile kitchens, emergency water supply, emergency food supply, heating, lights: Civil Protection

Temporary (Weeks/ Months)

Temporary housing, food supply, water supply, electricity, sewage: Local Authorities/ Civil Protection

#### Information

Internal reporting (Site management/ ECC)

Regular reporting on progress (at given intervals)

Specific reporting on milestones/ significant achievements or problems (ad hoc)

Reporting to media (ECC)

Press releases

Press conferences

Interviews

Liaison affected population (ECC)

Relatives call-centre and conference facilities

“I am alive” to/ from site

### Entities involved

Depending on local/ national organization of services and division of tasks/ responsibilities, the entities involved and their individual areas of work may differ. Table X provides a overview of entities that are most commonly involved, and for which responses they are mainly involved. Depending on the severity of the earthquake, resources may be drawn nationally, regionally and internationally (e.g. involving fire-fighters from several countries)

### Quantitative timeline

A major earthquake will lead to a series of activities/ tasks distributed over time. Annex B gives an example of how this could happen. In reality the times will vary, but the sequence of response-tasks will be as described below????.

# Information Exchanges

The information exchanges concern those between all of the entities and individuals involved as defined in clause 4.1.3. The general flows of information exchanges are common to the Emergemcy Scenarios in Parts 1 & 2 of this specification and are shown in Figure 5-1 below.

RJM: Reference to EMTEL???

Figure 5-1: Earthquake scenario information flows

This scenario has multi-disciplinary rescue teams: for example discipline A (Fire& Rescue team), Discipline  B (Health and medical emergency team) and Discipline C (police or state armed forces).

## Characteristics of Information Exchanges

### Communications services requirements

With respect to Figure 5-1, the efficient exchange of information a single discipline team, between ECCs and the mobile, and between a temporary task force/command centre and a permanent PSAP/ECC may be facilitated by a number of communication services, described below.

### Speech services

Speech services are currently the most instinctive and most used communication services in emergencies, and this is likely to remain the case for years to come. For speech services there exist several universal requirements, characterized by:

Speech intelligibility and quality: that received speech is capable of being understood reliably and some cases high speech quality is desirable.

Call setup-time: short call set-up times enable rapid communication of relevant information.

End to end delay: in addition to the call set-up delay, it is recognized that where a duplex voice communication system imposes an end to end delay of over 500 ms there is degradation in the voice quality (International telephone connections and circuits - General Recommendations on the transmission quality for an entire international telephone connection One-way transmission time, ITU-T Recommendation G.114).

Also underlying networks (e.g. satellite and terrestrial) should have the capability to handle prioritized calls correctly, including the capability of pre-emption of unprioritized calls. Transit networks should convey priority related signalling in order to support end-to-end priority.

#### Point To Point Speech Services

Point to point duplex voice communications are required for many instances to provide communications, particularly between different authorities e.g. between commanders of different emergency services, between emergency service staff and external specialists.

#### Group Speech Services

Some examples of groups are:

Talk group: Point-to -multipoint group addressed communication established within a selectable predefined area. The coverage is associated to the group number and may be different of the total coverage. Resources are allocated all the time.

Emergency services call (authority to authority): Two options are possible:

Automatic call set-up of a pre-emptive open channel.

Using a pre-emptive priority, a predefined user (e.g. ECC) shall establish a call chosen on an operational basis.

Intrusion: This service shall allow an authorized user to intervene in an ongoing authority-to-authority call.

Priority call: This service shall allow a call to proceed before any other call with lower priority. The priority level can be assigned according to various criteria.

Dynamic group number assignment: This service shall allow a served user or an authorized user to create, modify and delete a group (dynamic regrouping/group merging).

#### Push To Talk (PoC)/Command and Control (C&C) features

Communication should require as little bandwidth as possible. Preferably it should not occupy lines permanently (as most of the group communication services mentioned above do) but data or voice should only be transmitted if information is actually exchanged. This holds especially for emergency communications characterized by many short speech items transmitted between talk group members over a certain period of time (e.g. giving and receiving instructions in C&C communication).

To facilitate this simplex communication services like push to talk can be used. PoC helps to avoid network congestion by transmitting voice over a data channel (GPRS, UMTS) and thus can be used even in times of high traffic on the communication network. Furthermore PoC provides flexible management of user groups.

#### Video Tele-Conferencing

VTC may be required to enable effective coordination between services at a command level or below. VTC services may be utilized to provide reconnaissance information from the incident back to control rooms. Note that  near-real-time video streaming can be considered as a data service (see below).

#### Data services

Data services are used to provide a large number of applications which can have widely differing requirements in terms of capacity, timeliness and robustness of the data service. Ideally, the communication networks should support the required data throughput and minimize end to end delay, especially for applications such as real time video. Noting the extreme circumstances which may be in force during an emergency, it may be desirable for networks to degrade gracefully when user requirements exceed the agreed levels of service.

Table 1 shows the diverse needs of data applications. Where data applications share the use of a data transmission capability, provision of sufficient capacity and effective management must be provided to ensure application data is communicated appropriately.

Table 1: Requirements on data applications (Source: TS 102 181)

| Service | Throughput | Timeliness | Need for preservation of data integrity |
| --- | --- | --- | --- |
| Email | Medium | Low | Low |
| Imaging | High | Low | Variable |
| Digital mapping/ Geographical information services | High | Variable | Variable |
| Location services | Low | High | High |
| Video (real time) | High | High | Low |
| Video (slow scan) | Medium | Low | Low |
| Data base access (remote) | Variable | Variable | High |
| Data base replication | High | Low | High |
| Personnel monitoring | Low | High | High |

Throughput: data volume in a given time.

Timeliness: importance of the information arriving within an agreed timeframe.

Preservation of data integrity: how (reliable) free from bit errors the information transmission needs to be. 
E.g. a bitmap image with some errors is still useable; a jpg image with some bit errors may be unreadable.

#### Paging (short message) Services

Paging services are used by a variety of authorities in order to contact their personnel, and paging services are available from a variety of networks and technologies. The network needs to be able to identify the requested authorized emergency agent(s), and then deploy the appropriate technology to contact them. This requirement may encompass different communication network technologies, services and applications such as paging, presence, texting, etc.

#### Status Monitoring and Location Services

Status monitoring includes a wide variety of parameters, e.g. breathing air tank levels, accountability monitoring, distress buttons and vital signs monitoring. Location services provide real-time information regarding the position of personnel or vehicles to a Command Post (CP). This information may also include status information regarding the person or vehicle. The service may require frequent transmissions to update position; the amount of data transmitted is likely to be small when location is based on satellite-based solutions, but can be quite extensive when location is to be calculated inside buildings as other technologies may have to be used. Location reporting services may be one-way with no acknowledgement, necessitating a robust communication mechanism. Position information may be considered sensitive in some emergencies and may require security mechanisms to protect the data.

Table 2 shows a summary of characteristics of the identifed communication service. Satellite and terrestrial communication networks should be able to provide the required data rates and QoS provisioning parameters.

[HC: The table is copied from Widens project deliverable D2.1, but I could not obtain the original reference.  Can Anton or Julian help to identify a similar information, espcially if it is ETSI document, thanks ]

Table 2: Characteristics of the identified communication services (Source Widens project D2.1)

7.1.2	Communications flows

Based on an assessment of the currently used communication services within the public safety sector it can be concluded that public safety mobile communications are voice-based with widespread use of group calls (“network-centric”), also called talkgroups. These are called Push-to-talk calls (PTT calls) Point-to-point voice calls (P2P calls) are also used specially by emergency managers.

According to user comments, positioning information of emergency units deployed in the disaster area is also currently in used in most of Public Agencies that counts on narrowband data channels of TETRA technology. However, there is a trend towards using a range of data applications alongside traditional voice applications to enhance communications. Data services have widely differing requirements in terms of capacity, timeliness and robustness of the data service.

Some the communication flows between various entities (in Figure 1) are described below:

#### FRs – FRs

For example, the First Responders (FRs) in each emergency team (Discipline  A, B or C) has its own and unique talkgroup.

#### FRs – corresponding CP

Bidirectional voice communication is allowed between the FRs and their Command Post (CP) since they share the same voice group.

Bidirectional data communication is allowed also between FRs and their CP primarily for geo-positioning applications. Special data services are required for the Fire & Rescue discipline  in hot area since they may carry special equipment which needs to transmit data to the corresponding CP. Examples of this equipment are wearable biometric sensors, radiation or gas sensors, video cameras, positioning equipment. CPs should have equipment to receive, integrate and display all these data acquiring valuable risk management information. Crucial actions are allowed, i.e. FRs could be rescued if irregular vital constants are observed. FRs will receive alerts, positioning information, commands to proceed, etc, through voice communication or data displayed in their user interface.

#### CP – CP

In the case several CPs are deployed they all should have bidirectional communication among them sharing valuable risk management information from their corresponding Emergency Agency.

#### CP – EATF

All CPs deployed in the disaster area and the global coordination centre (Emergency Authority Task Force, EATF) in Figure 1, should have bidirectional voice and data communication among them sharing valuable risk management information or commands to proceed.

#### CPs – External entities

Certain CPs have bidirectional communications with external entities with or sometimes without the intervention of the EATF, such as Fire & Rescue communicate with medical vehicles with hospitals. In addition to current operational practices where just voice calls are performed, paramedical users have suggested to enable ambulances to send data files with injured victims lists or electrocardiogram (ECG) traces to the hospital to reduce reaction time attending the victims.

#### CPs – External information

It is desirable for CPs to have external connections in order to enhance effectiveness of the operational procedures. One example is access to detailed maps for geo-localization support units would receive detailed information of the target location. Another application could be accessing the Fire Risk Assessment Indices of the affected area which takes into account baseline vegetation information (vigour, condition, etc). Access near real time satellite images is a new service provided by current observation LEO satellites in charge of image acquisition of the hot spots within several hours from the start of the emergency.

### 7.1.2	Communications flows

[HC:  This is a forest fire example from MONET deliverable D2.4. I was wondering if we could scale it up (e.g. 10 time) for an earthquake scenario.  May be Anton and Egil could comment here]

First emergency units arrive on the biggest fire centre. Emergency responders establish command post and fire officials assess situation.

6 fire-fighters of each squad approach the wildfire in order to extinguish it, not separating more than 300m from their auto-pump vehicle since this is the maximum hose extension. Thus, the auto-pump team, the driver and a fire-fighter, remains in the auto-pump to maintain the water supply. The rest of the emergency responders remain also in the warm area.

Two Police patrols detect the smaller forest fire centre 5 kilometres away from the previous one. The police units alert habitants for evacuation and contact the Police CP in main fire centre to ask the BO for support units. Finally, three CPs and their corresponding FRs are set up in hot and warm areas of this second fire centre, starting the second emergency phase which involves higher number of communications since more emergency responders are present in the scenario.

It will be assumed that 15 affected people have to be carried to the nearest hospitals.

The players and vehicles (CP included) finally deployed in each fire centre are summarized in Table 3Error! Reference source not found..

Table 3: Example communications requirements for forest fire scenario (Source MONET project D2.4)

| COMMUNICATION REQUIREMENTS IN the biggest forest fire centre |
| --- |
| Public safety agency | Service in use | Users | SAT MANET/SAT | Comm. flow | Requirement level | Occurrence |
| fire brigade in hot area | PTT Voice Call | 120 | MANET/SAT | Fire Brigade CP from/to fire-fighters in hot area | Mandatory | 926,4 PTT/15 minutes during busiest hours 463,2 PTT/15 minutes during regular hours |
|  | Personnel monitoring | 120 | MANET/SAT | Fire-fighters in hot area to CP | Required | Nominal each 5s while moving. |
|  | Location services | 120 | MANET/SAT | Fire Brigade units (pedestrian) to CP | Mandatory | Nominal each 1,5 minutes while moving. Each 5 mins if stopped. |
|  | Real Time Video | 20 | 20 Fire-fighters to CP | 20 Fire-fighters in hot area to CP | Desirable | 20 transmitting continuously during all disaster |
| fire brigade in WARM area | P2P Voice Calls | 1CP | SAT | Fire Brigade CP to BO and other CPs | Mandatory | 12 P2P/h |
|  | PTT Voice Call | 40 | MANET/SAT | Fire Brigade CP from/to fire-fighters in warm area | Mandatory | 308,8 PTT/15 minutes during busiest hours 154,4 PTT/15 minutes during regular hours |
|  | Location services | 40+20 | MANET/SAT | Fire Brigade units (pedestrian and vehicles) to CP | Mandatory | Nominal each 1,5 minutes while moving. Each 5 minutes if stopped. |
|  | Real Time Video | 1CP | SAT | Fire Brigade CP to BO | Desirable | 1 transmitting continuously during all disaster |
| POLICE DEPARTMENT | P2P Voice Call | 1 | SAT | Police CP from/to BO and to other CPs | Mandatory | 12 P2P/h |
|  | PTT Voice Calls | 10 | MANET/SAT | Police CP from/to policemen | Mandatory | 77,2 PTT/15 minutes during busiest hour 38,6 PTT/15 minutes during regular hours |
|  | Location services | 10+5 | MANET/SAT | Police units (pedestrian and vehicles) to CP | Mandatory | Each 1,5 minutes while moving. Each 5 minutes if stopped. |
| Medical services | P2P Voice Call | 1CP | SAT | Police CP from/to BO and to other CPs Medical CP to hospitals | Mandatory | 12 P2P/h 30 P2P during all disaster considering 15 victims |
|  | PTT Voice Calls | 30 | MANET/SAT | Medical CP from/to doctors/nurses | Mandatory | 231,6 PTT/15 minutes during busiest hour 115,8PTT/15 minutes during regular hours |
|  | Location services | 30+10 | MANET/SAT | Medical units (pedestrian and vehicles) to CP | Mandatory | Each 1,5 minutes while moving. Each 5 minutes if stopped. |

### User requirements for Information Exchange

For each  information exchange, a list of factors that will impact the dimensioning of the communication deployment.

For each service, user requirements and dimensioning aids to be provided. User requirements include information such as the expected reliability and end-to-end delay experienced by the communication. Dimensioning aids encompass data such as the expected quality for data/voice communication (type of applications: delay for web browsing, SMS versus e-mail, Communication duration, voice versus videoconferencing, number of simultaneous users…). With a combination of user requirements and dimensioning aids, based on this document and according to a given technology it should be possible to assess the amount of resources required. However the detailed technological descriptions are not part of the proposed work.

During the process of dispatch, the following information will need to be exchanged between ECC and the resources:

Availability and position of resource

Particulars and location of site

Progress report of resource (e.g blocked roads)

Alternative routing of resource

Resource arriving on site

# Topology Model

A textual, graphical or mathematical topological model showing how end-users are deployed/move in their field of activity. This topological model may make reference to existing work but it must be part of the reference scenario.

It should include or define constraints impacting the networks formed from the various information exchanges. These constraints are  –  for example  –  derived from the mobility patterns of the users. From a technology standpoint, mobility patterns yield representative figures for wireless links lifetime and environment.

Annex A (informative):
Major Recent Earthquakes

| Europe |  |  |  | People | buildings |  |
| --- | --- | --- | --- | --- | --- | --- |
| Date | Country | Place | Mag | Killed | Injured | Affected | homeless | demolished | damaged | Cost |
|  |  |  |  |  |  | '000s | '000s |  |  | MEuro |
| 20/05/2012 | Italy | Emilia | 6 | 24 | 350 | 25 | 20 |  |  | 15800+ |
| 11/05/2011 | Spain | Lorca | 5.3 | 10 | 167 | 15 |  |  |  | 200 |
| 06/04/2009 | Italy | L'Aquila | 6.3 | 295 | 1600 | 56 | 50 |  | 10000 | 2500 |
| 07/09/1999 | Greece | Athens | 5.9 | 143 |  | 115 |  | 2,700 | 35,000 | 4200 |
| Outside Europe |  |  |  |  |  |  |  |  |  |  |
| 11/03/2011 | Japan | Honshu | 9 | 20000 |  | 370 |  |  |  | 210000 |
| 12/01/2010 | Haiti | Haiti | 7 | 222500 |  | 3700 |  | 105,000 | 188,383 | 8000 |
| 30/09/2009 | Indonesia | Padang | 7.5 | 1200 |  | 2500 |  |  |  | 2200 |
| 12/05/2008 | China | Eastern Sichuan | 7.9 | 87500 |  | 4600 |  |  |  | 85000 |

Sources: EMDAT, USGS

Annex B (informative):
Fictive example scenario timeline

Day 1:

0.00: Earthquake, power cut ECC, generator starts. Intranet (Fiber) seems to function locally. Internet connection lost

0.02: Members of public: Try calling emergency number, no connection.

0.05:

PSAP: Reports to ECC via intranet that they have a power cut, generator has been started but all incoming public lines are non-fuctional. ECC starts mobilizing resources according to plan, PMR not functioning.

On site: Able-bodied members of public start evacuating the injured to open spaces, first aid initiated.

0.07: ECC: Reports to RCC via satellite terminal that they have lost communication, information received that sensors have identified an EQ with EC within the area of the ECC.

0.10: Member of public reaches ECC via satellite terminal: Severe damages/ flashflood in central area of the city.

0.11: ECC: General alert submitted on PMR/ intranet, resources dispatched to emergency area.

0.12: ECC/ RCC: Requests: Air force resource (surveillance)

0.15: Emergency service vehicle (police) arrives on scene. Confirms report of serious damage including collapsed building.

0.30: First SITREP:

Collapsed buildings: Blocks of flats, shopping center, industrial site

Considerable damage to all kinds of infrastructure, including roads and telecoms.

0.50:

Additional resources (fire/ rescue and ambulance) arrive on scene

Request for Civil Protection assistance

1.10:

Fire/ rescue: Parts of area cleared safe and SAR activities start

Ambulance: Initial area for triage/ first aid established, activities started

1:15

Risk of chemical pollution is realized, expertise requested

1.29:

Explosion and fire in commercial center, fire fighters and smoke divers needed

SAR personnel to be withdrawn from areas at risk

Further details on dangerous substances requested from ECC.

1.45:

Affected individuals.

Estimated number of individuals affected: A

Un-injured individuals: B

Injured individuals: C

Individuals not accounted for: A – B – C

SAR: Ongoing, reported need for more resources, incl. rescue dogs

Health: Need for further resources, both specialists and nursing personnel

Area for safe haven is decided upon

2.15

Site manager reports need for further resources, exceeding those available regionally

ECC realizes that it will not be possible to evacuate all individuals out of the area, preparation of emergency shelters within safe haven is initiated

Press center established at ECC

2.35

Fire reported as extinguished, SAR can continue in affected area.

Assessment of hospital needs, plans made for referral to other health facilities regionally and nationally

3.30:

Affected individuals.

Estimated number of individuals affected: A

Un-injured individuals: B

Injured individuals: C

Individuals declared dead: D

Individuals not accounted for: A – B – C – D

NGOs, including rescue dogs, arrive on scene, are allocated tasks by site management

4.00:

Regional/ national resources arrive

A supply chain to the safe haven is established

Safer drinking water

Food

Pit latrines

Shelters (tents, heating, lights, blankets, matresses etc)

System for medical evacuation is established, the needs are bigger than the capacity

Triage/ first aid points are overloaded

Plans for referral to international health facilities in progress, systems for triage in that area are made and agreed with site management

5.00:

International resources start to arrive

Affected individuals.

Estimated number of individuals affected: A

Un-injured individuals: B

Injured individuals: C

Individuals declared dead: D

Individuals not accounted for: A – B – C – D

7.00

SAR activities continuing, need for replacement of peersonnel

Medical evacuation continuing

12.00

Affected individuals.

Estimated number of individuals affected: A

Un-injured individuals: B

Injured individuals: C

Individuals declared dead: D

Individuals not accounted for: A – B – C – D

Temporary GSM network made available in parts of the area

Centers for relatives established in non-affected areas, communication links (“I am alive”) starting to work.

Day 2:

SAR, triage and first aid activities continuing

Inventory of destroyed infrastructure

Plans for evacuation and temporary dwellings in progress

Storage for deceased being prepared

Days 3-5:

SAR activities continuing, but at a lesser scale

Triage/ first Aid at a much lesser scale

Medical evacuation completed.

Non-medical evacuation still ongoing

Infrastructure, particularly roads, electricity and telecoms still lacking but in progress

Supply chains for safe water and food established

Systems for sanitation in progress

Days 6-10:

Search activities still ongoing, but now more guired towards removing dead bodies

Identification of dead ongoing

Re-establsichment of construction of infrastructure ongoing

Days 11 ++

Activities gradually shift towards re-construction and re-establishment of services

Annex <X> (informative):
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/Files/other/EDRs_navigator.chm).

It shall not include references mentioned in the document.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

# History

| Document history |
| --- |
| V0.0.1 | Feb 2014 | TOC + contents definition |
| V0.0.2 | Feb 2014 | First scenario contents |
| V0.0.3 | Feb 2014 | Scenario update |
| V0.0.4 | April 2014 | Updated with text in 4 and 5 |
| V0.0.5 | April 2014 | Updated with Annex A, B and further text. etc. |
| V0.0.6 | April 2014 | Updated references |

# Footnotes

“Network-centric” refers to sharing of information between people and devices in a many-to-many (group) configuration, as is often used within the public safety sector)

SAT means the communication will go through satellite link. MANET/SAT means satellite access is used as back up.