Early draft ES 203 119-4 V0.0.1 (2014-09)

Methods for Testing and Specification (MTS);

The Test Description Language (TDL);

Extensions: Advanced Test Objective Specification

<

ETSI SPECIFICATION

Reference

DES/MTS-203119part 2

Keywords

language, MBT, methodology, testing, 
TSS&TP, TTCN-3, UML

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

The present document can be downloaded from:
http://www.etsi.org

The present document may be made available in electronic versions and/or in print. The content of any electronic and/or print versions of the present document shall not be modified without the prior written authorization of ETSI. In case of any existing or perceived difference in contents between such versions and/or in print, the only prevailing document is the print of the Portable Document Format (PDF) version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm except as authorized by written permission of ETSI.

The content of the PDF version shall not be modified without the written authorization of ETSI.

The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2014.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

# Contents

If you need to update the table of content you would need to first unlock it.
To unlock the Table of Contents: select the Table of Contents, click simultaneously: Ctrl + Shift + F11.
Then lock it: reselect the Table of Contents and then click simultaneously: Ctrl + F11.

Contents	3

Intellectual Property Rights	5

Foreword	6

Introduction	6

1	Scope	7

2	References	8

2.1	Normative references	8

2.2	Informative references	8

3	Definitions, symbols and abbreviations	9

3.1	Definitions	9

3.2	Symbols	9

3.3	Abbreviations	9

4	Basic principles	10

4.1	Introduction	10

4.2	Document Structure	10

4.3	Notational Conventions	10

4.4 	Conformance	10

5	Meta-Model Extensions	10

5.1	Overview	10

5.2	Abstract Syntax	10

5.3	Foundation Classifier Description	12

5.3.1	Entity	12

5.3.2	Event	12

5.3.3	PICS	13

5.4	Test Objective Classifier Description	13

5.4.1	StructuredTestObjective	13

5.4.2	PICSReference	14

5.4.3	InitialConditions	14

5.4.4	ExpectedBehaviour	14

5.4.5	FinalConditions	15

5.5	Events Classifier Description	15

5.5.1	EventSequence	15

5.5.2	EventOccurence	15

5.5.3	EntityReference	16

5.5.4	EventReference	16

5.6	Data Classifier Description	17

5.6.1	Value	17

5.6.2	DataReference	17

5.6.3	LiteralValue	18

5.6.4	LiteralValueReference	18

5.6.5	Content	18

5.6.6	ContentReference	19

6.	Concrete Syntax	19

6.1	Graphical Representation Format	19

6.1.1	StructuredTestObjective	19

6.1.2	Entity	22

6.1.3	Event	22

6.1.4	PICS	22

6.2	Textual Representation Format	22

6.2.1	Package	22

6.2.2	AnnotationType	23

6.2.3	Entity	24

6.2.4	Event	24

6.2.5	PICS	24

6.2.6	StructuredTestObjective	25

6.2.7	StructuredDataType	25

6.2.8	StructuredDataInstance	26

Proforma copyright release text block	26

Annexes	27

Annex A (normative): BNF Production Rules	27

A.1	Overview and Conventions	27

A.1	Production Rules	27

Annex B (informative): Examples	29

Annex <X+2> (informative): Title of informative annex (style H8)	29

Annex <X+3> (informative): Change History	29

Annex <X+4> (informative): Bibliography	30

History	30

A few examples:	31

<PAGE BREAK>

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This early draft ETSI Standard (ES) has been produced by ETSI Technical Committee Methods for Testing and Specification (MTS), and is now submitted for the ETSI standards Membership Approval Procedure.

The present document is part 4 of a multi-part deliverable on the Test Description Language as detailed below:

Part 1: Abstract Syntax and Associated Semantics

Part 2: Graphical Syntax

Part 3: Exchange Format

Part 4: Extensions: Advanced Test Objective Specification

# Introduction

Test purposes play an essential role in test specification processes at ETSI. Currently, test purposes are specified in TPLan or TPLan-like notations, whereas TDL treats test purposes, and test objectives in general as informal text without any additional structural constraints. This extension package for TDL refines and formalises test objective specification within TDL by introducing relevant meta-model concepts and a corresponding syntactical notation, both of which are related to TPLan. This enables test purpose specification to enter the modelling world and paves the way for improved tool support and better structured test objectives, as well as additional formal verification and validation facilities down the road by integrating and unifying the means for the specification of test purposes and test descriptions, while relying on the same underlying meta-model and benefiting from other related technologies built around this meta-model.

The present document describes the relevant abstract syntax (meta-model) extensions as well as the corresponding concrete syntactical notation.

Ed. Note: To be extended for the final draft.

# 1	Scope

The ES (ETSI Standard) shall be chosen when the document contains normative provisions and it is considered preferable or necessary that the document be submitted to the whole ETSI membership for its approval.

The scope shall always be clause 1 of each ETSI deliverable and shall start on a new page (more details can be found in clause 11 of the EDRs).

No text block identified. Forms of expression such as the following should be used:

The present document specifies the extensions to the TDL meta-model described in [1]  necessary to support advanced test objective specification, as well as the concrete syntactical notation for the advanced test objective specification. The notation also covers the minimal set of TDL elements that are required to construct a valid model which can enclose the test objectives. The intended use of the present document is to serve as the spefication for the required meta-model extensions and the corresponding concrete syntax which is to be used by users of these extensions.

Ed. Note: To be extended for the final draft.

# 2	References

The following text block applies. More details can be found in clause 12 of the EDRs.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication, ETSI cannot guarantee their long term validity.

## 2.1	Normative references

Clause 2.1 only shall contain normative (essential) references which are cited in the document itself. These references have to be publicly available and in English.

The following referenced documents are necessary for the application of the present document.

[1]	ETSI ES 203 119-1 (V1.2.1.): “Methods for Testing and Specification (MTS); The Test Description Language (TDL); Specification of the Abstract Syntax and Associated Semantics"

Ed. Note: To be extended for the final draft.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	ETSI TR 102 473: "<Title>".

[i.2]	ETSI TR 102 469: "<Title>".

Ed. Note: To be extended for the final draft.

# 3	Definitions, symbols and abbreviations

Ed. Note: Claise not included in the early draft.

Delete from the above heading the word(s) which is/are not applicable, (see clauses 13 and 14 of EDRs).

Definitions and abbreviations extracted from ETSI deliverables can be useful when drafting documents and can be consulted via the Terms and Definitions Interactive Database (TEDDI) (http://webapp.etsi.org/Teddi/).

## 3.1	Definitions

Clause numbering depends on applicability.

A definition shall not take the form of, or contain, a requirement.

The form of a definition shall be such that it can replace the term in context. Additional information shall be given only in the form of examples or notes (see below).

The terms and definitions shall be presented in alphabetical order.

For the purposes of the present document, the [following] terms and definitions [given in ... and the following] apply:

Definition format

<defined term>: <definition>

example 1: text used to clarify abstract rules by applying them literally

NOTE:	This may contain additional information.

## 3.2	Symbols

Clause numbering depends on applicability.

For the purposes of the present document, the [following] symbols [given in ... and the following] apply:

Symbol format

<symbol>	<Explanation>

<2nd symbol>	<2nd Explanation>

<3rd symbol>	<3rd Explanation>

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

Abbreviation format

<ACRONYM1>	<Explanation>

<ACRONYM2>	<Explanation>

<ACRONYM3>	<Explanation>

<PAGE BREAK>

# 4	Basic principles

Ed. Note: Claise not included in the early draft. Content may include

Extension facilities – adding support for the extension at the meta-model level and relations to TDL

Concrete syntax to meta-model mappings

## 4.1	Introduction

## 4.2	Document Structure

## 4.3	Notational Conventions

## 4.4 	Conformance

# 5	Meta-Model Extensions

The following clauses specify extensions to the abstract syntax for TDL that enable the support for advanced test objective specification by means of structured test objectives.

## 5.1	Overview

Ed. Note: Main principles and features to be added for the stable draft.

## 5.2	Abstract Syntax

Figure 5.1: Advanced Test Objective Specification Foundation Concepts

Figure 5.2: Structured Test Objective Concepts

Figure 5.3: Events Concepts

Figure 5.4: Data Concepts

## 5.3	Foundation Classifier Description

### 5.3.1	Entity

Semantics

An 'Entity' is a ‘PackageableElement’ that describes a participant in an event. User defined entities, such as IUT, SUT, Tester, etc. may be referenced in ‘EventOccurence’s as the source and/or target of an ‘EventReference’entity. Whether an ‘Entity’ corresponds a ‘ComponentInstance’ or a ‘GateInstance’ is not specified in advance. Whether an ‘Entity’ referenced in an ‘EventOcurrence’ is the source or target of an ‘EventReference’ depends on the interpretation of the corresponding ‘Event’ definition.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

### 5.3.2	Event

Semantics

An 'Event' is a ‘PackageableElement’ that describes a user defined event that may be referenced in ‘EventOccurence’s. The direction of an ‘Event’ with respect to the ‘Entity’ or ‘Entities’ referenced in the ‘EventOccurence’s depends on the interpretation of the ‘Event’, where ‘Annotation’s may be used to provide additional information regarding the kind of the event.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

### 5.3.3	PICS

Semantics

A 'PICS' is a ‘PackageableElement’ that may be referenced in ‘StructuredTestObjective’s.

Generalizations

PackageableElement

Properties

There are no properties specified.

Constraints

There are no constraints specified.

## 5.4	Test Objective Classifier Description

### 5.4.1	StructuredTestObjective

Semantics

A 'StructuredTestObjective' is a refinement of ‘TestObjective’ that enables the use of additional constructs in order formalise the description of ‘TestObjective’s. In addition to the ‘description’ and ‘objectiveURI’ properties inherited from ‘TestObjective’, a ‘StructuredTestObjective’ includes ‘PICS’ references, ‘InitialConditions’, ‘ExpectedBehaviour’, and ‘FinalConditions’.

Generalizations

PackageableElement

Properties

picsReference : PICSReference [*] {ordered}
An ordered set of ‘PICSReferences’ to ‘PICS’.

initialConditions : InitialConditions [0..1]
Initial conditions description for the ‘StructuredTestObjective’.

expectedBehaviour : ExpectedBehaviour [0..1]
Expected behaviour description for the ‘StructuredTestObjective’.

finalConditions : FinalConditions [0..1]
Final conditions description for the ‘StructuredTestObjective’.

Constraints

There are no constraints specified.

### 5.4.2	PICSReference

Semantics

A 'PICSReference' is an ‘Element’ that enables the referencing of ‘PICS’ within ‘StructuredTestObjective’s. An ‘Annotaiton’ may be used to add an operand describing how the referenced ‘PICS’ shall be interpreted and how it is related to other referenced ‘PICS’.

Generalizations

Element

Properties

pics : PICS [1] 
The referenced ‘PICS’.

Constraints

There are no constraints specified.

### 5.4.3	InitialConditions

Semantics

'InitialConditions' is an ‘Element’ containing an ‘EventSequence’ describing the initial conditions of a ‘StructuredTestObjective’.

Generalizations

Element

Properties

conditions : EventSequence [1] 
An ‘EventSequence’ containing the ‘EventOcurrences’ describing the initial conditions for the ‘StructuredTestObjective’.

Constraints

There are no constraints specified.

### 5.4.4	ExpectedBehaviour

Semantics

'ExpectedBehaviour' is an ‘Element’ containing an ‘EventSequence’ describing the expected behaviour of a ‘StructuredTestObjective’.

Generalizations

Element

Properties

whenClause : EventSequence [0..1] 
An ‘EventSequence’ containing the ‘EventOcurrences’ describing the stimuli for the ‘ExpectedBehaviour’ of the ‘StructuredTestObjective’.

thenClause : EventSequence [1] 
An ‘EventSequence’ containing the ‘EventOcurrences’ describing the expected reaction for the ‘ExpectedBehaviour’ of the ‘StructuredTestObjective’ or the resulting expected state.

Constraints

There are no constraints specified.

### 5.4.5	FinalConditions

Semantics

'FinalConditions' is an ‘Element’ containing an ‘EventSequence’ describing the final conditions of a ‘StructuredTestObjective’.

Generalizations

Element

Properties

conditions : EventSequence [1] 
An ‘EventSequence’ containing the ‘EventOcurrences’ describing the final conditions for the ‘StructuredTestObjective’.

Constraints

There are no constraints specified.

## 5.5	Events Classifier Description

### 5.5.1	EventSequence

Semantics

'EventSequence' is an ‘Element’ containing ‘EventOccurences’.

Generalizations

Element

Properties

events : EventOccurrence [1..*] {ordered} 
A sequence of ‘EventOccurrences’..

Constraints

There are no constraints specified.

### 5.5.2	EventOccurence

Semantics

An 'EventOcurrence' is an ‘Element’ describing a concrete occurrence of an ‘Event’, including qualified references to the ‘Event’, to the ‘Entity’ related to the occurrence of the ‘Event’ and to any other ‘Entity’s involved in the ‘EventOccurrence’. It also includes a ‘Value’ as argument describing the details of the ‘EventOccurrence’ such as the data being sent or received.

Generalizations

Element

Properties

entityReference : EntityReference [1] 
An ‘EntityReference’ to the ‘Entity’ related to the occurrence of the ‘Event’.

oppositeEntityReference : EntityReference [0..*] 
‘EntityReference’s to other ‘Entity’s involved in the ‘EventOcurrences’.

eventReference : EventReference [1] 
An ‘EventReference’ to the occurring ‘Event’.

eventArgument : Value [0..1] 
A ‘Value’ describing the details of the ‘EventOccurrence’.

Constraints

There are no constraints specified.

### 5.5.3	EntityReference

Semantics

An 'EntityReference' is an ‘Element’ that enables the referencing of ‘Entity’s within ‘EventOccurrence’s. ‘Comment’s or ‘Annotation’s may be used to add qualifiers describing peculiarities of the referenced ‘Entity’ related to the specific ‘EventOccurrence’.

Generalizations

Element

Properties

entity : Entity [1] 
The referenced ‘Entity’.

Constraints

There are no constraints specified.

### 5.5.4	EventReference

Semantics

An 'EventReference' is an ‘Element’ that enables the referencing of ‘Events’ within ‘EventOccurence’s. ‘Comment’s or ‘Annotaiton’s may be used to add qualifiers describing peculiarities of the referenced ‘Event’ related to the specific ‘EventOccurrence’.

Generalizations

Element

Properties

event : Event [1] 
The referenced ‘Event’.

Constraints

There are no constraints specified.

## 5.6	Data Classifier Description

### 5.6.1	Value

Semantics

A 'Value' is an abstract ‘Element’ that is refined into ‘DataReference’, ‘LiteralValue’, ‘LiteralValueReference’ and ‘ContentReference’. While ‘DataReference’ enables the referencing of ‘DataInstance’s defined in advance, the remaining ‘Value’ refinements enable the inline ad-hoc description of data and data structures, without the requirement of defining ‘DataType’s and ‘DataInstance’s in advance. ‘DataInstance’s and inline data descriptions may be combined to the extent that inline data descriptions may contain ‘DataReference’s to ‘DataInstance’s, but ‘DataInstance’s relying on declared ‘DataType’s may not reference inline data descriptions. ‘Comment’s or ‘Annotaiton’s may be used to add qualifiers describing further details related to the ‘Value’ withing to the specific context of its usage.

Generalizations

Element

Properties

content : Content [1] 
The referenced ‘Content’.

Constraints

There are no constraints specified.

### 5.6.2	DataReference

Semantics

A 'DataReference' is a ‘Value’ that enables the referencing of ‘DataInstance’s by means of ‘DataInstanceSpecification’ as an argument of ‘EventOccurence’s or as a value of ‘Content’.

Generalizations

Value

Properties

content : DataInstanceSpecification [1] 
Specification of the referenced ‘DataInstance’.

Constraints

‘DataInstanceSpecification’ restrictions
Only simple and structured data instances may be referenced.

### 5.6.3	LiteralValue

Semantics

A 'LiteralValue' is a ‘Value’ that represents any literal label used as an argument of ‘EventOccurence’s or as a value of ‘Content’. A ‘LiteralValue’ may contain ‘Content’ enabling the definition of a substructure of the ‘LiteralValue’ describing the details of the ‘LiteralValue’.

Generalizations

Value

Properties

content : Content [0..*] {ordered} 
The ‘Content’s of the ‘LiteralValue’.

Constraints

There are no constraints specified.

### 5.6.4	LiteralValueReference

Semantics

A 'LiteralValueReference' is a ‘Value’ that enables the referencing of ‘LiteralValues’ as an argument of ‘EventOccurence’s or as a value of ‘Content’.

Generalizations

Value

Properties

content : LiteralValue [1] 
The referenced ‘LiteralValue’.

Constraints

There are no constraints specified.

### 5.6.5	Content

Semantics

A 'Content' is an ‘Element’ that enables the specification of composite ‘LiteralValue’s which contain additional ‘Value’s.

Generalizations

Element

Properties

value : Value [0..1] 
A ‘Value’ assigned to the ‘Content’.

Constraints

There are no constraints specified.

### 5.6.6	ContentReference

Semantics

A 'ContentReference' is a ‘Value’ that enables the referencing of the ‘Content’ of ‘LiteralValues’ as an argument of ‘EventOccurence’s or as a value of ‘Content’.

Generalizations

Value

Properties

content : Content [1] 
The referenced ‘Content’.

Constraints

There are no constraints specified.

# 6.	Concrete Syntax

The following clauses specify the graphical representation format extensions for TDL related to the additional concepts specified in Clause 5, as well as a textual representation format for the additional concepts and the minimal set of required TDL concepts to facilitate the specification and representation of ‘StructuredTestObjective’s in pure text.

## 6.1	Graphical Representation Format

The concrete syntax notation specification for structured test objectives follows the notational conventions described in Clause [#reference#] of the Graphical Representation Format for TDL [#reference#].

### 6.1.1	StructuredTestObjective

Concrete Graphical Notation

Figure 6.1: Structured Test Objective Concrete Syntax

Figure 6.2: Structured Test Objective Alternative Concrete Syntax

Formal Description

context Element

QualifierLabel ::= self.comment.body | self.annotation.key.name

ArticleLabel ::= self.comment.name = ‘a’ | self.comment.name = ‘an’ | self.comment.name = ‘the’

ReferenceLabel ::= self.comment.name = ‘corresponding to’ | self.comment.name = ‘derived from

context StructuredTestObjective

TestObjectiveNameLabel ::= self.name

DescriptionLabel ::= self.description

URIofObjectiveLabel ::= self.objectiveURI

Foreach p : PICSReference in self.picsReferences

PICSSelectionLabel ::= [p.annotations.key.name] p.pics.name

InitialConditionsLabel ::= ‘with’ ‘{‘ <EventSequenceLabel> ‘}’

FinalConditionsLabel ::= ‘with’ ‘{‘ <EventSequenceLabel> ‘}’

ExpectedBehaviourLabel ::= ‘ensure’ ‘that’ ‘{‘

( `when` `{` <EventSequenceLabel> `}` `then` `{` <EventSequenceLabel> `}`) |

<EventSequenceLabel>

‘}’

context EventSequence

Foreach e : EventOccurence in self.events

EventSequenceLabel ::= [<QualifierLabel>] e.entityReference.entity.name

[<QualifierLabel>] e.eventReference.event.name

[EventArgumentLabel]

[<OppositeEntityLabel>]

Foreach o : EntityReference in e.oppositeEntityReference

OppositeEntityLabel ::= [<QualifierLabel>] o.entity.name

EventArgumentLabel ::= DataReferenceArgumentLabel | LiteralValueArgumentLabel |

LiteralValueReferenceArgumentLabel | ContentReferenceArgumentLabel

context DataReference

DataReferenceArgumentLabel ::= [<QualifierLabel>] StructuredDataSpecLabel

StructuredDataSpecLabel ::= self.content.structuredDataInstance.name [‘with’ <StructuredDataArgumentLabel>]

DataReferenceLabel ::= ReferenceLabel StructuredDataSpecLabel

context StructuredDataSpec

Foreach a : self.argument

StructuredDataArgumentLabel ::= a.tupleElement.name ‘indicating’ ‘value’ StructuredDataSpecLabel

context LiteralValue

LiteralValueArgumentLabel ::= [ArticleLabel] ‘new’ [<QualifierLabel>] self.name [<ContentLabel>]

ContentLabel ::=  ‘containing’ [<QualifierLabel>] self.name [ValueLabel]

ValueLabel ::= DataReferenceLabel | LiteralValueLabel | LiteralValueReferenceLabel | ContentReferenceLabel

LiteralValueLabel ::= ‘indicating’ ‘value’ [<QualifierLabel>] self.name [<ContentLabel>]

context LiteralValueReference

LiteralValueReferenceArgumentLabel ::= ‘the’ ‘value’ ‘of’ self.content.name

LiteralValueReferenceLabel ::= ReferenceLabel LiteralValueReferenceArgumentLabel

context ContentReference

ContentReferenceArgumentLabel ::= ‘the’ ‘value’ ‘contained’ ‘in’ self.content.name

ContentReferenceLabel ::= ReferenceLabel ContentReferenceArgumentLabel

Constraints

Comments

Editor Note: The two different notations on Figure 6.1 and Figure 6.2 are presented for consideration. Figure 6.1 represents an identical notation to the one currently in use, whereas Figure 6.2 represents a notation that is similar to the common shapes used in the Graphical Representation Format for TDL. One of the alternatives may be removed in the final draft.

Example

Figure 6.1: Structured Test Objective Concrete Syntax Example

### 6.1.2	Entity

### 6.1.3	Event

### 6.1.4	PICS

## 6.2	Textual Representation Format

The textual representation format covers the additional concepts and the minimal set of required TDL concepts to facilitate the specification and representation of ‘StructuredTestObjective’s in pure text. The syntax for the constituents of the ‘StructuredTestObjective’s, such as ‘InitialConditions’, ‘ExpectedBehaviour’, and ‘FinalConditions’ shall be identical to the corresponding compartment specifications in Clause 6.1.

### 6.2.1	Package

Syntax Notation

| Package | ::= | 'Package' Identifier '{' [ 'Domain' '{' [ 'pics' ':' { PICS }+ ';' ] [ 'entities' ':'{ Entity }+ ';' ] [ 'event' 'types' ':'{ EventType }+ ';' ] [ 'events' ':' { Event }+ ';' ] '}' ] [ 'Data' '{' { StructuredDataType } { StructuredDataInstance } '}' ] { PackageableElement } { Group } '}'; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

The syntax notation prescribes a certain structure to what is otherwise an ordered set of ‘PackageableElement’s, including the order of definitions for domain- and data-related definitions.

Example

Package p {

Domain {

pics :

- ALL

- SELECTED

- RANDOM ( "5" )

- PICS_PUBTRANSVEH

;

entities :

- IUT

- SUT

- Tester

- door

;

event types :

- radio

- wire

- mixed

;

events :

- sends

- receives (wire,radio)

- opened

- transmit (radio)

- sent

- closed

- reached

;

}

Data {

type INT ;

type STRING ;

type message containing

id of type INT,

name of type STRING,

content of type STRING ;

type encrypted_message containing

code of type STRING,

content of type message ;

type STATE ;

INT ONE; INT TWO; INT THREE; INT 1; INT 2; INT 3.2;

STRING s1; STRING s2; STRING s3; STRING "secret code"; STRING "Open Sesame";

STATE initial_state;

message	m1 with

id indicating value 1,

name indicating value s1,

content indicating value s2;

message	m2 with

id indicating value 3.2,

name indicating value s3,

content indicating value s2;

encrypted_message em1 with

code indicating value s3,

content indicating value m1 with

name indicating value s3;

encrypted_message em2 with

code indicating value "secret code",

content indicating value s2;

}

### 6.2.2	AnnotationType

Syntax Notation

| EventType | ::= | '-' Identifier; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

The EventType syntax notation describes a special use for ‘AnnotationType’s.

Example

event types :

- radio

- wire

- mixed

;

### 6.2.3	Entity

Syntax Notation

| Entity | ::= | '-' Identifier; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

Example

entites :

- IUT

- SUT

- Tester

;

### 6.2.4	Event

Syntax Notation

| Event | ::= | '-' Identifier [ '(' EventTypeReference { ',' EventTypeReference } ')' ]; |
| --- | --- | --- |

Formal Description

Identifier ::= self. Name

Constraints

Comments

Example

events :

- sends

- receives (wire,radio)

- opened

- transmit (radio)

- sent

- closed

- reached

;

### 6.2.5	PICS

Syntax Notation

| PICS | ::= | '-' Identifier [ '(' Qualifier ')' ]; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

Example

pics :

- ALL

- SELECTED

- RANDOM ( "5" )

;

### 6.2.6	StructuredTestObjective

Syntax Notation

| StructuredTestObjective | ::= | 'TestPurpose' '{' 'TP Id' Identifier 'Test objective' STRING 'Reference' [ STRING { ',' STRING } ] 'PICS Selection' { PICSReference } [ InitialConditions ] [ ExpectedBehaviour ] [ FinalConditions ] '}'; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

Example

TestPurpose {

TP Id "TP/CAM/INA/DOP/BV/02"

Test objective "Checks that CAM message includes DoorOpen information 30s after closed"

Reference "TS 102 637-2 [1], clauses 7.1 and 7.2"

PICS Selection PICS_PUBTRANSVEH

Initial conditions:

with {

the IUT having reached an initial_state

and

the IUT having sent a new valid CAM message

containing DoorOpen TaggedValue

}

Expected behaviour :

ensure that {

when {

the door is closed

}

then {

the IUT sends a new CAM message

containing DoorOpen TaggedValue

}

}

}

### 6.2.7	StructuredDataType

Syntax Notation

| StructuredDataType | ::= | 'type' Identifier [ 'containing' TupleElement { ',' TupleElement } ] ';'; |
| --- | --- | --- |

Formal Description

Identifier ::= self. name

Constraints

Comments

Example

type INT ;

type STRING ;

type message containing

id of type INT,

name of type STRING,

content of type STRING ;

type encrypted_message containing

code of type STRING,

content of type message ;

type STATE ;

### 6.2.8	StructuredDataInstance

Syntax Notation

| StructuredDataInstance | ::= | Identifier ( Identifier ¦ NumberAsIdentifier ) [ 'with' TupleElementInstance { ',' TupleElementInstance } ] ';'; |
| --- | --- | --- |

Formal Description

TypeIdentifier ::= self.type.name

Identifier ::= self. name

Constraints

Comments

Example

INT ONE; INT TWO; INT THREE; INT 1; INT 2; INT 3.2;

STRING s1; STRING s2; STRING s3; STRING "secret code"; STRING "Open Sesame";

STATE initial_state;

message	m1 with

id indicating value 1,

name indicating value s1,

content indicating value s2;

message	m2 with

id indicating value 3.2,

name indicating value s3,

content indicating value s2;

encrypted_message em1 with

code indicating value s3,

content indicating value m1 with

name indicating value s3;

encrypted_message em2 with

code indicating value "secret code",

content indicating value s2;

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, ETSI grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 8 style for the title and the Normal style for the text.

Specify if the annex is normative or informative.

<PAGE BREAK>

Annex A (normative):
BNF Production Rules

## A.1	Overview and Conventions

This annex describes the grammar for the representation of structured test objectives in pure text. It covers the additional concepts and the minimal set of required TDL concepts to facilitate the specification and representation of ‘StructuredTestObjective’s. The notations is based on the Extended Backus-Naur Form (EBNF) notation. The EBNF representation may be used either as a concrete syntax reference for Advanced Test Objective Specification with TDL for end users or as input to a parser generator tool. Table B.1 defines the syntactic conventions that are to be applied when reading the EBNF rules.

| Table A.1: Syntax definition conventions used |
| --- |
| ::= | is defined to be |
| abc | the non-terminal symbol abc |
| abc xyz | abc followed by xyz |
| abc ¦ xyz | alternative (abc or xyz) |
| [abc] | 0 or 1 instance of abc |
| {abc}+ | 1 or more instances of abc |
| {abc} | 0 or more instances of abc |
| 'a'-'z' | all characters from a to z |
| (...) | denotes a textual grouping |
| 'abc' | the terminal symbol abc |
| ; | production terminator |
| \ | the escape character |

## A.1	Production Rules

| Package | ::= | 'Package' Identifier '{' [ 'Domain' '{' [ 'pics' ':' { PICS }+ ';' ] [ 'entities' ':'{ Entity }+ ';' ] [ 'event' 'types' ':'{ EventType }+ ';' ] [ 'events' ':' { Event }+ ';' ] '}' ] [ 'Data' '{' { StructuredDataType } { StructuredDataInstance } '}' ] { PackageableElement } { Group } '}'; |
| --- | --- | --- |
| PackageableElement | ::= | StructuredTestObjective ; |
| GroupedElement | ::= | StructuredTestObjective ¦ Group; |
| Group | ::= | 'Group' Identifier '{' { GroupedElement } '}'; |
| PICS | ::= | '-' Identifier [ '(' Qualifier ')' ]; |
| PICSReference | ::= | [ 'and' ¦ 'or' ] Identifier; |
| Entity | ::= | '-' Identifier; |
| EventType | ::= | '-' Identifier; |
| EventTypeReference | ::= | Identifier; |
| Event | ::= | '-' Identifier [ '(' EventTypeReference { ',' EventTypeReference } ')' ]; |
| StructuredTestObjective | ::= | 'TestPurpose' '{' 'TP Id' Identifier 'Test objective' STRING 'Reference' [ STRING { ',' STRING } ] 'PICS Selection' { PICSReference } [ InitialConditions ] [ ExpectedBehaviour ] [ FinalConditions ] '}'; |
| InitialConditions | ::= | 'Initial conditions' ':' 'with' '{' EventSequence '}'; |
| ExpectedBehaviour | ::= | FullExpectedBehaviour ¦ PartialExpectedBehaviour; |
| FullExpectedBehaviour | ::= | 'Expected behaviour' ':' 'ensure that' '{' 'when' '{' EventSequence '}' 'then' '{' EventSequence '}' '}'; |
| PartialExpectedBehaviour | ::= | Expected behaviour' ':' 'ensure that' '{' EventSequence '}'; |
| FinalConditions | ::= | Final conditions’ ':' 'with' '{' EventSequence '}'; |
| EventSequence | ::= | EventOccurence { 'and' EventOccurence }; |
| EventOccurence | ::= | EntityReference EventReference Argument [ OppositeEntityReference { ',' OppositeEntityReference } ]; |
| EntityReference | ::= | ArticleQualifier Identifier; |
| OppositeEntityReference | ::= | [ DirectionQualifier ] [ ArticleQualifier ] Identifier; |
| EventReference | ::= | { Qualifier } Identifier; |
| Argument | ::= | LiteralValueArgument |
|  |  | ¦ DataReferenceArgument |
|  |  | ¦ ContentReferenceArgument |
|  |  | ¦ LiteralValueReferenceArgument; |
| Value | ::= | LiteralValue |
|  |  | ¦ DataReference |
|  |  | ¦ ContentReference |
|  |  | ¦ LiteralValueReference; |
| LiteralValueArgument | ::= | [ ArticleQualifier ] 'new’ { Qualifier } ( Identifier ¦ NumberAsIdentifier ) [ Content { ',' Content } ]; |
| LiteralValue | ::= | 'indicating value' { Qualifier } ( Identifier ¦ NumberAsIdentifier ) [ Content { ',' Content } ]; |
| Content | ::= | 'containing' { Qualifier } ( Identifier ¦ NumberAsIdentifier ) Value; |
| Identifier | ::= | STRING ¦ ID; |
| Qualifier | ::= | Identifier; |
| ArticleQualifier | ::= | 'a' ¦ 'an' ¦ 'the'; |
| DirectionQualifier | ::= | 'from' ¦ 'to'; |
| ReferenceQualifier | ::= | 'corresponding to' ¦ 'derived from' ¦ 'carrying the'; |
| StructuredDataSpec | ::= | ( Identifier ¦ NumberAsIdentifier ) [ 'with' ActualTupleElement { ',' ActualTupleElement } ] ; |
| ActualTupleElement | ::= | Identifier 'indicating value' StructuredDataSpec; |
| ContentReference | ::= | ReferenceQualifier 'the' 'value' 'contained' 'in' Identifier; |
| LiteralValueReference | ::= | ReferenceQualifier 'the' 'value' 'of' Identifier; |
| ContentReferenceArgument | ::= | 'the' 'value' 'contained' 'in' Identifier; |
| LiteralValueReferenceArgument | ::= | 'the' 'value' 'of' Identifier; |
| DataReference | ::= | Identifier ReferenceQualifier StructuredDataSpec; |
| DataReferenceArgument | ::= | [ ArticleQualifier ] StructuredDataSpec; |
| NumberAsIdentifier | ::= | ['-'] INT [ '.' INT ]; |
| StructuredDataType | ::= | 'type' Identifier [ 'containing' TupleElement { ',' TupleElement } ] ';'; |
| TupleElement | ::= | Identifier 'of' 'type' Identifier; |
| StructuredDataInstance | ::= | Identifier ( Identifier ¦ NumberAsIdentifier ) [ 'with' TupleElementInstance { ',' TupleElementInstance } ] ';'; |
| TupleElementInstance | ::= | Identifier 'indicating value' StructuredDataSpec; |
| ID | ::= | ['^'] ( 'a'-'z' ¦ 'A'-'Z' ¦ '_' ) { 'a'-'z' ¦ 'A'-'Z' ¦ '_' ¦ '0'-'9' ¦ '/' } ; |
| INT | ::= | '0'-'9' ; |
| SQ | ::= | '"' ; |
| DQ | ::= | "'" ; |
| STRING | ::= | ( DQ ¦ { ( '\\' ¦ ( 'b' ¦ 't' ¦ 'n' ¦ 'f' ¦ 'r' ¦ 'u' ¦ '"' ¦ "'" ¦ '\\' ) ) ¦ ( '\\' ¦ DQ ) } ¦ DQ ) ¦ ( SQ ¦ { ( '\\' ¦ ( 'b' ¦ 't' ¦ 'n' ¦ 'f' ¦ 'r' ¦ 'u' ¦ '"' ¦ "'" ¦ '\\' ) ) ¦ ( '\\' ¦ SQ ) } ¦ SQ ); |
| ML_COMMENT | ::= | '/*' '*/') ; |
| SL_COMMENT | ::= | '//' ( '\\n' ¦ '\\r' ) [ ['\\r'] '\\n' ]; |
| WS | ::= | { ' ' ¦ '\\t' ¦ '\\r' ¦ '\\n' }+ ; |

Annex B (informative):
Examples

This text shall only be used for ATSs using TTCN version 2 (TTCN-2):

This ATS has been produced using the Tree and Tabular Combined Notation version 2 (TTCN-2) according to ISO/IEC 9646-3 [<x>].

Annex <X+2> (informative):
Title of informative annex (style H8)

<Text>

<X+2.1	>First clause of the annex (style H1)

<Text>

<X+2.1.1>	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

Annex <X+3> (informative):
Change History

This informative annex is optional. If present, it describes the list of changes implemented in a new version of the deliverable.

Its format is tabular, it may contain the Change Request numbers and titles or textual explanations of the changes that lead to each new version number of the deliverable.

| date | Version | Information about changes |
| --- | --- | --- |
| October 2011 | v1.1.1 | First publication of the TS after approval by TC SPAN at SPAN#19 (30 September - 2 October 2011; Prague) |
| February 2012 | v1.2.1 | Implemented Change Requests: SPAN(12)20_019 Error message information clarifications SPAN(12)20_033 Revised error message information SPAN(12)20_046 update of figure 3 clause 9.2 These CRs were approved by TC SPAN#20 (3 - 5 February 2012; Sophia) Version 1.2.1 prepared by the Rapporteur |
| July 2013 | v1.3.1 | Implemented Changes: Correction needed because the previously approved version did not contain the last version of the ASN.1 and XML attachments. Version 1.3.1 prepared by the Rapporteur |

<PAGE BREAK>

Annex <X+4> (informative):
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/Files/other/EDRs_navigator.chm).

It shall not include references mentioned in the document.

Use the Heading 8 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Document history |
| --- |
| <Version> | <Date> | <Milestone> |

## A few examples:

| Document history |
| --- |
| V1.1.1 | April 2001 | Publication |
| V1.2.1 | February 2002 | Membership approval Procedure MV XXXX: yyyy-mm-dd to yyyy-mm-dd |
| V1.3.1 | June 2011 | Pre-Processing done before TB approval e-mail: mailto:edithelp@etsi.org |
| V1.3.2 | July 2013 | Clean-up done by editHelp! e-mail: mailto:edithelp@etsi.org |

Latest changes made on 2014-02-19

# Comments

Note that time constraints and states are not included in the early draft.

EventSequence, InitialCondtions, ExpectedBehaviour, FinalConditions – At the meta-model level likely no need for further distinctions => as a consequence they are likely to be merged/removed so that StructuredTestObjective directly contains 3-4 sequences of EventOccurence

May also be moved to an informative annex if normative specification is declined.

Textual or graphical representation? Combined domain representation?

Also include non-packageable concepts? Or leave them for the annex? (especially where constraints apply or examples are needed)

Note again that time constraints are not included yet as there is still ongoing work on the concept within Part 1

Note that these have been renamed in the meta-model and will be updated here accordingly

To be merged

To be renamed

Will require separate names for the different identifiers