TR 103 185 V0.0.2 (2014-03)

User Group;
Collection of user requirements from visually impaired people for e-accessibility to ICT products and services

<

TECHNICAL REPORT

Reference

DTR/USER-00041

Keywords

Accessibility, visual QoS, SLA, quality, service, user

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM, UMTSTM and the ETSI logo are Trade Marks of ETSI registered for the benefit of its Members.
3GPPTM and LTE™ are Trade Marks of ETSI registered for the benefit of its Members and
of the 3GPP Organizational Partners.
GSM® and the GSM logo are Trade Marks registered and owned by the GSM Association.

Contents

Intellectual Property Rights	5

Foreword	6

Introduction	6

1	Scope	7

2	References	8

2.1	Normative references	8

2.2	Informative references	8

3	Definitions, symbols and abbreviations	9

3.1	Definitions	9

3.2	Abbreviations	10

4	Web and document content accessibility.	12

4.1	Definition	12

4.2	Proposals	12

5	Terminal requirement for  vision impaired people	13

5.1	Introduction	13

5.2	Proposals for terminal characteristics	13

5.2.1	Ergonomy	13

5.2.2	Smartphones applications	14

5.2.3	Touchscreen  devices	14

5.2.4	Screen	14

5.2.6	WIFI connectivity	15

5.2.7	Receiving Sending SMS	15

5.2.8	Mails	15

5.2.9	Voice mail	15

FS	15

5.2.10	GPS	15

5.2.11	Documentation	15

5.2.12	General	16

7	Bar code	16

7.1	introduction	16

7.2	Bar codes applications / restrictions	16

7.3	Proposals	16

8	Kiosks: interactive information terminals	17

8.1	Introduction	17

8.2	Proposal	17

9 TV and TNT decoders	17

10 Interactions with machines (M2M)	17

Annex <X>: Bibliography	19

History	20

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://ipr.etsi.org).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Report (TR) has been produced by ETSI User Group (USER).

# Introduction

The Information Communication  Technology(ICT) can  significantly improve the living conditions of people with disabilities .New platforms such as smartphones  phablets and tablets, combined with attractive and innovative applications and services  open  now new horizons .

This document intend to gather some  requirements  for  communication tools/devices / Services/interfaces , for vision impaired people(blind ,or low vision ,or partially sighted people).

- Blindness is defined by the World Health Organization ( WHO)as vision in a person's best eye of less than 20/500 or a visual field of less than 10 degrees.( According to numbers from the WHO, 90% of blind people live in the developing world)

- Low vision generally refers to a severe visual impairment, not necessarily limited to distance vision. Low vision applies to all individuals with sight who are unable to read the newspaper at a normal viewing distance, even with the aid of eyeglasses or contact lense

- Partially sighted indicates some type of visual problem

According to WHO ,285 million people are estimated to be visually impaired worldwide: 39 million are blind and 246 have low vision.and about 65 % of all people who are visually impaired are aged 50 and older, while this age group comprises about 20 % of the world's population.

With an increasing elderly population in many countries, more people will be at risk of age-related visual impairment.

Vision impaired people face sometimes insurmountable difficulties when they want to access new technologies using a computer, Internet access, editing and printing a text, reading a document can be extremely complex tasks despite their simplicity to another user , but ICT  may to day give people with  vision disabilities  capabilities to improve their social and economic integration in their society if some specific requirements are taken into consideration when product and services are designed.

# 1	Scope

The present document aims at identifying use cases for vision impaired people for e-access to ICT products and services but also use cases to allow users to interact with machines or equipment (e.g. users terminal, user interface) via dedicated devices (M2M communications) in order to define appropriate protocols (NFC or similar).

The intention is not to define technical solutions but to forward the requirements to the appropriate ETSI Technical bodies

Equal access to services, to WEB content , to public places is now required by law in many countries.  Vision impaired people often use of specialized devices which can help them in the current life and also provide access  to entertainment (access to TV,  book reader  ….)

Being able to use computers, mobile phones and other tools for ,work, leisure and keeping in contact are key tools for blind and partially sighted people ,In the present document, some requirements and/ or proposals in possible assistive technology for the  vision impaired people are listed.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	ITU-T Recommendation E.800: "Telephone network and ISDN quality of service, network management and traffic engineering: Terms and definitions related to quality of service and network performance including dependability".

[i.2]	ITU-T Recommendation I.112: "Vocabulary of terms for ISDNs"

[i.3]	ITU-T Recommendation I.113: "Vocabulary of terms for broadband aspects of ISDN".

[i.4]	ITU-T Recommendation I.350: "General aspects of quality of service and network performance in digital networks, including ISDNs".

[i.5]	ITU-T Recommendation I.430: "Basic user-network interface - Layer 1 specification".

[i.6]	ITU-T Recommendation I.431: "Primary rate user-network interface - Layer 1 specification".

[i.7]	ITU-T Recommendations M 60: "Maintenance terminology and definitions".

[i.8]	ETSI EG 201 013: "Human Factors (HF); Definitions, abbreviations and symbols".

[i.9]	ETSI EG 201 219: "User requirements; Guidelines on the consideration of user requirements when managing the standardization process".

[i.10]	ETSI EG 201 769: "Speech Processing, Transmission and Quality Aspects (STQ); QoS parameter definitions and measurements; Parameters for voice telephony service required under the ONP Voice Telephony Directive 98/10/EC".

[i.11]	ETSI EG 202 009-1: "User Group; Quality of Telecom Services; Part 1: Methodology for identification of parameters relevant to the Users".

[i.12]	ETSI EG 202 308: "User Group; User interoperability criteria".

[i.13]	ETSI TR 102 276: “User Group User's Quality of Service Criteria for Internet Access in Europe”.

[i.14]	W3C Web Content Accessibility Guidelines (WCAG) 2.0

[i.15]

[i.16]

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

access: function that enables a service session from an end user equipment

NOTE	See EG 202 308 [i.12]

availability: likelihood with which the relevant components of the service function can be accessed as required by the contractual conditions (temporal and spatial)

NOTE:	Space covers the geographic coverage and resource size aspects.

call: any connection (fixed or temporary) capable of transferring information between two or more users of a telecommunications system. In this context a user may be a person or a machine

call set-up time: period starting when the address information required for setting up a call is received by the network (e.g. recognized on the calling user's access line) and finishing when the called party busy tone or ringing tone or answer signal is received by the calling party (e.g. recognized on the calling user's access line)

capability: the ability of an item to meet a demand of a given size under given internal conditions

connection: connection provides for transfer of information between endpoints

NOTE:	See ITU-T Recommendation I.113-504 modified [i.3].

connection set up time: time between end of dialling and start of display of the first screen of a web page

dependability in the supplier-customer interface: the ability to provide what was promised, dependably and accurately

fault: inability of an item to perform a required function, excluding that inability due to preventive maintenance, lack of external resources, or planned actions

NOTE:	See ITU-T Recommendation I.113-603 [i.3].

function: set of processes defined for the purpose of achieving a specified objective

NOTE:	See ITU-T Recommendation I.112-403 [i.2].

parameter: when a QoS criterion is defined with boundaries and scope unambiguously and clearly stated this then becomes a parameter

NOTE:	See TR 102 276 [i.13]

Post Dialling Delay (PDD): time in milliseconds between dialling the last digit and an audible tone being heard at the originating end

Quality of Service (QoS): collective effect of service performance which determines the degree of satisfaction of a user of the service

NOTE 1:	See ITU-T Recommendation E.800 [i.1].

NOTE 2:	The quality of service is characterized by the combined aspects of service support performance, service operability performance, serveability performance, service security performance and other factors specific to each service. The term "quality of service" is not used to express a degree of excellence in a comparative sense nor is it used in a quantitative sense for technical evaluations. In these cases a qualifying adjective (modifier) should be used.

NOTE 3:	Complementary definition on QoS requirements of the user/customer, QoS offered by service provider, QoS achieved by service provider, QoS perceived by the user/customer are given in ETR 003.

reliability: ability of an item to perform a required function under stated conditions for a given time period

NOTE 1:	See ITU-T Recommendations E.800 [E[i.1]] and M 60 [i.7].

service provider: organization that offers a telecommunication service to the customer and/or user

NOTE 1:	A service provider needs not to be a network operator (EG 201 769-1 [i.10]).

NOTE 2:	A service provider that is subject to the requirements of the ONP Voice Telephony Directive will in most cases also be a network operator.

speed: speed is the performance criterion that describes the time interval required to perform a function or the rate at which the function is performed (The function may or may not be performed with the desired accuracy)

NOTE:	See ITU-T Recommendation I.350 [i.4].

survey: Enquiry carried out to assess a particular QoS parameter, e.g. "Queue time at the information desk" or "percentage of cities of more than 5000 inhabitants with an information desk"

Terminal Equipment (TE): functional group on the user side of a user-network interface

NOTE 1:	See ITU-T Recommendation I.112-417 [i.2]

NOTE 2:	In ITU-T Recommendations I.430 [i.5] and I.431 [i.6], "TE" is used to indicate terminal terminating 
layer 1 aspects of TE1, TA and NT2 functional groups.

threshold: reference value to determine that a parameter is within the acceptable contractual fork

time to connect: time between the end of dialling and ringing or lift up or busy tone

usability: effectiveness, efficiency and satisfaction with which specified users can achieve specified goals (tasks) in a particular environment. In telecommunications, usability should also include the concepts of learnability and flexibility; and reference to the interaction of more than one user (the A and B parties) with each other and with the terminals and the telecommunications system, EG 201 013 [i.8].

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

ADSL	Asymmetric Digital Subscriber Line

CDR	Call Detail Record

CLR	Circuit Loudness Rating

CRM	Customer Relationship Management

DMOS	Degradation Mean Opinion Score

DNS	Domain Name System

GPRS 	General Packet Radio Service

GSM	Global System for Mobile

ISP	Internet Service Provider

ITSEC	Information Technology SECurity

LR	Loudness Rating

MMS	Multimedia Message Service

MO	Mobile Originate

MOS	Mean Opinion Score

MT	Mobile Terminate

PDD	Post Dialling Delay

POP	Post Office Protocol

POTS	Plain Old Telephony Service

PSQM	Perceptual Speech Quality Measurement

PSTN	Public Switched Telephone Network

QoS	Quality of Service

SLA	Service Level Agreement

SMS	Short Message Service

TE	Terminal Equipment

UMTS	Universal Mobile Telecommunications System

# 4	Web and document content accessibility.

## 4.1	Definition

A document is considered accessible  if it can be read and used by any user, regardless of the computer tool at its disposal: screen, screen reader voice synthesizer, braille display, keyboard or  others devices

Note: Note : A screen reader allows a totally blind person to hear what is on screen ,a screen reader read it out  in a  synthetic voice and its give a couple of extra ways of interacting with what on screen  from the keyboard.

## 4.2	Proposals

Several rules and principles should be taken into account  to provide the Web content & document accessibility.

As examples we may list:

Structuring the document by separating different content

Presenting Information and user interface components to users in ways they can perceive them.

E.g. Provide text alternatives to graphics;

Make accessible tables to display the data with an organization facilitating understanding

Use contrasting colors and pretty standard fonts;

Find an alternative to  font enrichment (bold, italic, underline)

Operability - User interface components and navigation must be operable.

Understandability - Information and the operation of user interface must be understandable.

Robustness - Content must be robust enough that it can be interpreted reliably by a wide variety of user agents, including assistive technologies.

If a content is not compliant with these rules, users with disabilities will not be able to use the Web

The best objective for any webmaster or document editor is to comply with "WCAG 2.0" Dec 2008 [i.14] specification.

Note:  the BrailleNet Association ( W3C member) has registered  a trademark “Accessiweb”  with the following missions:

- production and maintenance of Repositories from the work of W3C/WAI

- Training for web professionals and the general public.

- benchmarking the compliance of websites with accessibility standards W3C/WAI

- participation in European projects and carrying initiatives eAccessibility

Recommendation:For vision impaired people , it is really important to get on line ,to feel included in the society ,to be able to participate  in learning and in leasure, so  it is highly recommended that   any WEBSITE   comply  with "WCAG 2.0" Dec 2008 [i.14]  ( eg via  “accessiweb “ benchmarking process or equivalent)

# 5	Terminal requirement for  vision impaired people

There are many degrees of visual impairment ranging from difficulty in reading small characters through to total blindness.

With all mobile phones incorporating displays providing a range of options for users with visual impairments is important.

## 5.1	Introduction

The following criteria are highly recommended to improve accessibility to smartphone/phablet/ tablet ,  usage.

Terminals designed to meet requirements for visually impaired people need to offer appropriate ergonomy and include as basic functionalities  : Speech synthesis/ speech recognition/ and if possible physical-keypad.

## 5.2	Proposals for terminal characteristics

All parameters  regarding accessibility  should be  located in One Menu  :eg named "accessibility parameters".

### 5.2.1	Ergonomy

. In particular the following features are likely to be of interest:

On-off button   must be dedicated and distinct

Audible   / haptic / or visual  feedback when keys are pressed eg  Audible alert, visual and/or haptic signal.

On physical  AZERTY keyboards ,  key  5 , and letters F – J  are  marked.

Standardized colors : green to call  and red to hang Off are required

Volume  button + and -  must be dedicated and distinct.

Easy access to sim card / memory SD cards, battery .

Audible alert, visual and/or haptic is required for

Code pin ( acceptance/ denied)

Wireless network availability

Low battery level

Information on Calling line identity

Different ringing tone depending on caller identity.

the ability to assign different ring tones to different numbers stored in the phone allows vision impaired people to allocate a specific ring tone to a family member.

This feature ease to know who is trying to contact , when the phone rings without the need to even look at the display of the phone.

This feature can be enhanced with the ,Name announcement

Display on screen.

Calls history ( missed  , incoming , outgoing ,calls,

Key lock screen dedicated and perfectly distinct.

Dynamic key allocation to services / applications

Make easy contact  list ( from an incoming call)

Possibility to use voice  control to dial a number or to access phone functionalities

### 5.2.2	Smartphones applications

The Operating system of Standard Smartphones ( android phone/iPhone/windows phone ….) should  include  natively services /applications  such as speech recognition /speech synthesis / and screen reader functionalities …

However, most touch screen phones make navigation and keypad operation quite difficult.

For Android devices a guide has been edited to help application developpers to address the  services accessibility

http://eyes-free.googlecode.com/svn/trunk/documentation/android_access/index.html

### 5.2.3	Touchscreen  devices

Smartphones should natively include screen reader functionalities.

A screen reader will provide right information if the  applications fullfil recommendations  given by Worldwide web consortium

The issue of web accessibility has been addressed by the Web Accessibility Initiative (WAI) of the World Wide Web Consortium (W3C) has produced a series of recommendations, the Web Content Accessibility Guidelines, to help content developers producing websites or web applications

Speech synthesis

The voice should be clear and pleasant to hear, and the playback speed  must be  adjustable.

High definition sound is recommended and attenuation of ambient noise around the speaker's voice

Speech synthesis  provided by screen readers should be compatible with wireless headsets.

Speech recognition.

Voice recognition is also a very useful feature that can help people with a visual impairment. This allows the user to use voice commands for dialing and accessing features on the phone.

Speech recognition often needs cloud ressources , and in such a case data transmitted on the radio path to the speech recognition server must be encrypted.

If no encryption , no sensitive transaction  (consulting bank account, purchase internet, transfer order) requiring the sending of personal data (code number and credit card, bank references, in particular) should be performed via speech recognition.

In order to improve ergonomy ,availability of an API allowing additional software to provide additional screen reader services.

### 5.2.4	Screen

For people with low vision a  phone with a large screnn will be easier to use . Almost all displays are colour, with adjustable brightness, contrast and font size. These  srenns should be very bright, with high resolution and contrast, making colours intense and blacks very dark, in particular Screen color and font color must be customizable.This feature should be easily configurable and  for example  yellow font on a dark blue background is particularly appreciated by some visually impaired.

5.2.5  Shape

The shape of the device may also be something to consider. In this case a sliding or flip phone design may be of interest to make it easier to answer or hang up a call

### 5.2.6	WIFI connectivity

Setting access to a Wi-Fi hot spot is still a difficult  task .

Three Steps are required:

-Selection of right wifi network .this recognition can use Speech synthesis to identify the right netw-Enter the key : In some router or Adsl Boxes , the mac address is used as  a WIFI key .In such a case the mac address should be associated to a QR code containing same information. ( applications may  read the QR code and automatically configured  the wifi access .

Note an example is  the Wifi joiner application(An Android app that can add networks to phones by just scanning a QR code.)

-Get the confirmation of the succesfull connection?. This could be done by Speech synthesis or any solution giving a positive feedback

### 5.2.7	Receiving Sending SMS

FS

### 5.2.8	Mails

FS

### 5.2.9	Voice mail

### FS

Pre-recorded voice messages are needed.

### 5.2.10	GPS

New applications and services are now using GPS to guide the blind and visually impaired in their travels in the city For example application may  announce theclosest point of interest and may also locates the user.

A pedestrian GPS is considered as a key feature and should be natively  available.

For security reasons ,the mobile user could also be localized  by third parties if the regulation and /or  user allows this feature.

### 5.2.11	Documentation

Video tutorials  should be available.including physical description of the device.

Accessibility have to be considered:

for phone software maintenance ( eg update of firmware,)

for data synchronization ( between  Pc & phone …)

for web surfing ( eg with bookmarks..)

to access to application stores.( eg with clear information on applications rights/ costs …)

### 5.2.12	General

Accessibility have also to be considered:

for phone software maintenance ( eg update of firmware,)

for data synchronization ( between  Pc & phone …)

for web surfing ( eg with bookmarks..)

to access to application stores ( eg with clear information on applications rights/ costs …)

# 7	Bar code

## 7.1	introduction

The development of assistive technologies for the visually impaired can now provide access to cloud information as exists for every one via the Web,

To allow all these people to purchase product  / services  , with the  right level of information

A clear Identification of the products and of their use is needed .

Protection against fraud and / or counterfeiting becomes also a key requirement .

The GenCode more precisely BarCodeEAN _8 or 13 which is standardized and present on product packaging  need to be considered.

## 7.2	Bar codes applications / restrictions

Many useful applications are possible with bar codes:

Bus time schedule product information,  /Geo-localisation,/URl for web access, Food traceability  etc

However visually impaired people encounter severe difficulties to get all advantages of bar code information such as:

How to detect the presence of a 2D bar code?

How to use the flash when ambient light is too low?

How to save the information in the user’s database?

## 7.3	Proposals

It is proposed :

to expand the role of the linear barcode (EAN8 & EAN13) about customer experience rather than only product infos

to Educate bodies responsible for establishing rules of web accessibility (W3C) to advocate its presence whenever possible and desirable, therefore its ranking by the search engines, incidentally increase the visibility of commercial sites,

to  clearly differentiate product identification ( marking) and product information

to  facilitate the location thus capture all via a judicious positioning advantage of tactile cues

natural and specific family of packages.

to  create a data base

The EAN bar code that appears on a product is truly a serial number designating family product identification . It is the technical element used internally by professionals despite the emergence of 2D barcodes.

In order to get more information on product and services a  database is proposed :

This data base will be available online and placed under the supervision of the Public Authority, identifying the product information .

The content of data base will be fueled by the professional themselves willing to introduce their goods on the market,

# 8	Kiosks: interactive information terminals

## 8.1	Introduction

In Point Of Sales (POS) the Kiosk terminals usually identify the product to display the price.

## 8.2	Proposal

Depending on technologies several possibilities could be studied

A 2D code printed on the receipt could  provide  detailed information

A copy of Paper receipt could be sent electronically to a personal device ( such as a smartphone / tablet.etc)

An access to a point of sale  data base could provide the list of purchased product their prices  an all appropriate information on product.

# 9 TV and TNT decoders

# The TV has a major role in our society in particular access to information and culture, and digital  TV offer new opportunities to improve accessibility to  programs for people with disabilities.

Vocalization for digital television  is a key feature which allow visually impaired people to  follow a tv channel.

It is a process that can reproduce via a voice message, any textual information normally displayed by the receiver on the TV screen, as the setup menu the receiver's name and channel number, data of the electronic program guide, the selected audio track

# 10 Interactions with machines (M2M)

For furthers studies.

Annex <A>:
Title of annex (style H9)

<Text>

Annex 1
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself (see clause 12.2 of the EDRs http://portal.etsi.org/edithelp/Files/other/EDRs_navigator.chm).

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

- <Publication>: "<Title>".

OR

<Publication>: "<Title>".

# History

| Document history |
| --- |
| V0.0.1 | October 2013 | Early draft |
| V0.0.2 | March 2014 | Draft for USER#50 |