Project Deliverable

| Project Number: | Project Acronym: | Project Title: |
| --- | --- | --- |
| 216312 | Walter | Wireless Alliances for Testing Experiment and Research |

| Instrument: | Thematic Priority |
| --- | --- |
| STREP | The network of the future |

Title

D 5.2 WALTER Networked laboratory. Operational configuration

| Contractual Delivery Date: | Actual Delivery Date: |
| --- | --- |
| M14 | M15 |

| Start date of project: | Duration: |
| --- | --- |
| January, 1st 2008 | 24 months |

| Organization name of lead contractor for this deliverable: | Document version: |
| --- | --- |
| AT4 wireless | V1.1 |

| Dissemination level ( Project co-funded by the European Commission within the Seventh Framework Programme) |
| --- |
| PU | Public | X |
| PP | Restricted to other programme participants (including the Commission |  |
| RE | Restricted to a group defined by the consortium (including the Commission) |  |
| CO | Confidential, only for members of the consortium (including the Commission) |  |

Authors (organizations) :

AT4 wireless JRC TMC CSR inno

Abstract :

This deliverable describes the operational configuration of the test bed which will be used for the execution of the test procedures defined in Task 4.4. This document provides details on the specific solution taken by each laboratory for each of the test setups identified in D 4.5 WALTER Report on test bed architecture and specification.

Keywords :

Operational, configuration, test, setup, equipment, UWB, testbed.

Disclaimer

THIS DOCUMENT IS PROVIDED "AS IS" WITH NO WARRANTIES WHATSOEVER, INCLUDING ANY WARRANTY OF MERCHANTABILITY, NONINFRINGEMENT, FITNESS FOR ANY PARTICULAR PURPOSE, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION OR SAMPLE. Any liability, including liability for infringement of any proprietary rights, relating to use of information in this document is disclaimed. No license, express or implied, by estoppels or otherwise, to any intellectual property rights are granted herein. The members of the Wireless ALliance for Test, Experiments and Research ("WALTER") do not accept any liability for actions or omissions of WALTER members or third parties and disclaims any obligation to enforce the use of this document. This document is subject to change without notice.

Revision History

The following table describes the main changes done in the document since it was created.

| Revision | Date | Description | Author (Organisation) |
| --- | --- | --- | --- |
| V0.7 | 2009-03-11 | Creation | AT4 wireless TMC JRC |
| V0.8 | 2009-03-16 | Test setups updated Acronyms list updated Identities of laboratories have been made anonymous | AT4 wireless TMC JRC CSR |
| V1.1 | 2009-03-17 | Quality review | inno |

Table of Content

1.	Acronyms and Definitions	6

1.2.	Definitions	7

2.	Executive summary	8

3.	Regulatory (REG)	9

3.1.	Spectrum and Power Characteristics (SPC)	9

3.1.1.	ST_REG_SPC_001	9

3.1.2.	ST_REG_SPC_002	12

3.2.	Radiated Emissions (RE)	13

3.2.1.	ST_REG_RE_001	13

3.3.	Time-related Parameters (TP)	13

3.3.1.	ST_REG_TP_001	13

3.3.2.	ST_REG_TP_002	15

3.4.	Detect and Avoid (DAA)	16

3.4.1.	ST_REG_DAA_001	16

3.4.2.	ST_REG_DAA_002	17

3.5.	Electromagnetic Compatibility (EMC)	19

4.	Radiated Performance Testing (RPT)	20

4.1.	Transmission	20

4.1.1.	ST_RPT_TX_001	20

4.2.	Reception	22

4.2.1.	ST_RPT_RX_001	22

4.2.2.	ST_RPT_RX_002	23

4.2.3.	ST_RPT_RX_003	25

5.	Over the Air (OTA)	29

6.	Conformance (CON)	30

6.1.	PHY	30

6.1.1.	ST_CON_PHY_001	30

6.1.2.	ST_CON_PHY_002	33

6.2.	MAC	35

6.2.1.	ST_CON_MAC_001	35

6.3.	UPP	40

6.3.1.	ST_CON_UPP_001	41

7.	IOP (Interoperability)	42

7.1.	MAC	42

7.1.1.	ST_IOP_MAC_001	42

7.1.2.	ST_IOP_MAC_002	43

7.1.3.	ST_IOP_MAC_003	45

7.2.	Internet Protocol	48

7.2.1.	ST_IOP_IP_001	48

7.2.2.	ST_IOP_IP_002	50

7.3.	Application Interoperability (APP)	53

7.3.1.	ST_IOP_APP_001	53

8.	Coexistence (COE)	55

9.	Performance (PER)	56

9.1.	Sensitivity versus Temperature (S-T)	56

9.1.1.	ST_PER_S-T_001	56

9.2.	Output Power versus Temperature (P-T)	57

9.2.1.	ST_PER_P-T_001	57

10.	References	60

# Acronyms and Definitions

## Acronyms

| Acronym | Defined as |
| --- | --- |
| [AP] | Access Point |
| [BS] | Base Station |
| [COE] | Coexistence |
| [CON] | Conformance |
| [DAA] | Detect and Avoid |
| [DL] | Downlink |
| [DSO] | Digital Sampling Oscilloscope |
| [EIRP] | Equivalent Isotropically Radiated Power |
| [EMC] | Electromagnetic Compatibility |
| [ETSI] | European Telecommunications Standards Institute |
| [EUT] | Equipment Under Test |
| [INTD] | Interoperability Device |
| [IOP] | Interoperability |
| [LDC] | Low Duty Cycle |
| [LNA] | Low Noise Amplifier |
| [MAC] | Medium Access Control |
| [MAPS] | Multi-Axis Positioning System |
| [MS] | Mobile Station |
| [OTA] | Over the Air |
| [PCA] | Prioritized Contention Access |
| [PCT] | Protocol Conformance Testing |
| [PRF] | Pulse Repetition Frequency |
| [PSA] | Power Spectrum Analyzer |
| [PSD] | Power Spectral Density |
| [PHY] | Physical layer |
| [QE] | Qualified Equipment |
| [RCT] | Radio Conformance Testing |
| [RE] | Radiated Emissions |
| [RPT] | Radiated Performance Testing |
| [SPC] | Spectrum and Power Characteristics |
| [SS] | Subscriber Station |
| [STA] | Station |
| [TP] | Time-related Parameters |
| [TPC] | Transmit Power Control |
| [TS] | Test System |
| [UL] | Uplink |
| [UWB] | Ultra-Wide Band |

## Definitions

Single radio standard device:

It is a device that implements one wireless technology only.

Multiple radio standard device:

It is a device that implements two or more wireless technologies which can operate simultaneously.

# Executive summary

This deliverable describes the operational configuration of the test bed which will be used for the execution of the test procedures defined in Task 4.4. This document provides details on the specific solution taken by each laboratory for each of the test setups identified in D 4.5 WALTER Report on test bed architecture and specification [1].

This deliverable follows the structure of test categories and sub-categories defined in D 4.7 WALTER Test categories [2]. Each of the operational configurations identified here can be used for one or more than one test scenarios. The list of test scenarios supported by each setup is provided in D 4.5 [1] but has been included here as well for direct reference.

As some of the laboratories are not allowed to make their test setups public due to confidentiality issues, the three laboratories will be anonymously referred to as Laboratory 1, Laboratory 2 and Laboratory 3.

This deliverable contains the following chapters; the first one is the list of acronyms and definitions used in the document, the second one is the executive summary, the following sections contain the operational configurations for each of the test categories identified in WALTER and the final section is the list of reference documents.

# Regulatory (REG)

This section focuses on all tests required to check whether devices meet the requirements established by different regulatory domains such as the European Union, USA, China, etc. This sub-section covers different test areas including Spectrum and Power Characteristics (SPC), Radiated Emissions (RE), Time-Related Parameters (TP), Detect and Avoid (DAA) and Electromagnetic Compatibility (EMC).

The following sub-sections identify the operational configurations for each of the sub-categories mentioned above.

## Spectrum and Power Characteristics (SPC)

This test sub-category deals with a number of tests intended to measure the spectrum and power characteristics of the EUT (Equipment Under Test).

### ST_REG_SPC_001

This test setup covers the following test scenarios using a radiated configuration:

TSID_REG_SPC_001 Operating bandwidth

TSID_REG_SPC_002 Maximum value of mean power spectral density (PSD)

TSID_REG_SPC_003 Maximum value of peak power

TSID_REG_SPC_004 Transmit Power Control (TPC)

#### Operational configuration – Laboratory 1

Figure 1 shows the operational configuration employed by the Laboratory 1 for this test setup:

Figure 1 : ST_REG_SPC_001 – Laboratory 1

The test site employed is a semi-anechoic chamber (whose internal walls and ceiling are covered with radio absorbing material) with a metallic ground plane which simulates an ideal open area test site whose primary characteristic is a perfectly conducting ground plane of infinite extent.

The measurement antenna utilized in the previous configuration varies depending on the frequency range. From 30 MHz to 1 GHz for instance, a classical Biconical Log-Periodic Bilog antenna (Bilog hereinafter) is used. Above 1 GHz, waveguide horns are employed.

The positioner and table controller rotates the EUT in order to look for the position that maximizes the power received at the measurement antenna. This controller is also capable of modifying the measurement antenna height and rotating the antenna positioner in order to change the antenna polarization.

#### Operational configuration – Laboratory 2

Figure 2 shows the operational configuration employed by the Laboratory 2 for this test setup:

Figure 2 : ST_REG_SPC_001 – Laboratory 2

The measurement antenna used is a diagonal dual-polarized waveguide horn.

#### Operational configuration – Laboratory 3

Figure 3 shows the operational configuration employed by the Laboratory 3 for this test setup:

Figure 3 : ST_REG_SPC_001 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_SPC_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Meas. system | PSA, LNA | PSA, LNA | PSA or DSO, LNA |
| Meas. antenna | Bilog and waveguide horns | Waveguide horns | Log, waveguide horns |
| Antenna mast | Antenna positioner: Configurable polarization Configurable height | Antenna positioner: Configurable polarization Configurable height | Antenna positioner |
| EUT positioner | Rotating table | MAPS | Rotating table |
| EUT controller | Control PC | Control PC | Control PC |
| Additional elements | Positioner and table controller | MAPS and positioner controller | IOP device |

Table 1: Comparison matrix for ST_REG_SPC_001

### ST_REG_SPC_002

This test setup covers the following test scenarios using a conducted configuration:

TSID_REG_SPC_001 Operating bandwidth

TSID_REG_SPC_002 Maximum value of mean power spectral density (PSD)

TSID_REG_SPC_003 Maximum value of peak power

TSID_REG_SPC_004 Transmit Power Control (TPC)

#### Operational configuration – Laboratory 1

Figure 4 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 4 : ST_REG_SPC_002 – Laboratory 1

In this case, the spectrum analyzer is directly connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector).

When the EIRP (Equivalent Isotropically Radiated Power) values are required, the full characterization of the antenna along the entire frequency bands is needed.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and analyzer’s ports.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_SPC_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Shielded chamber |
| Measurement system | PSA | PSA | PSA |
| EUT controller | Control PC | Control PC | Control PC |

Table 2: Comparison matrix for ST_REG_SPC_002

## Radiated Emissions (RE)

The RE section deals with the characterization of the emissions radiated by the EUT and therefore, as stated in the ETSI harmonized standard EN 302 065 [3], this test must be done using a radiated configuration.

### ST_REG_RE_001

This test setup covers the test scenario TSID_REG_RE_002 Receiver Spurious Emissions.

#### Operational configuration – Laboratory 1

This operational configuration is the same as the one in ST_REG_SPC_001 (Figure 1).

#### Operational configuration – Laboratory 2

This operational configuration is the same as the one in ST_REG_SPC_001 (Figure 2).

#### Operational configuration – Laboratory 3

This operational configuration is the same as the one in ST_REG_SPC_001 (Figure 3).

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_RE_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Measurement system | PSA, LNA | PSA, LNA | PSA or DSO, LNA |
| Measurement antenna | Bilog and waveguide horns | Waveguide horns | Log and waveguide horns |
| Antenna mast | Antenna positioner: Configurable polarization Configurable height | Antenna positioner: Configurable polarization Configurable height | Antenna positioner |
| EUT positioner | Rotating table | MAPS | Rotating table |
| EUT controller | Control PC | Control PC | Control PC |
| Additional elements | Positioner and table controller | MAPS and positioner controller | IOP device |

Table 3: Comparison matrix for ST_REG_RE_001

## Time-related Parameters (TP)

This TP section is focused on those time-related parameters of the EUT that have impact on the regulatory rules.

### ST_REG_TP_001

This test setup covers the following test scenarios using a conducted configuration:

TSID_REG_TP_001 Pulse Repetition Frequency (PRF)

TSID_REG_TP_002 Low Duty Cycle (LDC)

TSID_REG_TP_004 Dwell Time

The standards do not specify test procedures for TSID_REG_TP_001 and TSID_REG_TP_002 and let vendors declare compliance with the requirements. Notwithstanding, this test setup can be used for testing these parameters.

#### Operational configuration – Laboratory 1

Figure 5 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 5 : ST_REG_TP_001 – Laboratory 1

The Digital Sampling Oscilloscope (DSO) or spectrum analyzer is directly connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector).

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and oscilloscope’s ports.

#### Operational configuration – Laboratory 2

This operational configuration is the same as the one employed for ST_REG_SPC_002.

#### Operational configuration – Laboratory 3

This operational configuration is the same as the one employed for ST_REG_SPC_002.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_TP_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Shielded chamber |
| Measurement system | PSA or DSO | PSA | PSA |
| EUT controller | Control PC | Control PC | Control PC |

Table 4: Comparison matrix for ST_REG_TP_001

### ST_REG_TP_002

This test setup covers the test scenario TSID_REG_TP_003 Transmitter Timeout and has to be done using a radiated configuration.

#### Operational configuration – Laboratory 1

Figure 6 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 6 : ST_REG_TP_002 – Laboratory 1

The protocol analyzer is capable of capturing and decoding all MAC (Medium Access Control) frames of the technology being tested.

The test site employed is a semi-anechoic chamber with a conducting ground plane.

The IOP device is employed in order to establish and keep a communication link with the EUT. It is neither a signalling unit nor a reference device but a second device provided by EUT’s vendor.

#### Operational configuration – Laboratory 2

Not implemented yet.

#### Operational configuration – Laboratory 3

This operational configuration is the same as the one employed for ST_REG_SPC_001 (Figure 3).

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_TP_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | N/A | Full-anechoic chamber |
| Measurement system | Protocol analyzer | N/A | PSA or DSO |
| EUT controller | Control PC | N/A | Control PC |
| IOP device | Yes | N/A | Yes |
| Measurement system controller | Control PC | N/A | Control PC |

Table 5: Comparison matrix for ST_REG_TP_002

## Detect and Avoid (DAA)

Detect And Avoid techniques are required for a number of technologies in order to coexist with others. These techniques allow the detection of other wireless systems that can be interfered when working in the same frequency bands, at the same time and at the same area, and then act accordingly in order to mitigate or eliminate the effects on the interfered system.

### ST_REG_DAA_001

This test setup covers the following test scenarios using a conducted configuration:

TSID_REG_DAA_001 Start-Up Test

TSID_REG_DAA_002 In-Operation Test

#### Operational configuration – Laboratory 1

Figure 7 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 7 : ST_REG_DAA_001 – Laboratory 1

The EUT will be able to keep a stable link with the IOP device in all test scenarios.

The spectrum analyzer will be able to detect the EUT level and the victim level in all the required dynamic range.

It is assumed that the time domain and frequency domain parameters of the EUT and the victim will be such that the signals can be differentiated.

The level generated by the IOP device will get to the spectrum analyzer port in a level that is significantly lower then the EUT level so the EUT level can be measured.

The 3-port splitter acts as a power splitter regardless the input port. The 2-port splitter acts a power splitter only through the EUT’s port. This element is required to provide high isolation between the IOP device’s port and the upper port in order to avoid the measurement of signals coming from the IOP device in the measurement system.

#### Operational configuration – Laboratory 2

Figure 8 illustrates the operational configuration employed by the Laboratory 2 for this test setup:

Figure 8 : ST_REG_DAA_001 – Laboratory 2

#### Operational configuration – Laboratory 3

Not implemented.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_DAA_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Measurement system | PSA | PSA | N/A |
| Victim signal generation | Vector signal generator | Signal generator | N/A |
| EUT controller | Control PC | Control PC | N/A |
| IOP device | Yes | Yes | N/A |
| Additional elements | Power splitters/combiners Variable attenuators LNA | Power splitters/combiners LNA | N/A |

Table 6: Comparison matrix for ST_REG_DAA_001

### ST_REG_DAA_002

This test setup covers the following test scenarios using a conducted configuration:

TSID_REG_DAA_001 Start-Up Test

TSID_REG_DAA_002 In-Operation Test

#### Operational configuration – Laboratory 1

Not implemented.

#### Operational configuration – Laboratory 2

Not implemented.

#### Operational configuration – Laboratory 3

Figure 9 illustrates the operational configuration employed by the Laboratory 3 for this test setup:

Figure 9 : ST_REG_DAA_002 – Laboratory 3

The RF circulators provide enough isolation in the reverse direction in order to avoid the presence of signals other than the EUT’s one in the spectrum analyzer.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_REG_DAA_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | N/A | N/A | Shielded chamber |
| Measurement system | N/A | N/A | PSA |
| Victim signal generation | N/A | N/A | Signal generator |
| EUT controller | N/A | N/A | Control PC |
| IOP device | N/A | N/A | Yes |
| Additional elements | N/A | N/A | Power splitters, variable attenuators, LNA and circulators |

Table 7: Comparison matrix for ST_REG_DAA_002

## Electromagnetic Compatibility (EMC)

The present sub-section contains the common requirements for radio communications equipment and associated ancillary equipment, in respect of Electromagnetic Compatibility (EMC). EMC requirements have been split into two categories: EMC emission and Immunity.

This test sub-category has been given low priority in WALTER (see D 4.8 WALTER Testing scope [4]); therefore, no test setups have been identified for EMC.

# Radiated Performance Testing (RPT)

This test category groups all measurements related to the radiated performance of the device, both in transmission mode and reception mode.

## Transmission

For the transmission mode, the following test setups have been identified.

### ST_RPT_TX_001

This test setup covers the test scenario TSID_RPT_TX_001 using a radiated configuration.

#### Operational configuration – Laboratory 1

Figure 10 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 10 : ST_RPT_TX_001 – Laboratory 1

The test site employed is a full-anechoic chamber that simulates free space conditions.

The control PC contains the necessary software in order to control and synchronize all the elements. All relevant data for the measurement are recorded in this PC.

The MAPS (Multi-Axis Positioning System) is a combined-axis system that mounts the phi-axis positioner on the theta-axis positioner to rotate the EUT along these two axes.

The emulator establishes and keeps a link with the EUT through the RF Relay Switch and the communication antenna during the whole test.

The RF Relay Switch receives the two polarizations of the measurement antenna (horizontal and vertical) and forwards the appropriate signal to the Spectrum Analyzer.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

Figure 11 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 11 : ST_RPT_TX_001 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_RPT_TX_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Full anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Measurement system | PSA | PSA | PSA or DSO |
| Measurement antenna | Horn antenna | Horn antenna | Horn/Log periodic antennae |
| Communication antenna | Conical antenna | Conical antenna | Horn antenna |
| Qualified equipment | Emulator (signaling unit) | Emulator (signaling unit) | Signal generator |
| EUT controller | Control PC | Control PC | Control PC |
| Positioning system | Combined-axis positioning system | Combined-axis positioning system | Distributed-axis positioning system |
| Additional elements | RF Relay switch | RF Relay switch | RF switches LNA |

Table 8: Comparison matrix for ST_RPT_TX_001

## Reception

For the reception mode, the following test setups have been identified.

### ST_RPT_RX_001

This test setup covers the following test scenarios using a radiated configuration:

TSID_RPT_RX-S_001 Total Isotropic Sensitivity

TSID_RPT_RX-S_002 Intermediate Channel Sensitivity

#### Operational configuration – Laboratory 1

Figure 12 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 12 : ST_RPT_RX_001 – Laboratory 1

The test site employed is a full-anechoic chamber that simulates free space conditions.

The control PC contains the necessary software in order to control and synchronize all the elements. All relevant data for the measurement are recorded in this PC.

The MAPS rotates the EUT along the phi and theta axes.

The emulator establishes and keeps a link with the EUT through the communication antenna during the whole test and measures the appropriate digital error rate at each point in order to find the sensitivity value.

The RF Relay Switch receives the two polarizations of the measurement antenna (horizontal and vertical) and forwards the appropriate UL signal to the Spectrum Analyzer. Likewise, it receives the DL signal from the emulator and forwards it to the communication antenna.

In those cases where the power level received from the measurement antenna is too low and the links need to be balanced, an additional Dynamic Range Extender (DRE) is needed. This additional element would receive the UL signal from a dedicated port in the QE and would forward the balanced DL signal to another dedicated port in the emulator. The UL and DL signals would be received or forwarded from or to the RF Relay Switch respectively.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_RPT_RX_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Full anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Measurement system | Emulator | Emulator | Emulator |
| Measurement antenna | Horn antenna | Horn antenna | Horn antenna |
| Qualified equipment | Emulator (signaling unit) | Emulator (signaling unit) | Emulator (signaling unit) |
| EUT controller | Control PC | Control PC | Control PC |
| Positioning system | Combined-axis positioning system | Combined-axis positioning system | Combined-axis positioning system |
| Additional elements | RF Relay switch LNA | RF Relay switch LNA | RF Relay switch LNA |

Table 9: Comparison matrix for ST_RPT_RX_001

### ST_RPT_RX_002

This test setup covers the following test scenarios using a radiated configuration:

TSID_RPT_RX-S_001 Total Isotropic Sensitivity

TSID_RPT_RX-S_002 Intermediate Channel Sensitivity

This setup is more appropriated than ST_RPT_RX_001 in cases where the power level received at the measurement antenna is too low to properly measure the sensitivity of the EUT.

#### Operational configuration – Laboratory 1

Figure 13 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 13 : ST_RPT_RX_002 – Laboratory 1

The test site employed is a full-anechoic chamber that simulates free space conditions.

The control PC contains the necessary software in order to control and synchronize all the elements. All relevant data for the measurement are recorded in this PC.

The MAPS rotates the EUT along the phi and theta axes.

The emulator establishes and keeps a link with the EUT through the communication antenna during the whole test and measures the appropriate digital error rate at each point in order to find the sensitivity value.

The RF Relay Switch receives the UL signal from the communication antenna and forwards it to the emulator. Likewise, it receives the DL signal from the QE and forwards it to the measurement antenna.

#### Operational configuration – Laboratory 2

Figure 14 illustrates the operational configuration employed by the Laboratory 2 for this test setup:

Figure 14 : ST_RPT_RX_002 – Laboratory 2

#### Operational configuration – Laboratory 3

Figure 15 illustrates the operational configuration employed by the Laboratory 3 for this test setup:

Figure 15 : ST_RPT_RX_002 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_RPT_RX_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Full anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Measurement system | Emulator | Emulator and PSA | Emulator and PSA |
| Measurement antenna | Horn antenna | Horn antenna | Horn antenna |
| Communication antenna | Conical antenna | Conical antennae | Log periodic antenna |
| Qualified equipment | Emulator (signaling unit) | Emulator (signaling unit) | Emulator (signaling unit) |
| EUT controller | Control PC | Control PC | Control PC |
| Positioning system | Combined-axis positioning system | Combined-axis positioning system | Combined-axis positioning system |
| Additional elements | RF Relay switch LNA | RF Relay switch | RF Relay switch LNA |

Table 10: Comparison matrix for ST_RPT_RX_002

### ST_RPT_RX_003

This test setup covers the following test scenarios using a radiated configuration:

TSID_RPT_RX-M_001 Desense on Radio Being Tested

TSID_RPT_RX-M_002 Desense on Combined Radio

#### Operational configuration – Laboratory 1

Figure 16 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 16 : ST_RPT_RX_003 – Laboratory 1

The test site employed is a full-anechoic chamber that simulates free space conditions.

The control PC contains the necessary software in order to control and synchronize all the elements. All relevant data for the measurement are recorded in this PC.

The MAPS rotates the EUT along the phi and theta axes.

All elements or links marked with the number “1” are related to the radio being tested and those marked with the number “2” are related to the combined radio.

The emulator 1 establishes and keeps a link (on which the measurement will take place) with the EUT through the communication antenna 1 and the measurement antenna during the whole test and measures the appropriate digital error rate at each point in order to find the sensitivity value.

The emulator 2 establishes and keeps a link with the EUT on the combined radio and through the communication antenna 2.

In those cases where the power level received from the measurement antenna is too low and the links need to be balanced, an additional DRE is needed. This additional element would receive the UL 1 signal from a dedicated port in the emulator 1 and would forward the balanced DL 1 signal to another dedicated port in the emulator 1. The UL and DL signals would be received or forwarded from or to the RF Relay Switch respectively. This improvement can be also applied to the combined radio.

#### Operational configuration – Laboratory 2

Figure 17 illustrates the operational configuration employed by the Laboratory 2 for this test setup. The use of the spectrum analyzer in this test setup is optional.

Figure 17 : ST_RPT_RX_003 – Laboratory 2

#### Operational configuration – Laboratory 3

Figure 18 illustrates the operational configuration employed by the Laboratory 3 for this test setup:

Figure 18 : ST_RPT_RX_003 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_RPT_RX_003 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Full anechoic chamber | Full anechoic chamber | Full anechoic chamber |
| Measurement system | Emulator | Emulator and PSA | Emulator and PSA |
| Measurement antenna | Horn antenna | Horn antenna | Horn antenna |
| Communication antennae | Conical antennae | Conical antennae | Log periodic antenna |
| Qualified equipment of radio being tested | Emulator (signaling unit) | Emulator (signaling unit) | Emulator (signaling unit) |
| Qualified equipment of combined radio | Emulator (signaling unit) | Emulator (signaling unit) | Emulator (signaling unit) |
| EUT controller | Control PC | Control PC | Control PC |
| Positioning system | Combined-axis positioning system | Combined-axis positioning system | Combined-axis positioning system |
| Additional elements | RF Relay switch | RF Relay switch Spectrum analyzer | RF Relay switch Spectrum analyzer |

Table 11: Comparison matrix for ST_RPT_RX_003

# Over the Air (OTA)

This test category groups all test scenarios related to those mechanisms for controlling the device over the air and related to those real-life environment test scenarios outside of an anechoic chamber.

# Conformance (CON)

Conformance testing is the act of determining to what extent a single implementation conforms to the individual requirements of a common set of technical parameters for a given technology, whether written in a technical specification or formalised as a standard.

In this test category, WALTER verifies whether the broadband device parameters or behaviours are compliant to specific standards. There are three sub-areas (identified in [1]) in this section, PHY, MAC and UPP (upper layers).

## PHY

This sub-category specifically deals with those test scenarios intended to measure physical layer aspects such as spectrum and power characteristics, digital error rates, constellation errors, and so on.

### ST_CON_PHY_001

This setup covers the following PHY test scenarios using a conducted test method:

TSID_CON_PHY_004 Floor Bit Error Rate / Packet Error Rate

TSID_CON_PHY_008 Receiver Sensitivity

#### WiMedia UWB Operational configuration – Laboratory 1

Figure 19 illustrates the operational configuration employed by the Laboratory 1 for WiMedia™ UWB (Ultra-Wide Band) devices. This setup covers the TSID_CON_PHY_004 test scenario only because there is no receiver sensitivity test scenario in the WiMedia specifications.

Figure 19 : ST_CON_PHY_001 (WiMedia UWB) – Laboratory 1

The Qualified Equipment (QE) is connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector). The QE is a well known reference unit capable of measuring the Bit Error Rate (BER) of the packets received from the EUT.

The variable attenuator is used to set a certain power level at the QE’s input port.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and QE’s ports.

#### WiMedia UWB Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### WiMedia UWB Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Not specified |
| Measurement system | Qualified equipment | Qualified equipment | Qualified equipment |
| Setup controller | Control PC | Control PC | Control PC |
| Variable attenuator | Yes | Yes | Yes |
| EUT controller | Control PC | Control PC | Control PC |

Table 12: Comparison matrix for ST_CON_PHY_001 (WiMedia UWB)

#### WiMAX Operational configuration – Laboratory 1

Figure 20 illustrates the operational configuration employed by the Laboratory 1 for WiMAX™ devices. This setup covers the TSID_CON_PHY_008 test scenario only because the TSID_CON_PHY_004 test scenario is not defined in the WiMAX specifications.

Figure 20 : ST_CON_PHY_001 (WiMAX) – Laboratory 1

The RCT (Radio Conformance Testing) Automatic Tester is connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector). The Automatic Tester is composed of a set of test equipments in a rack and is capable of measuring the EUT’s receiver sensitivity. The Control PC contains the necessary software and interfaces to control all features in the Automatic Tester.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and tester’s ports.

#### WiMAX Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### WiMAX Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Measurement system | RCT Automatic tester | RCT Automatic tester | N/A |
| Setup controller | Control PC | Control PC | N/A |
| EUT controller | Control PC | Control PC | N/A |

Table 13: Comparison matrix for ST_CON_PHY_001 (WiMAX)

#### Bluetooth Operational configuration – Laboratory 1

Figure 21 illustrates the operational configuration employed by the Laboratory 1 for Bluetooth® devices. This setup covers the two test scenarios included in ST_CON_PHY_001.

Figure 21 : ST_CON_PHY_001 (Bluetooth) – Laboratory 1

The RF Automatic Tester is connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector). The automatic tester is composed of a number of test equipment and allows the automatic execution of the tests covered by these scenarios without the presence of any other additional equipment.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and tester’s ports.

#### Bluetooth Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Bluetooth Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Measurement system | RF Automatic tester | RF Automatic tester | N/A |
| Setup controller | Control PC | Control PC | N/A |
| EUT controller | Control PC | Control PC | N/A |

Table 14: Comparison matrix for ST_CON_PHY_001 (Bluetooth)

### ST_CON_PHY_002

This test setup covers the PHY test scenarios listed next using a conducted test method:

TSID_CON_PHY_001 Spectral Mask

TSID_CON_PHY_002 Error Vector Magnitude

TSID_CON_PHY_003 Transmit Power Control

TSID_CON_PHY_005 Adjacent Channel Power Ratio

TSID_CON_PHY_006 Transmit Preamble

TSID_CON_PHY_007 Transmit Header

#### WiMedia UWB Operational configuration – Laboratory 1

Figure 22 illustrates the operational configuration employed by the Laboratory 1 for WiMedia UWB devices:

Figure 22 : ST_CON_PHY_002 (WiMedia UWB) – Laboratory 1

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and QE’s ports.

The Control PC contains all necessary software applications in order to control both the DSO and EUT. All relevant data is captured by the DSO and then transferred to the PC.

#### WiMedia UWB Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### WiMedia UWB Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Not specified |
| Measurement system | DSO | DSO | DSO |
| Setup controller | Control PC | Control PC | Control PC |
| EUT controller | Control PC | Control PC | Control PC |

Table 15: Comparison matrix for ST_CON_PHY_002 (WiMedia UWB)

#### WiMAX Operational configuration – Laboratory 1

This operational configuration is the same as the one used in ST_CON_PHY_001 for WiMAX devices (see Figure 20). It covers all the test scenarios identified in ST_CON_PHY_002 except for the TSID_CON_PHY_007 (which is not covered by the WiMAX specifications).

#### WiMAX Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### WiMAX Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Measurement system | RCT Automatic tester | RCT Automatic tester | N/A |
| Setup controller | Control PC | Control PC | N/A |
| EUT controller | Control PC | Control PC | N/A |

Table 16: Comparison matrix for ST_CON_PHY_002 (WiMAX)

#### Bluetooth Operational configuration – Laboratory 1

This operational configuration is the same as the one used in ST_CON_PHY_001 for Bluetooth devices (see Figure 21). It covers all the test scenarios identified in ST_CON_PHY_002 except for the TSID_CON_PHY_006 and TSID_CON_PHY_007 (which are not covered by the Bluetooth specifications).

#### Bluetooth Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Bluetooth Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_PHY_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Measurement system | RF Automatic tester | RF Automatic tester | N/A |
| Setup controller | Control PC | Control PC | N/A |
| EUT controller | Control PC | Control PC | N/A |

Table 17: Comparison matrix for ST_CON_PHY_002 (Bluetooth)

## MAC

This sub-category specifically deals with those test scenarios intended to measure MAC layer aspects (beaconing, bandwidth allocation, connection establishment, synchronization, security, etc.).

### ST_CON_MAC_001

This test setup covers the following test scenarios using a radiated configuration:

TSID_CON_MAC_001 Beacon Tests

TSID_CON_MAC_002 Reservation Tests

TSID_CON_MAC_003 Synchronization Tests

TSID_CON_MAC_004 Channel Selection Tests

TSID_CON_MAC_005 Fragmentation and Reassembly Tests

TSID_CON_MAC_006 Acknowledgement Tests

TSID_CON_MAC_007 Power Management Tests

TSID_CON_MAC_008 Security Tests

TSID_CON_MAC_009 Adjacent Channel Interference Tests

TSID_CON_MAC_010 PCA Tests

#### WiMedia UWB Operational configuration – Laboratory 1

Figure 23 illustrates the operational configuration employed by the Laboratory 1 for WiMedia devices. It covers the following test scenarios:

TSID_CON_MAC_001 Beacon Tests

TSID_CON_MAC_002 Reservation Tests

TSID_CON_MAC_003 Synchronization Tests

TSID_CON_MAC_007 Power Management Tests

TSID_CON_MAC_009 Adjacent Channel Interference Tests

TSID_CON_MAC_010 PCA Tests

Other test scenarios in ST_CON_MAC_001 are not included as they are not covered by the WiMedia specifications.

Figure 23 : ST_CON_MAC_001 (WiMedia UWB) – Laboratory 1

The test site employed is a semi-anechoic chamber with a conducting ground plane.

The Test System (TS) provides the necessary stimuli for the EUT and INTD (Interoperability Device) to show the behaviours to be analyzed. Its controller is a PC.

The protocol analyzer is capable of capturing and decoding over the air all MAC (Medium Access Control) frames present on the medium, including those from the TS, EUT and INTD. Its controller is a PC containing the necessary control software.

The EUT controller is any device capable of controlling the basic functions of the EUT in order to properly execute the tests (usually a PC). The controller used basically depends on the type of EUT being tested.

The INTD device is employed in order to establish and keep a communication link with the EUT. It is neither a signalling unit nor a reference device but a second device provided by EUT’s vendor.

The ACI (Adjacent Channel Interference) interferer is used for the ACI tests only and generates interference traffic in the channel adjacent to the channel under test.

#### WiMedia UWB Operational configuration – Laboratory 2

Figure 24 illustrates the operational configuration employed by the Laboratory 2 for WiMedia UWB devices:

Figure 24 : ST_CON_MAC_001 (WiMedia UWB) – Laboratory 2

#### WiMedia UWB Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_MAC_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Shielded chamber | Semi-anechoic chamber |
| Analyzer | Protocol analyzer | Protocol analyzer | Protocol analyzer |
| Test system | Tx-only and Tx-Rx | Tx-only and Tx-Rx | Tx-only and Tx-Rx |
| IOP device | Yes | Yes | Yes |
| Setup controller | Control PC | Control PC | Control PC |
| EUT/IOP controller | PC | PC | PC |
| Analyzer controller | PC | PC | PC |
| ACI interferer | Traffic generator | Traffic generator | Traffic generator |

Table 18: Comparison matrix for ST_CON_MAC_001 (WiMedia UWB)

#### WiMAX Operational configuration – Laboratory 1

Figure 25 illustrates the operational configuration employed by the Laboratory 1 for WiMAX devices. It covers all test scenarios identified in ST_CON_MAC_001 except for the TSID_CON_MAC_001 as this scenario is not covered by the WiMAX specifications.

Figure 25 : ST_CON_MAC_001 (WiMAX) – Laboratory 1

The PCT (Protocol Conformance Testing) Automatic Tester is connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector). The Automatic Tester is composed of a set of test equipments in a rack and is providing the necessary stimuli to perform the tests and monitoring the EUT’s behaviour in all tests. The Control PC contains the necessary software and interfaces to control all features in the Automatic Tester.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and tester’s ports.

#### WiMAX Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### WiMAX Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_MAC_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Test system | PCT Automatic tester | PCT Automatic tester | N/A |
| IOP device | N/A | N/A | N/A |
| Setup controller | Control PC | Control PC | N/A |
| EUT/IOP controller | PC | PC | N/A |

Table 19: Comparison matrix for ST_CON_MAC_001 (WiMAX)

#### Bluetooth Operational configuration – Laboratory 1

Figure 26 illustrates the operational configuration employed by the Laboratory 1 for Bluetooth devices. It covers all test scenarios identified in ST_CON_MAC_001.

Figure 26 : ST_CON_MAC_001 (Bluetooth) – Laboratory 1

For some test cases, the Protocol Automatic Tester is connected to the EUT via a RF cable (de-attaching the antenna and connecting it to the antenna connector). Other test cases are performed using a radiated configuration. In all cases, a dedicated test interface is used.

The automatic tester is composed of a number of test equipment and allows the automatic execution of the tests covered by these scenarios without the presence of any other additional equipment.

For those test cases that require extreme temperature conditions, a climate chamber for the EUT is used.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and tester’s ports.

#### Bluetooth Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Bluetooth Operational configuration – Laboratory 3

Not implemented yet.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_CON_MAC_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | N/A |
| Test system | Protocol Automatic tester | Protocol Automatic tester | N/A |
| IOP device | N/A | N/A | N/A |
| EUT controller | PC | PC | N/A |
| Additional elements | Climate chamber Variable attenuator | Climate chamber Variable attenuator | N/A |

Table 20: Comparison matrix for ST_CON_MAC_001 (Bluetooth)

## UPP

This sub-category specifically deals with those test scenarios intended to check whether the EUT is compliant to any implemented protocol above the MAC layer.

### ST_CON_UPP_001

The test setup covers the following scenarios:

TSID_CON_UPP_001 Association

TSID_CON_UPP_002 Registration and Enrolment

TSID_CON_UPP_003 Bridge

#### Operational configuration – Laboratory 1

Not implemented yet.

#### Operational configuration – Laboratory 2

Not implemented yet.

#### Operational configuration – Laboratory 3

Not implemented yet.

# IOP (Interoperability)

This area groups those requirements that are needed to demonstrate the ability of two systems to interoperate using the same communication protocol. WALTER has identified IOP test scenarios for the following layers or protocols:

MAC

Internet Protocol (IP)

Application Interoperability (APP)

## MAC

WALTER has developed a number of test descriptions oriented to prove multi-vendor interoperability (IOP) among WiMedia platforms. Platforms are not required to have received certification in order to apply for these tests. The base concept behind these IOP tests is the “advanced interoperability testing”, which combines interoperability and conformance (CON), i.e. some CON requirements can be checked while simultaneously testing interoperability.

### ST_IOP_MAC_001

This test setup covers the TSID_IOP_MAC_001 Point-To-Point test scenario using a radiated test method.

#### Operational configuration – Laboratory 1

Figure 27 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 27 : ST_IOP_MAC_001 – Laboratory 1

It is built of 2 WiMedia devices and 1 analyzer. Some test cases need the creation of events or specific conditions. For those test cases a frame generator is used. The different devices may be placed anywhere relative to each other, but they shall have line of sight connections during test operation.

#### Operational configuration – Laboratory 2

Figure 28 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 28 : ST_IOP_MAC_001 – Laboratory 2

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 2.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_MAC_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Shielded chamber | Shielded chamber |
| Analyzer | Protocol analyzer | Protocol analyzer | Protocol analyzer |
| Generator | Traffic generator | Traffic generator | Traffic generator |
| Setup controller | Control PC | Control PC | Control PC |

Table 21: Comparison matrix for ST_IOP_MAC_001

### ST_IOP_MAC_002

This test setup covers the TSID_IOP_MAC_002 Mesh test scenario using a radiated test method.

#### Operational configuration – Laboratory 1

Figure 29 illustrates the operational configuration employed by the Laboratory 1 for this test setup.

It is built of N WiMedia devices and 1 analyzer. Some test cases need the creation of events or specific conditions. For those test cases a frame generator is used.

During IOP tests, the different devices may be placed anywhere relative to each other, but they shall have line of sight connections during test operation.

In order to find out which device or devices are behaving incorrectly this test should be run using all possible combinations of devices. Example: A, B, C and D fail the mesh test. All possible mesh combinations with 2 and 3 devices should be run in order to find out the reason why this test failed.

Figure 29 : ST_IOP_MAC_002 – Laboratory 1

#### Operational configuration – Laboratory 2

Figure 30 illustrates the operational configuration employed by the Laboratory 2 for this test setup.

Figure 30 : ST_IOP_MAC_002 – Laboratory 2

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 2.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_MAC_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Shielded chamber | Shielded chamber |
| Analyzer | Protocol analyzer | Protocol analyzer | Protocol analyzer |
| Generator | Traffic generator | Traffic generator | Traffic generator |
| Setup controller | Control PC | Control PC | Control PC |

Table 22: Comparison matrix for ST_IOP_MAC_002

### ST_IOP_MAC_003

This test setup covers the TSID_IOP_MAC_003 Channel Sharing test scenario using a radiated test method.

#### Operational configuration – Laboratory 1

Figure 31 illustrates the operational configuration employed by the Laboratory 1 for this test setup.

It is built of N pairs of WiMedia devices. Within each pair, the 2 devices must share the same application and must be able to demonstrate operation. These pairs are spaced approximately equally within a 5 meter diameter circular area. The devices shall have line of sight connections during test operation. Some test cases need the creation of events or specific conditions. For those test cases a frame generator is used.

Note: The IOP_MAC test scenarios are mainly intended to check interoperability in plugfest events. In those cases the anechoic chamber cannot be used and the test would take place in a normal office or conference room.

Figure 31 : ST_IOP_MAC_003 – Laboratory 1

#### Operational configuration – Laboratory 2

Figure 32 illustrates the operational configuration employed by the Laboratory 2 for this test setup.

Figure 32 : ST_IOP_MAC_003 – Laboratory 2

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 2, except for the chamber, a shielded chamber is used instead.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_MAC_003 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Office room | Shielded chamber |
| Analyzer | Protocol analyzer | Protocol analyzer | Protocol analyzer |
| Generator | Traffic generator | Traffic generator | Traffic generator |
| Setup controller | Control PC | Control PC | Control PC |

Table 23: Comparison matrix for ST_IOP_MAC_003

## Internet Protocol

This sub-category groups all test scenarios that are needed to demonstrate that two or more devices are able to communicate using IP.

### ST_IOP_IP_001

This test setup covers the following test scenarios using a radiated conducted configuration:

TSID_IOP_IP_001 Ping

TSID_IOP_IP_002 Data Transfer

#### Operational configuration – Laboratory 1

Figure 33 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 33 : ST_IOP_IP_001 – Laboratory 1

This test setup is employed for the ping and data transfer tests in the WiMAX MIOT (Mobile Interoperability Test) test spec only [5].

When the EUT is the Base Station (BS) the Mobile Station (MS) is a well known reference unit which the EUT exchange ping commands and data with and vice versa.

The dummy units are mobile stations that are connected to the BS when the EUT is the MS. No data communications is established between the BS and the dummy stations.

An IP performance tester acts over the EUT and the qualified equipments. This element shall be capable of generating IP traffic and measuring performance metrics such as packet error rate, throughput, etc.

The attenuators control the power level present at the different units.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

Figure 34 illustrates the operational configuration employed by the Laboratory 3 for this test setup:

Figure 34 : ST_IOP_IP_001 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_IP_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Shielded chamber |
| Reference units | Stations from an approved test bed | Stations from an approved test bed | Qualified equipment |
| IP performance tester | Software running on the EUT and other units | Software running on the EUT and other units | Software running on the EUT and other units |
| Setup controller | Control PC | Control PC | Control PC |
| Additional elements | Splitter/combiner Variable attenuators Termination loads | Splitter/combiner Variable attenuators Termination loads | Variable attenuators Splitter/combiner |

Table 24: Comparison matrix for ST_IOP_IP_001

### ST_IOP_IP_002

This test setup covers the following test scenarios using a radiated configuration:

TSID_IOP_IP_001 Ping

TSID_IOP_IP_002 Data Transfer

#### Operational configuration – Laboratory 1

Figure 35 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 35 : ST_IOP_IP_002 – Laboratory 1

This test setup is employed for the ping and data transfer tests in most of Wi-Fi® test plans [6].

The IP performance tester software acts on the Console, the EUT and the qualified equipments such as Stations (STA) and Access Points (AP). This element shall be capable of generating IP traffic and measuring performance metrics such as packet error rate, throughput, etc.

There are two networks; the Wi-Fi network (which is the network on which the EUT communicates with the QE) and the Test and Control Network (on which the Console transmit the different control commands to the different elements in order to properly configure the test).

The Authentication Server is used in cases where security is required to be enabled.

The sniffer captures all traffic present in the wireless medium to properly give a test verdict.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

Figure 36 illustrates the intended operational configuration employed by the Laboratory 1 for this test setup:

Figure 36 : ST_IOP_IP_002 – Laboratory 3

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_IP_002 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Semi-anechoic chamber | Semi-anechoic chamber | Full anechoic chamber |
| Reference units | Units from an approved test bed | Units from an approved test bed | Units from an approved test bed |
| IP performance tester | Software running on the EUT and other units | Software running on the EUT and other units | Software running on the EUT and other units |
| Setup controller | Control PC | Control PC | Control PC |
| Additional elements | Authentication servers Switches Sniffer | Authentication servers Switches Sniffer | Oscilloscope LNA Measurement Antenna PCs for the IP generators/receivers |

Table 25: Comparison matrix for ST_IOP_IP_002

## Application Interoperability (APP)

This sub-category groups all test scenarios that are needed to demonstrate that two or more devices are able to communicate using application protocols such like FTP (File Transfer Protocol), audio and video streaming, etc.

### ST_IOP_APP_001

This test setup covers the following test scenarios using a radiated test method:

TSID_IOP_APP_001 Usability

TSID_IOP_APP_002 Object Push

TSID_IOP_APP_003 Advanced Audio Distribution

TSID_IOP_APP_004 Video Distribution

#### Operational configuration – Laboratory 1

Figure 37 illustrates the operational configuration employed by the Laboratory 1 for this test setup. The sniffer captures all traffic exchanged between the EUT and the QE. This data is then analyzed in order to check the interoperability between the devices.

Figure 37 : ST_IOP_APP_001 – Laboratory 1

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

This operational configuration is the same as the one defined for ST_IOP_IP_002 in Figure 36. The software running on the PC performs the application testing.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_IOP_APP_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Full anechoic chamber |
| Reference units | Units from an approved test bed | Units from an approved test bed | Units from an approved test bed |
| Analyzer | Dongle sniffer | Dongle sniffer | Software running on the EUT and other units |
| Setup controller | Control PC | Control PC | Control PC |
| Additional elements | N/A | N/A | Oscilloscope LNA Measurement Antenna PCs for the IP generators/receivers |

Table 26: Comparison matrix for ST_IOP_APP_001

# Coexistence (COE)

This area covers those test scenarios that are needed to demonstrate co-existence of wide-band implementations and their co-existence with other wireless technologies.

Within this test category, there are two cases (identified in [2]): Case 1 deals with single radio standard devices and Case 2 deals with multiple radio standard devices.

The definition of tests and test setups for this test category has been planned for Phase 2 of the WALTER Project. The final COE test setups will be described in the second release of this deliverable. However, the Laboratory 2 has implemented a preliminary test setup for COE test scenarios in which the UWB devices act as interferers and the WiMAX devices act as victims (see Figure 38).

Figure 38 : Preliminary COE test setup

# Performance (PER)

This category is composed of those test scenarios that are related to the implementation’s performance and the commercial assurances quoted by a manufacturer for that implementation. The performance criteria may also be subject to contractual requirements placed upon the manufacturer by the end-user.

## Sensitivity versus Temperature (S-T)

This test sub-category aims to check the EUT’s receiver sensitivity in extreme temperature conditions.

### ST_PER_S-T_001

This test setup covers the following test scenarios:

TSID_PER_S-T_001 Extreme High

TSID_PER_S-T_002 Extreme Low

#### Operational configuration – Laboratory 1

Figure 39 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 39 : ST_PER_S-T_001 – Laboratory 1

The emulator establishes and keeps a loop-back communication link with the EUT and measures its BER. The variable attenuator is used to set a certain power level at the EUT’s input port. The EUT sensitivity is the power level value at its input port at which the measured BER reaches a limit value.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and other equipment’s ports.

The climate chamber as well as other equipment is externally monitored by the test operator.

#### Operational configuration – Laboratory 2

The Laboratory 2 employs the same test configuration as the one employed by the Laboratory 1.

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 1.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_PER_S-T_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Shielded chamber |
| Qualified equipment | Emulator | Emulator | Emulator |
| Temperature control | Climate chamber | Climate chamber | Climate chamber |
| Setup controller | Control PC | Control PC | Control PC |
| Additional elements | Variable attenuator | Variable attenuator | Variable attenuator |

Table 27: Comparison matrix for ST_PER_S-T_001

## Output Power versus Temperature (P-T)

This test sub-category aims to check the EUT’s output power in extreme temperature conditions.

### ST_PER_P-T_001

This test setup covers the following test scenarios:

TSID_PER_P-T_001 Extreme High

TSID_PER_P-T_002 Extreme Low

#### Operational configuration – Laboratory 1

Figure 40 illustrates the operational configuration employed by the Laboratory 1 for this test setup:

Figure 40 : ST_PER_P-T_001 – Laboratory 1

The emulator is used to establish a communication link with the EUT. When this equipment is not capable of measuring the output power of the EUT, a spectrum analyzer or a power meter is used.

The shielded chamber greatly reduces the presence of interfering signals at the EUT’s and other equipment’s ports.

The climate chamber as well as other equipment is externally monitored by the test operator.

#### Operational configuration – Laboratory 2

Figure 41 illustrates the operational configuration employed by the Laboratory 2 for this test setup:

Figure 41 : ST_PER_P-T_001 – Laboratory 2

#### Operational configuration – Laboratory 3

The Laboratory 3 employs the same test configuration as the one employed by the Laboratory 2.

#### Comparison matrix

The following table shows the elements used by each laboratory in this test setup:

| ST_PER_P-T_001 | Laboratory 1 | Laboratory 2 | Laboratory 3 |
| --- | --- | --- | --- |
| Chamber | Shielded chamber | Shielded chamber | Shielded chamber |
| Qualified equipment | Emulator | Emulator | Emulator |
| Temperature control | Climate chamber | Climate chamber | Climate chamber |
| Setup controller | Control PC | Control PC | Control PC |
| Additional elements | Variable attenuator Power splitter Spectrum analyzer Power meter | N/A | N/A |

Table 28: Comparison matrix for ST_PER_P-T_001

# References

WALTER Project (Wireless Alliances for Testing Experiment and Research), “D 4.5 WALTER Report on test bed architecture and specification v1.0”. March, 2009.

WALTER Project (Wireless Alliances for Testing Experiment and Research), “D 4.7 WALTER test categories v1.4”. February, 2009.

ETSI EN 302 065 v1.1.1, “Electromagnetic compatibility and Radio spectrum Matters (ERM); Ultra WideBand (UWB) technologies for communication purposes; Harmonized EN covering the essential requirements of article 3.2 of the R&TTE Directive”. European Standard Telecommunication Institute (ETSI), February, 2008.

WALTER Project (Wireless Alliances for Testing Experiment and Research), “D 4.8 WALTER testing scope v1.3”. February, 2009.

WiMAX Forum, “WiMAX Forum™ Mobile InterOperability Test (MIOT) Release 1.0 Approved Specification (Revision 2.2.0)”. March, 2008.

Wi-Fi Alliance, “Wi-Fi 802.11 with WPA2, WPA, and WEP System Interoperability Test Plan with ASD Test Engine for IEEE 802.11a, b, & g Devices (Version 1.7)”. July, 2008.

# Footnotes

WiMedia is a trademark of the WiMedia Alliance.

"WiMAX", "WiMAX Forum", "WiMAX Certified", "WiMAX Forum Certified", “Mobile WiMAX”, “Fixed WiMAX”, the WiMAX Forum Logo and the WiMAX Forum Certified Logo are trademarks or registered trademarks of the WiMAX Forum.

The Bluetooth word mark is owned by the Bluetooth SIG, Inc. Other trademarks and trade names are of those respective owners.

Wi-Fi®, Wi-Fi Alliance®, WMM®, the Wi-Fi logo, the Wi-Fi CERTIFIED logo, and the Wi-Fi ZONE logo are registered trademarks of the Wi-Fi Alliance; and Wi-Fi CERTIFIED™, Wi-Fi ZONE™, WPA™, WPA2™, Wi-Fi Protected Access™, Wi-Fi Multimedia™, Wi-Fi Protected Setup™, and the Wi-Fi Alliance logo are trademarks of the Wi-Fi Alliance.